TD <>

Final draft ETSI ES 201 873-6 V3.3.1 (2008-01)

ETSI Standard

Methods for Testing and Specification (MTS);

The Testing and Test Control Notation version 3;

Part 6: TTCN-3 Control Interfaces (TCI)

Reference

RES/MTS-00090-6[3] ttcn3 tci

Keywords

control, interface, methodology, MTS, TCI, testing, TTCN

ETSI

650 Route des Lucioles

F-06921 Sophia Antipolis Cedex - FRANCE

Tel.: +33 4 92 94 42 00   Fax: +33 4 93 65 47 16

Siret N° 348 623 562 00017 - NAF 742 C

Association à but non lucratif enregistrée à la

Sous-Préfecture de Grasse (06) N° 7803/88

Important notice

Individual copies of the present document can be downloaded from:
http://www.etsi.org

The present document may be made available in more than one electronic version or in print. In any case of existing or perceived difference in contents between such versions, the reference version is the Portable Document Format (PDF). In case of dispute, the reference shall be the printing on ETSI printers of the PDF version kept on a specific network drive within ETSI Secretariat.

Users of the present document should be aware that the document may be subject to revision or change of status. Information on the current status of this and other ETSI documents is available at http://portal.etsi.org/tb/status/status.asp

If you find errors in the present document, please send your comment to one of the following services:
http://portal.etsi.org/chaircor/ETSI_support.asp

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© European Telecommunications Standards Institute 2008.

All rights reserved.

DECTTM, PLUGTESTSTM, UMTSTM, TIPHONTM, the TIPHON logo and the ETSI logo are Trade Marks of ETSI registered for the benefit of its Members.
3GPPTM is a Trade Mark of ETSI registered for the benefit of its Members and of the 3GPP Organizational Partners.

# Contents

Intellectual Property Rights	12

Foreword	12

1	Scope	13

2	References	13

2.1	Normative references	13

2.2	Informative references	14

3	Definitions and abbreviations	14

3.1	Definitions	14

3.2	Abbreviations	15

4	Introduction	15

5	Compliance	16

6	General structure of a TTCN-3 test system	16

6.1	Entities in a TTCN-3 test system	16

6.1.1	Test Management and Control (TMC)	18

6.1.1.1	Test Management (TM)	18

6.1.1.2	Coding and Decoding (CD)	18

6.1.1.3	Component Handling (CH)	18

6.1.1.4	Test Logging (TL)	20

6.1.2	TTCN-3 Executable (TE)	20

6.1.3	SUT Adaptor (SA)	20

6.1.4 	Platform Adaptor (PA)	20

6.2	Execution requirements for a TTCN-3 test system	20

7	TTCN-3 control interface and operations	20

7.1	Overview of the TCI	20

7.1.1	Correlation between TTCN-3 and TCI operation invocations	21

7.2	TCI data	22

7.2.1	General abstract data types	22

7.2.1.1	Management	22

7.2.1.2	Communication	23

7.2.2	Abstract TTCN-3 data types and values	23

7.2.2.1	Abstract TTCN-3 data types	24

7.2.2.2	Abstract TTCN-3 values	25

7.2.2.2.1	The abstract data type Value	26

7.2.2.2.2	The abstract data type IntegerValue	26

7.2.2.2.3	The abstract data type FloatValue	26

7.2.2.2.4	The abstract data type BooleanValue	26

7.2.2.2.5	The abstract data type ObjidValue	26

7.2.2.2.6	The abstract data type CharstringValue	27

7.2.2.2.7	The abstract data type UniversalCharstringValue	27

7.2.2.2.8	The abstract data type BitstringValue	28

7.2.2.2.9	The abstract data type OctetstringValue	28

7.2.2.2.10	The abstract data type HexstringValue	29

7.2.2.2.11	The abstract data type RecordValue	29

7.2.2.2.12	The abstract data type RecordOfValue	30

7.2.2.2.13	The abstract data type UnionValue	30

7.2.2.2.14	The abstract data type EnumeratedValue	31

7.2.2.2.15	The abstract data type VerdictValue	31

7.2.2.2.16	The abstract data type AddressValue	31

7.2.3	Abstract logging types	32

7.2.3.1	The abstract data type TciValueTemplate	32

7.2.3.2	The abstract data type TciNonValueTemplate	32

7.2.3.3	The Value List and Mismatch Types	32

7.2.3.4	The Status Types	33

7.3	TCI operations	33

7.3.1	The TCI-TM interface	34

7.3.1.1	TCI-TM required	34

7.3.1.1.1	tciRootModule	34

7.3.1.1.2	tciGetImportedModules	35

7.3.1.1.3	tciGetModuleParameters	35

7.3.1.1.4	tciGetTestCases	35

7.3.1.1.5	tciGetTestCaseParameters	35

7.3.1.1.6	tciGetTestCaseTSI	35

7.3.1.1.7	tciStartTestCase	36

7.3.1.1.8	tciStopTestCase	36

7.3.1.1.9	tciStartControl	36

7.3.1.1.10	tciStopControl	36

7.3.1.2	TCI-TM provided	36

7.3.1.2.1	tciTestCaseStarted	37

7.3.1.2.2	tciTestCaseTerminated	37

7.3.1.2.3	tciControlTerminated	37

7.3.1.2.4	tciGetModulePar	37

7.3.1.2.5	tciError	38

7.3.2	The TCI-CD interface	38

7.3.2.1	TCI-CD required	38

7.3.2.1.1	getTypeForName	39

7.3.2.1.2	getInteger	39

7.3.2.1.3	getFloat	39

7.3.2.1.4	getBoolean	39

7.3.2.1.5	getObjid	39

7.3.2.1.6	getCharstring	39

7.3.2.1.7	getUniversalCharstring	40

7.3.2.1.8	getHexstring	40

7.3.2.1.9	getBitstring	40

7.3.2.1.10	getOctetstring	40

7.3.2.1.11	getVerdict	40

7.3.2.1.12	tciErrorReq	40

7.3.2.2	TCI-CD provided	40

7.3.2.2.1	decode	41

7.3.2.2.2	encode	41

7.3.3	The TCI-CH interface	41

7.3.3.1	TCI-CH required	42

7.3.3.1.1	tciEnqueueMsgConnected	42

7.3.3.1.2	tciEnqueueCallConnected	42

7.3.3.1.3	tciEnqueueReplyConnected	43

7.3.3.1.4	tciEnqueueRaiseConnected	43

7.3.3.1.5	tciCreateTestComponent	43

7.3.3.1.6	tciStartTestComponent	44

7.3.3.1.7	tciStopTestComponent	44

7.3.3.1.8	tciConnect	44

7.3.3.1.9	tciDisconnect	44

7.3.3.1.10	tciMap	45

7.3.3.1.11	tciUnmap	45

7.3.3.1.12	tciTestComponentTerminated	45

7.3.3.1.13	tciTestComponentRunning	45

7.3.3.1.14	tciTestComponentDone	45

7.3.3.1.15	tciGetMTC	46

7.3.3.1.16	tciExecuteTestCase	46

7.3.3.1.17	tciReset	46

7.3.3.1.18	tciKillTestComponent	46

7.3.3.1.19	tciTestComponentAlive	46

7.3.3.1.20	tciTestComponentKilled	47

7.3.3.2	TCI-CH provided	47

7.3.3.2.1	tciSendConnected	47

7.3.3.2.2	tciSendConnectedBC	47

7.3.3.2.3	tciSendConnectedMC	47

7.3.3.2.4	tciCallConnected	48

7.3.3.2.5	tciCallConnectedBC	48

7.3.3.2.6	tciCallConnectedMC	49

7.3.3.2.7	tciReplyConnected	49

7.3.3.2.8	tciReplyConnectedBC	50

7.3.3.2.9	tciReplyConnectedMC	50

7.3.3.2.10	tciRaiseConnected	51

7.3.3.2.11	tciRaiseConnectedBC	51

7.3.3.2.12	tciRaiseConnectedMC	51

7.3.3.2.13	tciCreateTestComponentReq	52

7.3.3.2.14	tciStartTestComponentReq	52

7.3.3.2.15	tciStopTestComponentReq	52

7.3.3.2.16	tciConnectReq	52

7.3.3.2.17	tciDisconnectReq	53

7.3.3.2.18	tciMapReq	53

7.3.3.2.19	tciUnmapReq	53

7.3.3.2.20	tciTestComponentTerminatedReq	53

7.3.3.2.21	tciTestComponentRunningReq	53

7.3.3.2.22	tciTestComponentDoneReq	54

7.3.3.2.23	tciGetMTCReq	54

7.3.3.2.24	tciExecuteTestCaseReq	54

7.3.3.2.25	tciResetReq	54

7.3.3.2.26	tciKillTestComponentReq	54

7.3.3.2.27	tciTestComponentAliveReq	55

7.3.3.2.28	tciTestComponentKilledReq	55

7.3.4	The TCI-TL interface	55

7.3.4.1	TCI-TL provided	55

7.3.4.1.1	tliTcExecute	56

7.3.4.1.2	tliTcStart	56

7.3.4.1.3	tliTcStop	56

7.3.4.1.4	tliTcStarted	57

7.3.4.1.5	tliTcTerminated	57

7.3.4.1.6	tliCtrlStart	57

7.3.4.1.7	tliCtrlStop	58

7.3.4.1.8	tliCtrlTerminated	58

7.3.4.1.9	tliMSend_m	58

7.3.4.1.10	tliMSend_m_BC	59

7.3.4.1.11	tliMSend_m_MC	59

7.3.4.1.12	tliMSend_c	60

7.3.4.1.13	tliMSend_c_BC	60

7.3.4.1.14	tliMSend_c_MC	60

7.3.4.1.15	tliMDetected_m	61

7.3.4.1.16	tliMDetected_c	61

7.3.4.1.17	tliMMismatch_m	62

7.3.4.1.18	tliMMismatch_c	62

7.3.4.1.19	tliMReceive_m	63

7.3.4.1.20	tliMReceive_c	63

7.3.4.1.21	tliPrCall_m	64

7.3.4.1.22	tliPrCall_m_BC	64

7.3.4.1.23	tliPrCall_m_MC	65

7.3.4.1.24	tliPrCall_c	65

7.3.4.1.25	tliPrCall_c_BC	66

7.3.4.1.26	tliPrCall_c_MC	66

7.3.4.1.27	tliPrGetCallDetected_m	67

7.3.4.1.28	tliPrGetCallDetected_c	67

7.3.4.1.29	tliPrGetCallMismatch_m	68

7.3.4.1.30	tliPrGetCallMismatch_c	68

7.3.4.1.31	tliPrGetCall_m	69

7.3.4.1.32	tliPrGetCall_c	69

7.3.4.1.33	tliPrReply_m	70

7.3.4.1.34	tliPrReply_m_BC	70

7.3.4.1.35	tliPrReply_m_MC	71

7.3.4.1.36	tliPrReply_c	71

7.3.4.1.37	tliPrReply_c_BC	72

7.3.4.1.38	tliPrReply_c_MC	72

7.3.4.1.39	tliPrGetReplyDetected_m	73

7.3.4.1.40	tliPrGetReplyDetected_c	73

7.3.4.1.41	tliPrGetReplyMismatch_m	74

7.3.4.1.42	tliPrGetReplyMismatch_c	74

7.3.4.1.43	tliPrGetReply_m	75

7.3.4.1.44	tliPrGetReply_c	75

7.3.4.1.45	tliPrRaise_m	76

7.3.4.1.46	tliPrRaise_m_BC	76

7.3.4.1.47	tliPrRaise_m_MC	77

7.3.4.1.48	tliPrRaise_c	77

7.3.4.1.49	tliPrRaise_c_BC	78

7.3.4.1.50	tliPrRaise_c_MC	78

7.3.4.1.51	tliPrCatchDetected_m	79

7.3.4.1.52	tliPrCatchDetected_c	79

7.3.4.1.53	tliPrCatchMismatch_m	80

7.3.4.1.54	tliPrCatchMismatch_c	80

7.3.4.1.55	tliPrCatch m	81

7.3.4.1.56	tliPrCatch c	81

7.3.4.1.57	tliPrCatchTimeoutDetected	82

7.3.4.1.58	tliPrCatchTimeout	82

7.3.4.1.59	tliCCreate	82

7.3.4.1.60	tliCStart	83

7.3.4.1.61	tliCRunning	83

7.3.4.1.62	tliCAlive	83

7.3.4.1.63	tliCStop	84

7.3.4.1.64	tliCKill	84

7.3.4.1.65	tliCDoneMismatch	84

7.3.4.1.66	tliCDone	85

7.3.4.1.67	tliCKilledMismatch	85

7.3.4.1.68	tliCKilled	85

7.3.4.1.69	tliCTerminated	86

7.3.4.1.70	tliPConnect	86

7.3.4.1.71	tliPDisconnect	86

7.3.4.1.72	tliPMap	87

7.3.4.1.73	tliPUnmap	87

7.3.4.1.74	tliPClear	87

7.3.4.1.75	tliPStart	88

7.3.4.1.76	tliPStop	88

7.3.4.1.77	tliPHalt	88

7.3.4.1.78	tliEncode	89

7.3.4.1.79	tliDecode	89

7.3.4.1.80	tliTTimeoutDetected	89

7.3.4.1.81	tliTTimeoutMismatch	90

7.3.4.1.82	tliTTimeout	90

7.3.4.1.83	tliTStart	90

7.3.4.1.84	tliTStop	91

7.3.4.1.85	tliTRead	91

7.3.4.1.86	tliTRunning	91

7.3.4.1.87	tliSEnter	92

7.3.4.1.88	tliSLeave	92

7.3.4.1.89	tliVar	92

7.3.4.1.90	tliModulePar	93

7.3.4.1.91	tliGetVerdict	93

7.3.4.1.92	tliSetVerdict	93

7.3.4.1.93	tliLog	94

7.3.4.1.94	tliAEnter	94

7.3.4.1.95	tliALeave	94

7.3.4.1.96	tliANomatch	94

7.3.4.1.97	tliARepeat	95

7.3.4.1.98	tliADefaults	95

7.3.4.1.99	tliAActivate	95

7.3.4.1.100	tliADeactivate	96

7.3.4.1.101	tliAWait	96

7.3.4.1.102	tliAction	96

7.3.4.1.103	tliMatch	96

7.3.4.1.104	tliMatchMismatch	97

7.3.4.1.105	tliInfo	97

8	Java language mapping	97

8.1	Introduction	97

8.2	Names and scopes	98

8.2.1	Names	98

8.2.2	Scopes	98

8.2.2.1	TciParameterType	99

8.2.2.2	TciParameterPassingModeType	99

8.2.2.3	TciParameterListType	100

8.2.2.4	TciTypeClassType	100

8.2.2.5	TciTestComponentKindType	101

8.2.2.6	TciBehaviourIdType	101

8.2.2.7	TciTestCaseIdType	101

8.2.2.8	TciModuleIdType	101

8.2.2.9	TciModuleParameterIdType	101

8.2.2.10	TciModuleParameterListType	101

8.2.2.11	TciModuleParameterType	102

8.2.2.12	TciParameterTypeListType	102

8.2.2.13	TciModuleIdListType	102

8.2.3	Abstract type mapping	103

8.2.3.1	Type	103

8.2.4	Abstract value mapping	103

8.2.4.1	Value	104

8.2.4.2	IntegerValue	104

8.2.4.3	FloatValue	104

8.2.4.4	BooleanValue	105

8.2.4.5	ObjidValue	105

8.2.4.6	TciObjId	105

8.2.4.7	TciObjIdElement	105

8.2.4.8	CharstringValue	106

8.2.4.9	BitstringValue	106

8.2.4.10	OctetstringValue	107

8.2.4.11	UniversalCharstringValue	108

8.2.4.12	HexstringValue	108

8.2.4.13	RecordValue	109

8.2.4.14	RecordOfValue	110

8.2.4.15	UnionValue	110

8.2.4.16	EnumeratedValue	111

8.2.4.17	VerdictValue	111

8.2.4.18	AddressValue	112

8.2.5	Abstract logging types mapping	112

8.2.5.1	TciValueTemplate	112

8.2.5.2	TciNonValueTemplate	112

8.2.5.3	TciValueList	113

8.2.5.4	TciValueDifference	113

8.2.5.5	TciValueDifferenceList	113

8.3	Constants	114

8.4	Mapping of interfaces	115

8.4.1	The TCI-TM interface	115

8.4.1.1	TCI-TM provided	115

8.4.1.2	TCI-TM required	115

8.4.2	The TCI-CD interface	116

8.4.2.1	TCI-CD provided	116

8.4.2.2	TCI-CD required	116

8.4.3	The TCI-CH interface	116

8.4.3.1	TCI-CH provided	116

8.4.3.2	TCI-CH required	117

8.4.4	The TCI-TL interface	118

8.4.4.1	TCI-TL provided	118

8.5	Optional parameters	122

8.6	TCI initialization	122

8.7	Error handling	122

9	ANSI C language mapping	122

9.1	Introduction	122

9.2	Value interfaces	122

9.3	Logging interface	126

9.4	Operation interfaces	126

9.4.1	The TCI-TM interface	126

9.4.1.1	TCI-TM provided	126

9.4.1.2	TCI-TM required	127

9.4.2	The TCI-CD interface	127

9.4.2.1	TCI-CD provided	127

9.4.2.2	TCI-CD required	127

9.4.3	The TCI-CH interface	127

9.4.3.1	TCI-CH provided	127

9.4.3.2	TCI-CH required	128

9.4.4	The TCI-TL interface	128

9.4.4.1	TCI-TL provided	128

9.5	Data	133

9.6	Miscellaneous	134

10	W3C XML mapping	135

10.1	Introduction	135

10.2	Scopes	135

10.3	Type mapping	135

10.3.1	Mapping of simple types	135

10.3.1.1	TBoolean	135

10.3.1.2	TString	135

10.3.1.3	TInteger	135

10.3.1.4	TriTimerDurationType	135

10.3.1.5	TciParameterPassingModeType	135

10.3.1.6	TriStatusType	136

10.3.1.7	TciStatusType	136

10.3.1.8	ComponentStatusType	136

10.3.1.9	TimerStatusType	136

10.3.1.10	PortStatusType	136

10.3.2	Complex type mapping	136

10.3.2.1	TriPortIdType	136

10.3.2.2	TriComponentIdType	136

10.3.2.3	TriComponentIdListType	137

10.3.2.4	Port	137

10.3.2.5	Id	137

10.3.2.6	TriMessageType	138

10.3.2.7	TriParameterType	138

10.3.2.8	TriParameterListType	138

10.3.2.9	TriAddressType	139

10.3.2.10	TriAddressListType	139

10.3.2.11	TriExceptionType	139

10.3.2.12	TriSignatureIdType	139

10.3.2.13	TriTimerIdType	140

10.3.2.14	TriTimerDurationType	140

10.3.2.15	QualifiedName	140

10.3.2.16	TciBehaviourIdType	140

10.3.2.17	TciTestCaseIdType	141

10.3.2.18	TciParameterType	141

10.3.2.19	TciParameterListType	141

10.3.3	Abstract value mapping	141

10.3.3.1	Value	141

10.3.3.2	IntegerValue	143

10.3.3.3	FloatValue	143

10.3.3.4	BooleanValue	143

10.3.3.5	ObjidValue	144

10.3.3.6	VerdictValue	144

10.3.3.7	BitstringValue	145

10.3.3.8	HexstringValue	145

10.3.3.9	OctetstringValue	145

10.3.3.10	CharstringValue	146

10.3.3.11	UniversalCharstringValue	146

10.3.3.12	RecordValue	146

10.3.3.13	RecordOfValue	148

10.3.3.14	SetValue	149

10.3.3.15	SetOfValue	150

10.3.3.16	EnumeratedValue	151

10.3.3.17	UnionValue	152

10.3.3.18	AnytypeValue	153

10.3.3.19	AddressValue	154

10.3.4	Abstract logging types mapping	155

10.3.4.1	TciValueTemplate	155

10.3.4.2	TciNonValueTemplate	156

10.3.4.3	TciValueList	157

10.3.4.4	TciValueDifference	157

10.3.4.5	TciValueDifferenceList	157

10.4	Mapping of the operations on the logging interface	157

10.4.1	Event	158

10.4.2	The TCI-TL interface	158

10.4.2.1	TCI-TL provided	158

11	Use scenarios	176

11.1	Initialization, collecting information, logging	177

11.1.1	Use scenario: initialization	177

11.1.1.1	Sequence diagram	177

11.1.1.2	TTCN-3 fragment	177

11.1.2	Use scenario: requesting module parameters	177

11.1.2.1	Sequence diagram	178

11.1.2.2	TTCN-3 fragment	178

11.1.3	Use scenario: logging	178

11.1.3.1	Sequence diagram	179

11.1.3.2	TTCN-3 fragment	179

11.2	Execution of test cases and control	179

11.2.1	Use scenario: execution of control	179

11.2.1.1	Sequence diagram	179

11.2.1.2	TTCN-3 fragment	180

11.2.2	Use scenario: test case execution within control	180

11.2.2.1	Sequence diagram	180

11.2.2.2	TTCN-3 fragment	180

11.2.3	Use scenario: direct test case execution	180

11.2.3.1	Sequence diagram	181

11.2.3.2	TTCN-3 fragment	181

11.2.4	Use scenario: execute test case to TRI	181

11.2.4.1	Sequence diagram	181

11.2.4.2	TTCN-3 fragment	182

11.3	Component handling	182

11.3.1	Use scenario: local control component creation	182

11.3.1.1	Sequence diagram	182

11.3.1.2	TTCN-3 fragment	183

11.3.2	Use scenario: remote control component creation	183

11.3.2.1	Sequence diagram	183

11.3.2.2	TTCN-3 fragment	183

11.3.3	Use scenario: local MTC creation	184

11.3.3.1	Sequence diagram	184

11.3.3.2	TTCN-3 fragment	184

11.3.4	Use scenario: remote MTC creation	184

11.3.4.1	Sequence diagram	185

11.3.4.2	TTCN-3 fragment	185

11.3.5	Use scenario: component handling for test case execution within control	185

11.3.5.1	Sequence diagram	186

11.3.5.2	TTCN-3 fragment	186

11.3.6	Use scenario: component handling for direct test case execution	187

11.3.6.1	Sequence diagram	187

11.3.6.2	TTCN-3 fragment	188

11.3.7	Use scenario: propagation of map/connect	188

11.3.7.1	Sequence diagram	188

11.3.7.2	TTCN-3 fragment	188

11.3.8	Use scenario: propagation of unmap/disconnect	189

11.3.8.1	Sequence diagram	189

11.3.8.2	TTCN-3 fragment	189

11.4	Termination of test cases and control	189

11.4.1	Use scenario: stop a test case	189

11.4.1.1	Sequence diagram	190

11.4.1.2	TTCN-3 fragment	190

11.4.2	Use scenario: stop control	190

11.4.2.1	Sequence diagram	191

11.4.2.2	TTCN-3 fragment	191

11.4.3	Use scenario: termination of control after error	191

11.4.3.1	Sequence diagram	192

11.4.3.2	TTCN-3 fragment	192

11.4.4	Use scenario: termination of a test case after error	192

11.4.4.1	Sequence diagram	193

11.4.4.2	TTCN-3 fragment	194

11.4.5	Use scenario: reset	194

11.4.5.1	Sequence diagram	194

11.4.5.2	TTCN-3 fragment	194

11.5	Communication	194

11.5.1	Use scenario: local intercomponent communication	194

11.5.1.1	Sequence diagram	195

11.5.1.2	TTCN-3 fragment	195

11.5.2	Use scenario: internode communication between test components	195

11.5.2.1	Sequence diagram	196

11.5.2.2	TTCN-3 fragment	196

11.5.3	Use scenario: encoding	196

11.5.3.1	Sequence diagram	197

11.5.3.2	TTCN-3 fragment	197

11.5.4	Use scenario: decoding	197

11.5.4.1	Sequence diagram	198

11.5.4.2	TTCN-3 fragment	198

Annex A (normative):	IDL Specification of TCI	199

Annex B (normative):	XML Mapping for TCI TL Provided	215

B.1	TCI-TL XML Schema for Simple Types	215

B.2	TCI-TL XML Schema for Types	216

B.3	TCI-TL XML Schema for Values	218

B.4	TCI-TL XML Schema for Templates	223

B.5	TCI-TL XML Schema for Events	229

B.6	TCI-TL XML Schema for a Log	248

Annex C (informative):	Bibliography	252

History	253

# Intellectual Property Rights

IPRs essential or potentially essential to the present document may have been declared to ETSI. The information pertaining to these essential IPRs, if any, is publicly available for ETSI members and non-members, and can be found in ETSI SR 000 314: "Intellectual Property Rights (IPRs); Essential, or potentially Essential, IPRs notified to ETSI in respect of ETSI standards", which is available from the ETSI Secretariat. Latest updates are available on the ETSI Web server (http://webapp.etsi.org/IPR/home.asp).

Pursuant to the ETSI IPR Policy, no investigation, including IPR searches, has been carried out by ETSI. No guarantee can be given as to the existence of other IPRs not referenced in ETSI SR 000 314 (or the updates on the ETSI Web server) which are, or may be, or may become, essential to the present document.

# Foreword

This ETSI Standard (ES) has been produced by ETSI Technical Committee Methods for Testing and
Specification (MTS), and is now submitted for the ETSI standards Membership Approval Procedure.

The present document is part 6 of a multi-part deliverable. Full details of the entire series can be found in part 1 [1].

# 1	Scope

# 2	References

# 3	Definitions and abbreviations

# 4	Introduction

# 5	Compliance

# 6	General structure of a TTCN-3 test system

# 7	TTCN-3 control interface and operations

This clause defines a set of abstract data types used to represent data communicated between the TE and the TMC. In addition, it defines TCI operations in terms of their signatures, when they are to be used and what their effects on the TTCN-3 test system are.

This definition also includes a more detailed description of the input parameters required for each TCI operation call and its return value.

## 7.1	Overview of the TCI

## 7.2	TCI data

## 7.3	TCI operations

### 7.3.4	The TCI-TL interface

#### 7.3.4.1	TCI-TL provided

This clause specifies the operations the TL shall provide to the TE.

##### 7.3.4.1.91	tliGetVerdict

| Signature | void tliGetVerdict(in TString am, in TInteger ts, in TString src, in TInteger line, in TriComponentIdType c, in VerdictValue verdict) |
| --- | --- |
| In Parameters | am | An additional message. |
|  | ts | The time when the event is produced. |
|  | src | The source file of the test specification. |
|  | line | The line number where the request is performed. |
|  | c | The component which produces this event. |
|  | verdict | The current value of the local verdict. |
| Return Value | void |
| Constraint | Shall be called by TE to log the getverdict operation. This event occurs after the getverdict operation. |
| Effect | The TL presents all the information provided in the parameters of this operation to the user, how this is done is not within the scope of the present document. |

##### 7.3.4.1.92	tliSetVerdict

| Signature | void tliSetVerdict(in TString am, in TInteger ts, in TString src, in TInteger line, in TriComponentIdType c, in VerdictValue verdict, in TString reason) |
| --- | --- |
| In Parameters | am | An additional message. |
|  | ts | The time when the event is produced. |
|  | src | The source file of the test specification. |
|  | line | The line number where the request is performed. |
|  | c | The component which produces this event. |
|  | verdict | The value to be set to the local verdict. |
|  | reason | The optional reason of the setverdict statement |
| Return Value | void |
| Constraint | Shall be called by TE to log the setverdict operation. This event occurs after the setverdict operation. |
| Effect | The TL presents all the information provided in the parameters of this operation to the user, how this is done is not within the scope of the present document. |

##### 7.3.4.1.93	tliLog

| Signature | void tliLog (in TString am, in TInteger ts, in TString src, in TInteger line, in TriComponentIdType c, in TString log) |
| --- | --- |
| In Parameters | am | An additional message. |
|  | ts | The time when the event is produced. |
|  | src | The source file of the test specification. |
|  | line | The line number where the request is performed. |
|  | c | The component which produces this event. |
|  | log | The string to be logged. |
| Return Value | void |
| Constraint | Shall be called by TM or TE to log the TTCN-3 statement log. This event occurs after the TTCN-3 log operation. |
| Effect | The TL presents all the information provided in the parameters of this operation to the user, how this is done is not within the scope of the present document. |

##### 7.3.4.1.94	tliAEnter

| Signature | void tliAEnter(in TString am, in TInteger ts, in TString src, in TInteger line, in TriComponentIdType c) |
| --- | --- |
| In Parameters | am | An additional message. |
|  | ts | The time when the event is produced. |
|  | src | The source file of the test specification. |
|  | line | The line number where the request is performed. |
|  | c | The component which produces this event. |
| Return Value | void |
| Constraint | Shall be called by TE to log entering an alt. This event occurs after an alt has been entered. |
| Effect | The TL presents all the information provided in the parameters of this operation to the user, how this is done is not within the scope of the present document. |

# 8	Java language mapping

## 8.1	Introduction

This clause introduces the TCI Java language mapping. For efficiency reasons a dedicated language mapping is introduced instead of using the OMG IDL to Java language.

The Java language mapping for the TTCN-3 Control Interface defines how the IDL definitions described in clause 7 are mapped to the Java language. The language mapping is independent of the used Java version as only basic Java language constructs are used.

## 8.2	Names and scopes

## 8.3	Constants

## 8.4	Mapping of interfaces

}

### 8.4.4	The TCI-TL interface

#### 8.4.4.1	TCI-TL provided

public void tliGetVerdict(String am, int ts, String src, int line, TriComponentId c,

VerdictValue verdict);

public void tliSetVerdict(String am, int ts, String src, int line, TriComponentId c,

VerdictValue verdict, String reason);

public void tliLog(String am, int ts, String src, int line, TriComponentId c,

TString log);

## 8.5	Optional parameters

# 9	ANSI C language mapping

## 9.1	Introduction

This clause defines the TRI ANSI-C language mapping for the TCI data specified in clause 7.2 and for the TCI operations specified in clause 7.3.

## 9.2	Value interfaces

## 9.3	Logging interface

## 9.4	Operation interfaces

### 9.4.4	The TCI-TL interface

void tliGetVerdict(String am, int ts, String src, int line, TriComponentId c, VerdictValue verdict)

void tliSetVerdict

(String am, int ts, String src, int line, TriComponentId c, VerdictValue verdict, String reason)

void tliLog(String am, int ts, String src, int line, TriComponentId c, String log)

void tliAEnter(String am, int ts, String src, int line, TriComponentId c)

void tliALeave(String am, int ts, String src, int line, TriComponentId c)

void tliADefaults(String am, int ts, String src, int line, TriComponentId c)

void tliAActivate

(String am, int ts, String src, int line, TriComponentId c,QualifiedName name,

TciParameterListType tciPars, Value ref)

void tliADeactivate(String am, int ts, String src, int line, TriComponentId c, Value ref)

void tliANomatch(String am, int ts, String src, int line, TriComponentId c)

void tliARepeat(String am, int ts, String src, int line, TriComponentId c)

void tliAWait(String am, int ts, String src, int line, TriComponentId c)

void tliAction(String am, int ts, String src, int line, TriComponentId c, String action)

void tliMatch

(String am, int ts, String src, int line, TriComponentId c, Value expr, TciValueTemplate tmpl)

void tliMatchMismatch

(String am, int ts, String src, int line, TriComponentId c, Value expr, TciValueTemplate tmpl,

TciValueDifferenceList diffs);

void tliInfo

(String am, int ts, String src, int line, TriComponentId c, int level, String info)

## Data

## Miscellaneous

# 10	W3C XML mapping

## 10.1	Introduction

This clause introduces the TCI XML mapping [5], [6] and [7] for the logging interface of TCI. The XML mapping for the logging interface defines how the IDL definitions for TCI-TL described in clause 7 are mapped to XML. The complete schema definitions for this mapping are given in annex B.

## 10.2	Scopes

The IDL module tciInterface is mapped to an XML schema with the name space

## 10.4	Mapping of the operations on the logging interface

Every operation provided at the logging interface has a corresponding complex type definition in XML. These complex type definitions are extensions of Event.

### 10.4.1	Event

Event is mapped to the following complex type:

<!-- common definition for all events -->

<xsd:complexType name="Event" mixed="true">

<xsd:sequence>

<xsd:element name="am" type="SimpleTypes:TString"/>

</xsd:sequence>

<xsd:attribute name="ts" type="xsd:long" use="required"/>

<xsd:attribute name="src" type="SimpleTypes:TString" use="optional"/>

<xsd:attribute name="line" type="SimpleTypes:TInteger" use="optional"/>

<!-- general identifier structure for test components, ports and timer -->

<xsd:attribute name="name" type="SimpleTypes:TString" use="required"/>

<xsd:attribute name="id" type="SimpleTypes:TString " use="required"/>

<xsd:attribute name="type" type="SimpleTypes:TString" use="required"/>

</xsd:complexType>

Elements:

am	A message, to be used for further information in the log.

Attributes:

ts	The time when the event is produced.

src	The source file of the test specification.

line	The line number where the request is performed.

name	The name of the component which produces this event.

id	The id of the component which produces this event.

type	The type of the component which produces this event.

### 10.4.2	The TCI-TL interface

#### 10.4.2.1	TCI-TL provided

</xsd:complexType>

<!-- verdicts -->

<xsd:complexType name="tliGetVerdict">

<xsd:complexContent mixed="true">

<xsd:extension base="Events:Event">

<xsd:sequence>

<xsd:element name="verdict" type="Values:VerdictValue"/>

</xsd:sequence>

</xsd:extension>

</xsd:complexContent>

</xsd:complexType>

<xsd:complexType name="tliSetVerdict">

<xsd:complexContent mixed="true">

<xsd:extension base="Events:Event">

<xsd:sequence>

<xsd:element name="verdict" type="Values:VerdictValue"/>

<xsd:element name="reason" type="SimpleTypes:TString" minOccurs="0"/>

</xsd:sequence>

</xsd:extension>

</xsd:complexContent>

</xsd:complexType>

<!-- log -->

<xsd:complexType name="tliLog">

<xsd:complexContent mixed="true">

<xsd:extension base="Events:Event">

<xsd:sequence>

<xsd:element name="log" type="SimpleTypes:TString"/>

</xsd:sequence>

</xsd:extension>

</xsd:complexContent>

</xsd:complexType>

<!-- alt -->

# 11	Use scenarios

This clause contains use scenarios that should help users of the TCI and tool vendors providing the TCI understand the semantics of the operations defined within the present document.

The scenarios are defined in terms of UML sequence diagrams. The sequence diagram shows the interactions between the TCI entities. The scenarios are explained and where applicable underpinned with a TTCN-3 fragment corresponding to the scenario.

## 11.1	Initialization, collecting information, logging

Annex A (normative):
IDL Specification of TCI

This annex defines the TTCN-3 Control Interfaces using the Interface Definition Language (IDL).

void tliGetVerdict(

in TString am, in TInteger ts, in TString src, in TInteger line,

in TriComponentIdType c, in VerdictValue verdict

);

void tliSetVerdict(

in TString am, in TInteger ts, in TString src, in TInteger line,

in TriComponentIdType c, in VerdictValue verdict, in TString reason

);

void tliLog(

in TString am, in TInteger ts, in TString src, in TInteger line,

in TriComponentIdType c, in TString log

);

void tliAEnter(

in TString am, in TInteger ts, in TString src, in TInteger line,

in TriComponentIdType c

);

void tliALeave(

in TString am, in TInteger ts, in TString src, in TInteger line,

in TriComponentIdType c

);

void tliADefaults(

in TString am, in TInteger ts, in TString src, in TInteger line,

in TriComponentIdType c

);

void tliAActivate(

in TString am, in TInteger ts, in TString src, in TInteger line,

in TriComponentIdType c, in QualifiedName name, in TciParameterListType tciPars,

in Value ref

);

void tliADeactivate(

in TString am, in TInteger ts, in TString src, in TInteger line,

in TriComponentIdType c, in Value ref

);

void tliANomatch(

in TString am, in TInteger ts, in TString src, in TInteger line,

in TriComponentIdType c

);

void tliARepeat(

in TString am, in TInteger ts, in TString src, in TInteger line,

in TriComponentIdType c

);

void tliAWait(

in TString am, in TInteger ts, in TString src, in TInteger line,

in TriComponentIdType c

);

void tliAction(

in TString am, in TInteger ts, in TString src, in TInteger line,

in TriComponentIdType c, in TString action

);

void tliMatch(

in TString am, in TInteger ts, in TString src, in TInteger line,

in TriComponentIdType c, in Value expr, in TciValueTemplate tmpl

);

void tliMatchMismatch(

in TString am, in TInteger ts, in TString src,

in TInteger line, in TriComponentIdType c, in Value expr,

in TciValueTemplate tmpl, in TciValueDifferenceList diffs

);

void tliInfo(

in TString am, in TInteger ts, in TString src,

in TInteger line, in TriComponentIdType c,

in TInteger level, in TString info

);

};

};

Annex B (normative):
XML Mapping for TCI TL Provided

This annex defines a mapping for the logging interface of TCI using eXtended Markup Language (XML) schema definitions.

# B.5	TCI-TL XML Schema for Events

<!-- verdicts -->

<xsd:complexType name="tliGetVerdict">

<xsd:complexContent mixed="true">

<xsd:extension base="Events:Event">

<xsd:sequence>

<xsd:element name="verdict" type="Values:VerdictValue"/>

</xsd:sequence>

</xsd:extension>

</xsd:complexContent>

</xsd:complexType>

<xsd:complexType name="tliSetVerdict">

<xsd:complexContent mixed="true">

<xsd:extension base="Events:Event">

<xsd:sequence>

<xsd:element name="verdict" type="Values:VerdictValue"/>
                    <xsd:element name="reason" type="SimpleTypes:TString" minOccurs="0"/>

</xsd:sequence>

</xsd:extension>

</xsd:complexContent>

</xsd:complexType>

<!-- log -->

<xsd:complexType name="tliLog">

<xsd:complexContent mixed="true">

<xsd:extension base="Events:Event">

<xsd:sequence>

<xsd:element name="log" type="SimpleTypes:TString"/>

</xsd:sequence>

</xsd:extension>

</xsd:complexContent>

</xsd:complexType>

# B.6	TCI-TL XML Schema for a Log