# 8	Modules

The principal building blocks of TTCN-3 are modules. For example, a module may define a fully executable test suite or just a library. A module consists of a (optional) definitions part, and a (optional) module control part.

NOTE:	The term test suite is synonymous with a complete TTCN-3 module containing test cases and a control part.

## 8.1	Definition of a module

A module is defined with the keyword module.

NOTE 1:	The treatment of TTCN-3 modules in files, repositories and alike is outside the scope of the present document.

Syntactical Structure

module ModuleIdentifier [ LanguageSpec ] "{"

[ ModuleDefinitionsPart ]

[ ModuleControlPart ]

"}"

Semantic Description

A TTCN-3 module groups a set of (typically cohesive) TTCN-3 definitions. TTCN-3 modules have an explicit import interface to use definitions from other TTCN-3 or non-TTCN-3 modules. It is possible to hide definitions in a TTCN-3 module (see clause 8.2.5). TTCN-3 modules can be compiled/interpreted separately. They are reusable and parameterizable.

Module names are of the form of a TTCN-3 identifier. In addition, a module specification can carry an optional attribute identified by the language keyword that identifies the edition of the TTCN-3 language, in which the module is specified. The language strings are defined in clause 8.2.3.6.

NOTE 2:	The module identifier is the informal text name of the module.

Restrictions

No specific restrictions in addition to the general static rules of TTCN-3 given in clause 5.

Examples

module MyTestSuite language "TTCN-3:2003"

{ … }

## 8.2	Module definitions part

The module definitions part specifies the top-level definitions of the module and may import visible identifiers from other modules. Visibility rules are given in clause 8.2.4) Scope rules for declarations made in the module definitions part and imported declarations are given in clause 5.3. Those language elements which may be defined in a TTCN-3 module are listed in table 1. Every definition can be associated with attributes using the with statement defined in clause 27. Visible module definitions may be imported by other modules.

Syntactical Structure

{

(

TypeDef |

ConstDef |

TemplateDef |

ModuleParDef |

FunctionDef |

SignatureDef |

TestcaseDef |

AltstepDef |

ImportDef |

GroupDef |

ExtFunctionDef |

FriendDef

) [ WithStatement ]

[ ";" ]

}+

Semantic Description

Definitions in the module definitions part may be made in any order.

Such definitions, i.e. top level definitions outside of other scope units, are globally visible within the module. They. may be used elsewhere in the module. This includes identifiers imported from other modules.

Declarations of dynamic language elements such as variables or timers shall only be made in the control part, test cases, functions, altsteps or component types.

TTCN-3 does not support the declaration of variables in the module definitions part, i.e. global variables cannot be defined in TTCN-3. However, variables defined in a test component type may be used by all test cases, functions etc. running on components of that component type and variables defined in the control part provide the ability to keep their values independently of test case execution.

Restrictions

No specific restrictions in addition to the general static rules of TTCN-3 given in clause 5.

Examples

module MyModule

{	// This module contains definitions only

:

const integer MyConstant := 1;

type record MyMessageType { … }

:

function TestStep(){ … }

:

}

### 8.2.1	Module parameters

Module parameters define a set of values that are supplied by the test environment at run-time. Module parameters do not change their value during test execution. They can be used on right hand side of assignments, in expressions, in actual parameters, and in template definitions, but not within type definitions.

Syntactical Structure

Single type, single module parameter form:

[ Visibility ] modulepar ModuleParType ModuleParIdentifier [ ":=" Expression ] ";"

Single type, multiple module parameter form:

[ Visibility ] modulepar ModuleParType

{ ModuleParIdentifier [ ":=" Expression ] "," }

ModuleParIdentifier [ ":=" Expression ] ";"

Semantic Description

Module parameters behave as global constants at run-time.

Module parameters allow to customize a TTCN-3 test suite for a specific IUT, test setup or test campaign. Module parameters are declared by specifying the type and listing their identifiers following the keyword modulepar.

It is allowed to specify default values for module parameters. This shall be done by an assignment in the module parameter list. A default value can merely be assigned at the place of the declaration of the parameter.

If the test system does not provide an actual run-time value for a module parameter, the default value shall be used during test execution, otherwise the actual value provided by the test system. Actual run-time values shall be literals only.

Visible module parameters can be imported.

NOTE:	Typically, module parameters should be visible as invisible module parameters cannot be set by the importing module. Be careful when making a module parameter invisible.

Optional fields of record and set module parameters or module parameter fields can be initialized explicitly or implicitly. For implicit initialization of the optional fields of a module parameter or a module parameter field, an optional attribute with the value "implicit omit" (see clause 27.7) shall be associated with it either directly or via the attribute distribution (scoping) mechanism (see clause 27.1.1).

Restrictions

In addition to the general static rules of TTCN-3 given in clause 5, the following restrictions apply:

- During test execution these values shall be treated as constants.

- Module parameters shall not be of port type, default type or component type.

- A module parameter shall only be of type address if the address type is explicitly defined within the associated module.

- Module parameters shall be declared within the module definition part only.

- More than one occurrence of module parameters declaration is allowed but each parameter shall be declared only once (i.e. redefinition of the module parameter is not allowed).

- The Expression for the default value of a module parameter shall respect the limitations given in clause 16.1.4.

- Module parameters shall not be used in type or array definitions.

Examples

module MyTestSuiteWithParameters

{

// single type, single module parameter, which is per default public

modulepar boolean TS_Par0 := true;

// single type, multiple module parameters with an explicit public visibility

public modulepar integer TS_Par1, TS_Par2 := 1 + char2int(“a”);

...

}

### 8.2.2	Groups of definitions

In the module definitions part, definitions can be collected in named groups. Grouping is done to aid readability and to add logical structure to the module if required. If necessary, the dot notation shall be used to identify sub-groups within the group hierarchy uniquely, e.g. for the import of a specific sub-group.

Syntactical Structure

[ public ] group GroupIdentifier "{"

{ ModuleDefinition [ ";" ] }

"}"

Semantic Description

A group of definitions can be specified wherever a single definition is allowed. Groups may be nested, i.e. groups may contain other groups. This allows the test suite specifier to structure, among other things, collections of test data or functions describing test behaviour.

Groups and nested groups have no scoping. Please note however, attributes given to a group by an associated with statement apply to all elements of a group (see clause 27). Import statements may import groups so that all elements of a group are imported (see clause 8.2.3.3).

Restrictions

In addition to the general static rules of TTCN-3 given in clause 5, the following restrictions apply:

- Group identifiers across the whole module need not necessarily be unique. However, top-level group identifiers and all group identifiers of subgroups of a single group shall be unique.

- public visibility can be defined for groups only as they are always public.

Examples

module MyModule {

:

// A collection of definitions

group MyGroup {

const integer MyConst:= 1;

:

type record MyMessageType { … };

group MyGroup1 {	// Sub-group with definitions

type record AnotherMessageType { … };

const boolean MyBoolean := false

}

}

// A group of altsteps

group MyStepLibrary {

group MyGroup1 {	// Sub-group with the same name as the sub-group with definitions

altstep MyStep11() { … }

altstep MyStep12() { … }

:

altstep MyStep1n() { … }

}

group MyGroup2 {

altstep MyStep21() { … }

altstep MyStep22() { … }

:

altstep MyStep2n() { … }

}

}

:

}

// An import statement that imports MyGroup1 within MyStepLibrary

import from MyModule {

group MyStepLibrary.MyGroup1

}

### 8.2.3	Importing from modules

It is possible to re-use visible definitions specified in different modules using the import statement. Every definition in a TTCN-3 module has an associated visibility, which is by default public (see clause 8.2.5).

NOTE 1: 	As imports cannot be further imported by other modules, they are private only.

NOTE 2: 	Groups are public only. Importing a group means that only the visible elements of the group are being imported.

#### 8.2.3.1	General format of import

An import statement can be used anywhere in the module definitions part.

Syntactical Structure

import from ModuleId

(

( all [ except "{" ExceptSpec "}" ] )

|

( "{" ImportSpec "}" )

)

[ ";" ]

Semantic Description

TTCN-3 supports the import of the following definitions: module parameters, user defined types, signatures, constants, data templates, signature templates, functions, external functions, altsteps and test cases. Each definition has a name (defines the identifier of the definition, e.g. a function name), a specification (e.g. a type specification or a signature of a function) and in the case of functions, altsteps and test cases an associated behaviour description. Visible definitions only can be imported (see clause 8.2.5).

EXAMPLE:

|  | Name | Specification | Behaviour description |
| --- | --- | --- | --- |
| function | MyFunction | (inout MyType1 MyPar) return MyType2 runs on MyCompType | { const MyType3 MyConst := …; : // further behaviour } |

|  | Specification | Name | Specification |
| --- | --- | --- | --- |
| type | record | MyRecordType | { field1 MyType4, field2 integer } |

|  | Specification | Name | Specification |
| --- | --- | --- | --- |
| template | MyType5 | MyTemplate | := { field1 := 1, field2 := MyConst, // MyConst is a module constant field3 := ModulePar // ModulePar is module parameter } |

Behaviour descriptions have no effect on the import mechanism, because their internals are considered to be invisible to the importer when the corresponding functions, altsteps or test cases are imported. Thus, they are not considered in the following descriptions.

The specification part of an importable definition contains local definitions (e.g. field names of structured type definitions or values of enumerated types) and referenced definitions (e.g. references to type definitions, templates, constants or module parameters). For the examples above, this means:

|  | Name | Local definitions | Referenced definitions |
| --- | --- | --- | --- |
| function | MyFunction | MyPar | MyType1, MyType2, MyCompType |
| type | MyRecordType | field1, field2 | MyType4, integer |
| template | MyTemplate |  | MyType5, field1, field2, field3, MyConst, ModulePar |

NOTE 1:	The local definitions column refers to identifiers only that are newly defined in the importable definition. Values assigned to individual fields of importable definitions, e.g. in template definitions, may also be considered as local definitions, but they are not important for the explanation of the import mechanism.

NOTE 2:	The referenced definitions field1, field2 and field3 of template MyTemplate are the field names of MyType5, i.e. they are referenced via MyType5.

Referenced definitions are also importable definitions, i.e. the source of a referenced definition can again be structured into a name and a specification part and the specification part also contains local and referenced definitions. In other words, an importable definition may be built up recursively from other importable definitions.

The TTCN-3 import mechanism is related to the local and referenced definitions used in the specification part of the importable definitions. Table 8 specifies the possible local and referenced definitions of importable definitions.

Table 8: Possible local and referenced definitions of importable definitions

| Importable Definition | Possible Local Definitions | Possible Referenced Definitions |
| --- | --- | --- |
| Module parameter |  | Module parameter type |
| User-defined type (for all) | Parameter names | Parameter type |
| enumerated type | Concrete values |  |
| structured type | Field names, nested type definitions | Field types |
| port type |  | Message types, signatures |
| component type | Constant names, variable names, timer names and port names | Constant types, variable types, port types |
| Signature | Parameter names | Parameter types, return type, types of exceptions |
| Constant |  | Constant type |
| Data Template | Parameter names | Template type, parameter types, constants, module parameters, functions |
| Signature template |  | Signature definition, constants, module parameters functions |
| Function | Parameter names | Parameter types, return type, component type (runs on-clause) |
| External function | Parameter names | Parameter types, return type |
| Altstep | Parameter names | Parameter types, component type (runs on-clause) |
| Test case | Parameter names | Parameter types, component types (runs on- and system- clause) |

The TTCN-3 import mechanism distinguishes between the identifier of a referenced definition and the information necessary for the usage of a referenced definition within the imported definition. For the usage, the identifier of a referenced definition is not required and therefore not imported automatically.

If an imported definition has attributes (defined by means of a with statement) then the attributes shall also be imported. The mechanism to change attributes of imported definitions is explained in clause 27.1.3.

NOTE 3:	If the module has global attributes they are associated to definitions without these attributes.

The use of import on single definitions, groups of definitions, definitions of the same kind, etc. may lead to situations where the same definition is referred to more than once. Such cases shall be resolved by the system and definitions shall be imported only once.

NOTE 4:	The mechanisms to resolve such ambiguities, e.g. overwriting and sending warnings to the user, are outside the scope of the present document and should be provided by TTCN-3 tools.

All import statements and definitions within import statements are considered to be treated independently one after the other in the order of their appearance.

All TTCN-3 modules shall have their own name space in which all definitions shall be uniquely identified. Name clashes may occur due to import, e.g. import from different modules. Name clashes shall be resolved by prefixing the imported definition (which causes the name clash) by the identifier of the module from which it is imported. The prefix and the identifier shall be separated by a dot (.).

In cases where there are no ambiguities the prefixing need not (but may) be present when the imported definitions are used. When the definition is referenced in the same module where it is defined, the module identifier of the module (the current module) also may be used for prefixing the identifier of the definition.

Restrictions

In addition to the general static rules of TTCN-3 given in clause 5, the following restrictions apply:

- An import statement shall only be used in the module definitions part and not be used within a control part, function definition, and alike.

- Only top-level visible definitions of a module may be imported. Definitions which are top-level but invisible or which occur at a lower scope (e.g. local constants defined in a function) shall not be imported.

- Only direct importing from the source module of a definition (i.e. the module where the actual definition for the identifier referenced in the import statement resides) is allowed.

- A definition is imported together with its name and all local definitions.

NOTE 5:	A local definition, e.g. a field name of a user-defined record type, only has meaning in the context of the definitions in which it is defined, e.g. a field name of a record type can only be used to access a field of the record type and not outside this context.

A definition is imported together with all information of referenced definitions that are necessary for the usage of the referenced definition.

NOTE 6:	Import statements are transitive, e.g. if a module A imports a definition from module B that uses a type reference defined in module C, the corresponding information necessary for the usage of that type is automatically imported into module A. Identifiers of referenced definitions are not automatically imported.

If the referenced definitions are wished to be used in the importing module, they shall be explicitly imported from its source module.

When importing a function, altstep or test case the corresponding behaviour specifications and all definitions used inside the behaviour specifications remain invisible for the importing module.

Examples

EXAMPLE 1: 	Selected import examples.

module MyModuleA

{ 	:

// Scope of the imported definitions is global to MyModuleA

import from MyModuleB all; 	// import of all definitions from MyModuleB

import from MyModuleC {		// import of selected definitions from MyModuleC

type MyType1, MyType2;  // import of types MyType1 and MyType2

template all			// import of all templates

}

:

function MyBehaviourC()

{

// import cannot be used here

:

}

:

control

{

// import cannot be used here

:

}

}

EXAMPLE 2: 	Use of imported definitions and visibility of definitions referenced by them.

module ModuleONE {

modulepar integer ModPar1 := …;

type record RecordType_T1 {

integer	Field1_T1,

:

}

type record RecordType_T2 {

RecordType_T1	Field1_T2,

:

}

const integer MyConst := …;

template RecordType_T2 Template_T2 (RecordType_T1 TempPar_T2):= { // parameterized template

Field1_T2 := …,

:

}

} // end module ModuleONE

module ModuleTWO {

import from ModuleONE {

template Template_T2

}

// Only the names Template_T2 and TempPar_T2 will be visible in ModuleTWO. Please note, that

// the identifier TempPar_T2 can only be used when modifying Template_T2. All information

// necessary for the usage of Template_T2, e.g. for type checking purposes, are imported

// for the referenced definitions RecordType_T1, Field1_T2, etc., but their identifiers are

// not visible in ModuleTWO.

// This means, e.g. it is not possible to use the constant MyConst or to declare a

// variable of type RecordType_T1 or RecordType_T2 in ModuleTWO without explicitly importing
		// these types.

import from ModuleONE {

modulepar ModPar2

}

// The module parameter ModPar2 of ModuleONE is imported from ModuleONE and

// can be used like an integer constant

} // end module ModuleTWO

module ModuleTHREE {

import from ModuleONE all; 	// imports all definitions from ModuleONE

type port MyPortType {

inout RecordType_T2 	// Reference to a type defined in ModuleONE

}

type component MyCompType {

var integer MyComponentVar := ModPar2;

// Reference to a module parameter of ModuleONE

:

}

function MyFunction () return integer {

return MyConst			// Reference to a module constant of ModuleONE

}

testcase MyTestCase (out RecordType_T2 MyPar) runs on MyCompType {

:

MyPort.send(Template_T2); // Sending a template defined in ModuleONE

:

}

} // end ModuleTHREE

module ModuleFOUR {

import from ModuleTHREE {

testcase MyTestCase

}

// Only the name MyTestCase will be visible and usable in ModuleFOUR.

// Type information for RecordType_T2 is imported via ModuleTHREE from ModuleONE and

// Type information for MyCompType is imported from ModuleTHREE. All definitions

// used in the behaviour part of MyTestCase remain hidden for the user of ModuleFOUR.

} // end ModuleFOUR

EXAMPLE 3: 	Handling of name clashes.

module MyModuleA  {

:

type bitstring MyTypeA;

import from SomeModuleC {

type	MyTypeA,		// Where MyTypeA is of type character string

MyTypeB			// Where MyTypeB is of type character string

}

:

control {

:

var	SomeModuleC.MyTypeA MyVar1 := "Test String"; // Prefix must be used

var MyTypeA MyVar2 := '10110011'B; 				 // This is the original MyTypeA

:

var MyTypeB MyVar3 := "Test String"; 			 // Prefix need not be used …

var SomeModuleC.MyTypeB MyVar3 := "Test String"; // … but it can be if wished

:

}

}

NOTE 8:	Definitions with the same name defined in different modules are always assumed to be different, even if the actual definitions in the different modules are identical. For example, importing a type that is already defined locally, even with the same name, would lead to two different types being available in the module.

#### 8.2.3.2	Importing single definitions

Single visible definitions can be imported by referring to the definition kind and the definition name(s). The import of single definitions can be used in combination with imports of groups (see clause 8.2.3.3) and with imports of definitions of the same kind (see clause 8.2.3.4).

Syntactical Structure

import from ModuleId "{"

{

(

( type 		{ TypeDefIdentifier 	[ "," ] } ) |

( template 	{ TemplateIdentifier 	[ "," ] } ) |

( const 	{ ConstIdentifier 		[ "," ] } ) |

( testcase 	{ TestcaseIdentifier 	[ "," ] } ) |

( altstep 	{ AltstepIdentifier 	[ "," ] } ) |

( function 	{ FunctionIdentifier 	[ "," ] } ) |

( signature { SignatureIdentifier 	[ "," ] } ) |

( modulepar { ModuleParIdentifier 	[ "," ] } )

)

[ ";" ]

}

"}" [ ";" ]

Semantic Description

See clause 8.2.3. If an invisible definition is to be imported this leads to a compile-time error.

Restrictions

In addition to the general static rules of TTCN-3 given in clause 5, the following restrictions apply:

- The definition to be imported shall be defined in the module from which it is to be imported and shall be visible to the importing module.

- See the restrictions given in clause 8.2.3.

Examples

import from MyModuleA {

type MyType1						// imports one type definition from MyModuleA only

}

import from MyModuleB {

type MyType2, Mytype3, MyType4;		// imports three types,

template MyTemplate1;				// imports one template, and

const MyConst1, MyConst2			// imports two constants

}

#### 8.2.3.3	Importing groups

Groups of definitions may be imported. The import of groups can be used in combination with imports of single definitions (see clause 8.2.3.2) and with imports of definitions of the same kind (see clause 8.2.3.4).

It is allowed to import sub-groups (i.e. a group which is defined within another group) directly, i.e. without the groups in which the sub-group is embedded. If the name of a sub-group that should be imported is identical to the name of another sub-group in the same module (see clause 8.2.2), the dot notation shall be used to identify the sub-group to be imported uniquely.

If some visible definitions of a group are wished not to be imported, their kinds and identifiers shall be listed in the exception list within a pair of curly brackets following the except keyword. The all keyword is also allowed to be used in the exception list; this will exclude all definitions of the same kind from the import statement.

Syntactical Structure

import from ModuleId "{"

{

( group	{ FullGroupIdentifier [ except "{" ExceptSpec "}" ]	[ "," ] } )

[ ";" ]

}

"}" [ ";" ]

Semantic Description

The effect of importing a group is identical to an import statement that lists all visible definitions (including sub-groups) of this group except of those that are listed in the except specification. See also clause 8.2.3.

It is important to point out, that the except statement does not exclude the definitions listed from being imported in general; all statements importing definitions of the same kind can be seen as a shorthand notation for an equivalent list of identifiers of single definitions. The except statement excludes definitions from this single list only.

Restrictions

In addition to the general static rules of TTCN-3 given in clause 5, the following restrictions apply:

- The group to be imported shall be defined in the module from which it is to be imported.

- See the restrictions given in clause 8.2.3.

Examples

import from MyModule { group MyGroup } // includes all definitions from MyGroup

import from MyModule {

group MyGroup except {

type MyType3, MyType5;	// excludes the two types from the import statement,

template all			// excludes all templates defined in MyGroup

// from the import statement

// but imports all other visible definitions of MyGroup

}

}

import from MyModule {

group MyGroup

except { type MyType3 };// imports all visible types of MyGroup except MyType3

type MyType3				// imports MyType3 explicitly

}

#### 8.2.3.4	Importing definitions of the same kind

The all keyword may be used to import all visible definitions of the same kind of a module. The all keyword used with the constant keyword identifies all visible constants declared in the definitions part of the module the import statement refers to. Similarly the all keyword used with the function keyword identifies all visible functions and all visible external functions defined in the module the import statement denotes.

If some visible declarations of a kind are wished to be excluded from the given import statement, their identifiers shall be listed following the except keyword.

The import of visible definitions of the same kind can be used in combination with imports of single visible definitions (see clause 8.2.3.2) and with imports of groups (see clause 8.2.3.3).

Syntactical Structure

import from ModuleId "{"

{

(

( type 		all [ except { TypeDefIdentifier 	[ "," ] } ] ) |

( template 	all [ except { TemplateIdentifier 	[ "," ] } ] ) |

( const 	all [ except { ConstIdentifier 		[ "," ] } ] ) |

( testcase 	all [ except { TestcaseIdentifier 	[ "," ] } ] ) |

( altstep 	all [ except { AltstepIdentifier 	[ "," ] } ] ) |

( function 	all [ except { FunctionIdentifier 	[ "," ] } ] ) |

( signature all [ except { SignatureIdentifier 	[ "," ] } ] ) |

( modulepar all [ except { ModuleParIdentifier 	[ "," ] } ] )

)

[ ";" ]

}

"}" [ ";" ]

Semantic Description

The effect of importing definitions of the same kind is identical to an import statement that lists all visible definitions of that kind except of those that are listed in the except specification. See also clause 8.2.3.

NOTE:	If the list of all visible definitions of that kind except of those that are listed in the except specification is empty, the import statement has no effect. This case does not lead to a compile-time error.

Restrictions

In addition to the general static rules of TTCN-3 given in clause 5, the following restrictions apply:

- See the restrictions given in clause 8.2.3.

Examples

import from MyModule {

type all;				// imports all types of MyModule

template all			// imports all templates of MyModule

}

import from MyModule {

type all except MyType3, MyType5;	// imports all types except MyType3 and MyType5

template all						// imports all templates defined in Mymodule

}

#### 8.2.3.5	Importing all definitions of a module

All visible definitions of a module definitions part may be imported using the all keyword next to the module name.

If some visible definitions are wished not to be imported, their kinds and identifiers shall be listed in the exception list within a pair of curly brackets following the except keyword. The all keyword is also allowed to be used in the exception list; this will exclude all visible declarations of the same kind from the import statement.

NOTE:	If the list of all visible definitions of a module except of those that are listed in the except specification is empty, the import statement has no effect. This case does not lead to a compile-time error.

Syntactical Structure

import from ModuleId

all

[

{

except "{"

( group 	{ FullGroupIdentifier 	[ "," ] } | all ) |

( type 		{ TypeDefIdentifier 	[ "," ] } | all ) |

( template 	{ TemplateIdentifier 	[ "," ] } | all ) |

( const 	{ ConstIdentifier 		[ "," ] } | all ) |

( testcase 	{ TestcaseIdentifier 	[ "," ] } | all ) |

( altstep 	{ AltstepIdentifier 	[ "," ] } | all ) |

( function 	{ FunctionIdentifier 	[ "," ] } | all ) |

( signature { SignatureIdentifier 	[ "," ] } | all ) |

( modulepar { ModuleParIdentifier 	[ "," ] } | all )

"}"

[ ";' ]

}

]

[ ";" ]

Semantic Description

The effect of importing all visible definitions of a module is identical to an import statement that lists all importable definitions of that module except of those that are listed in the except specification. See also clause 8.2.3.

Restrictions

In addition to the general static rules of TTCN-3 given in clause 5, the following restrictions apply:

- If all visible definitions of a module are imported by using the all keyword, no other form of import (import of single definitions, import of the same kind, etc.) shall be used for the same import statement.

- In the set of except statements for an all import, only one except statement per kind of definition (i.e. for a group, type, etc.) is allowed.

Examples

import from MyModule all; 	// includes all definitions from MyModule

import from MyModule all except {

type MyType3, MyType5;	// excludes these two types from the import statement and

template all			// excludes all templates declared in MyModule,

// from the import statement

// but imports all other definitions of MyModule

}

#### 8.2.3.6	Import definitions from other TTCN-3 editions and from non-TTCN-3 modules

In cases when visible definitions are imported from modules from other TTCN-3 editions or from other sources than TTCN-3 modules, the language specification shall be used to denote the language (may be together with a version number) of the source (e.g. module, package, library or even file) from which definitions are imported. It consists of the language keyword and a subsequent textual declaration of the denoted language.

The use of the language specification is optional when importing from a TTCN-3 module of the same edition as the importing module. The following TTCN-3 language identifiers are defined:

"TTCN-3:2001" - to be used with modules complying with version 1.1.2 of the present document (see annex H).
	"TTCN-3:2003" - to be used with modules complying with version 2.2.1 of the present document (see annex H).
	"TTCN-3:2005" - to be used with modules complying with version 3.2.1 of the present document (see annex H).
	"TTCN-3:2008" - to be used with modules complying with version 3.3.2 of the present document (see annex H).
	"TTCN-3:2008 Amendment 1" - to be used with modules complying with version 3.4.1 of the present document
	(see annex H)
	"TTCN-3:2009" - to be used with modules complying with the present document.

Other language identifiers are defined in the language mapping parts of TTCN-3, i.e. in ES 201 873-7 [i.5], ES 201 873-8 [i.6] and ES 201 873-9 [i.7].

When an incompatibility is discovered between the language identification (including implicit identification by omitting the language specification) and the syntax of the module from which definitions are imported, tools shall provide reasonable effort to resolve the conflict.

Syntactical Structure

import from ModuleIdentifier [ language FreeText ] … [ ";" ]

Semantic Description

TTCN-3 supports the referencing of elements defined in other TTCN-3 editions (versioned elements) or other languages (foreign elements) from within TTCN-3 modules. Such elements can be used in a TTCN-3 module of a given edition only if they have a TTCN-3 view in that TTCN-3 edition. The term TTCN-3 view can be best explained by considering the case when the definition of a TTCN-3 element is based on another TTCN-3 element, the information content of the referenced element shall be available and is used for the new definition. For example, when a template is defined based on a structured type, the identifiers and types of fields of the base type shall be accessible and are used for the template definition. In a similar way, when a base type is a versioned or foreign element it shall provide the same information content as would be required from a TTCN-3 type declaration. The versioned or foreign element, naturally, may contain more information than required by TTCN-3. The TTCN-3 view of a versioned or foreign element means that part of the information carried by that element, which is necessary to use it in TTCN-3. Obviously, the TTCN-3 view of a versioned or foreign element may be the full set or a subset of the information content of that element but never a superset. There may be versioned or foreign element without a TTCN-3 view (zero TTCN-3 view), i.e. for some reason no TTCN-3 definition in the given edition could be based on them.

To make declarations of versioned or foreign element visible in TTCN-3 modules, their names shall be imported just like definitions in other TTCN-3 modules of the given edition. When imported, only the TTCN-3 view of the versioned or foreign element will be seen from the importing TTCN-3 module. There are two main differences between importing TTCN-3 elements of the same editions and versioned or foreign elements:

to import from a TTCN-3 module of another edition of from a non-TTCN-3 module the import statement shall contain an appropriate language identifier string;

only versioned or foreign elements with a TTCN-3 view of a given edition are importable into a TTCN-3 module of that edition.

Importing can be done automatically using the all directive, in which case all importable objects shall automatically be selected by the testing tool, or done manually by listing names of elements to be imported. Naturally, in the second case only importable elements are allowed in the list.

Restrictions

In addition to the general static rules of TTCN-3 given in clause 5, the following restrictions apply:

- The language specification may only be omitted if the referenced module contains TTCN-3 notation and the TTCN-3 version is known.

Examples

import from MyModule language "TTCN-3:2003" {

type MyType

}

NOTE:	The import mechanism is designed to allow the re-use of definitions from other TTCN-3 editions or from other language sources. The rules for importing definitions from specifications written in other languages, e.g. SDL packages, may follow the TTCN-3 rules or may have to be defined separately.

### 8.2.4	Definition of friend modules

Modules can define other modules to be friend.

Syntactical Structure

friend module ModuleIdentifier { "," ModuleIdentifier } ";"

Semantic Description

Friendship to modules is defined by the exporting module (the module that defines module definitions) not by the importing module (the module that uses the module definitions of another module). Friendship can be cyclic.

If a module is friend to a module from which it imports module definitions, all module definitions with public and friend visibility are visible to the friend module. For non-friend modules, public module definitions are visible only.

Restrictions

No specific restrictions in addition to the general static rules of TTCN-3 given in clause 5.

Examples

module MyModuleA {

friend module MyModuleB,MyModuleC;

}

module MyModuleB {

friend module MyModuleA;

}

module MyModuleC {

}

// MyModuleA is friend of MyModuleB

// MyModuleB is friend of MyModuleA

// MyModuleC is friend of MyModuleA

### 8.2.5	Visibility of definitions

### Module definitions have a visibility, which can be explicitly set. It is by default public except for import definitions which are private only. Group definitions are public only.

Syntactical Structure

[ public | friend | private ]

Semantic Description

The visibility controls if a module definition is importable by another module.

Three visibilities are distinguished:

- A module definition with public visibility is importable by any other module.

- A module definition with friend visibility is importable by friend modules only (see clause 8.2.4).

- A module definition with private visibility cannot be imported at all.

The visibility of groups is always public, the visibility of imports is always private. All other module definitions are by default public.

The visibility of a module definition defines the importability of a module definition by another module. If the module definition is part of a group definition, this has no effect on the importability of the module definition. The importability of a module definition by another module is summarized in table 4.

Table 4: Visibility and import of module definitions

| Visibility of module definition | Module definition importable directly by a non-friend module | Module definition importable directly by a friend module | Module definition importable via group import by a non-friend module | Module definition importable via group import by a friend module |
| --- | --- | --- | --- | --- |
| public | yes | yes | yes | yes |
| friend | no | yes | no | yes |
| private | no | no | no | no |

Restrictions

No specific restrictions in addition to the general static rules of TTCN-3 given in clause 5.

Examples

module MyModuleA {

friend module MyModuleC;

private type integer MyInteger;

friend type charstring MyString;

public type boolean MyBoolean;

}

module MyModuleB {

import from MyModuleA { type MyBoolean };

// MyString and MyInteger not visible

}

module MyModuleC {

import from MyModuleA { type MyString};

import from MyModuleA { type MyBoolean };

// MyInteger not visible

}

## 8.3	Module control part

The module control part may contain local definitions (i.e. constants or templates), local instances (i.e. variables or timers) and describe the selection, parameterization and execution order (possibly repetitive) of the actual test cases. A test case shall be defined in the module definitions part or imported from another module, and called in the control part.

The control part of a module calls the test cases with actual parameters and controls their execution. Program statements can be used to specify the selection and execution order of the test cases. Definitions made in the module control part have local visibility, i.e. can be used within the control part only.

This is explained in more detail in clause 26.

EXAMPLE:

module MyTestSuite

{ 	// This module contains definitions …

:

const integer MyConstant := 1;

type record MyMessageType { … }

template MyMessageType MyMessage := { … }

:

function MyFunction1() { … }

function MyFunction2() { … }

:

testcase MyTestcase1() runs on MyMTCType { … }

testcase MyTestcase2() runs on MyMTCType { … }

:

// … and a control part so it is executable

control

{

var boolean MyVariable; // local control variable

:

execute( MyTestCase1()); // sequential execution of test cases

execute( MyTestCase2());

:

}

}

…

// The BNF extensions are in clause A.1.6.1.0 General and in the additional clause A.1.6.1.13Friend module definitions

Annex A (normative):
BNF and static semantics

# A.1	TTCN-3 BNF

This annex defines the syntax of TTCN-3 using extended BNF (henceforth just called BNF).

## A.1.1	Conventions for the syntax description

Table A.1 defines the metanotation used to specify the extended BNF grammar for TTCN-3.

Table A.1: The syntactic metanotation

| ::= | is defined to be |
| --- | --- |
| abc xyz | abc followed by xyz |
| ¦ | alternative |
| [abc] | 0 or 1 instances of abc |
| {abc} | 0 or more instances of abc |
| {abc}+ | 1 or more instances of abc |
| (...) | textual grouping |
| Abc | the non-terminal symbol abc |
| "abc" | a terminal symbol abc |

## A.1.2	Statement terminator symbols

In general all TTCN-3 language constructs (i.e. definitions, declarations, statements and operations) are terminated with a semi-colon (;). The semi-colon is optional if the language construct ends with a right-hand curly brace (}) or the following symbol is a right-hand curly brace (}), i.e. the language construct is the last statement in a statement block.

## A.1.3	Identifiers

TTCN-3 identifiers are case sensitive and may only contain lowercase letters (a-z) uppercase letters (A-Z) and numeric digits (0-9). Use of the underscore ( _ ) symbol is also allowed. An identifier shall begin with a letter (i.e. not a number and not an underscore).

## A.1.4	Comments

Comments written in free text may appear anywhere in a TTCN-3 specification.

Block comments shall be opened by the symbol pair /* and closed by the symbol pair */.

EXAMPLE 1:

/* This is a block comment

spread over two lines */

Block comments shall not be nested.

/* This is not /* a legal */ comment */

Line comments shall be opened by the symbol pair // and closed by a <newline>.

EXAMPLE 2:

// This is a line comment

// spread over two lines

EXAMPLE 3:

// The following is not legal

const // This is MyConst integer MyConst := 1;

// A block comment should have been used instead

const /* This is MyConst */ integer MyConst := 1;

// A line comment like this works as well

const // This is MyConst

integer MyConst := 1;

## A.1.5	TTCN-3 terminals

TTCN-3 terminal symbols and reserved words are listed in tables A.2 and A.3.

Table A.2: List of TTCN-3 special terminal symbols

| Begin/end block symbols | { } |
| --- | --- |
| Begin/end list symbols | ( ) |
| Alternative symbols | [ ] |
| To symbol (in a range) | .. |
| Line comments and Block comments | /* */ // |
| Line/statement terminator symbol | ; |
| Arithmetic operator symbols | + / - |
| Concatenation operator symbol | & |
| Equivalence operator symbols | != == >= <= |
| String enclosure symbols | " ' |
| Wildcard/matching symbols | ? * |
| Assignment symbol | := |
| Communication operation assignment | -> |
| Bitstring, hexstring and Octetstring values | B H O |
| Float exponent | E |

The predefined function identifiers defined in table 13 and described in annex C shall also be treated as reserved words.

Table A.3: List of TTCN-3 terminals which are reserved words

| action activate address alive all alt altstep and and4b any anytype bitstring boolean break case call catch char charstring check clear complement component connect const continue control create deactivate default disconnect display do done else encode enumerated error except exception execute extends extension external | fail false float for friend from function getverdict getcall getreply goto group halt hexstring if ifpresent import in inconc infinity inout integer interleave kill killed label language length log map match message mixed mod modifies module modulepar mtc | noblock none not not4b nowait null octetstring of omit on optional or or4b out override param pass pattern permutation port present private procedure public raise read receive record recursive rem repeat reply return running runs | select self send sender set setverdict signature start stop subset superset system template testcase timeout timer to trigger true type union universal unmap value valueof var variant verdicttype while with xor xor4b |
| --- | --- | --- | --- |

The TTCN-3 terminals listed in table A.3 shall not be used as identifiers in a TTCN-3 module. These terminals shall be written in all lowercase letters.

## A.1.6	TTCN-3 syntax BNF productions

### A.1.6.0	TTCN-3 module

TTCN3Module ::= TTCN3ModuleKeyword TTCN3ModuleId

"{"

[ModuleDefinitionsPart]

[ModuleControlPart]

"}"

[WithStatement] [SemiColon]

TTCN3ModuleKeyword ::= "module"

TTCN3ModuleId ::= ModuleId

ModuleId ::= GlobalModuleId [LanguageSpec]

GlobalModuleId ::= ModuleIdentifier

ModuleIdentifier ::= Identifier

LanguageSpec ::= LanguageKeyword FreeText

LanguageKeyword ::= "language"

### A.1.6.1	Module definitions part

#### A.1.6.1.0	General

ModuleDefinitionsPart ::= ModuleDefinitionsList

ModuleDefinitionsList ::= {ModuleDefinition [SemiColon]}+

ModuleDefinition ::= [Visibility] (TypeDef |

ConstDef |

TemplateDef |

ModuleParDef |

FunctionDef |

SignatureDef |

TestcaseDef |

AltstepDef |

ImportDef |

GroupDef |

ExtFunctionDef |

ExtConstDef [

FriendModuleDef) [WithStatement]

Visibility ::= "public" | "friend" | "private"

#### A.1.6.1.1	Typedef definitions

TypeDef ::= TypeDefKeyword TypeDefBody

TypeDefBody ::= StructuredTypeDef | SubTypeDef

TypeDefKeyword ::= "type"

StructuredTypeDef ::= RecordDef |

UnionDef |

SetDef |

RecordOfDef |

SetOfDef |

EnumDef |

PortDef |

ComponentDef

RecordDef ::= RecordKeyword StructDefBody

RecordKeyword ::= "record"

StructDefBody ::= (StructTypeIdentifier [StructDefFormalParList] | AddressKeyword)

"{" [StructFieldDef {"," StructFieldDef}] "}"

StructTypeIdentifier ::= Identifier

StructDefFormalParList ::= "(" StructDefFormalPar {"," StructDefFormalPar} ")"

StructDefFormalPar ::= 	FormalValuePar

StructFieldDef ::= (Type | NestedTypeDef) StructFieldIdentifier [ArrayDef] [SubTypeSpec]

[OptionalKeyword]

NestedTypeDef ::= NestedRecordDef |

NestedUnionDef |

NestedSetDef |

NestedRecordOfDef |

NestedSetOfDef |

NestedEnumDef

NestedRecordDef ::= RecordKeyword "{" [StructFieldDef {"," StructFieldDef}] "}"

NestedUnionDef ::= UnionKeyword "{" UnionFieldDef {"," UnionFieldDef} "}"

NestedSetDef ::= SetKeyword "{" [StructFieldDef {"," StructFieldDef}] "}"

NestedRecordOfDef ::= RecordKeyword [StringLength] OfKeyword (Type | NestedTypeDef)

NestedSetOfDef ::= SetKeyword [StringLength] OfKeyword (Type | NestedTypeDef)

NestedEnumDef ::= EnumKeyword "{" EnumerationList "}"

StructFieldIdentifier ::= Identifier

OptionalKeyword ::= "optional"

UnionDef ::= UnionKeyword UnionDefBody

UnionKeyword ::= "union"

UnionDefBody ::= (StructTypeIdentifier [StructDefFormalParList] | AddressKeyword)

"{" UnionFieldDef {"," UnionFieldDef} "}"

UnionFieldDef ::= (Type | NestedTypeDef) StructFieldIdentifier [ArrayDef] [SubTypeSpec]

SetDef ::= SetKeyword StructDefBody

SetKeyword ::= "set"

RecordOfDef ::= RecordKeyword [StringLength] OfKeyword StructOfDefBody

OfKeyword ::= "of"

StructOfDefBody ::= (Type | NestedTypeDef) (StructTypeIdentifier | AddressKeyword) [SubTypeSpec]

SetOfDef ::= SetKeyword [StringLength] OfKeyword StructOfDefBody

EnumDef ::= EnumKeyword (EnumTypeIdentifier | AddressKeyword)

"{" EnumerationList "}"

EnumKeyword ::= "enumerated"

EnumTypeIdentifier ::= Identifier

EnumerationList ::= Enumeration {"," Enumeration}

Enumeration ::= EnumerationIdentifier ["("[Minus] Number ")"]

EnumerationIdentifier ::= Identifier

SubTypeDef ::= Type (SubTypeIdentifier | AddressKeyword)  [ArrayDef] [SubTypeSpec]

SubTypeIdentifier ::= Identifier

SubTypeSpec ::= AllowedValues [StringLength] | StringLength

/* STATIC SEMANTICS - AllowedValues shall be of the same type as the field being subtyped */

AllowedValues ::= "(" (ValueOrRange {"," ValueOrRange}) | CharStringMatch ")"

ValueOrRange ::= RangeDef | ConstantExpression

/* STATIC SEMANTICS - RangeDef production shall only be used with integer, charstring, universal charstring or float based types */

/* STATIC SEMANTICS - When subtyping charstring or universal charstring range and values shall not be mixed in the same SubTypeSpec */

RangeDef ::= LowerBound ".." UpperBound

StringLength ::= LengthKeyword "(" SingleConstExpression [".." UpperBound] ")"

/* STATIC SEMANTICS - StringLength shall only be used with String types or to limit set of and record of. SingleConstExpression and UpperBound shall evaluate to non-negative integer values (in case of UpperBound including infinity) */

LengthKeyword ::= "length"

PortType ::= [GlobalModuleId Dot] PortTypeIdentifier

PortDef ::= PortKeyword PortDefBody

PortDefBody ::= PortTypeIdentifier PortDefAttribs

PortKeyword ::= "port"

PortTypeIdentifier ::= Identifier

PortDefAttribs ::= MessageAttribs | ProcedureAttribs | MixedAttribs

MessageAttribs ::= MessageKeyword

"{" {MessageList [SemiColon]}+ "}"

MessageList ::= Direction AllOrTypeList

Direction ::= InParKeyword | OutParKeyword | InOutParKeyword

MessageKeyword ::= "message"

AllOrTypeList ::= AllKeyword | TypeList

/* NOTE: The use of AllKeyword in port definitions is deprecated */

AllKeyword ::= "all"

TypeList ::= Type {"," Type}

ProcedureAttribs ::= ProcedureKeyword

"{" {ProcedureList  [SemiColon]}+ "}"

ProcedureKeyword ::= "procedure"

ProcedureList ::= Direction AllOrSignatureList

AllOrSignatureList ::= AllKeyword | SignatureList

SignatureList ::= Signature {"," Signature}

MixedAttribs ::= MixedKeyword

"{" {MixedList [SemiColon]}+ "}"

MixedKeyword ::= "mixed"

MixedList ::= Direction ProcOrTypeList

ProcOrTypeList ::= AllKeyword | (ProcOrType {"," ProcOrType})

ProcOrType ::= Signature | Type

ComponentDef ::= ComponentKeyword ComponentTypeIdentifier

[ExtendsKeyword ComponentType {"," ComponentType}]

"{" [ComponentDefList] "}"

ComponentKeyword ::= "component"

ExtendsKeyword ::= "extends"

ComponentType ::= [GlobalModuleId Dot] ComponentTypeIdentifier

ComponentTypeIdentifier ::= Identifier

ComponentDefList ::= {ComponentElementDef [SemiColon]}

ComponentElementDef ::= PortInstance | VarInstance | TimerInstance | ConstDef

PortInstance ::= PortKeyword PortType PortElement {"," PortElement}

PortElement ::= PortIdentifier [ArrayDef]

PortIdentifier ::= Identifier

#### A.1.6.1.2	Constant definitions

ConstDef ::= ConstKeyword Type ConstList

ConstList ::= SingleConstDef  {"," SingleConstDef}

SingleConstDef ::= ConstIdentifier [ArrayDef] AssignmentChar ConstantExpression

ConstKeyword ::= "const"

ConstIdentifier ::= Identifier

#### A.1.6.1.3	Template definitions

TemplateDef ::= TemplateKeyword [TemplateRestriction] BaseTemplate [DerivedDef]

AssignmentChar TemplateBody

BaseTemplate ::= (Type | Signature) TemplateIdentifier  ["(" TemplateFormalParList ")"]

TemplateKeyword ::= "template"

TemplateIdentifier ::= Identifier

DerivedDef ::= ModifiesKeyword TemplateRef

ModifiesKeyword ::= "modifies"

TemplateFormalParList ::= TemplateFormalPar {"," TemplateFormalPar}

TemplateFormalPar ::= FormalValuePar | FormalTemplatePar

/* STATIC SEMANTICS - FormalValuePar shall resolve to an in parameter */

TemplateBody ::= (SimpleSpec | FieldSpecList | ArrayValueOrAttrib) [ExtraMatchingAttributes]

/* STATIC SEMANTICS - Within TeplateBody the ArrayValueOrAttrib can be used for array, record, record of and set of types. */

SimpleSpec ::= SingleValueOrAttrib

FieldSpecList ::= "{"[FieldSpec {"," FieldSpec}] "}"

FieldSpec ::= FieldReference AssignmentChar TemplateBody

FieldReference ::= StructFieldRef | ArrayOrBitRef | ParRef

StructFieldRef ::= StructFieldIdentifier| PredefinedType | TypeReference

/* STATIC SEMANTICS - PredefinedType and TypeReference shall be used for anytype value notation only. PredefinedType shall not be AnyTypeKeyword.*/

ParRef ::= SignatureParIdentifier

/* STATIC SEMANTICS - SignatureParIdentifier shall be a formal parameter identifier from the associated signature definition */

SignatureParIdentifier ::= ValueParIdentifier

ArrayOrBitRef ::= "[" FieldOrBitNumber "]"

/* STATIC SEMANTICS - ArrayRef shall be optionally used for array types and TTCN-3 record of and set of. The same notation can be used for a Bit reference inside an TTCN-3 charstring, universal charstring, bitstring, octetstring and hexstring type */

FieldOrBitNumber ::= SingleExpression

/* STATIC SEMANTICS - SingleExpression will resolve to a value of integer type */

SingleValueOrAttrib ::= MatchingSymbol |

SingleExpression |

TemplateRefWithParList

/* STATIC SEMANTIC - VariableIdentifier (accessed via singleExpression) may only be used in in-line template definitions to reference variables in the current scope */

ArrayValueOrAttrib ::= "{" ArrayElementSpecList "}"

ArrayElementSpecList ::= ArrayElementSpec {"," ArrayElementSpec}

ArrayElementSpec ::= NotUsedSymbol | PermutationMatch | TemplateBody

NotUsedSymbol ::= Dash

MatchingSymbol ::= Complement |

AnyValue |

AnyOrOmit |

ValueOrAttribList |

Range |

BitStringMatch |

HexStringMatch |

OctetStringMatch |

CharStringMatch |

SubsetMatch |

SupersetMatch

ExtraMatchingAttributes ::= LengthMatch | IfPresentMatch | LengthMatch  IfPresentMatch

BitStringMatch ::= "'" {BinOrMatch} "'" "B"

BinOrMatch ::= Bin | AnyValue | AnyOrOmit

HexStringMatch ::= "'" {HexOrMatch} "'" "H"

HexOrMatch ::= Hex | AnyValue | AnyOrOmit

OctetStringMatch ::= "'" {OctOrMatch} "'" "O"

OctOrMatch ::= Oct | AnyValue | AnyOrOmit

CharStringMatch ::= PatternKeyword Pattern {"&" (Pattern | ReferencedValue)}

PatternKeyword ::= "pattern"

Pattern ::= """ { PatternElement } """

PatternElement ::=

("\" ("?" | "*" | "\" | "[" | "]" | "{" | "}" | """ | "|" | "(" | ")" | "#" | "+" |

"d" | "w" | "t" | "n" | "r" | "s" | "b")) |
         ("?" | "*" | "\" | "|" | "+") |

("[" ["^"] [ {PatternChar ["-" PatternChar]} "]") |

("{" ReferencedValue "}") |

("\" "N" "{" (ReferencedValue | Type) "}") |

(""" """) |

("(" PatternElement ")") |

("#" (Num | ("(" Num "," [Num] ")") | ("(" "," Num ")")) |

PatternChar

PatternChar ::= Char | PatternQuadruple

PatternQuadruple ::= "\" "q" "(" Group "," Plane "," Row "," Cell ")"

Complement ::= ComplementKeyword ValueOrAttribList

ComplementKeyword ::= "complement"

ValueList ::= "(" ConstantExpression {"," ConstantExpression} ")"

SubsetMatch ::= SubsetKeyword ValueList

SubsetKeyword ::= "subset"

SupersetMatch ::= SupersetKeyword ValueList

SupersetKeyword ::= "superset"

PermutationMatch ::= PermutationKeyword PermutationList

PermutationKeyword ::= "permutation"

PermutationList ::= "(" TemplateBody { "," TemplateBody } ")"

/* STATIC SEMANTICS: Restrictions on the content of TemplateBody are given in clause B.1.3.3 */

AnyValue ::= "?"

AnyOrOmit ::= "*"

ValueOrAttribList ::= "(" TemplateBody {"," TemplateBody}+ ")"

LengthMatch ::= StringLength

IfPresentMatch ::= IfPresentKeyword

IfPresentKeyword ::= "ifpresent"

PresentKeyword ::= "present"

Range ::= "(" LowerBound ".." UpperBound ")"

LowerBound ::= SingleConstExpression | Minus InfinityKeyword

UpperBound ::= SingleConstExpression | InfinityKeyword

/* STATIC SEMANTICS - LowerBound and UpperBound shall evaluate to types integer, charstring, universal charstring or float. In case LowerBound or UpperBound evaluates to types charstring or universal charstring, only SingleConstExpression may be present and the string length shall be 1*/

InfinityKeyword ::= "infinity"

TemplateInstance ::= InLineTemplate

TemplateRefWithParList ::= [GlobalModuleId Dot] TemplateIdentifier [TemplateActualParList] |

TemplateParIdentifier

TemplateRef ::= [GlobalModuleId Dot] TemplateIdentifier | TemplateParIdentifier

InLineTemplate ::= [(Type | Signature) Colon] [DerivedRefWithParList AssignmentChar]

TemplateBody

DerivedRefWithParList ::= ModifiesKeyword TemplateRefWithParList

TemplateActualParList ::= "(" TemplateActualPar {"," TemplateActualPar} ")"

TemplateActualPar ::= TemplateInstance

/* STATIC SEMANTICS - When the corresponding formal parameter is not of template type the TemplateInstance production shall resolve to one or more SingleExpressions */

TemplateOps ::= MatchOp | ValueofOp

MatchOp ::= MatchKeyword "(" Expression "," TemplateInstance")"

MatchKeyword ::= "match"

ValueofOp ::= ValueofKeyword "(" TemplateInstance")"

ValueofKeyword ::= "valueof"

#### A.1.6.1.4	Function definitions

FunctionDef ::= FunctionKeyword FunctionIdentifier

"("[FunctionFormalParList] ")" [RunsOnSpec] [ReturnType]

StatementBlock

FunctionKeyword ::= "function"

FunctionIdentifier ::= Identifier

FunctionFormalParList ::= FunctionFormalPar {"," FunctionFormalPar}

FunctionFormalPar ::= FormalValuePar |

FormalTimerPar |

FormalTemplatePar |

FormalPortPar

ReturnType ::= ReturnKeyword [TemplateKeyword | RestrictedTemplate] Type

ReturnKeyword ::= "return"

RunsOnSpec ::= RunsKeyword OnKeyword ComponentType

RunsKeyword ::= "runs"

OnKeyword ::= "on"

MTCKeyword ::= "mtc"

StatementBlock ::= "{" [FunctionDefList] [FunctionStatementList]  "}"

FunctionDefList::= {(FunctionLocalDef | FunctionLocalInst)[SemiColon]}+

FunctionStatementList::= {FunctionStatement}+

FunctionLocalInst ::= VarInstance | TimerInstance

FunctionLocalDef ::= ConstDef | TemplateDef

FunctionStatement ::= ConfigurationStatements |

TimerStatements |

CommunicationStatements |

BasicStatements |

BehaviourStatements |

VerdictStatements |

SUTStatements

FunctionInstance ::= FunctionRef "(" [FunctionActualParList] ")"

FunctionRef ::= [GlobalModuleId Dot] (FunctionIdentifier | ExtFunctionIdentifier ) |

PreDefFunctionIdentifier

PreDefFunctionIdentifier ::= Identifier

/* STATIC SEMANTICS - The Identifier shall be one of the pre-defined TTCN-3 Function Identifiers from Annex C of ES 201 873-1 */

FunctionActualParList ::= FunctionActualPar {"," FunctionActualPar}

FunctionActualPar ::= TimerRef |

TemplateInstance |

Port |

ComponentRef

/* STATIC SEMANTICS - When the corresponding formal parameter is not of template type the TemplateInstance production shall resolve to one or more SingleExpressions i.e. equivalent to the Expression production */

#### A.1.6.1.5	Signature definitions

SignatureDef ::= SignatureKeyword SignatureIdentifier

"("[SignatureFormalParList] ")" [ReturnType | NoBlockKeyword]

[ExceptionSpec]

SignatureKeyword ::= "signature"

SignatureIdentifier ::= Identifier

SignatureFormalParList ::= SignatureFormalPar {"," SignatureFormalPar}

SignatureFormalPar ::= 	FormalValuePar

ExceptionSpec ::= ExceptionKeyword "(" ExceptionTypeList ")"

ExceptionKeyword ::= "exception"

ExceptionTypeList ::= Type {"," Type}

NoBlockKeyword ::= "noblock"

Signature ::= [GlobalModuleId Dot] SignatureIdentifier

#### A.1.6.1.6	Testcase definitions

TestcaseDef ::= TestcaseKeyword TestcaseIdentifier

"("[TestcaseFormalParList] ")" ConfigSpec

StatementBlock

TestcaseKeyword ::= "testcase"

TestcaseIdentifier ::= Identifier

TestcaseFormalParList ::= TestcaseFormalPar {"," TestcaseFormalPar}

TestcaseFormalPar ::= FormalValuePar |

FormalTemplatePar

ConfigSpec ::= RunsOnSpec [SystemSpec]

SystemSpec ::= SystemKeyword ComponentType

SystemKeyword ::= "system"

TestcaseInstance ::= ExecuteKeyword "(" TestcaseRef "(" [TestcaseActualParList] ")"

["," TimerValue] ")"

ExecuteKeyword ::= "execute"

TestcaseRef ::= [GlobalModuleId Dot] TestcaseIdentifier

TestcaseActualParList ::= TestcaseActualPar {"," TestcaseActualPar}

TestcaseActualPar ::= TemplateInstance

/* STATIC SEMANTICS - When the corresponding formal parameter is not of template type the TemplateInstance production shall resolve to one or more SingleExpressions i.e. equivalent to the Expression production */

#### A.1.6.1.7	Altstep definitions

AltstepDef ::= AltstepKeyword AltstepIdentifier

"("[AltstepFormalParList] ")" [RunsOnSpec]

"{" AltstepLocalDefList AltGuardList "}"

AltstepKeyword ::= "altstep"

AltstepIdentifier ::= Identifier

AltstepFormalParList ::= FunctionFormalParList

AltstepLocalDefList ::= {AltstepLocalDef [SemiColon]}

AltstepLocalDef ::= VarInstance | TimerInstance | ConstDef | TemplateDef

AltstepInstance ::= AltstepRef "(" [FunctionActualParList] ")"

AltstepRef ::= [GlobalModuleId Dot] AltstepIdentifier

#### A.1.6.1.8	Import definitions

ImportDef ::= ImportKeyword ImportFromSpec (AllWithExcepts | ("{" ImportSpec "}"))

ImportKeyword ::= "import"

AllWithExcepts ::= AllKeyword [ExceptsDef]

ExceptsDef ::= ExceptKeyword "{" ExceptSpec "}"

ExceptKeyword ::= "except"

ExceptSpec ::= {ExceptElement [SemiColon]}

ExceptElement ::= ExceptGroupSpec |

ExceptTypeDefSpec |

ExceptTemplateSpec |

ExceptConstSpec |

ExceptTestcaseSpec |

ExceptAltstepSpec |

ExceptFunctionSpec |

ExceptSignatureSpec |

ExceptModuleParSpec

ExceptGroupSpec ::= GroupKeyword (ExceptGroupRefList | AllKeyword)

ExceptTypeDefSpec ::= TypeDefKeyword (TypeRefList | AllKeyword)

ExceptTemplateSpec ::= TemplateKeyword (TemplateRefList | AllKeyword)

ExceptConstSpec ::= ConstKeyword (ConstRefList | AllKeyword)

ExceptTestcaseSpec ::= TestcaseKeyword (TestcaseRefList | AllKeyword)

ExceptAltstepSpec ::= AltstepKeyword (AltstepRefList | AllKeyword)

ExceptFunctionSpec ::= FunctionKeyword (FunctionRefList | AllKeyword)

ExceptSignatureSpec ::= SignatureKeyword  (SignatureRefList | AllKeyword)

ExceptModuleParSpec ::= ModuleParKeyword  (ModuleParRefList | AllKeyword)

ImportSpec ::= {ImportElement [SemiColon]}

ImportElement ::= ImportGroupSpec |

ImportTypeDefSpec |

ImportTemplateSpec |

ImportConstSpec |

ImportTestcaseSpec |

ImportAltstepSpec |

ImportFunctionSpec |

ImportSignatureSpec |

ImportModuleParSpec

ImportFromSpec ::= FromKeyword ModuleId [RecursiveKeyword]

RecursiveKeyword ::= "recursive"

ImportGroupSpec ::= GroupKeyword (GroupRefListWithExcept | AllGroupsWithExcept)

GroupRefList ::= FullGroupIdentifier {"," FullGroupIdentifier}

GroupRefListWithExcept ::= FullGroupIdentifierWithExcept {"," FullGroupIdentifierWithExcept}

AllGroupsWithExcept ::= AllKeyword [ExceptKeyword GroupRefList]

FullGroupIdentifier ::= GroupIdentifier {Dot GroupIdentifier}

FullGroupIdentifierWithExcept ::= FullGroupIdentifier [ExceptsDef]

ExceptGroupRefList ::= ExceptFullGroupIdentifier {"," ExceptFullGroupIdentifier}

ExceptFullGroupIdentifier ::= FullGroupIdentifier

ImportTypeDefSpec ::= TypeDefKeyword (TypeRefList | AllTypesWithExcept)

TypeRefList ::= TypeDefIdentifier {"," TypeDefIdentifier}

AllTypesWithExcept ::= AllKeyword [ExceptKeyword TypeRefList]

TypeDefIdentifier ::= StructTypeIdentifier |

EnumTypeIdentifier |

PortTypeIdentifier |

ComponentTypeIdentifier |

SubTypeIdentifier

ImportTemplateSpec ::= TemplateKeyword (TemplateRefList | AllTemplsWithExcept)

TemplateRefList ::= TemplateIdentifier {"," TemplateIdentifier}

AllTemplsWithExcept ::= AllKeyword [ExceptKeyword TemplateRefList]

ImportConstSpec ::= ConstKeyword (ConstRefList | AllConstsWithExcept)

ConstRefList ::= ConstIdentifier {"," ConstIdentifier}

AllConstsWithExcept ::= AllKeyword [ExceptKeyword ConstRefList]

ImportAltstepSpec ::= AltstepKeyword (AltstepRefList | AllAltstepsWithExcept)

AltstepRefList ::= AltstepIdentifier {"," AltstepIdentifier}

AllAltstepsWithExcept ::= AllKeyword [ExceptKeyword AltstepRefList]

ImportTestcaseSpec ::= TestcaseKeyword (TestcaseRefList | AllTestcasesWithExcept)

TestcaseRefList ::= TestcaseIdentifier {"," TestcaseIdentifier}

AllTestcasesWithExcept ::= AllKeyword [ExceptKeyword TestcaseRefList]

ImportFunctionSpec ::= FunctionKeyword (FunctionRefList | AllFunctionsWithExcept)

FunctionRefList ::= FunctionIdentifier {"," FunctionIdentifier}

AllFunctionsWithExcept ::= AllKeyword [ExceptKeyword FunctionRefList]

ImportSignatureSpec ::= SignatureKeyword  (SignatureRefList | AllSignaturesWithExcept)

SignatureRefList ::= SignatureIdentifier {"," SignatureIdentifier}

AllSignaturesWithExcept ::= AllKeyword [ExceptKeyword SignatureRefList]

ImportModuleParSpec ::= ModuleParKeyword  (ModuleParRefList | AllModuleParWithExcept)

ModuleParRefList ::= ModuleParIdentifier {"," ModuleParIdentifier}

AllModuleParWithExcept ::= AllKeyword [ExceptKeyword ModuleParRefList]

#### A.1.6.1.9	Group definitions

GroupDef ::= GroupKeyword GroupIdentifier

"{" [ModuleDefinitionsPart] "}"

GroupKeyword ::= "group"

GroupIdentifier ::= Identifier

#### A.1.6.1.10	External function definitions

ExtFunctionDef ::= ExtKeyword FunctionKeyword ExtFunctionIdentifier

"("[FunctionFormalParList] ")" [ReturnType]

ExtKeyword ::= "external"

ExtFunctionIdentifier ::= Identifier

#### A.1.6.1.11	External constant definitions

ExtConstDef ::= ExtKeyword ConstKeyword Type ExtConstIdentifierList

ExtConstIdentifierList ::= ExtConstIdentifier { "," ExtConstIdentifier }

ExtConstIdentifier ::= Identifier

#### A.1.6.1.12	Module parameter definitions

ModuleParDef ::= ModuleParKeyword ( ModulePar | ("{" MultitypedModuleParList "}"))

ModuleParKeyword ::= "modulepar"

MultitypedModuleParList ::= { ModulePar [SemiColon] }

ModulePar ::= ModuleParType ModuleParList

ModuleParType ::= Type

ModuleParList ::= ModuleParIdentifier [AssignmentChar Expression]

{"," ModuleParIdentifier [AssignmentChar Expression]}

ModuleParIdentifier ::= Identifier

#### A.1.6.1.13	Friend module definitions

FriendModuleDef ::= "friend" "module" TTCN3ModuleId {"," TTCN3ModuleId } [SemiColon]

### A.1.6.2	Control part

#### A.1.6.2.0	General

ModuleControlPart ::= ControlKeyword

"{" ModuleControlBody "}"

[WithStatement] [SemiColon]

ControlKeyword ::= "control"

ModuleControlBody ::= [ControlStatementOrDefList]

ControlStatementOrDefList ::= {ControlStatementOrDef [SemiColon]}+

ControlStatementOrDef ::= FunctionLocalDef |

FunctionLocalInst |

ControlStatement

ControlStatement ::= TimerStatements |

BasicStatements |

BehaviourStatements |

SUTStatements |

StopKeyword

#### A.1.6.2.1	Variable instantiation

VarInstance ::= VarKeyword ((Type VarList)

| (( TemplateKeyword | RestrictedTemplate ) Type TempVarList))

VarList ::= SingleVarInstance {"," SingleVarInstance}

SingleVarInstance ::= VarIdentifier [ArrayDef] [AssignmentChar VarInitialValue]

VarInitialValue ::= Expression

VarKeyword ::= "var"

VarIdentifier ::= Identifier

TempVarList ::= SingleTempVarInstance {"," SingleTempVarInstance}

SingleTempVarInstance ::= VarIdentifier [ArrayDef] [AssignmentChar TempVarInitialValue]

TempVarInitialValue ::= TemplateBody

VariableRef ::= (VarIdentifier | ValueParIdentifier) [ExtendedFieldReference]

#### A.1.6.2.2	Timer instantiation

TimerInstance ::= TimerKeyword TimerList

TimerList ::= SingleTimerInstance{"," SingleTimerInstance}

SingleTimerInstance ::= TimerIdentifier [ArrayDef] [AssignmentChar TimerValue]

TimerKeyword ::= "timer"

TimerIdentifier ::= Identifier

TimerValue ::= Expression

TimerRef ::= (TimerIdentifier | TimerParIdentifier) {ArrayOrBitRef}

#### A.1.6.2.3	Component operations

ConfigurationStatements ::= ConnectStatement |

MapStatement |

DisconnectStatement |

UnmapStatement |

DoneStatement |

KilledStatement |

StartTCStatement |

StopTCStatement |

KillTCStatement

ConfigurationOps ::= CreateOp | SelfOp | SystemOp | MTCOp | RunningOp | AliveOp

CreateOp ::= ComponentType Dot CreateKeyword ["(" SingleExpression ")"] [AliveKeyword]

SystemOp ::= SystemKeyword

SelfOp ::= "self"

MTCOp ::= MTCKeyword

DoneStatement ::= ComponentId Dot DoneKeyword

KilledStatement ::= ComponentId Dot KilledKeyword

ComponentId ::= ComponentOrDefaultReference | (AnyKeyword | AllKeyword) ComponentKeyword

DoneKeyword ::= "done"

KilledKeyword ::= "killed"

RunningOp ::= ComponentId Dot RunningKeyword

RunningKeyword ::= "running"

AliveOp ::= ComponentId Dot AliveKeyword

CreateKeyword ::= "create"

AliveKeyword ::= "alive"

ConnectStatement ::= ConnectKeyword SingleConnectionSpec

ConnectKeyword ::= "connect"

SingleConnectionSpec ::= "(" PortRef "," PortRef ")"

PortRef ::= ComponentRef Colon Port

ComponentRef ::= ComponentOrDefaultReference | SystemOp | SelfOp | MTCOp

DisconnectStatement ::= DisconnectKeyword [SingleOrMultiConnectionSpec]

SingleOrMultiConnectionSpec ::= SingleConnectionSpec |

AllConnectionsSpec |

AllPortsSpec |

AllCompsAllPortsSpec

AllConnectionsSpec ::= "(" PortRef ")"

AllPortsSpec ::= "(" ComponentRef ":" AllKeyword PortKeyword ")"

AllCompsAllPortsSpec ::= "(" AllKeyword ComponentKeyword ":" AllKeyword PortKeyword ")"

DisconnectKeyword ::= "disconnect"

MapStatement ::= MapKeyword SingleConnectionSpec

MapKeyword ::= "map"

UnmapStatement ::= UnmapKeyword [SingleOrMultiConnectionSpec]

UnmapKeyword ::= "unmap"

StartTCStatement ::= ComponentOrDefaultReference Dot StartKeyword "(" FunctionInstance ")"

StartKeyword ::= "start"

StopTCStatement ::= StopKeyword | (ComponentReferenceOrLiteral Dot StopKeyword) |

(AllKeyword ComponentKeyword Dot StopKeyword)

ComponentReferenceOrLiteral ::= ComponentOrDefaultReference | MTCOp | SelfOp

KillTCStatement ::= KillKeyword | (ComponentReferenceOrLiteral Dot KillKeyword) |

(AllKeyword ComponentKeyword Dot KillKeyword)

ComponentOrDefaultReference ::= VariableRef | FunctionInstance

KillKeyword ::= "kill"

#### A.1.6.2.4	Port operations

Port ::= (PortIdentifier | PortParIdentifier) {ArrayOrBitRef}

CommunicationStatements ::= SendStatement |

CallStatement |

ReplyStatement |

RaiseStatement |

ReceiveStatement |

TriggerStatement |

GetCallStatement |

GetReplyStatement |

CatchStatement |

CheckStatement |

ClearStatement |

StartStatement |

StopStatement |

HaltStatement

SendStatement ::= Port Dot PortSendOp

PortSendOp ::= SendOpKeyword "(" SendParameter ")" [ToClause]

SendOpKeyword ::= "send"

SendParameter ::= TemplateInstance

ToClause ::= ToKeyword ( AddressRef |

AddressRefList |

AllKeyword ComponentKeyword )

AddressRefList ::= "(" AddressRef {"," AddressRef} ")"

ToKeyword ::= "to"

AddressRef ::= TemplateInstance

CallStatement ::= Port Dot PortCallOp  [PortCallBody]

PortCallOp ::= CallOpKeyword "(" CallParameters ")" [ToClause]

CallOpKeyword ::= "call"

CallParameters ::= TemplateInstance ["," CallTimerValue]

CallTimerValue ::= TimerValue | NowaitKeyword

NowaitKeyword ::= "nowait"

PortCallBody ::= "{" CallBodyStatementList "}"

CallBodyStatementList ::= {CallBodyStatement [SemiColon]}+

CallBodyStatement ::= CallBodyGuard  StatementBlock

CallBodyGuard ::= AltGuardChar CallBodyOps

CallBodyOps ::= GetReplyStatement | CatchStatement

ReplyStatement ::= Port Dot PortReplyOp

PortReplyOp ::= ReplyKeyword "(" TemplateInstance [ReplyValue]")" [ToClause]

ReplyKeyword ::= "reply"

ReplyValue ::= ValueKeyword Expression

RaiseStatement ::= Port Dot PortRaiseOp

PortRaiseOp ::= RaiseKeyword "(" Signature "," TemplateInstance ")" [ToClause]

RaiseKeyword ::= "raise"

ReceiveStatement ::= PortOrAny Dot PortReceiveOp

PortOrAny ::= Port | AnyKeyword PortKeyword

PortReceiveOp ::= ReceiveOpKeyword ["(" ReceiveParameter ")"] [FromClause] [PortRedirect]

ReceiveOpKeyword ::= "receive"

ReceiveParameter ::= TemplateInstance

FromClause ::= FromKeyword ( AddressRef |

AddressRefList |

AnyKeyword ComponentKeyword )

FromKeyword ::= "from"

PortRedirect ::= PortRedirectSymbol (ValueSpec [SenderSpec] | SenderSpec)

PortRedirectSymbol ::= "->"

ValueSpec ::= ValueKeyword VariableRef

ValueKeyword ::= "value"

SenderSpec ::= SenderKeyword VariableRef

SenderKeyword ::= "sender"

TriggerStatement ::= PortOrAny Dot PortTriggerOp

PortTriggerOp ::= TriggerOpKeyword ["(" ReceiveParameter ")"] [FromClause] [PortRedirect]

TriggerOpKeyword ::= "trigger"

GetCallStatement ::= PortOrAny  Dot PortGetCallOp

PortGetCallOp ::= GetCallOpKeyword ["(" ReceiveParameter ")"] [FromClause]

[PortRedirectWithParam]

GetCallOpKeyword ::= "getcall"

PortRedirectWithParam ::= PortRedirectSymbol RedirectWithParamSpec

RedirectWithParamSpec ::= ParamSpec [SenderSpec] |

SenderSpec

ParamSpec ::= ParamKeyword ParamAssignmentList

ParamKeyword ::= "param"

ParamAssignmentList ::= "(" (AssignmentList | VariableList) ")"

AssignmentList ::= VariableAssignment {"," VariableAssignment}

VariableAssignment ::= VariableRef AssignmentChar ParameterIdentifier

ParameterIdentifier ::= ValueParIdentifier

VariableList ::= VariableEntry  {"," VariableEntry}

VariableEntry ::= VariableRef | NotUsedSymbol

GetReplyStatement ::= PortOrAny Dot PortGetReplyOp

PortGetReplyOp ::= GetReplyOpKeyword ["(" ReceiveParameter [ValueMatchSpec] ")"]

[FromClause] [PortRedirectWithValueAndParam]

PortRedirectWithValueAndParam ::= PortRedirectSymbol RedirectWithValueAndParamSpec

RedirectWithValueAndParamSpec ::= ValueSpec [ParamSpec] [SenderSpec] |

RedirectWithParamSpec

GetReplyOpKeyword ::= "getreply"

ValueMatchSpec ::= ValueKeyword TemplateInstance

CheckStatement ::= PortOrAny Dot PortCheckOp

PortCheckOp ::= CheckOpKeyword ["(" CheckParameter ")"]

CheckOpKeyword ::= "check"

CheckParameter ::= CheckPortOpsPresent | FromClausePresent | RedirectPresent

FromClausePresent ::= FromClause [PortRedirectSymbol SenderSpec]

RedirectPresent ::= PortRedirectSymbol SenderSpec

CheckPortOpsPresent ::= PortReceiveOp | PortGetCallOp | PortGetReplyOp | PortCatchOp

CatchStatement ::= PortOrAny Dot PortCatchOp

PortCatchOp ::= CatchOpKeyword ["("CatchOpParameter ")"] [FromClause] [PortRedirect]

CatchOpKeyword ::= "catch"

CatchOpParameter ::= Signature "," TemplateInstance | TimeoutKeyword

ClearStatement ::= PortOrAll Dot PortClearOp

PortOrAll ::= Port | AllKeyword PortKeyword

PortClearOp ::= ClearOpKeyword

ClearOpKeyword ::= "clear"

StartStatement ::= PortOrAll Dot PortStartOp

PortStartOp ::= StartKeyword

StopStatement ::= PortOrAll Dot PortStopOp

PortStopOp ::= StopKeyword

StopKeyword ::= "stop"

HaltStatement ::= PortOrAll Dot PortHaltOp

PortHaltOp ::= HaltKeyword

HaltKeyword ::= "halt"

AnyKeyword ::= "any"

#### A.1.6.2.5	Timer operations

TimerStatements ::= StartTimerStatement | StopTimerStatement | TimeoutStatement

TimerOps ::= ReadTimerOp | RunningTimerOp

StartTimerStatement ::= TimerRef Dot StartKeyword ["(" TimerValue ")"]

StopTimerStatement ::= TimerRefOrAll Dot StopKeyword

TimerRefOrAll ::= TimerRef | AllKeyword TimerKeyword

ReadTimerOp ::= TimerRef Dot ReadKeyword

ReadKeyword ::= "read"

RunningTimerOp ::= TimerRefOrAny  Dot RunningKeyword

TimeoutStatement ::= TimerRefOrAny  Dot TimeoutKeyword

TimerRefOrAny ::= TimerRef | AnyKeyword TimerKeyword

TimeoutKeyword ::= "timeout"

### A.1.6.3	Type

Type ::= PredefinedType | ReferencedType

PredefinedType ::= BitStringKeyword |

BooleanKeyword |

CharStringKeyword |

UniversalCharString |

IntegerKeyword |

OctetStringKeyword |

HexStringKeyword |

VerdictTypeKeyword |

FloatKeyword |

AddressKeyword |

DefaultKeyword |

AnyTypeKeyword

BitStringKeyword ::= "bitstring"

BooleanKeyword ::= "boolean"

IntegerKeyword ::= "integer"

OctetStringKeyword ::= "octetstring"

HexStringKeyword ::= "hexstring"

VerdictTypeKeyword ::= "verdicttype"

FloatKeyword ::= "float"

AddressKeyword ::= "address"

DefaultKeyword ::= "default"

AnyTypeKeyword ::= "anytype"

CharStringKeyword ::= "charstring"

UniversalCharString ::= UniversalKeyword CharStringKeyword

UniversalKeyword ::= "universal"

ReferencedType ::= [GlobalModuleId Dot] TypeReference [ExtendedFieldReference]

TypeReference ::= StructTypeIdentifier[TypeActualParList] |

EnumTypeIdentifier |

SubTypeIdentifier |

ComponentTypeIdentifier

TypeActualParList ::= "(" TypeActualPar {"," TypeActualPar} ")"

TypeActualPar ::= ConstantExpression

ArrayDef ::= {"[" ArrayBounds [".." ArrayBounds] "]"}+

ArrayBounds ::= SingleConstExpression

/* STATIC SEMANTICS - ArrayBounds will resolve to a non negative value of integer type */

### A.1.6.4	Value

Value ::= PredefinedValue | ReferencedValue

PredefinedValue ::= BitStringValue |

BooleanValue |

CharStringValue |

IntegerValue |

OctetStringValue |

HexStringValue |

VerdictTypeValue |

EnumeratedValue |

FloatValue |

AddressValue |

OmitValue

BitStringValue ::= Bstring

BooleanValue ::= "true" | "false"

IntegerValue ::= Number

OctetStringValue ::= Ostring

HexStringValue ::= Hstring

VerdictTypeValue ::= "pass" | "fail" | "inconc" | "none" | "error"

EnumeratedValue ::= EnumerationIdentifier

CharStringValue ::= Cstring | Quadruple

Quadruple ::= CharKeyword "(" Group "," Plane "," Row "," Cell ")"

CharKeyword ::= "char"

Group ::= Number

Plane ::= Number

Row ::= Number

Cell ::= Number

FloatValue ::= FloatDotNotation | FloatENotation

FloatDotNotation ::= Number Dot DecimalNumber

FloatENotation ::= Number [Dot DecimalNumber] Exponential [Minus] Number

Exponential ::= "E"

ReferencedValue ::= ValueReference [ExtendedFieldReference]

ValueReference ::= [GlobalModuleId Dot] (ConstIdentifier | ExtConstIdentifier |

ModuleParIdentifier ) |

ValueParIdentifier |

VarIdentifier

Number ::= (NonZeroNum {Num}) | "0"

NonZeroNum ::= "1" | "2" | "3" | "4" | "5" | "6" | "7" | "8" | "9"

DecimalNumber ::= {Num}+

Num ::= "0" | NonZeroNum

Bstring ::= "'" {Bin} "'" "B"

Bin ::= "0" | "1"

Hstring ::= "'" {Hex} "'" "H"

Hex ::= Num | "A" | "B" | "C" | "D" | "E" | "F"| "a" | "b" | "c" | "d" | "e" | "f"

Ostring ::= "'" {Oct} "'" "O"

Oct ::= Hex Hex

Cstring ::= """ {Char} """

Char ::= /* REFERENCE - A character defined by the relevant CharacterString type. For charstring a character from the character set defined in ISO/IEC 646. For universal charstring a character from any character set defined in ISO/IEC 10646 */

Identifier ::= Alpha{AlphaNum | Underscore}

Alpha ::= UpperAlpha | LowerAlpha

AlphaNum ::= Alpha | Num

UpperAlpha ::= "A" | "B" | "C" | "D" | "E" | "F" | "G" | "H" | "I" | "J" | "K" | "L" | "M" | "N" | "O" | "P" | "Q" | "R" | "S" | "T" | "U" | "V" | "W" | "X" | "Y" | "Z"

LowerAlpha ::= "a" | "b" | "c" | "d" | "e" | "f" | "g" | "h" | "i" | "j" | "k" | "l" | "m" | "n" | "o" | "p" | "q" | "r" | "s" | "t" | "u" | "v" | "w" | "x" | "y" | "z"

ExtendedAlphaNum ::= /* REFERENCE - A graphical character from the BASIC LATIN or from the LATIN-1 SUPPLEMENT character sets defined in ISO/IEC 10646  (characters from char (0,0,0,32) to char (0,0,0,126), from char (0,0,0,161) to char (0,0,0,172) and from char (0,0,0,174) to char (0,0,0,255) */

FreeText ::= """ {ExtendedAlphaNum} """

AddressValue ::= "null"

OmitValue ::= OmitKeyword

OmitKeyword ::= "omit"

### A.1.6.5	Parameterization

InParKeyword ::= "in"

OutParKeyword ::= "out"

InOutParKeyword ::= "inout"

FormalValuePar ::= [(InParKeyword | InOutParKeyword | OutParKeyword)] Type ValueParIdentifier

ValueParIdentifier ::= Identifier

FormalPortPar ::= [InOutParKeyword] PortTypeIdentifier PortParIdentifier

PortParIdentifier ::= Identifier

FormalTimerPar ::= [InOutParKeyword] TimerKeyword TimerParIdentifier

TimerParIdentifier ::= Identifier

FormalTemplatePar ::= [( InParKeyword | OutParKeyword | InOutParKeyword )]

( TemplateKeyword | RestrictedTemplate ) Type TemplateParIdentifier

TemplateParIdentifier ::= Identifier

RestrictedTemplate ::= OmitKeyword | ( TemplateKeyword TemplateRestriction )

TemplateRestriction ::= "(" OmitKeyword | ValueKeyword | PresentKeyword ")"

### A.1.6.6	With statement

WithStatement ::= WithKeyword WithAttribList

WithKeyword ::= "with"

WithAttribList ::= "{" MultiWithAttrib "}"

MultiWithAttrib ::= {SingleWithAttrib [SemiColon]}

SingleWithAttrib ::= AttribKeyword  [OverrideKeyword] [AttribQualifier] AttribSpec

AttribKeyword ::= EncodeKeyword |

VariantKeyword |

DisplayKeyword |

ExtensionKeyword |
                       OptionalKeyword

EncodeKeyword ::= "encode"

VariantKeyword ::= "variant"

DisplayKeyword ::= "display"

ExtensionKeyword ::= "extension"

OverrideKeyword ::= "override"

AttribQualifier ::= "(" DefOrFieldRefList ")"

DefOrFieldRefList ::= DefOrFieldRef {"," DefOrFieldRef}

DefOrFieldRef ::= DefinitionRef | FieldReference | AllRef

DefinitionRef ::= StructTypeIdentifier |

EnumTypeIdentifier |

PortTypeIdentifier |

ComponentTypeIdentifier |

SubTypeIdentifier |

ConstIdentifier |

TemplateIdentifier |

AltstepIdentifier |

TestcaseIdentifier |

FunctionIdentifier |

SignatureIdentifier |

VarIdentifier |

TimerIdentifier |

PortIdentifier |

ModuleParIdentifier |

FullGroupIdentifier

AllRef ::= ( GroupKeyword AllKeyword [ExceptKeyword "{" GroupRefList "}"]) |

( TypeDefKeyword AllKeyword [ExceptKeyword "{" TypeRefList "}"]) |

( TemplateKeyword AllKeyword [ExceptKeyword "{" TemplateRefList "}"]) |

( ConstKeyword AllKeyword [ExceptKeyword "{" ConstRefList "}"]) |

( AltstepKeyword AllKeyword [ExceptKeyword "{" AltstepRefList "}"]) |

( TestcaseKeyword AllKeyword [ExceptKeyword "{" TestcaseRefList "}"]) |

( FunctionKeyword AllKeyword [ExceptKeyword "{" FunctionRefList "}"]) |

( SignatureKeyword AllKeyword [ExceptKeyword "{" SignatureRefList "}"]) |

( ModuleParKeyword AllKeyword [ExceptKeyword "{" ModuleParRefList "}"])

AttribSpec ::= FreeText

### A.1.6.7	Behaviour statements

BehaviourStatements ::= TestcaseInstance |

FunctionInstance |

ReturnStatement |

AltConstruct |

InterleavedConstruct |

LabelStatement |

GotoStatement |

RepeatStatement |

DeactivateStatement |

AltstepInstance |

ActivateOp |

BreakStatement |

ContinueStatement

VerdictStatements ::= SetLocalVerdict

VerdictOps ::= GetLocalVerdict

SetLocalVerdict ::= SetVerdictKeyword "(" SingleExpression { "," LogItem } ")"

SetVerdictKeyword ::= "setverdict"

GetLocalVerdict ::= "getverdict"

SUTStatements ::= ActionKeyword "(" [ActionText ] {StringOp ActionText} ")"

ActionKeyword ::= "action"

ActionText ::= FreeText | Expression

ReturnStatement ::= ReturnKeyword  [Expression]

AltConstruct ::= AltKeyword "{" AltGuardList "}"

AltKeyword ::= "alt"

AltGuardList ::= {GuardStatement | ElseStatement [SemiColon]}

GuardStatement ::= AltGuardChar (AltstepInstance [StatementBlock] | GuardOp StatementBlock)

ElseStatement ::= "["ElseKeyword "]" StatementBlock

AltGuardChar ::= "[" [BooleanExpression] "]"

GuardOp ::= TimeoutStatement |

ReceiveStatement |

TriggerStatement |

GetCallStatement |

CatchStatement |

CheckStatement |

GetReplyStatement |

DoneStatement |

KilledStatement

InterleavedConstruct ::= InterleavedKeyword "{" InterleavedGuardList "}"

InterleavedKeyword ::= "interleave"

InterleavedGuardList ::= {InterleavedGuardElement [SemiColon]}+

InterleavedGuardElement ::= InterleavedGuard InterleavedAction

InterleavedGuard ::= "[" "]" GuardOp

InterleavedAction ::= StatementBlock

LabelStatement ::= LabelKeyword LabelIdentifier

LabelKeyword ::= "label"

LabelIdentifier ::= Identifier

GotoStatement ::= GotoKeyword LabelIdentifier

GotoKeyword ::= "goto"

RepeatStatement ::= "repeat"

ActivateOp ::= ActivateKeyword "(" AltstepInstance ")"

ActivateKeyword ::= "activate"

DeactivateStatement ::= DeactivateKeyword ["(" ComponentOrDefaultReference ")"]

DeactivateKeyword ::= "deactivate"

BreakStatement ::= "break"

ContinueStatement ::= "continue"

### A.1.6.8	Basic statements

BasicStatements ::= Assignment | LogStatement | LoopConstruct | ConditionalConstruct |

SelectCaseConstruct | StatementBlock

Expression ::= SingleExpression | CompoundExpression

CompoundExpression ::= FieldExpressionList | ArrayExpression

/* STATIC SEMANTICS - Within CompoundExpression the ArrayExpression can be used for Arrays, record, record of and set of types. */

FieldExpressionList ::= "{" FieldExpressionSpec {"," FieldExpressionSpec} "}"

FieldExpressionSpec ::= FieldReference AssignmentChar NotUsedOrExpression

ArrayExpression ::= "{" [ArrayElementExpressionList] "}"

ArrayElementExpressionList ::= NotUsedOrExpression  {"," NotUsedOrExpression}

NotUsedOrExpression ::= Expression | NotUsedSymbol

ConstantExpression ::= SingleConstExpression | CompoundConstExpression

SingleConstExpression ::= SingleExpression

/* STATIC SEMANTICS - SingleConstExpression shall not contain Variables or Module parameters and shall resolve to a constant Value at compile time */

BooleanExpression ::= SingleExpression

/* STATIC SEMANTICS - BooleanExpression shall resolve to a Value of type Boolean */

CompoundConstExpression ::= FieldConstExpressionList | ArrayConstExpression

/* STATIC SEMANTICS - Within CompoundConstExpression the ArrayConstExpression can be used for arrays, record, record of and set of types. */

FieldConstExpressionList ::= "{" FieldConstExpressionSpec {"," FieldConstExpressionSpec} "}"

FieldConstExpressionSpec ::= FieldReference AssignmentChar ConstantExpression

ArrayConstExpression ::= "{" [ArrayElementConstExpressionList] "}"

ArrayElementConstExpressionList ::= ConstantExpression {"," ConstantExpression}

Assignment ::= VariableRef AssignmentChar (Expression | TemplateBody)

/* STATIC SEMANTICS - The Expression on the right hand side of Assignment shall evaluate to an explicit value of a type compatible with the type of the left hand side for value variables and shall evaluate to an explicit value, template (literal or a template instance) or a matching mechanism compatible with the type of the left hand side for template variables. */

SingleExpression ::= XorExpression { "or" XorExpression }

/* STATIC SEMANTICS - If more than one XorExpression exists, then the XorExpressions shall evaluate to specific values of compatible types */

XorExpression ::= AndExpression { "xor" AndExpression }

/* STATIC SEMANTICS - If more than one AndExpression exists, then the AndExpressions shall evaluate to specific values of compatible types */

AndExpression ::= NotExpression { "and" NotExpression }

/* STATIC SEMANTICS - If more than one NotExpression exists, then the NotExpressions shall evaluate to specific values of compatible types */

NotExpression ::= [ "not" ] EqualExpression

/* STATIC SEMANTICS - Operands of the not operator shall be of type boolean or derivatives of type Boolean. */

EqualExpression ::= RelExpression { EqualOp RelExpression }

/* STATIC SEMANTICS - If more than one RelExpression exists, then the RelExpressions shall evaluate to specific values of compatible types */

RelExpression ::= ShiftExpression [ RelOp ShiftExpression ]

/* STATIC SEMANTICS - If both ShiftExpressions exist, then each ShiftExpression shall evaluate to a specific integer, Enumerated or float Value or derivatives of these types */

ShiftExpression ::= BitOrExpression { ShiftOp BitOrExpression }

/* STATIC SEMANTICS - Each Result shall resolve to a specific Value. If more than one Result exists the right-hand operand shall be of type integer or derivatives and if the shift op is "<<" or ">>" then the left-hand operand shall resolve to either bitstring, hexstring or octetstring type or derivatives of these types. If the shift op is "<@" or "@>" then the left-hand operand shall be of type bitstring, hexstring, octetstring, charstring, universal charstring, record of, set of, or array, or derivatives of these types */

BitOrExpression ::= BitXorExpression { "or4b" BitXorExpression }

/* STATIC SEMANTICS - If more than one BitXorExpression exists, then the BitXorExpressions shall evaluate to specific values of compatible types */

BitXorExpression ::= BitAndExpression { "xor4b" BitAndExpression }

/* STATIC SEMANTICS - If more than one BitAndExpression exists, then the BitAndExpressions shall evaluate to specific values of compatible types */

BitAndExpression ::= BitNotExpression { "and4b" BitNotExpression }

/* STATIC SEMANTICS - If more than one BitNotExpression exists, then the BitNotExpressions shall evaluate to specific values of compatible types */

BitNotExpression ::= [ "not4b" ] AddExpression

/* STATIC SEMANTICS - If the not4b operator exists, the operand shall be of type bitstring, octetstring or hexstring or derivatives of these types. */

AddExpression ::= MulExpression { AddOp MulExpression }

/* STATIC SEMANTICS - Each MulExpression shall resolve to a specific Value. If more than one MulExpression exists and the AddOp resolves to StringOp then the MulExpressions shall be valid operands for StringOp. If more than one MulExpression exists and the AddOp does not resolve to StringOp then the MulExpression shall both resolve to type integer or float or derivatives of these types.*/

MulExpression ::= UnaryExpression { MultiplyOp UnaryExpression }

/* STATIC SEMANTICS - Each UnaryExpression shall resolve to a specific Value. If more than one UnaryExpression exists then the UnaryExpressions shall resolve to type integer or float or derivatives of these types. */

UnaryExpression ::= [ UnaryOp ] Primary

/* STATIC SEMANTICS - Primary shall resolve to a specific Value of type integer or float or derivatives of these types.*/

Primary ::= OpCall | Value | "(" SingleExpression ")"

ExtendedFieldReference ::= {(Dot ( StructFieldIdentifier | TypeDefIdentifier))

| ArrayOrBitRef }+

/* STATIC SEMANTIC - The TypeDefIdentifier shall be used only if the type of the VarInstance or ReferencedValue in wich the ExtendedFieldReference is used is anytype.*/

OpCall ::= ConfigurationOps |

VerdictOps |

TimerOps |

TestcaseInstance |

FunctionInstance |

TemplateOps |

ActivateOp

AddOp ::= "+" | "-" | StringOp

/* STATIC SEMANTICS - Operands of the "+" or "-" operators shall be of type integer or float or derivations of integer or float (i.e. subrange) */

MultiplyOp ::= "*" | "/" | "mod" | "rem"

/* STATIC SEMANTICS - Operands of the "*", "/", rem or mod operators shall be of type integer or float or derivations of integer or float (i.e. subrange) */

UnaryOp ::= "+" | "-"

/* STATIC SEMANTICS - Operands of the "+" or "-" operators shall be of type integer or float or derivations of integer or float (i.e. subrange) */

RelOp ::= "<" | ">" | ">=" | "<="

/* STATIC SEMANTICS - the precedence of the operators is defined in Table 6 */

EqualOp ::= "==" | "!="

StringOp ::= "&"

/* STATIC SEMANTICS - Operands of the list operator shall be bitstring, hexstring, octetstring, (universal) character string, record of, set of, or array types, or derivates of these types */

ShiftOp ::= "<<" | ">>" | "<@" | "@>"

LogStatement ::= LogKeyword "(" LogItem { "," LogItem } ")"

LogKeyword ::= "log"

LogItem ::= FreeText | TemplateInstance

LoopConstruct ::= ForStatement |

WhileStatement |

DoWhileStatement

ForStatement ::= ForKeyword "(" Initial SemiColon Final SemiColon Step ")"

StatementBlock

ForKeyword ::= "for"

Initial ::= VarInstance | Assignment

Final ::= BooleanExpression

Step ::= Assignment

WhileStatement ::= WhileKeyword "(" BooleanExpression ")"

StatementBlock

WhileKeyword ::= "while"

DoWhileStatement ::= DoKeyword StatementBlock

WhileKeyword "(" BooleanExpression ")"

DoKeyword ::= "do"

ConditionalConstruct ::= IfKeyword "(" BooleanExpression ")"

StatementBlock

{ElseIfClause}[ElseClause]

IfKeyword ::= "if"

ElseIfClause ::= ElseKeyword  IfKeyword "(" BooleanExpression ")"  StatementBlock

ElseKeyword ::= "else"

ElseClause ::= ElseKeyword  StatementBlock

SelectCaseConstruct ::= SelectKeyword "(" SingleExpression ")" SelectCaseBody

SelectKeyword ::= "select"

SelectCaseBody ::= "{" { SelectCase }+ "}"

SelectCase ::= CaseKeyword ( "(" TemplateInstance {"," TemplateInstance } ")" | ElseKeyword )

StatementBlock

CaseKeyword ::= "case"

### A.1.6.9	Miscellaneous productions

Dot ::= "."

Dash ::= "-"

Minus ::= Dash

SemiColon ::= ";"

Colon ::= ":"

Underscore ::= "_"

AssignmentChar ::= ":="

# Comments

Here is a double semantical use of the term “visibility” – but I think the difference is understandable from the context – plese check as well.