## 8.1bis	Importing from ASN.1 modules

ASN.1 definitions are public by default (see clause 8.2.5 of ES 201 873-1 [1]).

When importing from ASN.1 modules, it is mandatory to use one of the following language identifier strings:

"ASN.1:2002"	for ASN.1 version 2002;

"ASN.1:1997"	for ASN.1 version 1997;

"ASN.1:1994"	for ASN.1 version 1994;

"ASN.1:1988"	for ASN.1 version 1988 (CCITT Blue Book).

NOTE 1:	Language identifiers "ASN.1:1997", "ASN.1:1994" and "ASN.1:1988" refer to versions of ASN.1 based on superseded ITU-T Recommendations (including the base document and all published Amendments and Technical Corrigenda published so far complementing the base document). The only purpose to include them into the present document is to allocate unique identifiers if protocol modules based on these ASN.1 versions are used with TTCN-3. When ASN.1 version 1997 is supported, the support of Amendment 3 to ITU-T Recommendation X.680 [2] is not considered.

NOTE 2:	When "ASN.1:1988" is supported, the ASN.1 definitions will be imported from such modules according to the syntactical and semantical rules of CCITT Recommendation X.208 [13] (Blue Book).

NOTE 3:	References to the 1994, 1997 and the Blue Book (1988) versions of ASN.1 can be found in annex D.

When importing ASN.1 types, values and value sets, first they have to be transformed to TTCN-3 types and values respectively, according to the rules given in clause 8 and in clause 9.1 of the present document and import the resulted definitions afterwards based on the rules defined below.

NOTE 4:	ASN.1 value sets are semantically equivalent to subtypes. Hence, in the present document they are not handled separately but all rules specified for ASN.1 types also apply to ASN.1 value sets.