### 5.3.1	Connection

TriComponentIdType	A value of type TriComponentIdType includes an identifier, a name and the component type. The distinct value of the latter is the component type name as specified in the TTCN-3 ATS. This abstract type is mainly used to resolve TRI communication operations on TSI ports that have mappings to many test component ports. It is also used to resolve TCI component handling.

NOTE:	For the handling of TCI operations on any or all components, the component type name can also be set to “ANY” or “ALL”. In that case, both the identifier and the component name are to be ignored.