TD <>

Draft ETSI ES XXX XXX V0.0.1 (yyyy-mm)

ETSI Standard

Methods for Testing and Specification (MTS);

Testing and Test Control Notation version 3 Extension;

Package xx: xxx

Reference

<Workitem>

Keywords

<keyword>

ETSI

650 Route des Lucioles

F-06921 Sophia Antipolis Cedex - FRANCE

Tel.: +33 4 92 94 42 00   Fax: +33 4 93 65 47 16

Siret N° 348 623 562 00017 - NAF 742 C

Association à but non lucratif enregistrée à la

Sous-Préfecture de Grasse (06) N° 7803/88

Important notice

Individual copies of the present document can be downloaded from:
http://www.etsi.org

The present document may be made available in more than one electronic version or in print. In any case of existing or perceived difference in contents between such versions, the reference version is the Portable Document Format (PDF). In case of dispute, the reference shall be the printing on ETSI printers of the PDF version kept on a specific network drive within ETSI Secretariat.

Users of the present document should be aware that the document may be subject to revision or change of status. Information on the current status of this and other ETSI documents is available at http://portal.etsi.org/tb/status/status.asp

If you find errors in the present document, please send your comment to one of the following services:
http://portal.etsi.org/chaircor/ETSI_support.asp

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© European Telecommunications Standards Institute yyyy.

All rights reserved.

DECTTM, PLUGTESTSTM, UMTSTM, TIPHONTM, the TIPHON logo and the ETSI logo are Trade Marks of ETSI registered for the benefit of its Members.
3GPPTM is a Trade Mark of ETSI registered for the benefit of its Members and of the 3GPP Organizational Partners.

Contents

Intellectual Property Rights	5

Foreword	5

1	Scope	6

2	References	6

2.1	Normative references	6

2.2	Informative references	7

3	Definitions, symbols and abbreviations	7

3.1	Definitions	7

3.2	Abbreviations	8

4	Package conformance and compatibility	8

4	Package concepts for the core language	9

4.1	Time and Sampling	9

4.1.1	Time	10

4.1.2	Sampling	10

4.2	Data streams	11

4.2.3 	Data stream access operations	14

4.2.4	Data stream navigation operations	18

4.2.5	Data stream extraction and application operations	19

4.3	The assert statement	22

4.4	Control structures for continuous and hybrid behavior	23

4.4.1	 Modes	23

4.4.2	Atomic modes: the cont statement	29

4.4.3	Parallel mode composition: the par statement	30

4.4.4	Sequential mode composition: the seq statement	32

4.4.5	Parametrizable modes	33

4.5 	 The wait statement	34

5	Package semantics	34

6	TRI extensions for the package	34

6.1	triStartClock (TE → PA)	34

6.2	triReadClock (TE → PA)	35

6.3	triNextSampling (TE → PA, SA → PA)	35

6.4	triBeginWait (TE → PA)	36

6.5	triProcessStep (PA → TE)	36

6.6	triEndWait (PA → TE)	37

6.7	triSetStreamValue (TE → SA)	38

6.8	triGetStreamValue (TE → SA)	39

7	TCI extensions for the package	39

7.1	tciSetStreamValue	40

7.2	tciGetStreamValue	40

8	xxx extensions for the package	41

8.1	User defined subdivisions of clause(s) from here onwards	41

A.1	First clause of the annex	41

A.1.1	First subdivided clause of the annex	41

A.1	First clause of the annex	41

A.1.1	First subdivided clause of the annex	41

B.1	Testing an Advanced Cruise Control	42

B.2	Testing a window lifter application	45

First clause of the annex	47

B.1.1	First subdivided clause of the annex	47

History	49

# Intellectual Property Rights

IPRs essential or potentially essential to the present document may have been declared to ETSI. The information pertaining to these essential IPRs, if any, is publicly available for ETSI members and non-members, and can be found in ETSI SR 000 314: "Intellectual Property Rights (IPRs); Essential, or potentially Essential, IPRs notified to ETSI in respect of ETSI standards", which is available from the ETSI Secretariat. Latest updates are available on the ETSI Web server (http://webapp.etsi.org/IPR/home.asp).

Pursuant to the ETSI IPR Policy, no investigation, including IPR searches, has been carried out by ETSI. No guarantee can be given as to the existence of other IPRs not referenced in ETSI SR 000 314 (or the updates on the ETSI Web server) which are, or may be, or may become, essential to the present document.

# Foreword

This ETSI Standard (ES) has been produced by ETSI Technical Committee Methods for Testing and Specification (MTS), and is now submitted for the ETSI standards Membership Approval Procedure.

The present document relates to the multi-part standard covering the Testing and Test Control Notation version 3, as identified below:

ES 201873 Part 1:	"TTCN-3 Core Language";

ES 201873 Part 2:	"TTCN-3 Tabular presentation Format (TFT)";

ES 201873 Part 3:	"TTCN-3 Graphical presentation Format (GFT)";

ES 201873 Part 4:	"TTCN-3 Operational Semantics";

ES 201873 Part 5:	"TTCN-3 Runtime Interface (TRI)";

ES 201873 Part 6:	"TTCN-3 Control Interface (TCI)";

ES 201873 Part 7:	"Using ASN.1 with TTCN-3";

ES 201873 Part 8:	"The IDL to TTCN-3 Mapping";

ES 201873 Part 9:	"Using XML schema with TTCN-3";

ES 201873 Part 10:	"TTCN-3 Documentation Comment Specification".

# 1	Scope

The present document defines the xxx package of TTCN-3. TTCN-3 can be used for the specification of all types of reactive system tests over a variety of communication ports. Typical areas of application are protocol testing (including mobile and Internet protocols), service testing (including supplementary services), module testing, testing of CORBA based platforms, APIs, etc. TTCN-3 is not restricted to conformance testing and can be used for many other kinds of testing including interoperability, robustness, regression, system and integration testing. The specification of test suites for physical layer protocols is outside the scope of the present document.

TTCN-3 packages are intended to define additional TTCN-3 concepts, which are not mandatory as concepts in the TTCN-3 core language, but which are optional as part of a package which is suited for dedicated applications and/or usages of TTCN-3.

This package defines …

While the design of TTCN-3 package has taken into account the consistency of a combined usage of the core language with a number of packages, the concrete usages of and guidelines for this package in combination with other packages is outside the scope of the present document.

# 2	References

References are either specific (identified by date of publication and/or edition number or version number) or non-specific.

For a specific reference, subsequent revisions do not apply.

Non-specific reference may be made only to a complete document or a part thereof and only in the following cases:

if it is accepted that it will be possible to use all future changes of the referenced document for the purposes of the referring document;

for informative references.

Referenced documents which are not found to be publicly available in the expected location might be found at http://docbox.etsi.org/Reference.

For online referenced documents, information sufficient to identify and locate the source shall be provided. Preferably, the primary source of the referenced document should be cited, in order to ensure traceability. Furthermore, the reference should, as far as possible, remain valid for the expected life of the document. The reference shall include the method of access to the referenced document and the full network address, with the same punctuation and use of upper case and lower case letters.

NOTE:	While any hyperlinks included in this clause were valid at the time of publication ETSI cannot guarantee their long term validity.

## 2.1	Normative references

The following referenced documents are indispensable for the application of the present document. For dated references, only the edition cited applies. For non-specific references, the latest edition of the referenced document (including any amendments) applies.

[1]	ETSI ES 201 873-1: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; Part 1: TTCN-3 Core Language".

[2]	ETSI ES 201 873-4: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; Part 4: TTCN-3 Operational Semantics".

[3]	ETSI ES 201 873-5: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; Part 5: TTCN-3 Runtime Interface (TRI)".

[4]	ETSI ES 201 873-6: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; Part 6: TTCN-3 Control Interface (TCI)".

[5]	ISO/IEC 9646-1: "Information technology - Open Systems Interconnection -Conformance testing methodology and framework; Part 1: General concepts"

[6]	…

## 2.2	Informative references

The following referenced documents are not essential to the use of the present document but they assist the user with regard to a particular subject area. For non-specific references, the latest version of the referenced document (including any amendments) applies.

[i.1]	ETSI ES 201 873-2: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; Part 2: TTCN-3 Tabular presentation Format (TFT)".

[i.2]	ETSI ES 201 873-3: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; Part 3: TTCN-3 Graphical presentation Format (GFT)".

[i.5]	ETSI ES 201 873-7: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; Part 7: Using ASN.1 with TTCN-3".

[i.6]	ETSI ES 201 873-8: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; Part 8: The IDL to TTCN-3 Mapping".

[i.7]	ETSI ES 201 873-9: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; Part 9: Using XML schema with TTCN-3".

[i.8]	ETSI ES 201 873-10: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; Part 10: TTCN-3 Documentation Comment Specification".

[i.9]	ITU-T Recommendation T.50 (1992): "International Reference Alphabet (IRA) (Formerly International Alphabet No. 5 or IA5) - Information technology - 7-bit coded character set for information interchange".

[i.10]	ISO/IEC 8859-1: "Information technology - 8-bit single-byte coded graphic character sets - Part 1: Latin alphabet No. 1", 1998.

[i.11]	Object Management Group (OMG): "The Common Object Request Broker: Architecture and Specification - IDL Syntax and Semantics". Version 2.6, FORMAL/01-12-01, December 2001.

[i.12]	Draft ETSI ES xxx: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3 Extension; Testing and Test Control Notation version 3 Extension; Package xx".

# 3	Definitions, symbols and abbreviations

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in ETSI ES 201873-1 [1], ETSI ES 201873-4 [2], ETSI ES 201873-5 [3], ETSI ES 201873-6 [4], ISO/IEC 9646-1 [5] and the following apply:

…

## 3.2	Abbreviations

For the purposes of the present document, the abbreviations given in ETSI ES 201873-1 [1], ETSI ES 201873-4 [2], ETSI ES 201873-5 [3], ETSI ES 201873-6 [4], ISO/IEC 9646-1 [5] and the following] apply:

<ACRONYM1>	<Explanation>

<ACRONYM2>	<Explanation>

<ACRONYM3>	<Explanation>

# 4	Package conformance and compatibility

The package presented in this document is identified by the package tag

(Needed for package version – reference previous package versions in the bibliography annex

"<Package>:<Year>" - to be used with modules complying with version xxx of the present document (see annex <bibliography>).)

"<Package>:<Year>" - to be used with modules complying with the present document.

For an implementation claiming to conform to this package version, all features specified in the present document shall be implemented consistently with the requirements given in the present document and in ES 201 873-4 [1] and ES 201 873-4 [2].

The package presented in this document is compatible to

Please choose the appropriate ones – and provide the version number.

ES 201873 Part 1 version xxx

ES 201873 Part 2 version xxx

ES 201873 Part 3 version xxx

ES 201873 Part 4 version xxx

ES 201873 Part 5 version xxx

ES 201873 Part 6 version xxx

ES 201873 Part 7 version xxx

ES 201873 Part 8 version xxx

ES 201873 Part 9 version xxx

ES 201873 Part 10 version xxx

If later versions of those parts are available and should be used instead, the compatibility the package presented in this document has to be checked individually.

The package presented in this document is also compatible to

Please choose the appropriate ones – and provide the version number.

ES XXXXXX Package xxx version xxx

ES XXXXXX Package xxx version xxx

and can be used together with those packages/this package.

If later versions of those packages are available and should be used instead, the compatibility to the package presented in this document has to be checked individually.

# 4	Package concepts for the core language

Systems can communicate its data or signals, either in discrete form (e.g. as an integer value) or in continuous form (e.g. real values). With respect to this difference signals are classified into four categories in the literature [3,4,5]. The categories distinguish whether the time and value domain of a signal is of discrete or continuous nature:

- Analogue signals are continuous in the time and value domain. Analog signals are the most 'natural' signal category, characterized by physical units (e.g. current, voltage, velocity) and measured with sensors. Typical examples of the physical quantities used in the area of embedded system development are the vehicle velocity, the field intensity of a radio station etc. Analog signals can be described as a piecewise function over time (eg vx = f (t)) .

- Time quantified signals are discrete signals in the time domain. The signal values are defined only at predetermined time points (sampling points). Typical examples of time quantified signals are the time-value pairs of a recorded signal. A typical representation of a time quantified signal is aseries or an array of real numbers. Even if the original signal is a synthetic function it can only be reconstructed from a time quantified signal with considerable mathematical effort.

- Value quantified signals are time-continuous signals with discrete values. Typical examples of a value quantified signal are data that are derived from analogue signal and which are dedicated to further processing, e.g.  an A /D converted sensor signals that is provides to an electrical control unit.

- Digital signals are discrete on the time  and value domain. Includes the set of possible signal values, only two elements, one speaks of binary signals. Typical examples of binary signals are switching positions or flags. Using digital signals, including the occurrence of events can be modeled.

Thus on a theoretical level, we distinguish between the continuous and discrete evolution of time and values. In a discrete system, the changes of states are processed at fixed and finite time steps. In a continuous system state changes occur for infinitesimally small time steps. Important mathematical models for continuous systems are ordinary differential equations. A mixed system–which shows continuous and discrete dynamics– is known as a hybrid system [17,18]. Hybrid system can be modeled with hybrid automatons.  Examples for systems that show such variable dynamics are often found in the area of embedded control systems e.g. in the automotive and aircraft industry.

In the general case, a test description notation for embedded software systems shall support all of four categories of signals mentioned above. TTCN-3 currently supports the signal categories (2) and (4). The extension of the language with respect to a support of the signal categories (1) and (3) is the content of this document.

TTCN-3  is a procedural testing language, thus test behavior is defined by algorithms that typically assign (send) messages to ports and evaluate (receive) messages from ports. For the evaluation of different alternatives of expected (sets of) message, or timeouts, the port queues and the timeout queues are frozen when the evaluation starts. This kind of snapshot semantics guarantees a consistent view on the test system input during an individual evaluation step. Whereas the snapshot semantics provides means for a pseudo parallel evaluation of messages from several ports, there is no notion of simultaneous stimulation and time triggered evaluation. To enhance the core language to the requirements of continuous and hybrid behavior we introduce:

- the notions of time and sampling,

- the notions of streams, stream ports and stream variables

- the definition of an automaton alike control flow structure to support the specification of hybrid behavior.

## 4.1	Time and Sampling

For TTCN-3 embedded we adopted the concept of a global clock and enhance it with the notion of sampling and sampled time.  As in TTCN-3, all time values in are denoted as float values and represent time in seconds. For sampling we intend to support simple discrete sampling models as well as dynamic sampling models on specification and execution level.

A discrete sampling model of the form t=k*bdelta, where t describes the time progress, d specifies the number of executed sampling steps and, bdelta yields the minimal achievable step size,  is used as an overall basis to model discrete samplings with larger step size or dynamic sampling. The basic sampling bdelta is a property of a concrete testsystem and not intended to be specified as part of the test case specification. However, as a consequence of this underlying model, user defined samplings can only provide step sizes that are multiples of bdelta.

In TTCN-3 embedded each reference to time, either used for the definition and evaluation of signals but as well by means of ordinary TTCN-3 timers, is considered to  completely synchronized to the global clock and the sampling.

### 4.1.1	Time

For the specification of time-dependent signal sequences, it is necessary to be able to track the passage of time. The access of time is guaranteed by a globally available clock whose current value can be accessed by means of the now symbol. Time progress starts at the beginning of each test case execution, thus time values are related to the start of the test case execution. The symbol now can be applied in each expression inside of test case definitions and function definitions. It is not allowed for the TTCN-3 control part.

EXAMPLE 1:

// Use of now to retrieve the actual time since the test case has started

var float actualTime := now;

Syntactical Structure:

OpCall ::= ConfigurationOps | VerdictOps | TimerOps | TestcaseInstance |

FunctionInstance | TemplateOps | ActivateOp | NowOperation

NowOperation ::= NowKeyword

NowKeyword ::= "now"

### 4.1.2	Sampling

TTCN-3 embedded provides a globally valid base sampling rate, which is defined by the test system. In addition, sampling rates can be set separately and as part of the test specification by means of stepsize annotation. A stepsize annotation can be applied to individual modules, test cases, groups, component types and stream port types and effects either the statements that are contained in one of these entities or in case of component types and stream port types the respective instances.

EXAMPLE 1:

// sets the stepsize for a module

module myModule{

…

} with {stepsize “0.0001”};

EXAMPLE 2:

// sets the stepsize for a testcase

testcase myTestcase() runs on myComponent{

…

} with {stepsize “0.0001”};

EXAMPLE 3:

// sets the stepsize for all instances of the port type StreamOut

type port StreamOut stream { out float} with {stepsize “0.0001”};

Syntactical Structure:

WithStatement ::= WithKeyword WithAttribList

WithKeyword ::= "with"

WithAttribList ::= "{" MultiWithAttrib "}"

MultiWithAttrib ::= {SingleWithAttrib [SemiColon]}

SingleWithAttrib ::= AttribKeyword [OverrideKeyword] [AttribQualifier] AttribSpec

AttribKeyword ::= EncodeKeyword |

VariantKeyword |

DisplayKeyword |

StepsizeKeyword |

ExtensionKeyword

StepsizeKeyword ::= "stepsize"

## 4.2	Data streams

In computer science the term data stream are used to describe a continuous or discrete sequence of data. Normally the length of a stream cannot be established in advance. The data rate, i.e. the number of records per time unit time, can vary. Data streams are continuously processed and are particularly suited to represent dynamically evolving variables over a course of time. Thus, streams are an ideal representation of the different discrete and continuous signals mentioned in the beginning of section 4.

While in standard TTCN-3 interactions between the test components and the SUT are realized by sending and receiving messages through ports, the interaction between continuous systems can be represented by means of so called streams. In contrast to scalar values, a stream represents the whole allocation history applied to a port. In computer science, streams are widely used to describe finite or infinite data flows. To represent the relation to time, so called timed streams [6] are used. Timed streams additionally provide timing information for each stream value and thus enable the traceability of timed behaviour. TTCN-3 embedded provides timed streams. In the following we will use the term measurement (record) to denote the unity of a stream value and the related timing in timed streams. Thus, concerning the recording of continuous data, a measurement record represents an individual measurement, consisting of a stream value that represents the data side and timing information that represents the temporal perspective of such a measurement.

Currently TTCN-3 offers no direct support for the specification, management and modification of data streams. We propose introduce two different but not complementary representations of timed data streams in TTNC-3. The term timed considers the fact that we are interested in the time and value domain of signal. As a consequence we consider a stream to consist of a sequence of data sets, which each provide information about the timing and the value perspective of a signal value.

- Static perspective:  The static perspective provides a direct mapping between a timed stream and the TTCN-3 data structures record and recordof. This kind of mapping is referred to below as the data representation of a data stream and allows random access to all elements of the data stream that have been known at this time.

- Dynamic perspective: To provide online access to stream data, we extend the existing concepts of TTCN-3 port type and port, so that they support access to data streams that are connected to the respective ports. So called stream ports reference exactly one data stream and provide access to the dynamically changing values of the data stream.

#### 4.2.1	Data Streams: static perspective

A TTCN-3 data stream can mapped directly to existing TTCN-3 data structures. The mapping considers each stream to be represented by means of  a TTCN-3 recordof data structure, which itself consists of individual entities, so called measurement records, that each represent a real measurement on a stream.

A measurement record itself is represented by means of a TTCN-3 record data structure. It has a generic value field that allows the application of values for all existing TTCN-3 data types. Moreover, it has a field called delta, which denotes the temporal distance to the preceding measurement of the same stream. Thus a record of measurement is best formalized by the following parameterizable TTCN-3 data structure.

EXAMPLE 1:

type record Measurement<T>{

T value,

float delta

}

The following example shows the specification of a data structure that can represents timed data streams of arbitrary data types.

EXAMPLE 2:

type recordof Measurement<T> MyStreamType;

The static perspective of data streams can be used for the evaluation of streams as well as for the piecewise definition of streams or stream templates. Thus streams and template streams can be defined manually and automatically by means of record structures  and directly applied to the SUT by means of dedicated application operation. The following example shows a short specification of a sampled stream.

EXAMPLE 3:

var MyStreamType<float> myStreamVar := {

{value:=0.0, delta:=0.1},

{value:=0.2, delta:=0.2},

{value:=0.1, delta:=0.1},

{value:=0.0, delta:=0.3}

}

Please note: For the creation of larger streams a manual approach is not feasible. In this case we propose to use the data processing capabilities of TTCN-3 to programmatically/algorithmically construct the dedicated record structures.

Please note: The data structures presented in this section serve for illustration purposes only. They show how timed data streams can be mapped to existing TTCN-3 data structures and thus can be processed easily by using the existing TTCN-3 language features and operators. TTCN-3 embedded does not offer the type declarations from above as part of the language extensions explicitly. On the other hand we make sure that TTCN-3 embedded functions, when they return stream data in the record representation (static perspective), will provide data structures that are fully compatible to the scheme explained above.

#### 4.2.2	Data Streams: dynamic perspective

In TTCN-3 ports are used for the communication with the outside world, i.e. the communication with other test components and the SUT. To be able to initiate, modify and evaluate a stream based communication between the entities of a test system, TTCN-3 embedded extends the concepts of TTCN-3 port types and ports with the notion of stream-based communication and stream ports. Stream ports are the endpoints of a stream based communication between the test components and the SUT. Thus stream ports in TTCN-3 embedded are used to provide access to streams, their values and the respective timing information. A stream port in TTCN-3 embedded references exactly one data stream and thus provides access to the respective stream values and timing information.

The language concepts and extensions to define stream ports and to access stream data are explained in the following sections.

##### 4.2.2.1	Defining stream port types

Ports facilitate communication between test components and between test components and the test system interface. TTCN-3 actually supports message-based and procedure-based ports. TTTCN-3 embedded additionally allows the definition of stream-based ports. Thus each TTCN-3 port shall be defined as being message-based, procedure-based (or both at the same time as described by clause 8.4.1), or stream-based.

Stream-based ports shall be identified by the keyword stream. Ports in TTCN-3 are directional. The directions are specified by the keywords in (for the in direction), out (for the out direction) and inout (for both directions). Each stream port type definition shall have one and only one entry indicating the allowed type together with the allowed communication direction.

EXAMPLE 1:

// Stream-based port which allows stream values of type float to be received

type port StreamIn stream { in float }

//Stream-based port which allows stream values of type float to be send

type port StreamOut stream { out float }

Syntactical Structure:

PortDef ::= PortKeyword PortDefBody

PortDefBody ::= PortTypeIdentifier PortDefAttribs

PortKeyword ::= "port"

PortTypeIdentifier ::= Identifier

PortDefAttribs ::= StreamAttribs

| MessageAttribs

| ProcedureAttribs

| MixedAttribs

StreamAttribs ::= StreamKeyword "{" StreamDirection Type "}"

StreamList ::= Direction AllOrTypeList

StreamDirection ::= InParKeyword | OutParKeyword

StreamKeyword ::= "stream"

Please note:

##### 4.2.2.2 	Defining data stream ports

The definition of stream-based ports is basically similar to the definition of message-based and procedure-based ports. The component type defines which ports are associated with a component. These definitions shall be made in the module definitions part. The port names in a component definition are local to that component i.e. another component may have ports with the same names. A component type can have ports with different communication characteristics (e.g. stream-based ports, message-based ports, and procedure based).

EXAMPLE 1:

type port StreamIn stream { in float }

type port StreamOut stream { out float }

type component SUT {

port StreamIn A,B;

port StreamOut C,D;

}

Outgoing stream ports start to emit stream values directly after the component, which contains the respective stream port, has been started. The same applies for incoming stream ports. They start receiving data directly after their component has been started. Both incoming and outgoing stream ports are updated for each sampling step. If no explicit step size is defined by means of step size annotations on module level, test case level, port type level etc. the port is initially sampled with the test systems’ base sampling, which is the smallest available step size.

Outgoing stream ports may already be initialized before its first use, so that their values before and at time 0.0 (start of the test) are defined. The initialization occurs in the context of their declaration.

EXAMPLE 2:

type component SUT {

port StreamIn A,B;

port StreamOut C:=1.0,D:=2.0;

}

We assume that outgoing stream ports, when they are not explicitly initialized, are automatically initialized with a default values. The default values for the various TTCN-3 basic data types can be found in the following table.

| float | Integer | boolean | charstring | Bitstring | octetstring |
| --- | --- | --- | --- | --- | --- |
| 0.0 | 0 | False | "" | '0'B | '00'O |

The initial stream port value for outgoing stream port applies to the time point 0.0 and for the following sample steps as long as not other stream value is set. The value initialization for incoming streams is in responsibility of the data provider. Hence either the system adapter or the emitting component (in case of a PTC) is responsible to initialize the streams.

Syntactical Structure

PortInstance ::= PortKeyword PortType PortElement {"," PortElement}

PortElement ::= PortIdentifier [ArrayDef] [AssignmentChar PortInitialValue]

PortIdentifier ::= Identifier

PortInitialValue ::= Expression

## 4.2.3 	Data stream access operations

Similar to message-based and procedure-based communication TTCN-3 embedded allows to examine the elements of incoming stream-based ports controls the data provision at outgoing stream based ports. In general we provide access to the actual measurement record of a stream (i.e. stream values, their timing and sampling information) by means of stream data operation. Moreover we provide access to the preceding measurement records by means of dedicated navigation operations. Last but not least, we are able to extract record structured stream data like they are explained in Section 4.2.1 by means of stream eval statements.

In contrast to message-based and procedure-based communication, we decided to integrate stream data operation and stream navigation operation on expression level. Thus, we are able to directly assign value to streams and read values from streams by means of ordinary TTCN-3 assignments.

Please note: the stream access operation are designated for the usage inside a sampled environment. Thus, they will be used in particular within the hybrid machine alike control flow structures described in Section 4.4.

Below the complete syntactical integration of stream data operation, stream navigation operation and  stream eval statements is shown.  In the following chapters, we will define and explain the operations and statements individually.

Syntactical Structure

OpCall ::= 					  ConfigurationOps |

VerdictOps |

TimerOps |

TestcaseInstance |

FunctionInstance |

TemplateOps |

ActivateOp |

StreamDataOps|

StreamNavigationOps

CommunicationStatements ::= 	SendStatement |

CallStatement |

ReplyStatement |

RaiseStatement |

ReceiveStatement |

TriggerStatement |

GetCallStatement |

GetReplyStatement |

CatchStatement |

CheckStatement |

ClearStatement |

StartStatement |
StopStatement |

StreamEvalStatements

StreamDataOps ::= 				StreamValueOp |

StreamTimestampOp |

StreamDeltaOp |

StreamNavigationOps ::= 		( StreamPrevOp | StreamAtOp )

[ Dot StreamDataOp ]

StreamEvalStatements ::= 		StreamHistoryStatement | StreamMatchStatement

##### 4.2.3.1	The value operation

Each data stream connected to a stream port allows accessing its current value by means of the value operation. In case of incoming streams, the value operation yields the actual value that is available at a stream port.

EXAMPLE 1:

// accessing the actual input value of a stream 
var float myVar:=streamInPort.value;

EXAMPLE 2:

// accessing the actual input value of a stream

// and compare it with a given expectation 
if (streamInPort.value>= 100.0) {…};

Please note: The value, which is provided by means of the value operation, is the value that has been measured at the beginning of the actual sampling period.

In case of outgoing streams, the value operation yields a handle that allows assigning data to a stream. The assignment has to respect type compatibility with the data type of the stream.

EXAMPLE 2:

// setting the actual output value of a stream

streamOutPort.value:= 100.0;

Moreover, the use of the value operation can be combined in such a way that TTCN-3 embedded supports the specification of complex equations and equation systems.

EXAMPLE 2:

// calculating the Ohms’ law

voltage.value:= amperage.value * resistance.value;

Please note: the effectiveness of the stream port valuation is delayed. A value, which has been assigned to a stream port value handle, becomes effective inside and outside the component at the beginning of the next sampling step.

Syntactical Structure

StreamValueOp ::= Port Dot PortValueOp

PortValueOp ::= ValueOpKeyword

ValueOpKeyword ::= "value"

##### 4.2.3.2	The timstamp operation

Similar to the value operation the timestamp operation allows to access the time related information of the actual measurement record. Thus, the application of the timestamp operation on a stream port yields the exact time point at which the actual stream port value has been measured. The exact measurement time denotes the moment when a stream value has been made available at the test system's input and thus strongly dependent on the sampling rate.

The time point is provided as a floating-point number (float) and has the physical unit seconds. The time information is completely synchronized with the test system clock described in Section 4.1.

EXAMPLE 1:

// access of the measurement time 
// for the current measurement record 
var float measurementTime1:=streamport.timestamp;

Syntactical Structure

StreamValueOp ::= Port Dot PortTimestampOp

PortTimestampOp ::= TimestampOpKeyword

TimestampOpKeyword ::= "timestamp"

Please note: Data streams are used to represent measurements in a dynamic measurement process. A measurement record that is taken from a data stream is usually historical information, i.e. it represents the state of the system (i.e. the SUT) at a time in the past.

##### 4.2.3.3	The delta operation

In TTCN-3 embedded the step size of a data stream can dynamically change during a test execution. The change can be initiated either by the test specification or by means of the measurement system (i.e. the system adapter). The delta operation provides access to the actual step size of a port.

In addition to the timestamp operator TTCN-3 embedded allows to obtain the step size that has been used to measure a certain value. This information is provided by the delta operation, which can be used in a similar way as the value and the timestamp operation. The delta operator returns the size of the sampling step (in seconds) that precedes the measurement of the respective measurement record.

Semantics: The delta operation allows read and write access to the actual step size of a port. When the delta operation is used for reading, it yields the actual step size for a given port. When the delta operation is used for writing it sets the length of the step size in the future. The step size is given as a floating-point number (float) and has the unit seconds.

Please note: A value, which has been assigned to a stream port delta handle, affects the length of the next sampling period, not the actual one. Thus, it cannot be used to shorten or lengthen the actual sampling step.

EXAMPLE 1:

var float actualStepSize;

// reads the actual stream size from a port 
actualStepSize: = streamport.delta;

EXAMPLE 2:

// sets the actual step size for a port
streamport.delta:= 0.001;

Syntactical Structure

StreamValueOp ::= Port Dot PortDeltaOp

PortDeltaOp ::= DeltaOpKeyword

DeltaOpKeyword ::= "delta"

## 4.2.4	Data stream navigation operations

Beside access to the actual values of  a stream, TTTCN-3 embedded provides additional access to the history of  streams by means of so called stream navigation operations. The result of a navigation operation is a handle, which allows the application of the value, timestamp or delta operation for preceding stream states. Such a state is identified by means of two different operations. The at operation deamands time indicies that denote the time that has passed since the beginning of the testcase. The prev operation backtracks the sample steps beginning with the actual step and demands an integer index value to define the number of sampling steps to step back.

Please note: the stream navigation operation are designated for the usage inside a sampled environment. Thus, they will be used in particular within the hybrid machine alike control flow structures described in Section 4.4.

##### 4.2.4.1 	The prev operation

The prev operation returns a handle to obtain stream related information for previous states of a stream.

Semantics: The prev operation can be parameterized with an index parameter i and returns a handle to retrieve values, timestamps and sampling step sizes for preceding stream states. The index parameter denotes the number of measurements (i.e. sampling steps) to step back in stream history.

Please note: an application of the prev operation needs the combination with the value operation, the timestamp operation or the delta operation to provide meaningful results.

EXAMPLE 1:

port.prev(0).value; // provides access to the actual stream value
port.prev.value;    // provides access to the actual stream value
port.prev(1).value; // provides access to the previous stream value
port.prev(2).value; // provides access to the stream value 2 steps ago

EXAMPLE 2:

port.prev(0).timestamp; // provides access to the timestamp 
                        // that denotes the beginning the actual sampling step
port.prev.delta;        // provides access to the length of the last sampling step
port.prev(1).timestamp; // provides access to the timestamp 
                        // that denotes the beginning the preceding sampling step
port.prev(1).delta;     // provides access to the length of the sampling step 2 steps ago

Syntactical Structure

StreamValueOp ::= Port Dot PortPrevOp

PortPrevOp ::= PrevOpKeyword ["(" IndexValue ")"]

IndexValue ::= Expression

PrevOpKeyword ::= "prev"

##### 4.2.4.2 	The at operator

The at operation returns a handle to obtain stream related information for previous states of a stream, which are identified by means of a timestamp value.

Semantics: The at operation can be parameterized with an index parameter i and returns a handle to retrieve values, timestamps and sampling step sizes for preceding stream states. The index parameter represents a timestamp that identifies a measurement (i.e. sampling steps) at a certain place in time. The timestamp denotes the time that has passed since the start of the testcase (see Section 4.1). It references the measurement that has either the same timestamp or, if such a measurement does not exist, the measurement with the next smaller timestamp.

Please note: an application of the prev operation needs the combination with the value operation, the timestamp operation or the delta operation to provide meaningful results.

EXAMPLE 1:

port.at(now).value; 	// provides access to the actual stream value
port.at(0).value; 	// provides access to the initial stream value 
                     // (i.e. the stream value at beginning of the test case)
port.at(10.0).value; // provides the stream value at the time point 10.0 
                     //(i.e. 10. Seconds after the beginning of the test case)

EXAMPLE 2:

port.at(now).timstamp; 	  // provides access to the beginning of the actual sampling step 
port.at(0).timstamp;      // provides access to the beginning of the initial sampling 
                          // step (i.e. always 0.0) 
                       
port.at(10.0).timestamp;  // provides access to the beginning of the sampling step 
                          // at time point 10.0

Syntactical Structure

StreamAtOp ::= Port Dot PortAtOp

PortAtOp ::= AtOpKeyword ["(" TimeIndexValue ")"]

TimeIndexValue ::= Expression

AtOpKeyword ::= "at"

## 4.2.5	Data stream extraction and application operations

Beside access to individual values of  a stream, TTTCN-3 embedded  additionally support the extraction and application of stream segments that are represented by means of the record of data structure (data perspective) described in Section 4.2.1. The history operation allows to extract arbitrary stream segments. The apply operation is used to apply extracted or manually or programmatically defined stream segments to stream ports and the find operation is used to identify stream segments at ports by means of stream template expressions.

Please note: the history operation is mainly dedicated to be used in a non sampled environment while the apply and the find operation are mainly dedicated to be used in a sampled environment. Thus, the latter will be used in particular within the hybrid machine alike control flow structures described in Section 4.4.

##### 4.2.5.1	The history operation

The history function allows obtaining the complete or partial history of a stream as a TTCN-3 recordof structure (see section 4.1, data representation). The history operation has two parameters that denote the start time and end time of the desired stream segment.

Semantics: The History function provides a recordof based data representation of a stream. The operation has two parameters that denote the start time and end time of the stream segment that is designated for export. The parameters are each of type float and represent the time that has passed since the beginning of the respective test case. Time values are given in units of seconds. The first parameter describes the measurement time of the first stream entry to be considered for history export. The second parameter denotes the time of the last record.  If the specified start time value is greater than end time value the history operation results in an empty recordof structure.

EXAMPLE 1:

myStreamRec:= port.history(0.0, now);

EXAMPLE 2:

type record BoolStreamMeasurement {boolean value,float timestamp}

type port BoolStreamType {in boolean}

type component{ port myPort BoolStreamType}

var record of BoolStreamMeasurement myStreamRec;

…

myStreamRec:= myPort.history(0.0, now);

Syntactical Structure

StreamHistoryStatement ::= Port Dot PortHistoryOp

PortHistoryOp ::= HistoryOpKeyword ["(" StartValue [, EndValue]")"]

StartValue ::= Expression

EndValue ::= Expression

HistoryOpKeyword ::= "history"

##### 4.2.5.2	The apply operation

The apply operation is used to apply stream data to a stream port that are represented by means of a TTCN-3 recordof structure.  The apply operation executes the measurement records contained in the recordof structure one after the other as individual sampling steps. Thus the application of the apply operation outside of a sampled environment (par, seq or cont mode, see section 4.4) is time consuming. The application inside a sampled environment executes exactly one measurement  record at a time and returns.

EXAMPLE 1:

type port FloatIn {in float}

type port FloatOut {out float}

type component{ port myInPort FloatIn;

port myOutPort FloatOut }

type record StreamMeasurement {boolean value, float delta};

var record of StreamMeasurement myStreamRec;

testcase myTestcase () runs on tester{

// measure on all incoming ports for 100 seconds

wait(100.0);

// get the all measurements at myInport until now

myStreamRec:= myInPort.history(0.0, now);

// and apply the measured data to myOutPort.

myOutPort.apply(myStreamRec); // lasts 100 seconds

}

Please note:  In fact the application of an apply operation in a non sampled environment transforms to the following sampled structure.

EXAMPLE 2:

var integer count = 0;

cont{

port.apply(recordstructure);

}

until{

[true]{if(sizeof(recordstructure)>count){count:= count+1; continue}}

}

Syntactical Structure

StreamMatchStatement ::= Port Dot PortApplyOp

PortMatchOp ::= ApplyKeyword "(" ApplyParameter ")"

ApplyKeyword ::= "apply"

ApplyParameter ::= TemplateInstance

##### 4.2.5.3	The find operation

The find operation is used to search a stream pattern which is represented by means of a TTCN-3 recordof  structure at an incoming stream port.

EXAMPLE 1:

type port FloatIn {in float}

type port FloatOut {out float}

type component{ port myInPort FloatIn;

port myOutPort FloatOut }

type record StreamMeasurement {boolean value, float delta};

template streamTmpl record of StreamMeasurement myStreamRec{

{value:= (0.0..0.2), delta:=0.0},

{value:= (0.0..0.2), delta:=1.0},

{value:= (0.0..0.2), delta:=1.0},

{value:= (0.0..0.2), delta:=2.0},

};

testcase myTestcase () runs on tester{

// and search the template at myOutPort.

myOutPort.find(streamTmpl);

}

EXAMPLE 2:

type port FloatIn {in float}

type port FloatOut {out float}

type component{ port myInPort FloatIn;

port myOutPort FloatOut }

type record StreamMeasurement {boolean value, float delta};

template streamTmpl record of StreamMeasurement myStreamRec{

{value:= (0.0..0.2), delta:=0.0},

{value:= (0.0..0.2), delta:=1.0},

{value:= (0.0..0.2), delta:=1.0},

{value:= (0.0..0.2), delta:=2.0},

};

testcase myTestcase () runs on tester{

// and search the template at myOutPort.

cont{

myOutPort.value:= 10.0 + now;

}

until(myOutPort.find(streamTmpl))

}

Syntactical Structure

StreamMatchStatement ::= Port Dot FindOp

PortMatchOp ::= FindKeyword "(" FindParameter ")"

FindKeyword ::= "find"

FindParameter ::= TemplateInstance

## 4.3	The assert statement

The assert statement is used as a short hand for the specification of expected system behaviour.

Semantics: The assert statement specifies one or a list of predicates that express the expectation on the SUT. A predicate consist of an arbitrary TTCN-3 boolean expression. If one of the predicates fail, the assert statement automatically sets the verdict to fail. The assert statement is allowed at any place in the TTCN-3source code that allows the application of the setverdict statement.  To assess continuous data it will be used in particular within the hybrid machine alike control flow structures described in Section 4.4.

EXAMPLE 1:

assert(a.value==4.0);

EXAMPLE 2:

assert(a.value==4.0, b.value ==5.0, d.value ==445.0);

Syntactical Structure

VerdictStatements ::= SetLocalVerdict | AssertStatement

AssertStatement ::= AssertKeyword "(" AssertionList ")"

AssertKeyword ::= "assert"

AssertionList ::= Expression {, Expression }

Please note: the semantics of the assert statement can be mapped to existing TTCN-3 statements in the following way:

assert (pred1, pred2,...,predn);

is fully equivalent to

if(! pred1) setverdict(fail);
if(! Pred2) setverdict(fail);
...
if(! predn) setverdict(fail);

## 4.4	Control structures for continuous and hybrid behavior

Actually, the TTCN-3 control flow structures do not allow the parallel and sampled application and assessment of stream values at ports. The

In fact, the concepts defined in Section 4.1, 4.2 and 4.3 allow the construction, application and assessment of individual streams. For more advanced test behavior, such as concurrent application and assessment of multiple streams and the detection of complex events (e.g. zero crossing or flag changes), we need stronger concepts. For this purpose, we combine the concepts defined in the last sections with state-machine-like specification concepts, so called modes. A mode expresses a certain runtime mode of a system or a system under test. This kind of runtime mode is characterized by a defined behaviour at ports and a set of predicates that limit the applicability of the behavior. Unlike ordinary behavioral TTCN-3 statements, a mode do applies its behavior over time (at least for one sampling step). On a conceptual level modes fit best with the behavioral properties of a TTCN-3 alt statement.

## 4.4.1		Modes

The term mode is a common term for the discrete and countable macro states of a dynamic hybrid system. The term serves to distinguish the macro states from the infinite number of micro-states in a continuous system. Whereas the macro states are the subject of specification, the micro states resulting from the combination of macro-states with the continuous evaluation of data at streams. Modes and the transitions between modes can be written down in a state-machine-like structure, which is closely defined in the theory of hybrid automatons [1, 2].

For realizing hybrid automaton in TTCN-3embedded, we will introduce the cont statement, the seq statement and the par statement. While the cont statement is used for the specification of atomic modes, the par and seq statement are used to combine modes to larger constructs by means of parallel and sequential composition.

Modes in general are characterized by their internal behavior (i.e. the assignment and assessment of values at stream ports) and a set of predicates, which are used to control the mode's activity. Thus, a simple mode specification in TTCN-3 embedded consists of three syntactical compartments:

- an obligatory body to specify the mode's internal behavior;

- an invariant block that defines predicates that must not be hurt while the mode is active;

- and a transition block that defines the exit condition to end the mode's activity.

Example 1 shows the definition of a simple atomic mode consisting of two assignments to stream ports, an invariant that checks the state of an outgoing stream port and a transition that checks the valuation of an incoming stream port.

EXAMPLE 1:

cont{//body

to_Set_Point.value:=3.0*now;
  to_Engine_Perturbation.value:=0.0;

}
inv{//invariant
  to_Set_Point.value>20000.0;

}

until{//transition
  [ti_Engine_Speed.value>2000.0]{to_Engine_Perturbation.value:=2.0;}
}

In general, composite modes show nearly the same structural setup than atomic modes. The only differences refer to their behavioral descriptions. While atomic modes contain assignments and assert statements, composite modes contain other modes. As far as invariants and transitions are concerned, the structural setup and the behavior of composite modes both are identical to atomic modes. While a mode is active, each invariant of a composite mode has to hold. Additionally, each transition of a composite mode ends the activity of the mode when it fires. Example 2 shows the setup of a parallel mode that contains two sequential modes, which each of them containing further atomic modes.

EXAMPLE 2:

par { // overall perturbation and assessment

seq{// perturbation sequence

cont{// stimulation action 1}

cont{// stimulation action 2}

...

}

seq{// assessment sequence

cont{// assessment action 1}

cont{// assessment action 1}

...

}

}

inv{//invariant

}

until{//transition
}

Syntactical Structure

ModeSpecification ::= ( BasicMode | ComplexMode ) 
[ InvariantBlock ] [ UntilBlock ]

InvariantBlock ::= InvKeyword "{" InvariantList "}"

InvKeyword ::= "inv"

InvariantList ::= [BooleanExpression {, BooleanExpression }]

UntilBlock ::= UntilKeyword "{" UntilGuardList "}"

UntilKeyword ::= "until"

UntilGuardList ::= {UntilGuardStatement} | "(" [BooleanExpression] ")"

UntilGuardStatement ::= UntilGuardChar GuardOp StatementBlock)

UntilGuardChar ::= "[" [BooleanExpression] "]"

BasicMode ::= ContKeyword "{" BasicModeOp "}"

ContKeyword ::= "cont"

BasicModeOp ::= Assignment | …..

ComplexMode ::= (SeqKeyword | ParKeyword) "{" ModeList "}"

ParKeyword ::= "par"

SeqKeyword ::= "seq"

ModeList ::= { ModeSpecification }

#### 4.4.1.1		Definition of the invariant block

An invariant block contains boolean predicates (expressions) which characterize the applicability of a mode. Thus, an invariant block is always related to its containing mode specification and it specifies the terms and conditions of validity for a mode that shall be checked during runtime.

Semantics: For each mode, all invariants are checked for each sampling step when the mode is active. During a mode is active the invariants of a mode must not be violated. If an invariant of an active mode is violated the mode must be able to switch to another mode that has valid invariants during the respective sampling step. If this is not possible, the test system must set verdict an error verdict. The invariants block is always checked at the beginning of each sampling step, even before the body of each mode is executed.

Example 1 shows the definition of an atomic mode that sets the outport port A continuously with the value of 3.0. Moreover, the invariant prescribes condition on the incoming ports B, C and D. When one of the invariants is violated by the actual value at ports, mode execution is stopped.

EXAMPLE 1:

type port StreamIn stream { in float }

type port StreamOut stream { out float }

type component SUT {

port StreamIn A,B;

port StreamOut C,D;

}

cont{A.value:=3;}

inv {B.value > 3,C.value >=3*D.value;}

The specification of invariants allows the easy definition of ending conditions for the execution of modes. Based on a simple sequential control flow paradigm, this supports the specification of sequences of modes, that are executed one after the other whenever the invariant state of the active mode changes.

EXAMPLE 2:

cont{ A.value:=3;} inv {B.value >3,C.value >=3*D.value;}

cont{ A.value:=5;} inv {B.value <=3,C.value >=3*D.value;}

Syntactical Structure

InvariantBlock ::= InvKeyword "{" InvariantList "}"

InvKeyword ::= "inv"

InvariantList ::= [BooleanExpression {, BooleanExpression }]

#### 4.4.1.2	Definition of the until block

Alternatively the definition of the until block allows the specification of explicit transitions between modes.  Thus, the entries (transitions) in an until block do specify the exit conditions for their containing mode and provide an optional explicit definition of the mode to switch to (target mode). The until block can contain several alternative transitions with each specify different exit conditions and target modes.

#### 4.4.1.2.1	Definition of transition guards and events

The until block defines a number of transitions between modes. A transition contains either a guard or a trigger event specification or both. The guard and the trigger event specification are both used to determine whether a transition can fire or not. A Guard is modeled as a boolean TTCN-3 expression. A trigger event is modeled by means of TTCN-3 receiving operations (receive statement, trigger statement, getcall statement etc.). The predicate or the TTCN-3 receiving operations may be followed by an optional statement block, which contain instructions to be executed upon activation of the transition. The syntax of the until block is basically inspired by the syntax of TTCN-3 alt statement. The syntactical structure of transitions is more or less similar to the syntactical structure of a TTCN-3 alternative.

Semantics: A transition is considered to be activated if either the guard expression is satisfied or a valid receiving event occurred at the specified TTCN-3 receiving operation. Transitions are checked for each active mode at each sampling step. If a transition becomes active then the optional statement block is executed once. Afterwards the enclosing mode and all his child modes are deactivated. The control flow is continued with the activation of the follow up mode. The transitions in an until block are checked in the given order. If multiple transitions exist, the first transition that fulfills the activation conditions is activated.

EXAMPLE 1:

cont{ //mode

A.value:=3;

}

until { // transitions

[C.value > 4.0] MPort1.receive(TemplExp) { log(“statement block 1”); }

[C.value > 4.0 and D.value > E.value]{ log(“statement block 1”); }

[] Port2.receive(TemplExp) { log(“statement block 1”); }

}

In addition, we allow the following abbreviations or shorthand notations for the specification of simple transitions.

EXAMPLE 2:

until(A.value > 3.0);

// shorthand for until{[ A.value > 3.0]{}}

EXAMPLE 3:

until {p.receive(tmpl)};

// shorthand for until{[]p.receive(tmpl){}}

In the optional statement block of a transition any TTCN-3 statement is principally allowed, except:

- blocking instructions (i.e. receive statements, alt-statements) shall not be used. Such constructs may block the execution of the statement block with the consequence, that the next sampling step is missed.

- each type of control flow related statement that leads to the leaving of the enclosing mode  (e.g. goto, return).

Syntactical Structure

UntilBlock ::= UntilKeyword "{" UntilGuardList "}"

AltKeyword ::= "until"

UntilGuardList ::= {UntilGuardStatement} | "(" [BooleanExpression] ")"

UntilGuardStatement ::= UntilGuardChar [GuardOp] StatementBlock [GotoStatement]

UntilGuardChar ::= "[" [BooleanExpression | ModePredicate ] "]"

#### 4.4.1.2.2	Definition of follow up modes

TTCN-3 embedded allows the explicit definition of follow up modes by means of the goto statement. Thus a mode specification can have a preceding label that defines the target for a goto jump. Moreover each transition can have an optional goto statement that refers to an arbitrary label. If such a transition is activated, the optional statement block is executed and afterwards the execution is continued at the label position with the activation of the following mode. Examples 1 shows the application of labels and goto statements in the context of modes.

EXAMPLE 1:

label state1;

cont{ //mode

A.value:=3;

}

until(C.value > 2.0)

label state2;

cont{ //mode

A.value:=4;

} until { // transitions

[C.value > 4.0] { log(“statement block 1”) } goto state1;

[D.value > E.value]{ log(“statement block 2”) } goto state2;

[] Port2.receive(TemplExp) { log(“statement block 1”); }

}

Besides the restriction that already exists for the use of the goto statement in standard TTCN-3, TTCN-3 embedded defines additional restrictions for the use of the goto statement in the context of modes. Goto jumps are only allowed in a sequential environment, thus inside sequential modes or on the top level of a composition, i.e. directly on testcase level. Moreover, goto jumps are not allowed to break the composition hierarchy, thus it is not possible to jump to a parent mode or into a child mode. Jumps are only allowed between modes on the same hierarchy level.

However, if no follow up mode is explicitly defined by means of a goto statement the sequential ordering of mode specification implicitly defines the follow up mode. Thus, when two atomic modes follow each other in the specification, the second mode is the follow up mode for all active transition transitions of the preceding mode.

EXAMPLE 2:

cont{ A.value:=3;} until (B.value >3);

cont{ A.value:=5;} until (C.value >=3*D.value)

cont{ A.value:=7;} until (C.value >=3)

Syntactical Structure

UntilBlock ::= UntilKeyword "{" UntilGuardList "}"

AltKeyword ::= "until"

UntilGuardList ::= {UntilGuardStatement} | "(" [BooleanExpression] ")"

UntilGuardStatement ::= UntilGuardChar [GuardOp] StatementBlock [GotoStatement]

UntilGuardChar ::= "[" [BooleanExpression | ModePredicate ] "]"

#### 4.4.1.3	Local predicate symbols in the context of modes

To enable an explicit treatment of some exceptional situations, we introduce the symbols notinv and finshed that each represents special predicates with a mode local valuation.

The keyword notinv can be used as a predicate that indicates the violation of any local mode invariant. Thus, if one of the invariants of a mode is violated and the mode is active, the evaluation of the notinv symbol yields true for all expressions in the contained until block.  Otherwise it yields false. Thus, the notinv symbol allows the explicit handling of occurring invariant violation by means of transitions.

EXAMPLE 1:

cont{ //mode

A.value:=3;

}

until { // transitions

[notinv] { log(“Invariant violated”); }

[] Port2.receive(TemplExp) { log(“Invariant not violated”); }

}

The finished keyword can be used as a predicate to handle the proper termination of a composite mode. A proper termination is given when the termination is triggered by the status of the child elements of a composite mode and not by its transitions or invariants. If and only if a mode is terminated by the status of its child elements the term finished yields true. Thus, the finished symbol allows the explicit handling of proper mode terminations by means of transitions.

EXAMPLE 2:

par{ //mode

cont{ //inner mode 1

A.value:=3.0;

}until(C.value>3.0)

cont{ //inner mode 2

B.value:=3.0;

}until(

} until(D.value>3.0)

until { // transitions

[finished] { log(“finished by childs’ state”); }

[D.value  > 4.0] { log(“not finished by childs’ state”); }

}

Syntactical Structure

UntilGuardChar ::= "[" [ BooleanExpression | ModePredicate ] "]"

ModePredicate ::= NotinvKeyword | FinishedKey

NotinvKeyword ::= "notinv"

FinishedKeyword ::= "finished"

#### 4.4.1.4	Local time expressions in the context of modes

Basically, within a mode there is continuous access to the time that has elapsed since the beginning of the test case by using the keyword now.

EXAMPLE 1:

cont{ A.value:=3.0;} until (now > 4.0)

// executes the content of the body block until

// the overall test case time has reached 4.0 seconds

We additionally provide we provide access to the time that has elapsed since the activation of the enclosing mode construct. The access is provided by means of the symbol duration, which is applicable in expressions in all mode related substructures like the body block, the invariant block and the until block.

EXAMPLE 2:

cont{ A.value:=3.0;} until (duration > 4.0)

// executes the content of the body block for 4.0 seconds

Please note: the valuation of the symbol duration depends on its context. Thus, it may differ dependent on its place of application

The following example shows the application of the duration symbol in two different modes. Both modes are activated at different times and thus the application of the duration symbol in the second cont mode yields different results than the application of the duration symbol in the enclosing par mode.

EXAMPLE 3:

par{

cont{ A.value:=2.0;} until (duration > 4.0)

cont{ A.value:=3.0;} until (duration > 4.0)

} until(duration > 6.0)

Syntactical Structure

OpCall ::= ConfigurationOps | VerdictOps | TimerOps | TestcaseInstance |

FunctionInstance | TemplateOps | ActivateOp | ClockOperation |

NowOperation | DurationOperation

DurationOperation ::= DurarationKeyword

DurationKeyword ::= "duration"

#### 4.4.1.5	The repeat statement

The repeat statement causes the reexecution of a par statement, seq statement or cont statement, i.e. the execution of the par statement, seq statement  or cont is activated again and executed with the next sampling step. Please note: in case of the execution of the repeat statement the local time of the respective mode (see duration symbol in Section 4.4.1.3) is reset, in case of composite modes the child modes are activates according to the kind (parallel or sequential) of the mode.

#### 4.4.1.6	The continue statement

The continue statement causes the further execution of a par statement, seq statement or cont statement, i.e. the execution of the par statement, seq statement  or cont is continued with the next sampling step without a reset to the local time (see duration symbol in Section 4.4.1.3).

## 4.4.2	Atomic modes: the cont statement

The cont statement is used to define atomic modes. Atomic modes directly define the test behaviour at stream ports by means of value allocation and value assessments. A cont mode may contain assignments and assert statements and forms the leaves of a hierarchical mode structure.

When a cont statement is an activated, all contained elements are executed repetitively for each sample step. The execution ends when a transition fires or an invariant is violated.

EXAMPLE 1:

// executes the assignments at each sample step

cont { // Mode 1

Port1.value := 10.0;

Port2.value := 2.0 * duration;

}

until (duration > 5.0)

assignment and evaluation of instruction in a theoretical sense continuous, ie executed at each step, provided for sampling. Cont, the instruction allowed the organization of periodic assignments and periodic revision of values or variables of stream and stream ports.

EXAMPLE 2:

cont { // mode 1

outport1.value := inport1.prev.value *2;

streamvar.value := inport1.prev(5).value;

}

EXAMPLE 3:

cont { // mode 1

outport1.value := inport1.prev.value *2;

streamvar.value := inport1.prev(5).value;

}

inv{

streamvar.value > 200.0;

}

until { // Transition

[streamvar.value >150] { streamvar.value =0; }

[streamvar.value >180] {}

}

Syntactical Structure

ModeSpecification ::= ( BasicMode | ComplexMode ) 
[ InvariantBlock ] [ UntilBlock ]

BasicMode ::= ContKeyword "{" BasicModeOp "}"

ContKeyWord ::= "cont"

BasicModeOp ::= Assignment | …..

## 4.4.3	Parallel mode composition: the par statement

The parallel composition of modes is specified by means of the par statement. A parallel composition may contain sequential modes, parallel modes and atomic modes. In case of its activation, a parallel composition leads to a parallel execution of all composed (i.e. contained) modes.

The general structure of the par statement is similar to the cont statement and the seq statement. It consists of a body part, which defines the overall behavior of the mode. In case of the par statement the body part contains the mode definitions that are to be composed in parallel. The body part is followed by an optional invariant and a transition part (see Section ) . Both define the exit conditions that are checked during execution.  While being active, each invariant of a composite mode has to hold. Additionally, each transition of a composite mode ends the activity of the mode when it fires. Furthermore, each mode provides access to an individual local clock that returns the time that has passed since the mode has been activated. The value of the local clock can be obtained by means of the keyword

Semantics: the activation of a parallel mode leads to the parallel activation of all child modes. During execution, the parallel mode is responsible to check the status of all contained modes. The execution of a parallel mode ends, either when a transition in the transition block has fired or when the execution of a child modes has been completed. The second situation is called a proper termination of a sequential mode and forces the local symbol finished to yield true (see Section 4.4.1.3).

EXAMPLE 1:

var integer count := 0;

par{

cont{

x.value:=1;

y.value:=2;

}

until { // Transition

[z.value> 3.0] { }

[] Port2.receive {}

}

cont{

x.value:=2;

y.value:=1;

}

until { // Transition

[z.value> 10.0] { }

[] Port1.receive {}

}

}

until { // Transition

[finished] {if(count > 1) {count++; continue}}

}

Please note: the symbol finished yields true only during the distinct sample step when a child of a parallel mode has finished. Moreover, it yields true for every child element that has finished. Thus, it serves as a notification event, which can be used to model complex termination conditions for parallel modes.

EXAMPLE 1:

par{

cont{

x.value:=1;

y.value:=2;

}

until { // Transition

[z.value> 1.0] { }

[] Port1.receive(msg1) {}

}

cont{

x.value:=2;

y.value:=1;

}

until { // Transition

[z.value> 10.0] { }

[] Port1.receive() {}

}

}

until { // Transition

[z.value > 11.0] { }

[] Port1.receive(msg) {}

}

Syntactical Structure

ModeSpecification ::= ( BasicMode | ComplexMode ) 
[ InvariantBlock ] [ UntilBlock ]

ComplexMode ::= (SeqKeyword | ParKeyword) "{" ModeList "}"

ParKeyword ::= "par"

SeqKeyword ::= "seq"

ModeList ::= { ModeSpecification }

## 4.4.4	Sequential mode composition: the seq statement

The sequential composition of  modes is specified by means of the seq statement. A sequential composition may contain sequential modes, parallel modes and atomic modes. In case of its activation, a sequential composition leads to a sequential execution of all composed (i.e. contained) modes.

The general structure of the seq statement is similar to the cont statement and the par statement. It consists of a body part, which defines the overall behavior of the mode. In case of the seq statement the body part contains the mode definitions that are to be composed. The body part is followed by an invariant and a transition part (see Section ) . Both define the exit conditions that are checked during execution. While being active, each invariant of a composite mode has to hold. Additionally, each transition of a composite mode ends the activity of the mode when it fires. Furthermore, each mode provides access to an individual local clock that returns the time that has passed since the mode has been activated. The value of the local clock can be obtained by means of the keyword

Semantics: the activation of a sequential mode leads to the activation of its first child mode. During execution, the sequential mode is responsible to schedule the contained modes in their sequential order. Thus, when the first child mode has finished, the second mode is activated, when the second mode has finished the next mode has finished  and so forth. The execution of a sequential mode ends, either when a transition in the transition block is fired or when the execution of all child modes has been completed. The second situation is called a proper termination of a sequential mode and forces the local symbol finished to yield true (see Section 4.4.1.3).

The following example defines the sequential execution of two atomic modes, which are composed sequentially by means of a sequential mode.

EXAMPLE 1:

seq{

cont{

x.value:=1;

y.value:=2;

}

until { // Transition

[z.value> 2.0] { }

[] Port1.receive() {}

}

cont{

x.value:=2;

y.value:=1;

}

until { // Transition

[z.value> 1.0] { }

[] Port1.receive() {}

}

}

until { // Transition

[z.value> 12.0] { }

[] Port1.receive(msg) {}

}

Syntactical Structure

ModeSpecification ::= ( BasicMode | ComplexMode ) 
[ InvariantBlock ] [ UntilBlock ]

ComplexMode ::= (SeqKeyword | ParKeyword) "{" ModeList "}"

ParKeyword ::= "par"

SeqKeyword ::= "seq"

ModeList ::= { ModeSpecification }

## 4.4.5	Parametrizable modes

To provide a higher degree of flexibility, it is possible to specify parametrizable modes. Values, templates, ports, and modes can be used as mode parameters.  The definition of parametrizable modes is similar to the definition of TTCN-3 functions.

Please note: unlike functions parametrizable modes are not called in the sense of a function call but inserted by means of a substitution mechanism at compile time. Thus, the recursive application of parametrizable modes is not possible.

#### 4.4.5.1 	Mode types

Mode types are the set of identifiers of mode definitions with a specific parameter list and runs on clauses. They denote those modes defined in the test suite that have a compatible parameter list and compatible runs on clauses.

Syntactical Structure

type mode BehaviourTypeIdentifier
"(" [ { ( FormalValuePar | FormalTimerPar | FormalTemplatePar | FormalPortPar ) [","] } ] ")"

[ runs on ( ComponentType | self ]

EXAMPLE 1:

type mode ModeType assert_mode() runs on Tester :=

#### 4.4.5.2 	Parametrizable mode definitions

A paremtrizable mode definition allows the definition of reusable and parametrizable modes.  A parametrizable mode may be defined within a module.

EXAMPLE 1:

mode myMode runs on tester

cont{assert(engine_speed >= 500.0)}

In a module, the behaviour of a mode can be defined by using the statements and operations described in Section. If a mode uses variables, constants, timers and ports that are declared in a component type definition. The component type shall be referenced using the runs on keywords in the mode header. The one exception to this rule is if all component-wide information used within the mode is passed in as parameters. A mode without runs on clause shall never invoke a functions or modes with a runs on clause locally.

EXAMPLE 2:

type mode ModeType assert_mode() runs on Tester

mode myMode runs on tester cont{assert(engine_speed >= 500.0)}

mode mySecondMode pert_seq_2(in float startVal,

in float increase,

in ModeType assertion)

runs on Tester

par{

seq{// perturbation sequence

cont{to_Set_Point:=startVal} until (duration>=2.0)

cont{to_Set_Point:=startVal + duration/to_Set_Point.delta*increase}

until (duration>=5.0)

}

assertion();

}

testcase myTestcase runs on EngineTester {

// reusable mode application

pert_seq_2(1000.0, 10.0, assert_mode);

pert_seq_2(5000.0, 1.0, cont{assert(engine_speed >= 0.0)});

}

## 4.5 		The wait statement

The wait statement suspends the execution of a component until a given point in time. The time point is specified as a float value and relates to the internal clock.

The execution of wait statement suspends the execution of the related component until the point in time specified by its argument. If the argument holds a value that precedes the actual clock value an error verdict shall be set.

EXAMPLE 1:

streamoutport.value = 10.0;

wait(100.0 + now); 				// suspends the execution of a component

// until 100.0 seconds after the start of the testcase

streamoutport.value = 12.0;

Please note: The wait statement has no impact on sampling. All stream ports of the given component are still sampled with respect to their sampling rate.

Syntactical Structure:

WaitStatement::=  wait “(” Expression “)”

# 5	Package semantics

# 6	TRI extensions for the package

## 6.1	triStartClock (TE → PA)

| Signature | TriStatus triStartClock(in long ticksPerSecond) |
| --- | --- |
| In Parameters | ticksPerSecond the precision of the clock given in ticks per second |
| Out Parameters | n.a |
| Return Value | The return status of the operation. The return status indicates the success (TRI_OK) or failure (TRI_Error) of the operation. |
| Constraints | n.a. |
| Effect | The operation starts the test system clock with a given precision. The precision is defined by the in parameter ticksPerSecond. The parameter specifies the number of time units (ticks) that characterizes a second . |

## 6.2	triReadClock (TE → PA)

| Signature | TriStatus triReadClock(out long timepoint) |
| --- | --- |
| In Parameters | n.a. |
| Out Parameters | timepoint current time |
| Return Value | The return status of the operation. The return status indicates the success (TRI_OK) or failure (TRI_Error) of the operation. |
| Constraints | There was a preceding invocation of triStartClock(int lont ticksPerSecond) |
| Effect | The operation yields the actual clock value. The clock value is given by the out parameter timepoint, which represents the number of time units (ticks) that has elapsed since the start of the clock ( see triStartClock). |

## 6.3	triNextSampling (TE → PA, SA → PA)

| Signature | TriStatus triNextSampling(in long timepoint, in TriPortIDType port) |
| --- | --- |
| In Parameters | timepoint point in time when the execution of the next sample step for a given stream port shall be started port the stream port the sample step is requested for |
| Out Parameters | n.a. |
| Return Value | The return status of the operation. The return status indicates the success (TRI_OK) or failure (TRI_Error) of the operation. |
| Constraints | There was a preceding invocation of triStartClock(int lont ticksPerSecond) |
| Effect | The operation signals that the next sample step for a given port shall start at the specified point of time timepoint. At this point in time the PA will issue a triProcessStep(in TriPortIDListType ports) operation to inform the TE which ports shall be sampled next. The paremeter timepoint is expressed as the number of time units (ticks), that has elapsed since the the start of the clock (see triStartClock). A call to this operation returns immediately. The operation merely triggers the corresponding triNextStep operation. If timepoint represent a point of time in the past then the operation returns a TRI_Error value and has no other effect. |

## 6.4	triBeginWait (TE → PA)

| Signature | TriStatus triBeginWait(in long timepoint, in TriComponentIDType component) |
| --- | --- |
| In Parameters | timepoint point in time until execution of a component should be suspended component component whose execution should be suspended |
| Out Parameters | n.a. |
| Return Value | The return status of the operation. The return status indicates the success (TRI_OK) or failure (TRI_Error) of the operation. |
| Constraints | There was a preceding invocation of triStartClock(int lont ticksPerSecond) |
| Effect | The operation signals that the execution of component component should be suspended until the specified point of time timepoint. At this point in time the PA will issue a triEndWait(component) operation. timepoint is expressed as the number of time units (ticks), that has elapsed since the the start of the clock (see triStartClock). A call to this operation returns immediately. The operation merely triggers the corresponding triEndWait operation, it does not schedule the execution of the component. If timepoint represent a point of time in the past then the operation returns a TRI_Error value and has no other effect. |

## 6.5	triProcessStep (PA → TE)

| Signature | void triProcessStep(in TriPortIDListType ports) |
| --- | --- |
| In Parameters | Ports a list of ports that shall be sampled at the operation call |
| Out Parameters | n.a. |
| Return Value | n .a |
| Constraints | There was a preceding invocation of triNextSampling(timepoint, port) |
| Effect | The operation signals that the point in time timepoint that was specified in the corresponding triNextSampling(timepoint, port) has been reached. |

## 6.6	triEndWait (PA → TE)

| Signature | void triEndWait(in TriComponentIDType component) |
| --- | --- |
| In Parameters | component component of the corresponding triBeginWait operation |
| Out Parameters | n.a. |
| Return Value | n .a |
| Constraints | There was a preceding invocation of triBeginWait(timepoint, component) |
| Effect | The operation signals that the point in time timepoint that was specified in the corresponding triBeginWait(timepoint, component) has been reached. |

## 6.7	triSetStreamValue (TE → SA)

| Signature | TriStatusType triSetStreamValue( in TriComponentIdType componentId, in TriPortIdType tsiPortId, in TriAddressType SUTaddress, in TriMessageType streamValue) |
| --- | --- |
| In Parameters | componentId identifier of the sending test component tsiPortId identifier of the test system interface port via which the message is sent to the SUT Adaptor SUTaddress (optional) destination address within the SUT streamValue the encoded stream value (message) to be sent |
| Out Parameters | n.a. |
| Return Value | The return status of the triSetStreamValue operation. The return status indicates the local success (TRI_OK) or failure (TRI_Error) of the operation. |
| Constraints | The TE calls this operation when it executes a new sampling step on a sampled output stream port, which has been mapped to a TSI port. The TE calls the operation for all sampling steps of all outgoing stream ports if no system component has been specified for a test case, i.e. only a MTC test component is created for a test case. The encoding of streamValue has to be done in the TE prior to this TRI operation call. |
| Effect | The SA can update the message to the SUT. The triSetStreamValue operation returns TRI_OK in case it has been completed successfully. Otherwise TRI_Error shall be returned. Notice that the return value TRI_OK does not imply that the SUT has received streamValue. |

## 6.8	triGetStreamValue (TE → SA)

| Signature | TriStatusType triGetStreamValue( in TriComponentIdType componentId, in TriPortIdType tsiPortId, in TriAddressType SUTaddress, out TriMessageType streamValue) |
| --- | --- |
| In Parameters | componentId identifier of the sending test component tsiPortId identifier of the test system interface port via which the message is sent to the SUT Adaptor SUTaddress (optional) destination address within the SUT |
| Out Parameters | streamValue the encoded stream value (message) that has been received from the SUT |
| Return Value | The return status of the triGetStreamValue operation. The return status indicates the local success (TRI_OK) or failure (TRI_Error) of the operation. |
| Constraints | The TE calls this operation when it executes a new sampling step on a sampled input stream port, which has been mapped to a TSI port. The TE calls the operation for all sampling steps of all outgoing stream ports if no system component has been specified for a test case, i.e. only a MTC test component is created for a test case. The decoding of streamValue has to be done in the TE after to this TRI operation call. |
| Effect | The SA can update the stream value at stream the input port. The triGetStreamValue operation returns TRI_OK in case it has been completed successfully. Otherwise TRI_Error shall be returned. |

# 7	TCI extensions for the package

If needed for the package definition.

<Text>

## 7.1	tciSetStreamValue

| Signature | TriStatusType tciSetStreamValue( in TriComponentIdType componentId, in TriPortIdType tsiPortId, in TriAddressType SUTaddress, in TriMessageType streamValue) |
| --- | --- |
| In Parameters | componentId identifier of the sending test component tsiPortId identifier of the test system interface port via which the message is sent to the SUT Adaptor SUTaddress (optional) destination address within the SUT streamValue the encoded stream value (message) to be sent |
| Out Parameters | n.a. |
| Return Value | The return status of the triSetStreamValue operation. The return status indicates the local success (TRI_OK) or failure (TRI_Error) of the operation. |
| Constraints | The CH calls this operation when it executes a new sampling step on a sampled output stream port, which has been mapped to a test component port. |
| Effect | The CH can update the message to the SUT. The triSetStreamValue operation returns TRI_OK in case it has been completed successfully. Otherwise TRI_Error shall be returned. Notice that the return value TRI_OK does not imply that the SUT has received streamValue. |

## 7.2	tciGetStreamValue

| Signature | TriStatusType tciGetStreamValue( in TriComponentIdType componentId, in TriPortIdType tsiPortId, in TriAddressType SUTaddress, out TriMessageType streamValue) |
| --- | --- |
| In Parameters | componentId identifier of the sending test component tsiPortId identifier of the test system interface port via which the message is sent to the SUT Adaptor SUTaddress (optional) destination address within the SUT |
| Out Parameters | streamValue the encoded stream value (message) that has been received from the SUT |
| Return Value | The return status of the triGetStreamValue operation. The return status indicates the local success (TRI_OK) or failure (TRI_Error) of the operation. |
| Constraints | The CH calls this operation when it executes a new sampling step on a sampled input stream port, which has been mapped to a test component port. The CH calls the operation for all sampling steps of all outgoing stream ports. |
| Effect | The CH can update the respective stream input port on the test component. The tciGetStreamValue operation returns TRI_OK in case it has been completed successfully. Otherwise TRI_Error shall be returned. |

# 8	xxx extensions for the package

If needed for the package definition.

<Text>

## 8.1	User defined subdivisions of clause(s) from here onwards

<Text>

<PAGE BREAK>

Annex A (normative):
BNF and static semantics

Each annex shall start on a new page (insert a page break between annex A and B, annex B and C, ...).

Use the Heading 8 style for the title and the Normal style for the text.

# A.1	First clause of the annex

<Text>

## A.1.1	First subdivided clause of the annex

<Text>

<PAGE BREAK>

Annex <B> (normative):
Title of normative annex

If needed for the package definition.

Each annex shall start on a new page (insert a page break between annex A and B, annex B and C, ...).

Use the Heading 8 style for the title and the Normal style for the text.

# A.1	First clause of the annex

<Text>

## A.1.1	First subdivided clause of the annex

<Text>

<PAGE BREAK>

Annex B (informative):
Example Test Specification with TTCN-3 embedded

If needed for the package definition.

Each annex shall start on a new page.

Use the Heading 8 style for the title and the Normal style for the text.

## B.1	Testing an Advanced Cruise Control

An ACC is a cruise control that automatically detects vehicles running ahead and --- in the case of a slow vehicle ahead (the target) --- it adjusts the actual speed (v_acc) so that a safe distance to the detected vehicle is guaranteed (the distance control mode). When there is no vehicle ahead, an ACC works like any other cruise control (the velocity control mode). Today there are different variants of ACC's available. We use a simplified example here (see Figure 1) that does not match the requirements of a real product but that is sufficient to demonstrate the new features that we have introduced for TTCN-3 embedded.

Abbildung 1 – The Advanced Cruise Control

| Symbol | Direction | Unit | Datatype |
| --- | --- | --- | --- |
| v_target | Out | m/s | Double |
| phi_gas | Out | % | Double |
| leverpos | Out |  | Enumeration |
| d_des | In | m/s | Double |
| acc_mode | In |  | Boolean |
| v_acc | In | m/s | Double |

In this example we test the changeover between distance control mode --- when there is a slow vehicle ahead --- and velocity control mode --- without any vehicle ahead. This forms one of the more complex tasks of an ACC and can be tested by the following test behavior (for a similar test specification (see CON04).

- Accelerate the vehicle phi_gas:=100 until velocity v_acc rises to more than 40 m/s. Than switch on the cruise control leverpos:=HOLD_ACC

- Activate Distance Control Mode

- Now, we introduce a vehicle ahead by setting the target velocity to v_target:= 35+sin(t) m/s. The initial distance d_init:=90 m was set before the test execution using the parameter interface in Matlab/Simulink. The ACC should switch to distance control mode after a few seconds. The safe distance to the vehicle ahead can be calculated with v_acc/2*df. The symbol df represents a distance factor that is set to the value of 2.0 here.

- Accelerate Target: To test whether the ACC switches back to velocity control mode, we accelerate the target vehicle using a smooth ramp. The ACC should now adjust the actual velocity according to the vehicle ahead as long as the velocity exceeds 40 m/s. We allow a tolerance of 10 % here. Afterwards, the ACC should switch back to velocity control mode.

EXAMPLE 1:

module ACCTEST{

type port FloatOut stream {out float};

type port FloatIn stream {in float};

type port BoolIn stream {in float};

type enumerated Lever { MIDDLE, 
HOLD_ACC, 
HOLD_DEC, 
OFF };

type port LeverOut message { out Lever };

type component ACCTester {

port FloatOut v_target, phi_gas;

port FloatIn d_des, v_acc;

port BoolIn acc_mode;

port LeverOut leverpos;

}

…

}with {stepsize:= “0.1”}

EXAMPLE 2:

const float INIT_SPEED:= 40.0;

const float INIT_T_SPEED:= 35.0;

const float TIMEOUT:= 20000.0;

testcase ACC_Mode_Test() runs on ACCTester {

setverdict(pass);

var float df:= 2.0;

cont {

phi_gas.value:= phi_gas.value+duration;

}

until{

[v_acc.value >= INIT_SPEED]{leverpos.send(HOLD_ACC)}

}

cont {

v_target.value:= 35.0+sin(now)

}

until{

[acc_mode.value]{assert(duration>3.0)}

}

cont {

v_target.value:= 35.0 + duration;

}

until(v_target.value > 40.0)

cont {} until(duration>2)

assert(not (acc_mode.value))

}

## B.2	Testing a window lifter application

Abbildung 2 – The Lifter Application

The following test program tests a window lifter application with the following properties. The Window lifter can be controlled by driver commands and passenger commands. The commands are either up, down or neutral. When a driver or a passenger enters and holds the up command the window position increases until the window is closed. When a driver or a passenger enters and holds the down command the window position decreases until the window is completely open. The window controller has an obstacle detection mechanism, that is when an obstacle is introduced during the window is closed, the obstacle must be detected and the closing process should stop immediately.

We introduce the following test case to test the basic mechanisms of the window lifter:

- Driver presses down button. The window opens (i.e. the position value increases)

- When the position reaches the value 4, the up button is pressed and the window is closing (i.e. the position value decreases).

- We check whether the decrease holds for 4 seconds

- Finally we close the window completely.

EXAMPLE 1:

type port StreamIn stream {in float}

type port StreamOut stream {out float}

type component Tester {

port StreamOut Driver_Up;

port StreamOut Driver_Down;

port StreamOut Passenger_Up;

port StreamOut Passenger_Down;

port StreamOut Obstacle;

port StreamOut ObstacleSize;

port StreamIn position;

port StreamIn move_up;

port StreamIn move_down;

}

EXAMPLE 2:

testcase DriverUpDown () runs on Tester {

setverdict(pass);

Driver_Up.value:= 0.0;

Driver_Down.value:=1.0;

log("Start test case");

log("Window Down");

cont {assert( position.value >= position.prev.value)}

until {[duration > 4.0] {Driver_Down.value:= 0.0}}

log("Window Up");

Driver_Up:=1.0;

log(position);

cont {} until {[duration > 0.2] {}}

log("Check Window Up");

cont {assert( position <= position.prev.value )}

until {[duration > 4.0] {}}

// Clean up

cont {} until {[position.value < 0.0] {}}

Driver_Up:=0.0;

Driver_Down:=0.0;

} //testcase

We introduce the following test case to test the obstacle detection mechanism:

- The driver presses down button. The window opens (i.e. the position value increases)

- When the position reaches the value 8, the down button is released and after a while the up button is pressed and the window is closing (i.e. the position value decreases).

- When the position reaches the value 3, an obstacle is introduced and the window stops closing immediately.

- We check whether the window stops and holds the position for at least 2 second.

- Afterwards the obstacle is removed and the window closed completely.

EXAMPLE 3:

testcase PassengerUpDownObstacle () runs on Tester {

setverdict(pass);

Passenger_Up.value:= 0.0;

Passenger_Down.value:=1.0;

log("Start test case");

log("Window Down");

cont {} until {[duration > 0.2] {}}

cont {assert( position.value >= position.prev.value )}

until {[duration > 4.0] {Passenger_Down.value:= 0.0}}

log("Window Up");

Passenger_Up.value:= 1.0;

log(position);

cont {} until {[duration > 0.2] {}}

log("Check Window Up");

cont { assert( position.value <= position.prev.value )}

until {[position < 4.0] {Obstacle:=1.0;}}

cont {assert( position <= position.prev.value )}

until {[position.value < 4.0] {Obstacle.value:=1.0;}}

cont {assert( position.value >3.5 )}

until {[duration > 2.0] {}}

Obstacle.value:=0.0;

cont {} until {[position.value < 0.0] {}}

Passenger_Up.value:= 0.0;

Passenger_Down.value:=0.0;

} //testcase

Figure 3 shows the signal shapes of the logged test data.

Abbildung 3 – Logged Data of The Window Lifter Application

# First clause of the annex

<Text>

## B.1.1	First subdivided clause of the annex

<Text>

<PAGE BREAK>

Annex <y> (informative):
Bibliography

The annex entitled "Bibliography" is optional.

It shall contain a list of standards, books, articles, or other sources on a particular subject which are not mentioned in the document itselft  (see clause 12.2 of the EDRs http://portal.etsi.org/edithelp/other/EDRs_Navigator.chm).

It shall not include the following:

normative references (such references shall be listed in clause 2.1);

informative references (such references shall be listed in clause 2.2).

Use the Heading 8 style for the title and B1+ or Normal for the text.

<Publication>: "<Title>".

OR

<Publication>: "<Title>".

[1]	ALUR, Rajeev ; COURCOUBETIS, Costas ; HENZINGER, Thomas A. ; HO, Pei-Hsin: Hybrid Automata: An Algorithmic Approach to the Specification and Verification of Hybrid Systems. In: Hybrid Systems, 1992, S. 209–229

[2] 	ALUR, Rajeev (Hrsg.) ; HENZINGER, Thomas A. (Hrsg.) ; SONTAG, Eduardo D. (Hrsg.): Hybrid Systems III: Verification and Control, Proceedings of the DIMACS/SYCONWorkshop, October 22-25, 1995, Ruttgers University, New Brunswick, NJ, USA. Bd. 1066. Springer, 1996 (Lecture Notes in Computer Science). – ISBN 3–540–61155–X

[3]	M. Conrad, E. Sax: Mixed Signals. In: E. Broekman, E. Notenboom: Testing Embedded Software. Addison-Wesley, London (GB), 2003, S. 229-249

[4] 	DIN 40146 Begriffe der Nachrichtenübertragung

[5] 	M. Conrad. Modell-basierter Test eingebetteter Software im Automobil: Auswahl und Beschreibung von Testszenarien. Dissertation, Deutscher Universitätsverlag, Wiesbaden (D), 2004

[6]	BROY, Manfred: Refinement of Time. In: BERTRAN, M. (Hrsg.) ; RUS, Th. (Hrsg.):Transformation-Based Reactive System Development, ARTS’97, TCS, 44 - 63

<PAGE BREAK>

# History

| Document history |
| --- |
| <Version> | <Date> | <Milestone> |
| 0.1 | 28.11.2008 | Initial Draft by TEMEA |

# Comments

not correct anymore, please change