# 4	Introduction

TTCN-3 comments (see clause A.1.4 of ES 201 873-1 [1]) can also be used to include specific information for the purpose of documenting the TTCN-3 source code itself. This part of the TTCN-3 standard defines the syntax and the use of such documentation-purpose comments.

## 4.1	Conformance and compatibility

For an implementation claiming to conform to the present document, all features  specified in the present document shall be implemented consistently with the requirements given in the present document and in ES 201 873-1 [1].

This document is compatible to

ES 201 873 Part-1, all versions up to and including  v4.2.1

If later versions of those parts are available and should be used instead, the compatibility of the documentation tags presented in this document has to be checked individually.

## 4.2	Syntactical conventions

Descriptions of the syntactical structures in the present document use the following convention: tag names (which include the @ character) shall appear in the documentation block as they are given in the syntactical rule. The freetext refers to a text complying with the rules for TTCN-3 comments of the core language specification (ES 201 873-1 [1]), the internal structure of which is not defined by the present document with one exception: if the commercial at ("@") character has be included in the documentation text, i.e. in freetext, a pair of at-characters ("@@") shall be used on the same line with no intervening space characters. Other terminals (e.g. Identifier) are started with a capital character. It is recommended that names used as Identifiers are checked by TTCN-3 documentation tools.