## B.3.20	Whitespace control

Syntactical structure(s)

variant """ whitespace ( preserve | replace | collapse ) """

Applicable to (TTCN-3)

Types or fields of structured types generated for XSD components with the whitespace facet.

Description

The encoding instruction designates that the value of the received XML attribute shall be normalized before decoding as below (see also clause 3.3.3 of XML 1.1 [5]).

preserve: no normalization shall be done, the value is not changed (this is the behaviour required by XML Schema Part 2 [9] for element content).

replace: all occurrences of HT(9) (horizontal tabulation), LF(10) (line feed) and CR(13) (carriage return) shall be replaced with an SP(32) (space) character.

collapse: after the processing implied by replace, contiguous sequences of SP(32) (space) characters are collapsed to a single SP(32) (space) character, and leading and trailing SP(32) (space) characters are removed.