Contents

Contents	3

Intellectual Property Rights	5

Foreword	5

1 Scope	6

2 References	6

2.1 Normative references	6

2.2 Informative references	7

3 Definitions, symbols and abbreviations	8

3.1 Definitions	8

3.2 Abbreviations	8

4 Package conformance and compatibility	8

4 Package concepts for the core language	9

4.1 Time and Sampling	10

4.1.1 The now operator	10

4.1.2 Define the default step size for sampling	11

4.2 Data streams	12

4.2.1 Data Streams: static perspective	13

4.2.2 Data Streams: dynamic perspective	14

4.2.2.1 Defining stream port types	14

4.2.2.2  Defining data stream ports 	15

4.2.3  Data stream access operations	16

4.2.3.1 The value operation	17

4.2.3.2 The timestamp operation	19

4.2.3.3 The delta operation	19

4.2.4 Data stream navigation operations	20

4.2.4.1  The prev operation	20

4.2.4.2  The at operation	22

4.2.5 Data stream extraction and application operations	23

4.2.5.1 The history operation	23

4.2.5.2 The values operation	24

4.2.5.3 The apply operation	25

4.2.5.4 The find operation	27

4.2.5.4 The violates operation	28

4.3 The assert statement	30

4.4 Control structures for continuous and hybrid behavior	31

4.4.1  Modes	31

4.4.1.1 Definition of the until block	35

4.4.1.1.1 Definition of transition guards and events	35

4.4.1.1.2 Definition of follow up modes	36

4.4.1.1.3 The repeat statement	37

4.4.1.1.4 The continue statement	37

4.4.1.2  Definition of invariant blocks	38

4.4.1.3 Definition of the onentry block	39

4.4.1.4 Definition of the onexit block	40

4.4.1.5 Local predicate symbols in the context of modes	40

4.4.1.6 Local temporal expressions in the context of modes	41

4.4.2 Atomic modes: the cont statement	42

4.4.3 Parallel mode composition: the par statement	43

4.4.4 Sequential mode composition: the seq statement	44

4.4.5 Parametrizable modes	45

4.4.5.1  Mode types	46

4.4.5.2  Parametrizable mode definitions	46

4.5   The wait statement	47

4.6   Predefined functions	47

5 Package semantics	48

6 TRI extensions for the package	48

6.1 triStartClock (TE → PA)	48

6.2 triReadClock (TE → PA)	48

6.3 triNextSampling (TE → PA, SA → PA)	48

6.4 triBeginWait (TE → PA)	49

6.5 triProcessStep (PA → TE)	50

6.6 triEndWait (PA → TE)	50

6.7 triSetStreamValue (TE → SA)	51

6.8 triGetStreamValue (TE → SA)	51

7 TCI extensions for the package	54

7.1 tciSetStreamValue 	55

7.2 tciGetStreamValue 	55

8 xxx extensions for the package	56

8.1 User defined subdivisions of clause(s) from here onwards	56

A.1 First clause of the annex	57

A.1.1 First subdivided clause of the annex	57

A.1 First clause of the annex	57

A.1.1 First subdivided clause of the annex	57

C.1 sin	59

C.2 cos	59

C.3 tan	59

C.4 loge	59

C.5 log	59

C.7 pow	59

C.8 sqrt	59

C.9 root	59

C.10 max	60

C.11 min	60

C.12 pi	60

C.13 abs	60

C.14 lengthof	60

B.1 Testing an Advanced Cruise Control	61

B.2 Testing a window lifter application	64

First clause of the annex	66

B.1.1 First subdivided clause of the annex	66

History	68

# Intellectual Property Rights

IPRs essential or potentially essential to the present document may have been declared to ETSI. The information pertaining to these essential IPRs, if any, is publicly available for ETSI members and non-members, and can be found in ETSI SR 000 314: "Intellectual Property Rights (IPRs); Essential, or potentially Essential, IPRs notified to ETSI in respect of ETSI standards", which is available from the ETSI Secretariat. Latest updates are available on the ETSI Web server (http://webapp.etsi.org/IPR/home.asp).

Pursuant to the ETSI IPR Policy, no investigation, including IPR searches, has been carried out by ETSI. No guarantee can be given as to the existence of other IPRs not referenced in ETSI SR 000 314 (or the updates on the ETSI Web server) which are, or may be, or may become, essential to the present document.

# Foreword

This ETSI Standard (ES) has been produced by ETSI Technical Committee Methods for Testing and Specification (MTS), and is now submitted for the ETSI standards Membership Approval Procedure.

The present document relates to the multi-part standard covering the Testing and Test Control Notation version 3, as identified below:

ES 201873 Part 1:	"TTCN-3 Core Language";

ES 201873 Part 2:	"TTCN-3 Tabular presentation Format (TFT)";

ES 201873 Part 3:	"TTCN-3 Graphical presentation Format (GFT)";

ES 201873 Part 4:	"TTCN-3 Operational Semantics";

ES 201873 Part 5:	"TTCN-3 Runtime Interface (TRI)";

ES 201873 Part 6:	"TTCN-3 Control Interface (TCI)";

ES 201873 Part 7:	"Using ASN.1 with TTCN-3";

ES 201873 Part 8:	"The IDL to TTCN-3 Mapping";

ES 201873 Part 9:	"Using XML schema with TTCN-3";

ES 201873 Part 10:	"TTCN-3 Documentation Comment Specification".

# 1	Scope

The present document defines the xxx package of TTCN-3. TTCN-3 can be used for the specification of all types of reactive system tests over a variety of communication ports. Typical areas of application are protocol testing (including mobile and Internet protocols), service testing (including supplementary services), module testing, testing of CORBA based platforms, APIs, etc. TTCN-3 is not restricted to conformance testing and can be used for many other kinds of testing including interoperability, robustness, regression, system and integration testing. The specification of test suites for physical layer protocols is outside the scope of the present document.

TTCN-3 packages are intended to define additional TTCN-3 concepts, which are not mandatory as concepts in the TTCN-3 core language, but which are optional as part of a package which is suited for dedicated applications and/or usages of TTCN-3.

This package defines concepts for testing systems using continuous signals as opposed to discrete messages and the characterization of the progression of such signals by use of streams. For both the production as well as the evaluation of continuous signals the concept of mode is introduced. Also, the signals can be processed as history-traces. Finally, basic mathematical functions that are useful for analyzing such traces are defined for TTCN-3. It is thus especially useful for testing systems which communicate with the physical world via sensors and actuators.

While the design of TTCN-3 package has taken into account the consistency of a combined usage of the core language with a number of packages, the concrete usages of and guidelines for this package in combination with other packages is outside the scope of the present document.

# 2	References

References are either specific (identified by date of publication and/or edition number or version number) or non-specific.

For a specific reference, subsequent revisions do not apply.

Non-specific reference may be made only to a complete document or a part thereof and only in the following cases:

if it is accepted that it will be possible to use all future changes of the referenced document for the purposes of the referring document;

for informative references.

Referenced documents which are not found to be publicly available in the expected location might be found at http://docbox.etsi.org/Reference.

For online referenced documents, information sufficient to identify and locate the source shall be provided. Preferably, the primary source of the referenced document should be cited, in order to ensure traceability. Furthermore, the reference should, as far as possible, remain valid for the expected life of the document. The reference shall include the method of access to the referenced document and the full network address, with the same punctuation and use of upper case and lower case letters.

NOTE:	While any hyperlinks included in this clause were valid at the time of publication ETSI cannot guarantee their long term validity.

## 2.1	Normative references

The following referenced documents are indispensable for the application of the present document. For dated references, only the edition cited applies. For non-specific references, the latest edition of the referenced document (including any amendments) applies.

[1]	ETSI ES 201 873-1: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; Part 1: TTCN-3 Core Language".

[2]	ETSI ES 201 873-4: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; Part 4: TTCN-3 Operational Semantics".

[3]	ETSI ES 201 873-5: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; Part 5: TTCN-3 Runtime Interface (TRI)".

[4]	ETSI ES 201 873-6: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; Part 6: TTCN-3 Control Interface (TCI)".

[5]	ISO/IEC 9646-1: "Information technology - Open Systems Interconnection -Conformance testing methodology and framework; Part 1: General concepts"

[6]	…

## 2.2	Informative references

The following referenced documents are not essential to the use of the present document but they assist the user with regard to a particular subject area. For non-specific references, the latest version of the referenced document (including any amendments) applies.

[i.1]	ETSI ES 201 873-2: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; Part 2: TTCN-3 Tabular presentation Format (TFT)".

[i.2]	ETSI ES 201 873-3: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; Part 3: TTCN-3 Graphical presentation Format (GFT)".

[i.3]	ETSI ES 201 873-7: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; Part 7: Using ASN.1 with TTCN-3".

[i.4]	ETSI ES 201 873-8: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; Part 8: The IDL to TTCN-3 Mapping".

[i.5]	ETSI ES 201 873-9: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; Part 9: Using XML schema with TTCN-3".

[i.6]	ETSI ES 201 873-10: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; Part 10: TTCN-3 Documentation Comment Specification".

[i.7]	ITU-T Recommendation T.50 (1992): "International Reference Alphabet (IRA) (Formerly International Alphabet No. 5 or IA5) - Information technology - 7-bit coded character set for information interchange".

[i.8]	ISO/IEC 8859-1: "Information technology - 8-bit single-byte coded graphic character sets - Part 1: Latin alphabet No. 1", 1998.

[i.9]	Object Management Group (OMG): "The Common Object Request Broker: Architecture and Specification - IDL Syntax and Semantics". Version 2.6, FORMAL/01-12-01, December 2001.

[i.10]	Draft ETSI ES xxx: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3 Extension; Testing and Test Control Notation version 3 Extension; Package xx".

# 3	Definitions, symbols and abbreviations

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in ETSI ES 201873-1 [1], ETSI ES 201873-4 [2], ETSI ES 201873-5 [3], ETSI ES 201873-6 [4], ISO/IEC 9646-1 [5] and the following apply:

…

## 3.2	Abbreviations

For the purposes of the present document, the abbreviations given in ETSI ES 201873-1 [1], ETSI ES 201873-4 [2], ETSI ES 201873-5 [3], ETSI ES 201873-6 [4], ISO/IEC 9646-1 [5] and the following] apply:

<ACRONYM1>	<Explanation>

<ACRONYM2>	<Explanation>

<ACRONYM3>	<Explanation>

# 4	Package conformance and compatibility

The package presented in this document is identified by the package tag

(Needed for package version – reference previous package versions in the bibliography annex

"<Package>:<Year>" - to be used with modules complying with version xxx of the present document (see annex <bibliography>).)

"<Package>:<Year>" - to be used with modules complying with the present document.

For an implementation claiming to conform to this package version, all features specified in the present document shall be implemented consistently with the requirements given in the present document and in ES 201 873-4 [1] and ES 201 873-4 [2].

The package presented in this document is compatible to

Please choose the appropriate ones – and provide the version number.

ES 201873 Part 1 version xxx

ES 201873 Part 2 version xxx

ES 201873 Part 3 version xxx

ES 201873 Part 4 version xxx

ES 201873 Part 5 version xxx

ES 201873 Part 6 version xxx

ES 201873 Part 7 version xxx

ES 201873 Part 8 version xxx

ES 201873 Part 9 version xxx

ES 201873 Part 10 version xxx

ES 202 784 version xxx

ES 202 781 version xxx

ES 202 782 version xxx

ES 202 785 version xxx

If later versions of those parts are available and should be used instead, the compatibility the package presented in this document has to be checked individually.

The package presented in this document is also compatible to

Please choose the appropriate ones – and provide the version number.

ES XXXXXX Package xxx version xxx

ES XXXXXX Package xxx version xxx

and can be used together with those packages/this package.

If later versions of those packages are available and should be used instead, the compatibility to the package presented in this document has to be checked individually.

# 4	Package concepts for the core language

Systems can communicate its data or signals, either in discrete form (e.g. as an integer value) or in continuous form (e.g. real values). With respect to this difference signals are classified into four categories in the literature [3,4,5]. The categories distinguish whether the time and value domain of a signal is of discrete or continuous nature:

- Analogue signals are continuous in the time and value domain. Analog signals are the most 'natural' signal category, characterized by physical units (e.g. current, voltage, velocity) and measured with sensors. Typical examples of the physical quantities used in the area of embedded system development are the vehicle velocity, the field intensity of a radio station etc. Analog signals can be described as a piecewise function over time (e.g. vx = f (t)) .

- Time quantified signals are discrete signals in the time domain. The signal values are defined only at predetermined time points (sampling points). Typical examples of time quantified signals are the time-value pairs of a recorded signal. A typical representation of a time quantified signal is a series or an array of real numbers. Even if the original signal is a synthetic function it can only be reconstructed from a time quantified signal with considerable mathematical effort.

- Value quantified signals are time-continuous signals with discrete values. Typical examples of a value quantified signal are data that are derived from analogue signal and which are dedicated to further processing, e.g.  an A/D converted sensor signals that is provides to an electrical control unit.

- Digital signals are discrete on the time  and value domain. Includes the set of possible signal values, only two elements, one speaks of binary signals. Typical examples of binary signals are switching positions or flags. Using digital signals, including the occurrence of events can be modeled.

Thus on a theoretical level, we distinguish between the continuous and discrete evolution of time and values. In a discrete system, the changes of states are processed at fixed and finite time steps. In a continuous system state changes occur for infinitesimally small time steps. Important mathematical models for continuous systems are ordinary differential equations. A mixed system–which shows continuous and discrete dynamics– is known as a hybrid system [17,18]. Hybrid systems can be modeled with hybrid automatons.  Examples for systems that show such variable dynamics are often found in the area of embedded control systems e.g. in the automotive and aircraft industry.

In the general case, a test description notation for embedded software systems shall support all of four categories of signals mentioned above. TTCN-3 currently supports the signal categories (2) and (4). The extension of the language with respect to a support of the signal categories (1) and (3) is the content of this document.

TTCN-3 is a procedural testing language, thus test behavior is defined by algorithms that typically send messages to ports and receive messages from ports. For the evaluation of different alternatives of expected messages, or timeout events, the port queues and the timeout queues are frozen when the evaluation starts. This kind of snapshot semantics guarantees a consistent view on the test system input during an individual evaluation step. Whereas the snapshot semantics provides means for a pseudo parallel evaluation of messages from several ports, there is no notion of simultaneous stimulation and time triggered evaluation. To enhance the core language to the requirements of continuous and hybrid behavior we introduce:

- the notions of time and sampling,

- the notions of streams, stream ports and stream variables,

- the definition of an automaton alike control flow structure to support the specification of hybrid behavior.

## 4.1	Time and Sampling

The TTCN-3 extensions defined in this package adopt the concept of a global clock and enhance it with the notion of sampling and sampled time.  As in TTCN-3, all time values are denoted as float values and represent time in seconds. For sampling we intend to support simple equidistant sampling models as well as dynamic sampling models.

On technical level an equidistant sampling model of the form t=k*bdelta, where t describes the time progress, d specifies the number of executed sampling steps and, bdelta yields the minimal achievable step size for a given test system,  is used as an overall basis to model equidistant samplings with larger step size or dynamic sampling.

The basic sampling with its minimal step size bdelta is a property of a concrete testsystem and not intended to be specified as part of the test case specification. However, as a consequence of this underlying model, a test system is able to execute user defined samplings if and only if all specified sampling rates at test specification level  provide step sizes that are multiples of bdelta.

When using the TTCN-3 extenstion defined in this package, each reference to time, either used for the definition and evaluation of signals but as well by means of ordinary TTCN-3 timers, is considered to  completely synchronized to the global clock and the base sampling.

### 4.1.1	The now operator

For the specification of time-dependent signal sequences, it is necessary to be able to track the passage of time. The access of time is guaranteed by a globally available clock whose current value can be accessed by means of the now operator. Time progress starts at the beginning of each test case execution, thus time values are related to the start of the test case execution.

Syntactical Structure

now

Semantic Description

Evaluation of the now operator yields the current value of the clock which is the duration of time since the start of the currently running test case.

Restrictions

The now operator shall only be applied from within a test case, i.e., by test cases, functions and altsteps executed on test components. The now operator  shall neither directly nor indirectly be called by TTCN-3 control part.

Examples

EXAMPLE 1:

// Use of now to retrieve the actual time since the test case has started

var float actualTime := now;

### 4.1.2	Define the default step size for sampling

For sampling, a globally valid base sampling rate  defined by the test system is provided. In addition, sampling rates can be set separately and as part of the test specification by means of stepsize attribute.

Syntactic Structure

stepsize StepSizeValue

Semantic Description

The StepSizeValue is a string-literal which must contain a decimal number. This number interpreted as seconds is used as the default rate of  sampling values over the stream ports to which are affected by this stepsize attribute. The actual sampling rate of a specific port can be changed dynamically with the delta operation.

Restrictions

A  stepsize attribute can only appear in a with-annotation. A stepsize attribute can be applied to individual modules, test cases, groups, component types and stream port types and effects either the statements that are contained in one of these entities or in case of component types and stream port types the respective instances.

Examples

EXAMPLE 1:

// sets the stepsize for a module

module myModule{

…

} with {stepsize “0.0001”};

EXAMPLE 2:

// sets the stepsize for a testcase

testcase myTestcase() runs on myComponent{

…

} with {stepsize “0.0001”};

EXAMPLE 3:

// sets the stepsize for all instances of the port type StreamOut

type port StreamOut stream { out float} with {stepsize “0.0001”};

## 4.2	Data streams

In computer science the term data stream is used to describe a continuous or discrete sequence of data. Normally the length of a stream cannot be established in advance. The data rate, i.e. the number of samples per time unit, can vary. Data streams are continuously processed and are particularly suited to represent dynamically evolving variables over a course of time. Thus, streams are an ideal representation of the different discrete and continuous signals mentioned in the beginning of section 4.

While in standard TTCN-3 interactions between the test components and the SUT are realized by sending and receiving messages through ports, the interaction between continuous systems can be represented by means of so called streams. In contrast to scalar values, a stream represents the whole allocation history applied to a port. In computer science, streams are widely used to describe finite or infinite data flows. To represent the relation to time, so called timed streams [6] are used. Timed streams additionally provide timing information for each stream value and thus enable the traceability of timed behavior. The TTCN-3 extension defined by this package provides timed streams. In the following we will use the term measurement (record) to denote the unity of a stream value and the related timing in timed streams. Thus, concerning the recording of continuous data, a measurement record represents an individual measurement, consisting of a stream value that represents the data side and timing information that represents the temporal perspective of such a measurement.

Standard TTCN-3 offers no direct support for the specification, management and modification of data streams. In this TTCN-3 extension, we introduce two different but not complementary representations of timed data streams. The term timed considers the fact that we are interested in the time and value domain of a signal. As a consequence we consider a stream to consist of a sequence of samples, which each provide information about the timing and the value perspective of the sample.

- Static perspective:  The static perspective provides a direct mapping between a timed stream and the TTCN-3 data structures record and record of. This kind of mapping is referred to below as the static representation of a data stream and allows random access to all elements of the data stream.

- Dynamic perspective: To provide dynamic online access to data streams, we extend the existing concepts of TTCN-3 port type and port to provide access to data streams and their content. A so called stream port references exactly one data stream and provides access to the dynamically changing values of the referenced data stream.

Please note: to represent streams in this document we use a tabular notation. The table has two rows by which the first one represents the value perspective of a stream and the second represents the temporal perspective. The temporal perspective is defined by means of timestamps that are synchronized with the overall clock. The columns represent the samples of the stream.

EXAMPLE 1:

Example 1 shows a stream with the length of 1.4 seconds and float values that change between 1.0 and 1.5

#### 4.2.1	Data Streams: static perspective

A TTCN-3 data stream can be mapped directly to existing TTCN-3 data structures. The mapping considers each stream to be represented by means of a TTCN-3 record of data structure. This structure itself consists of individual entities, so called samples, each sample representing either a measurement on an incoming stream or stimulus that is dedicated to be applied to an outgoing stream.

A sample itself is represented by means of a TTCN-3 record data structure. The record consists of two fields. It has a generic value field that allows the instantiation of values for arbitrary predefined or user defined TTCN-3 data types. The value field represents what we call the value of a stream. Its data type is aligned with the data type of the corresponding stream.

The second field denotes the temporal perspective of a sample. It denotes the temporal distance to the preceding sample (the sampling step size delta). The second field is of type float and represents time values that have the physical unit second. Example 1 shows the exemplary definition of a data structure to specify individual samples.

EXAMPLE 1:

type record Sample<T>{

T value,

float delta

}

Given such a structure, a timed data stream of an arbitrary data type is modeled as a record of samples.

EXAMPLE 2:

type record of Sample<T> MyStreamType;

The static representation of data streams can be used for the online and offline evaluation of streams as well as for the piecewise in-memory definition of streams or stream templates, which are to be applied to stream ports in the subsequent test case execution. Thus, the static representation of streams can be used to assess incoming streams and to define outgoing or reference streams and template streams mostly by means of ordinary TTCN-3 operations and control structures and as such provide an ideal interface between ordinary TTCN-3 concepts and the concepts defined in this package. The following example shows a short specification of a sampled stream.

EXAMPLE 3:

var MyStreamType<float> myStreamVar := {

{value:=0.0, delta:=0.1},

{value:=0.2, delta:=0.2},

{value:=0.1, delta:=0.1},

{value:=0.0, delta:=0.3}

}

If the stream definition from above is applied to an outgoing stream port directly with the beginning of a test case, the result will look as follows.

EXAMPLE 4:

Please note: each stream port is initialized with a value that defines the valuation of a stream at time 0.0. Thus the first sample in Example 4 is not defined by the specification in Example 3 but by the base initialization of the stream port. More information is provided in the following sections.

NOTE 1: in order to create larger streams a manual specification approach is not feasible. In this case we propose to use the data processing capabilities of TTCN-3 to programmatically/algorithmically construct the dedicated record structures.

NOTE 2: The data structures presented in this section serve for illustration purposes only. They show how timed data streams can be mapped to standard TTCN-3 data structures and thus can be processed easily by using the existing TTCN-3 language features and operators. The TTCN-3 extensions provided in this package do not include type declarations from above.

#### 4.2.2	Data Streams: dynamic perspective

In standard TTCN-3 ports are used for the communication among test components and between test components and the SUT. To be able to initiate, modify and evaluate a stream based communication between the entities of a test system, this package extends the concepts of standard TTCN-3 port types and ports with the notion of stream-based communication and stream ports. Stream ports are the endpoints of a stream based communication. Thus stream ports in TTCN-3 embedded are used to provide access to streams, their values and the respective timing information. A stream port references exactly one data stream and thus provides access to the respective stream values and timing information.

##### 4.2.2.1	Defining stream port types

The TTCN-3 port concept of message-based and procedure-based ports is extended with stream-based ports. Stream ports support stream-based communication.

Syntactical Structure

type port PortTypeIdentifier stream "{"

( in | out | inout ) StreamValueType

"}"

Semantic Description

Stream port types shall be declared by using the keyword stream. Stream ports are directional. The directions are specified by the keywords in (for the in direction), out (for the out direction) and inout (for both directions).

The specified StreamValueType references the type of values which can be sent or received (depending on the direction of the port) over ports of the type PortTypeIdentifier.

Restrictions

Each stream port type definition shall have one and only one entry indicating the allowed type together with the allowed communication direction.

EXAMPLE 1:

// Stream-based port which allows stream values of type float to be received

type port StreamIn stream { in float }

//Stream-based port which allows stream values of type float to be sent

type port StreamOut stream { out float }

##### 4.2.2.2 	Declaration and instantiation of stream ports

The declaration of stream-based ports is similar to the declaration of message-based and procedure-based ports. The component type declares which ports are associated with a component. A component type can have ports with different communication characteristics (e.g. stream-based ports, message-based ports, and procedure based). All ports are instantiated together with the component that owns the port, i.e., when the component is created.

Outgoing stream ports start to emit stream values directly after the component, which contains the respective stream port, has been started. The same applies for incoming stream ports. They start receiving data directly after their component has been started. Both incoming and outgoing stream ports are updated for each sampling step. If no explicit step size is defined by means of step size annotations on module level, test case level, port type level etc. the port is initially sampled with the test systems’ base sampling, which is the smallest available step size.

Outgoing stream ports may already be initialized before its first use, so that their values before the start of their component are defined. The initialization occurs in the context of their declaration.

Outgoing stream ports, when they are not explicitly initialized, are automatically initialized with implicit default values. The implicit default values for the various TTCN-3 basic data types can be found in the following table.

| float | integer | boolean | charstring | bitstring | octetstring |
| --- | --- | --- | --- | --- | --- |
| 0.0 | 0 | FALSE | "" | '0'B | '00'O |

The initial stream port value for outgoing stream port applies to the time point 0.0 and for the following sample steps as long as no other stream value is set. The value initialization for incoming streams is in responsibility of the data provider. Hence either the system adapter or the emitting component (in case of a PTC) is responsible to initialize the streams.

Syntactical Structure

port StreamPortTypeReference

{ StreamPortIdentifier [ ":=" StreamDefaultValue ]  [","] }+ [";"]

Semantic Description

A stream port PortInstance named StreamPortIdentifier is declared inside a component type definition using a StreamPortTypeReference which is a type-reference expression for an existing stream port type.  Optionally, a StreamDefaultValue can be supplied which defines the value of the stream before the first sampling over this port.

Restrictions

The StreamDefaultValue shall be of the type StreamValueType in the port type definition referenced by StreamPortTypeReference.

Examples

EXAMPLE 1:

type port StreamIn stream { in float }

type port StreamOut stream { out float }

type component SUT {

port StreamIn A,B;

port StreamOut C,D;

}

EXAMPLE 2:

type component SUT {

port StreamIn A,B;

port StreamOut C:=1.0,D:=2.0;

}

## 4.2.3 	Data stream access operations

Similar to message-based and procedure-based communication incoming streams can be examined and outgoing streams can be controlled. In general, we provide access to the actual sample of a stream (i.e. the stream value, the respective timing and sampling information) by means of stream data operations. Moreover, we provide access to the preceding samples by means of dedicated navigation operations. Last but not least, we are able to extract record structured stream data as explained in Section 4.2.1 by means of stream evaluation statements.

In contrast to message-based and procedure-based communication, we integrate stream data operations and stream navigation operations on expression level. Thus, we are able to directly assign values to streams and read values from streams by means of ordinary TTCN-3 assignments.

##### 4.2.3.1	The value operation

Each data stream connected to a stream port allows accessing its current value by means of the value operation. In case of incoming streams, the value operation yields the actual value that is available at a stream port.

Syntactical Structure

( StreamPortReference | StreamPortSampleReference ) "." value

Semantic Description

The value operation can be applied to either a StreamPortReference expression or a StreamPortSampleReference expression which is yielded by the application of a navigation operation on a StreamPortReference. In the first case, it yields the current value of the stream port; in the second case it yields the value in the referenced sampling.

When using a StreamPortReference to an outgoing stream port, the value operation expression can also be used on the left hand side of an assignment or as an out parameter to a function.

When using a value operation expression as a value expression the type of the value is the StreamValueType of the referenced stream port.

Restrictions

If the value operation expression is used as the target of an assignment, the type of the assigned value shall be compatible with the StreamValueType of the referenced stream port.

Examples

EXAMPLE 1:

// accessing the actual input value of a stream 
var float myVar:=streamInPort.value;

EXAMPLE 2:

// accessing the actual input value of a stream

// and compare it with a given expectation 
if (streamInPort.value>= 100.0) {…};

NOTE 1: The value, which is provided by means of the value operation, is the value that has been measured at the beginning of the actual sampling period.

EXAMPLE 2:

// setting the actual output value of a stream

streamOutPort.value:= 100.0;

Note 2: The use of the value operation can be combined in such a way that the specification of complex equations and equation systems is supported.

EXAMPLE 2:

// calculating the Ohms’ law

voltage.value:= amperage.value * resistance.value;

NOTE 3: The effectiveness of the stream port evaluation is delayed. A value, which has been assigned to a stream port value handle, becomes effective inside and outside the component at the beginning of the next sampling step.

##### 4.2.3.2	The timestamp operation

Similar to the value operation the timestamp operation allows to access the time related information of the actual sample.

Syntactical Structure

( StreamPortReference | StreamPortSampleReference ) "." timestamp

Semantic Description

The timestamp operation can be applied to a stream port referenced by a StreamPortReference expression or a StreamPortSampleReference referring to a specific sample of a stream port.

The application of the timestamp operation on a StreamPortReference yields the exact time point at which the actual stream port value has been measured. The application of the timestamp operation on a StreamPortSampleReference yields the exact time point at which the referenced sample has been measured. The exact sample time denotes the moment when a stream value has been made available at the test system's input and thus strongly dependent on the sampling rate.

The time point is provided as a floating-point number (float) and has the physical unit seconds. The time information is completely synchronized with the test system clock described in Section 4.1.

Restrictions

The timestamp operation always yields a non-negative float value.

Examples

EXAMPLE 1:

// access of the sample time 
// for the current sample
var float measurementTime1:=streamport.timestamp;

Note: Data streams are used to represent samples in a dynamic measurement process. A sample that is taken from a data stream is usually historical information, i.e. the result of a timestamp operation refer to the state of the system (i.e. the SUT) at a time in the past.

##### 4.2.3.3	The delta operation

The step size of a data stream can dynamically change during a test execution. The change can be initiated either by the test specification or by means of the measurement system (i.e. the system adapter). The delta operation provides access to the actual step size of a port.

In addition to the timestamp operator TTCN-3 embedded allows to obtain the step size that has been used to measure a certain value. This information is provided by the delta operation. The delta operation can be used in a similar way than the value and the timestamp operation. It returns the size of the last sampling step (in seconds).

Syntactical Structure

( StreamPortReference | StreamPortSampleReference ) "." delta

Semantic Description

When used on a StreamPortReference, the delta operation allows read and write access to the actual step size of a port. When the delta operation is used for reading on a StreamPortReference, it yields the actual step size for a given port. When the delta operation is used for writing on a StreamPortReference it sets the length of the step size for future writing and reading at the given port. The step size is defined as a float number and has the unit seconds.

When used on a StreamPortSampleReference it yields the actual step size active at the time of the referenced sample measurement.

NOTE: A value, which has been assigned to a stream port delta handle, affects the length of the next sampling period, not the actual one. Thus, it cannot be used to shorten or lengthen the actual sampling step.

Restrictions

When used on a StreamPortSampleReference, the delta operation only allows read access.

Examples

EXAMPLE 1:

var float actualStepSize;

// reads the actual stream size from a port 
actualStepSize: = streamport.delta;

EXAMPLE 2:

// sets the actual step size for a port
streamport.delta:= 0.001;

## 4.2.4	Data stream navigation operations

Beside access to the actual values of a stream, additional access to the history of  streams by means of so called stream navigation operations is provided. The result of a navigation operation is a handle, which allows the application of the value, timestamp or delta operation for preceding stream states. Such a state is identified by means of two different operations. The at operation demands a time index of type float that denotes the time that has passed since the beginning of the test case. The prev operation backtracks the sample steps beginning with the actual step and demands an integer index value to define the number of sampling steps to step back.

##### 4.2.4.1 	The prev operation

The prev operation returns a handle to obtain stream related information for previous states of a stream.

Syntactic Structure

StreamPortReference "." prev [ "(" PrevIndex ")" ]

Semantic Description

The prev operation can be applied to a stream port StreamPortReference. It can optionally be parameterized with an integer index parameter PrevIndex and returns a StreamPortSampleReference handle to retrieve values, timestamps and sampling step sizes for preceding stream states. The index parameter denotes the number of samples to step back in stream history.  If no parameter list is given, this is equivalent with the index 1.

Restrictions

The prev operation can only appear as an operand to a value, timestamp or delta read operation.

NOTE: The application of the prev operation needs the combination with the value operation, the timestamp operation or the delta operation to provide meaningful results.

Examples

EXAMPLE 1:

port.prev(0).value; // provides access to the actual stream value
port.prev.value;    // provides access to the previous stream value
port.prev(1).value; // provides access to the previous stream value
port.prev(2).value; // provides access to the stream value 2 steps ago

NOTE: The expressions  port.prev and port.prev(1) yield identical results.

EXAMPLE 2:

port.prev(0).timestamp; // provides access to the timestamp 
                        // that denotes the beginning the actual sampling step
port.prev(0).delta;        // provides access to the length of the last sampling step
port.prev(1).timestamp; // provides access to the timestamp 
                        // that denotes the beginning the preceding sampling step
port.prev(1).delta;     // provides access to the length of the sampling step 2 steps ago

EXAMPLE 3:

port.prev(0).value; 		// yields 1.4
port.prev.value;    		// yields 1.1
port.prev(1).value; 		// yields 1.1
port.prev(2).value; 		// yields 1.0

port.prev(0).timestamp; // yields 1.4
port.prev(0).delta;     // yields 0.1
port.prev(1).timestamp; // yields 1.3
port.prev(1).delta;     // yields 0.1

##### 4.2.4.2 	The at operation

The at operation returns a handle to obtain stream related information for previous states of a stream, which are identified by means of a timestamp value.

Syntactical Structure

StreamPortReference "." at [ "(" Timepoint ")" ]

Semantic Description

The at operation can be applied to a stream port StreamPortReference. The at operation can optionally be parameterized with a float parameter Timepoint and returns a StreamPortSampleReference handle to retrieve values, timestamps and sampling step sizes for preceding stream states. The Timepoint parameter represents a time stamp that identifies a sample at a certain place in time. The time stamp denotes the time that has passed since the start of the test case (see Section 4.1). It references the sample that has either the same time stamp or, if such a sample does not exist, the sample with the next smaller time stamp.

Restrictions

The at operation can only appear as an operand to a value, timestamp or delta read operation.

NOTE: The application of the at operation has to be done in combination with a value operation, a timestamp operation or a delta operation to provide meaningful results.

Examples

EXAMPLE 1:

port.at(now).value; 	// provides access to the actual stream value
port.at(0).value; 	// provides access to the initial stream value 
                     // (i.e. the stream value at beginning of the test case)
port.at(10.0).value; // provides the stream value at the time point 10.0 
                     // (i.e. 10. Seconds after the beginning of the test case)

EXAMPLE 2:

port.at(now).timstamp; 	  // provides access to the beginning of the actual sampling step 
port.at(0).timstamp;      // provides access to the beginning of the initial sampling 
                          // step (i.e. always 0.0) 
                       
port.at(10.0).timestamp;  // provides access to the beginning of the sampling step 
                          // at time point 10.0

EXAMPLE 3:

port.at(now).value; 			// yields 1.4
port.at(0).value; 			// yields 1.2
port.at(1.0).value; 			// yields 1.5
port.at(1.09).value; 		// yields 1.5

port.at(now).timstamp; 	 	// yields 1.4
port.at(0).timstamp;      	// yields 0.0                       
port.at(1.09).timestamp;  	// yields 1.0

## 4.2.5	Data stream extraction and application operations

Beside access to individual values of a stream, this package supports the extraction and application of stream segments that are represented by means of the record of data structure (data perspective) described in Section 4.2.1. The history operation allows to extract arbitrary stream segments. The apply operation is used to apply extracted or manually or programmatically defined stream segments to stream ports and the find and violates operations are used to identify stream segments at ports by means of stream template expressions.

##### 4.2.5.1	The history operation

The history operation allows obtaining the complete or partial history of a stream as a TTCN-3 record of structure (see section 4.1, data representation). The history operation has two parameters that denote the start time and end time of the desired stream segment.

Syntactical Structure

StreamPortReference "." history "(" StartTime "," EndTime ")"

Semantic Description

The history operation provides a record of based sample representation of a stream. The operation has two parameters StartTime and EndTime that denote the start time and end time of the stream segment that is designated for export. The parameters are each of type float and represent the time that has passed since the beginning of the respective test case. Time values are given in units of seconds. The first parameter describes the measurement time of the first stream entry to be considered for history export. The second parameter denotes the time of the last record.  If the specified start time value is greater than the specified end time value the history operation results in an empty record of structure.

Restrictions

The EndTime parameter shall not have a value greater than now.

Examples

EXAMPLE 1:

myStreamRec:= myPort.history(0.0, now);

EXAMPLE 2:

type record BoolSample {boolean v,float t}

type port BoolStreamType stream {in boolean}

type component MyStreamComponent {port myPort BoolStreamType}

var record of BoolSample myStreamRec;

…

myStreamRec:= myPort.history(0.0, now);

EXAMPLE 3:

myStreamRec:= port.history(0.0, now);

// yields

// {{1.2,0.0}, {1.4,0.1},{1.5,0.1},{1.7,0.1},{1.7,0.1},{1.5,0.1},{1.2,0.1},{1.0,0.1},

// {1.1,0.1},{1.4,0.1},{1.5,0.1},{1.2,0.1},{1.0,0.1},{1.1,0.1},{1.4,0.1}}

##### 4.2.5.2	The values operation

The values function allows obtaining the complete or partial history of a stream as a TTCN-3 record of structure without any timing information.

Syntactical Structure

StreamPortReference "." values "(" StartTime "," EndTime ")"

Semantic Description

The value operation has two parameters StartTime and EndTime that denote the start time and end time of the desired stream segment.

The history function provides a record of based value representation of a stream. The parameters are each of type float and represent the time that has passed since the beginning of the respective test case. Time values are given in units of seconds. The first parameter describes the measurement time of the first stream entry to be considered for history export. The second parameter denotes the time of the last record.  If the specified start time value is greater than end time value the history operation results in an empty record of structure.

The result of the value operation applied to a stream port of type T is a value of record of T.

Restrictions

The EndTime parameter shall not have a value greater than now.

Examples

EXAMPLE 1:

myStreamRec:= port.values(0.0, now);

EXAMPLE 2:

type port BoolStreamType {in boolean}

type component{ port myPort BoolStreamType}

var record of boolean myStreamRec;

…

myStreamRec:= myPort.values(0.0, now);

EXAMPLE 3:

myStreamRec:= port.history(0.0, now);

// yields

// {1.2, 1.4, 1.5, 1.7, 1.7, 1.5, 1.2, 1.0, 1.1, 1.4, 1.5, 1.2, 1.0, 1.1, 1.4}

##### 4.2.5.3	The apply operation

The apply operation is used to apply stream data to a stream port that are represented by means of a TTCN-3 record of structure.  The apply operation applies the sample records contained in the record of data structure one after the other in time to the given port.

Syntactical Structure

StreamPortReference "." apply "(" Samples ")"

Semantic Description

Application of the apply operation to the stream port StreamPortReference, it will consecutively write the values of the given record of Samples to the port, using the sampling deltas from Samples as deltas for writing the values, as well.

The application of an apply operation  p.apply(v)  is equivalent to the following construction:

cont{

var integer i := 0;

p.value := v[i].value;

if (i+1 < lengthof(v)) {

p.delta := v[i+1].delta;

}

}

until{

[true]{if(lengthof(v)>count){i:= i+1; continue}}

}

Examples

EXAMPLE 1:

type port FloatIn {in float}

type port FloatOut {out float}

type component{ port myInPort FloatIn;

port myOutPort FloatOut }

type record Sample {boolean value, float delta};

var record of Sample myStreamRec;

testcase myTestcase () runs on tester{

// measure on all incoming ports for 100 seconds

wait(100.0);

// get the all sampless at myInport until now

myStreamRec:= myInPort.history(0.0, now);

// and apply the measured data to myOutPort.

myOutPort.apply(myStreamRec); // lasts 100 seconds

}

EXAMPLE 2:

var MyStreamType<float> myStream := {

{0.0, 0.1},

{0.2, 0.2},

{0.1, 0.1},

{0.0, 0.3}

}

port.apply(myStream);

// yield -> see table below

## 4.3	The assert statement

The assert statement is used as a short hand for the specification of expected system behavior.

Syntactical Structure

assert "(" Predicate { "," Predicate } ")"

Semantic Description

The assert statement specifies one or a list of predicates that express the expectation on the SUT. A predicate consist of an arbitrary TTCN-3 boolean expression. If one of the predicates fail, the assert statement automatically sets the verdict to fail. The assert statement is allowed at any place in the TTCN-3 source code that allows the application of the setverdict statement.  To assess continuous data it will be used in particular within the hybrid machinealike control flow structures described in Section 4.4.

NOTE: the semantics of the assert statement can be mapped to existing TTCN-3 statements in the following way:

assert (pred1, pred2,...,predn);

is fully equivalent to

if(! pred1) setverdict(fail);
	if(! Pred2) setverdict(fail);
	...
	if(! predn) setverdict(fail);

Examples

EXAMPLE 1:

assert(a.value==4.0);

EXAMPLE 2:

assert(a.value==4.0, b.value ==5.0, d.value ==445.0);

## 4.4	Control structures for continuous and hybrid behavior

This section introduces control flow structures that allow the parallel and sampled application and assessment of stream values at ports. The concepts defined in Section 4.1, 4.2 and 4.3 allow the construction, application and assessment of individual streams. For more advanced test behavior, such as concurrent application and assessment of multiple streams and the detection of complex events (e.g. zero crossing or flag changes at multiple ports), we need stronger concepts. For this purpose, we combine the concepts defined in the last sections with state-machine-like specification concepts, so called modes.

A mode expresses a certain runtime mode of a system or an SUT. This kind of runtime mode is characterized by a defined behavior at ports and a set of predicates that limit the applicability of the behavior. Unlike ordinary behavioral TTCN-3 statements, a mode applies its behavior over time (at least for one sampling step).

## 4.4.1		Modes

The term mode is used to specify the discrete and countable macro states of a dynamic hybrid system. It mainly serves to distinguish the macro states of a hybrid system from the theoretically infinite number of micro-states.  By means of modes, this package provides a layer of abstraction that helps distinguishing between the discrete changes of a hybrid system (or test system) that are relevant from the users (and testers) perspective and the discrete changes that are introduced by the underlying test execution environment in order to map continuous behavior to a computational environment (which is naturally discrete). The interpretation and calculation of micro steps depend on the underlying technical environment, i.e. the sampling. Thus, a micro step is calculated by the combination of the active macro-states with the sampled evaluation of data at the stream ports.

Figure 1 Abstract test specification for a continuous system that show the values v and x

Modes and the transitions between modes can be written down in a state-machine-like structure, which is closely defined in the theory of hybrid automatons [1, 2]. Firgure 1 shows an abstract test specification that consists of three atomic modes, transitions, invariants and assertions.

For realizing such hybrid automatons, three new block statements are introduced, the cont statement, the seq statement and the par statement. While the cont statement is used for the specification of atomic modes, the par and seq statement are used to aggregate modes to larger constructs by means of parallel and sequential composition.

Modes in general are characterized by their duration and their internal behavior (i.e. the assignment and assessment of values at stream ports). The duration, or better the duration of the mode's activity, is defined by a set of predicates, which relates to time or the valuation of  (stream) ports, variables etc.

Syntactical Structure

( cont | par | seq ) "{" 
		{Declaration} 
		[OnEntryBlock] 
		[InvariantBlock] 
		Body
		[OnExitBlock] 
	"}" 
   [UntilBlock]

A mode specification consists of several syntactical compartments:

- local declarations to be used inside the mode;

- an optional onentry block, that defines behavior that has to be executed once at the activation of the mode;

- an optional invariant block that defines predicates that must not be hurt while the mode is active;

- an obligatory body to specify the mode's internal behavior;

- an optional onexit block that defines the behavior that has to be executed once at the deactivation of the mode;

- and an optional transition block (UntilBlock) that defines the exit conditions to end the mode's activity.

Atomic modes may be composed to composite modes. Composite modes show nearly the same structural setup as atomic modes. The only differences refer to their behavioral descriptions. While atomic modes contain assignments, assert statements and the inv, onexit, onentry blocks described above, composite modes contain other modes instead of statements. As far as invariants, onentry and onexit blocks and transitions are concerned, the structural setup and the behavior of composite modes both are identical to atomic modes.

Semantic Description

While a mode is active, each invariant of a composite mode has to hold. Additionally, each transition of a composite mode ends the activity of the mode when it applies.

When a mode is entered, its onentry-block is executed. When a mode is exited, its onexit-block is executed.

For every step of an active mode, the contents (either modes or statements) of the mode are executed.

Examples

Example 1 shows the definition of an atomic mode consisting of two assignments to stream ports, an invariant that checks the state of an outgoing stream port, an onentry block that initializes the variable x, and an onexit block that resets the stream port to_Set_Point to the value of 0.0, and transitions that check the valuation of an incoming stream port.

EXAMPLE 1:

cont{//body

onentry{x:=10.0;}

inv{//invariant
  		to_Set_Point.value>20000.0;
}

to_Set_Point.value:=3.0*now;
   to_Engine_Perturbation.value:=0.0+x;

onexit{to_Set_Point.value:=0.0}

}
until{//transition
  [ti_Engine_Speed.value>2000.0]{to_Engine_Perturbation.value:=2.0;}
  [ti_Engine_Speed.value>3000.0]{to_Engine_Perturbation.value:=1.0;}
}

Example 2 shows the setup of a parallel mode that contains two sequential modes, which each of them containing further atomic modes.

EXAMPLE 2:

par { // overall perturbation and assessment

inv{//invariant

}

seq{// perturbation sequence

cont{// stimulation action 1}

cont{// stimulation action 2}

...

}

seq{// assessment sequence

cont{// assessment action 1}

cont{// assessment action 1}

...

}

}

until{//transition
}

#### 4.4.1.1	Definition of the until block

The until block allows the specification of exit conditions for modes and additionally the specification of explicit transitions between modes. The entries of the until block are called transitions. Each transition specifies conditions for their activation (i.e. guards and trigger events) and may provide an explicit definition of the mode that has to be activated next (target mode). An until block can contain several alternative transitions that each specify different exit conditions and target modes.

#### 4.4.1.1.1	Definition of transition guards and events

The until block defines a number of transitions between modes. A transition contains either a guard or a trigger event specification or both. The guard and the trigger event specification are both used to determine whether a transition can fire or not. A guard is modeled as a boolean TTCN-3 expression. A trigger event is modeled by means of TTCN-3 receiving operations (receive statement, trigger statement, getcall statement etc.). The predicate or the TTCN-3 receiving operations may be followed by an optional statement block, which contain instructions to be executed upon activation of the transition. At the end of the transition there may be a goto clause which specifies the follow-up mode.

Syntactical Structure

until "{"

{ "[" [Guard] "]" [TriggerEvent] [StatementBlock] [goto Target] }

"}"

Semantic Description

A transition is considered to be activated if the guard expression is satisfied and a valid receiving event occurred at the specified TTCN-3 receiving operation and the invariant of the target mode holds. Transitions are checked for each active mode at each sampling step. If a transition becomes active then the optional statement block is executed once. Afterwards the enclosing mode and all his child modes are deactivated. The control flow is continued with the activation of the follow-up mode. The transitions in an until block are checked in the given order. If multiple transitions exist, the first transition that fulfills the activation conditions is activated.

Restrictions

In the optional statement block of a transition any TTCN-3 statement is principally allowed, except:

- blocking instructions (i.e. receive statements, alt-statements) shall not be used. Such constructs may block the execution of the statement block with the consequence, that the next sampling step is missed.

- each type of control flow related statement that leads to the leaving of the enclosing mode  (e.g. goto, return).

EXAMPLE 1:

cont{ //mode

A.value:=3;

}

until { // transitions

[C.value > 4.0] MPort1.receive(TemplExp) { log(“statement block 1”); }

[C.value > 4.0 and D.value > E.value]{ log(“statement block 1”); }

[] Port2.receive(TemplExp) { log(“statement block 1”); }

}

#### 4.4.1.1.2	Definition of follow up modes

The explicit definition of follow up modes by means of a goto clause is possible. Each mode specification can have a preceding label that defines the target for a goto clause. Moreover each transition can have an optional goto clause that refers to an mode label.

Semantic Description

If a transition with a goto clause is activated, the optional statement block is executed and afterwards the execution is continued at the label position with the activation of the following mode.

Restrictions

Besides the restrictions that already exist for the use of the goto statement, this package defines additional restrictions for the use of the goto clause in the context of modes. Goto jumps are only allowed in a sequential environment, either inside seq modes or on the top level of a composition, i.e. directly on testcase level. Moreover, goto jumps are not allowed to violate the composition hierarchy, thus it is not possible to jump to a parent mode or into a child mode. Jumps are only allowed between modes on the same hierarchy level.

However, if no follow up mode is explicitly defined by means of a goto statement the sequential ordering of mode specification implicitly defines the follow up mode. Thus, when two atomic modes follow each other in the specification, the second mode is the follow up mode for all active transition transitions of the preceding mode that do not have an explicit goto clause.

Examples

Examples 1 shows the application of labels and goto statements in the context of modes.

EXAMPLE 1:

label state1;

cont{ //mode

A.value:=3;

}

until{[C.value > 2.0]}

label state2;

cont{ //mode

A.value:=4;

} until { // transitions

[C.value > 4.0] { log(“statement block 1”); } goto state1

[D.value > E.value]{ log(“statement block 2”); } goto state2

[] Port2.receive(TemplExp) { log(“statement block 1”); }

}

EXAMPLE 2:

cont{ A.value:=3;} until {[B.value >3]}

cont{ A.value:=5;} until {[C.value >=3*D.value]}

cont{ A.value:=7;} until {[C.value >=3]}

#### 4.4.1.1.3	The repeat statement

The control flow of a mode's transition's statement block may end in a repeat statement.

Semantic Description

The repeat statement causes the re-execution of a par statement, seq statement or cont statement, i.e. the execution of the par statement, seq statement or cont is activated again and executed with the next sampling step.

NOTE 1: In case of the execution of the repeat statement the local time of the respective mode (see duration symbol in Section 4.4.1.3) is reset, in case of composite modes the child modes are first deactivated and then again activated according to the kind (parallel or sequential) of the mode. Moreover, the respective onentry and onexit blocks are executed.

Examples

EXAMPLE 1:

cont{ //mode

A.value:=4;

} until { // transitions

[C.value > 4.0] { log(“statement block 1”); goto state1};

[D.value > E.value]{ log(“repeat the execution”); repeat};

[] Port2.receive(TemplExp) { log(“statement block 1”); }

}

NOTE 2: The repeat statement is functional equivalent to the use of a goto clause that addresses a label directly above the current mode.

#### 4.4.1.1.4	The continue statement

The control flow of a mode's transition's statement block may end with a continue statement.

Semantic Description

The continue statement causes the further execution of a par statement, seq statement or cont statement, i.e. the execution of the par statement, seq statement  or cont is continued with the next sampling step without a reset to the local time (see duration symbol in Section 4.4.1.3). The onentry and onexit blocks are not executed.

Examples

EXAMPLE 1:

cont{ //mode

A.value:=4;

} until { // transitions

[C.value > 4.0] { log(“statement block 1”); goto state1};

[D.value > E.value]{ log(“continue the execution”); continue};

[] Port2.receive(TemplExp) { log(“statement block 1”); }

}

#### 4.4.1.2		Definition of invariant blocks

Syntactical Structure

inv "{" Predicate {"," Predicate} "}"

Semantic Description

An invariant block contains boolean predicates (expressions) which characterize the applicability of a mode. Thus, an invariant block is always related to its containing mode specification and it specifies the conditions that shall be valid for a mode during runtime.

For each mode, all invariants are checked for each sampling step when the mode is active. While a mode is active the invariants of a mode shall not be violated. If an invariant of an active mode is violated, the mode must be able to switch to another mode that has valid invariants during the respective sampling step. If this is not possible, the test system must set an error verdict. The invariants block is always checked at the beginning of each sampling step, even before the body of each mode is executed.

Examples

Example 1 shows the definition of an atomic mode that sets the out port A continuously with the value of 3.0. Moreover, the invariant prescribes conditions on the incoming ports B, C and D. When one of the invariants is violated by the actual value at ports, mode execution is stopped.

EXAMPLE 1:

type port StreamIn stream { in float }

type port StreamOut stream { out float }

type component SUT {

port StreamIn A,B;

port StreamOut C,D;

}

cont{

A.value:=3;

inv {B.value > 3,C.value >=3*D.value}

}

The specification of invariants allows the easy definition of ending conditions for the execution of modes. Based on a simple sequential control flow paradigm, this supports the specification of sequences of modes, that are executed one after the other whenever the invariant state of the active mode changes.

EXAMPLE 2:

cont{

A.value:=3;
inv {B.value >3,C.value >=3*D.value}

}

cont{

A.value:=5; 
inv {B.value <=3,C.value >=3*D.value}

}

#### 4.4.1.3	Definition of the onentry block

The onentry block contains a statement list that is to be executed once and only once during the activation of a mode.

Syntactical Structure

onentry StatementBlock

Semantic Description

The onentry block is executed as part of the activation procedure of a mode. To successfully start the onentry block all invariants must satisfy their conditions. The onentry blocks of hierarchically ordered modes are executed sequentially, beginning with the onentry block of the outer-most mode to the inner modes.

Restrictions

In an onentry block of a mode any TTCN-3 statement is principally allowed, except:

- blocking instructions (i.e. receive statements, alt-statements) shall not be used. Such constructs would potentially block the execution of the statement block with the consequence, that the next sampling step is missed.

- each type of control flow related statement that leads to the leaving of the mode  (e.g. goto, return).

Examples

Example 1 shows the definition of an atomic mode that sets the sampling of a port during its activation time.

EXAMPLE 1:

cont{

onentry {A.delta:=0.001;}

A.value:=3;

}

#### 4.4.1.4	Definition of the onexit block

The onexit block contains a statement list that is to be executed once and only once during the deactivation of a mode.

Syntactical Structure

onexit StatementBlock

Semantic Description

The onexit block is executed as part of the deactivation procedure of a mode. The execution of the onexit block is triggered either by an activated transition or the violation of an invariant that lead to the leaving of the mode. In case of an active transition the onexit block is executed directly after the execution of the transition's optional action block. The onexit blocks of hierarchically ordered modes are executed sequentially, beginning with the onexit blocks of the inner-most modes towards the outer modes.

Restrictions

In an onexit block of a mode any TTCN-3 statement is principally allowed, except:

- blocking instructions (i.e. receive statements, alt-statements) shall not be used. Such constructs would potentially block the execution of the statement block with the consequence, that the next sampling step is missed.

- each type of control flow related statement that leads to the leaving of the mode  (e.g. goto, return).

Examples

Example 1 shows the definition of an atomic mode that sets the sampling of a port during its deactivation time.

EXAMPLE 1:

cont{

A.value:=3.0;

onexit {A.value:=1.0;}

} until {[B.value> 3.0]}

#### 4.4.1.5	Local predicate symbols in the context of modes

To enable an explicit treatment of some exceptional situations, we introduce the keywords notinv and finshed that represent special predicates with a mode local evaluation.

Semantic Description

The keyword notinv can be used as a predicate that indicates the violation of any local mode invariant. Thus, if one of the invariants of a mode is violated and the mode is active, the evaluation of the notinv symbol yields true for all expressions in the contained until block.  Otherwise it yields false. Thus, the notinv symbol allows the explicit handling of occurring invariant violation by means of transitions.

The finished keyword can be used as a predicate to handle the proper termination of a composite mode. A proper termination is given when the termination is triggered by the status of the child elements of a composite mode and not by its transitions or invariants. If and only if a mode is terminated by the status of its child elements the term finished yields true. Thus, the finished predicate allows the explicit handling of proper mode terminations by means of transitions.

Examples

EXAMPLE 1:

cont{ //mode

A.value:=3;

}

until { // transitions

[notinv] { log(“Invariant violated”); }

[] Port2.receive(TemplExp) { log(“Invariant not violated”); }

}

EXAMPLE 2:

par { //mode

cont { //inner mode 1

A.value:=3.0;

} until {[C.value>3.0]}

cont { //inner mode 2

B.value:=3.0;

} until {[D.value>3.0]}

} until { // transitions

[finished] { log(“finished by childs’ state”); }

[D.value  > 4.0] { log(“not finished by childs’ state”); }

}

​

#### 4.4.1.6	The duration operator

Within a mode there is continuous access to the time that has elapsed since the beginning of the test case by using the now operator. It is also possible to  access the time that has elapsed since the activation of the enclosing mode construct. The access is provided by means of the duration operator, which is applicable in expressions in all mode related substructures like the body block, the invariant block and the until block.

NOTE: The evaluation of the duration operator depends on its context. Thus, it may differ dependent on its place of application

Examples

EXAMPLE 1:

cont{ A.value:=3.0;} until {[now > 4.0]}

// executes the content of the body block until

// the overall test case time has reached 4.0 seconds

EXAMPLE 2:

cont{ A.value:=3.0;} until {[duration > 4.0]}

// executes the content of the body block for 4.0 seconds

The following example shows the application of the duration operator in two different modes. Both modes are activated at different times and thus the application of the duration symbol in the second cont mode yields different results than the application of the duration operator in the enclosing par mode.

EXAMPLE 3:

par{

cont{ A.value:=2.0;} until (duration > 4.0)

cont{ A.value:=3.0;} until (duration > 4.0)

} until{[duration > 6.0]}

​

## 4.4.2	Atomic modes: the cont statement

Syntactical Structure

The syntactical structure and context for the cont statement is part of the syntactical structure provided in clause 4.4.1.

Semantic Description

The cont statement is used to define atomic modes. Atomic modes directly define the test behavior at stream ports by means of value allocation and value assessments. A cont mode may contain assignments and assert statements and forms the leaves of a hierarchical mode structure.

When a cont statement is activated, all contained elements are executed repetitively for each sample step. The execution ends when a transition fires or an invariant is violated.

Restrictions

- A cont mode shall not invoke any potentially blocking behavior.

- A cont mode cannot contain other modes.

Examples

EXAMPLE 1:

// executes the assignments at each sample step

cont { // Mode 1

Port1.value := 10.0;

Port2.value := 2.0 * duration;

}

until (duration > 5.0)

NOTE: Assignment and evaluation of the cont  mode is,  in a theoretical sense, continuous, i.e. executed at each step, provided for sampling. The cont mode allows the organization of periodic assignments and periodic revisions of values or variables of stream and stream ports.

EXAMPLE 2:

cont { // mode 1

outport1.value := inport1.prev.value *2;

streamvar.value := inport1.prev(5).value;

}

EXAMPLE 3:

cont { // mode 1

outport1.value := inport1.prev.value *2;

streamvar.value := inport1.prev(5).value;

inv {

streamvar.value > 200.0

}

}

until { // Transition

[streamvar.value >150] { streamvar.value =0; }

[streamvar.value >180] {}

}

## 4.4.3	Parallel mode composition: the par statement

The parallel composition of modes is specified by means of the par statement. A parallel composition may contain sequential modes, parallel modes and atomic modes.

Syntactical Structure

The syntactical structure and context for the cont statement is part of the syntactical structure provided in clause 4.4.1.

The general structure of the par statement is similar to the cont statement and the seq statement. It consists of a body part, which defines the overall behavior of the mode. In case of the par statement the body part contains the mode definitions that are to be composed in parallel. The mode can define an optional invariant and a transition part, as well as onentry and onexit blocks.

Semantic Description

In case of its activation, a parallel composition leads to a parallel execution of all composed (i.e. contained) modes.

While being active, each invariant of a composite mode has to hold. Additionally, each transition of a composite mode ends the activity of the mode when it fires. Furthermore, each mode provides access to an individual local clock that returns the time that has passed since the mode has been activated. The value of the local clock can be obtained by means of the duration keyword

The activation of a parallel mode leads to the parallel activation of all child modes. During execution, the parallel mode is responsible to check the status of all contained modes. The execution of a parallel mode ends, either when a transition in the transition block has fired or when the execution of at least one child mode has been completed. The second situation is called a proper termination of a parallel mode and forces the local symbol finished to yield true (see Section 4.4.1.3).

Examples

EXAMPLE 1:

var integer count := 0;

par{

cont{

x.value:=1;

y.value:=2;

}

until { // Transition

[z.value> 3.0] { }

[] Port2.receive {}

}

cont{

x.value:=2;

y.value:=1;

}

until { // Transition

[z.value> 10.0] { }

[] Port1.receive {}

}

}

until { // Transition

[finished] {if(count > 1) {count++; continue}}

}

NOTE 1: The predicate finished yields true only during the distinct sample step when a child of a parallel mode has finished. Moreover, it yields true for every child element that has finished. Thus, it serves as a notification event, which can be used to model complex termination conditions for parallel modes.

NOTE 2: For parallel execution, it is always possible that several children modes terminate at the same time. Thus, counting the finished child modes to determine if all child modes have finished is not reliable. Instead, the child modes should set conditions that can be queried in the finished

EXAMPLE 2:

par{

cont{

x.value:=1;

y.value:=2;

}

until { // Transition

[z.value> 1.0] { }

[] Port1.receive(msg1) {}

}

cont{

x.value:=2;

y.value:=1;

}

until { // Transition

[z.value> 10.0] { }

[] Port1.receive() {}

}

}

until { // Transition

[z.value > 11.0] { }

[] Port1.receive(msg) {}

}

## 4.4.4	Sequential mode composition: the seq statement

The sequential composition of modes is specified by means of the seq statement. A sequential composition may contain sequential modes, parallel modes and atomic modes.

Syntactical Structure

The syntactical structure and context for the cont statement is part of the syntactical structure provided in clause 4.4.1.

The general structure of the seq statement is similar to the cont statement and the par statement. It consists of a body part, which defines the overall behavior of the mode. In case of the seq statement the body part contains the mode definitions that are to be composed.

Semantic Description

In case of its activation, a sequential composition leads to a sequential execution of the composed (i.e. contained) modes.

While being active, each invariant of a composite mode has to hold. Additionally, each transition of a composite mode ends the activity of the mode when it fires. Furthermore, each mode provides access to an individual local clock that returns the time that has passed since the mode has been activated. The value of the local clock can be obtained by means of the duration keyword

The activation of a sequential mode leads to the activation of its first child mode. During execution, the sequential mode is responsible to schedule the contained modes in their sequential order. Thus, when a child mode has finished, the target mode of the exit transition is activated. Per default, the target mode is the next mode is the sequence\. The execution of a sequential mode ends either when a transition in the transition block is fired or when the execution of the last child mode has been completed. The second situation is called a proper termination of a sequential mode and forces the local symbol finished to yield true (see Section 4.4.1.3).

Examples

The following example defines the sequential execution of two atomic modes, which are composed sequentially by means of a sequential mode.

EXAMPLE 1:

seq{

cont{

x.value:=1;

y.value:=2;

}

until { // Transition

[z.value> 2.0] { }

[] Port1.receive() {}

}

cont{

x.value:=2;

y.value:=1;

}

until { // Transition

[z.value> 1.0] { }

[] Port1.receive() {}

}

}

until { // Transition

[z.value> 12.0] { }

[] Port1.receive(msg) {}

}

## 4.4.5	Parameterizable modes

To provide a higher degree of flexibility, it is possible to specify parameterizable modes. Values, templates, ports, and modes can be used as mode parameters. The definition of parameterizable modes is similar to the definition of TTCN-3 functions.

NOTE: Unlike functions parameterizable modes are not called in the sense of a function call but inserted by means of a substitution mechanism at compile time. Thus, the recursive application of parameterizable modes is not possible.

#### 4.4.5.1 	Mode types

Mode types are the set of identifiers of mode definitions with a specific parameter list and runs on clauses. They denote those modes defined in the test suite that have a compatible parameter list and compatible runs on clauses.

Syntactical Structure

type mode BehaviorTypeIdentifier
"(" { ( FormalValuePar | FormalTimerPar | FormalTemplatePar | FormalPortPar | FormalModePar )    [","] } ")"

[ runs on ( ComponentType | self ]

EXAMPLE 1:

type mode ModeType assert_mode() runs on Tester;

#### 4.4.5.2 	Parameterizable mode definitions

A parameterizable mode definition allows the definition of reusable and parameterizable modes.  A parametrizable mode may be defined within a module.

Syntactical Structure

mode ModeName

["(" { ( FormalValuePar | FormalTimerPar | FormalTemplatePar | FormalPortPar | FormalModePar ) [","] }  ")"]

[ runs on ComponentType ]

( ContMode | ParMode | SeqMode )

Semantic Description

In a module, the behavior of a mode can be defined by using the statements and operations described in Sections 4.4.1 – 4.4.4.

Restrictions

- If a mode uses variables, constants, timers and ports that are declared in a component type definition, the component type shall be referenced using the runs on keywords in the mode header. The one exception to this rule is if all component-wide information used within the mode is passed in as parameters.

- A mode without runs on clause shall never invoke functions or modes with a runs on clause locally.

Examples

EXAMPLE 1:

mode myMode runs on Tester

cont{assert(engine_speed >= 500.0)}

EXAMPLE 2:

type mode assert_mode() runs on Tester;

mode assertion1()  runs on Tester cont{assert(engine_speed >= 500.0)}

mode assertion2() runs on Tester cont{assert(engine_speed >= 0.0)}

mode pert_seq_2(in float startVal,

in float increase,

in assert_mode assertion)

runs on Tester

par{

seq{// perturbation sequence

cont{to_Set_Point:=startVal} until {[duration>=2.0]}

cont{to_Set_Point:=startVal + duration/to_Set_Point.delta*increase}

until {[duration>=5.0]}

}

assertion();

}

testcase myTestcase runs on EngineTester {

// reusable mode application

pert_seq_2(1000.0, 10.0, assertion1);

pert_seq_2(5000.0, 1.0, assertion2);

}

## 4.5 		The wait statement

Syntactical Structure

wait "(" Expression ")"

Semantic Description

The wait statement suspends the execution of a component until a given point in time. The time point is specified as a float value and relates to the internal clock.

The execution of the wait statement suspends the execution of the related component until the point in time specified by its argument. If the argument holds a value that precedes the actual clock value an error verdict shall be set.

EXAMPLE 1:

streamoutport.value = 10.0;

wait(100.0 + now); 				// suspends the execution of a component

// until 100.0 seconds after the start of the testcase

streamoutport.value = 12.0;

Please note: The wait statement has no impact on sampling. All stream ports of the given component are still sampled with respect to their sampling rate.

## 4.6 		Predefined functions

| Category | Function | Keyword |
| --- | --- | --- |
| Length/size functions | Return the length of a value of any string type, record of type or stream port type. | lengthof |
|  | Return the number of elements in a record, record of, template, set, set of, array | sizeof |
| Trigonometric functions | The sine of an angle is the ratio of the length of the opposite side to the length of the hypotenuse | sin |
|  | The cosine of an angle is the ratio of the length of the adjacent side to the length of the hypotenuse. | cos |
|  | The tangent of an angle is the ratio of the length of the opposite side to the length of the adjacent side. | tan |
| Arithmetic functions | natural logarithm | loge |
|  | logarithmic function | log |
|  | the power function | pow |
|  | exponent with base e | exp |
|  | maximum of two numbers | max |
|  | minimum of two numbers | min |
|  | the constant pi | pi |
|  | the absolute value of a number | abs |
|  | the sqare root of a given number | sqrt |
| Other functions | generate a random float number | rnd |

# 5	Package semantics

Not available

# 6	TRI extensions for the package

## 6.1	triStartClock (TE → PA)

| Signature | TriStatus triStartClock(in long ticksPerSecond) |
| --- | --- |
| In Parameters | ticksPerSecond the precision of the clock given in ticks per second |
| Out Parameters | n.a |
| Return Value | The return status of the operation. The return status indicates the success (TRI_OK) or failure (TRI_Error) of the operation. |
| Constraints | n.a. |
| Effect | The operation starts the test system clock with a given precision. The precision is defined by the in parameter ticksPerSecond. The parameter specifies the number of time units (ticks) that characterizes a second . |

## 6.2	triReadClock (TE → PA)

| Signature | TriStatus triReadClock(out long timepoint) |
| --- | --- |
| In Parameters | n.a. |
| Out Parameters | timepoint current time |
| Return Value | The return status of the operation. The return status indicates the success (TRI_OK) or failure (TRI_Error) of the operation. |
| Constraints | There was a preceding invocation of triStartClock(int lont ticksPerSecond) |
| Effect | The operation yields the actual clock value. The clock value is given by the out parameter timepoint, which represents the number of time units (ticks) that has elapsed since the start of the clock ( see triStartClock). |

## 6.3	triNextSampling (TE → PA, SA → PA)

| Signature | TriStatus triNextSampling(in long timepoint, in TriPortIDType port) |
| --- | --- |
| In Parameters | timepoint point in time when the execution of the next sample step for a given stream port shall be started port the stream port the sample step is requested for |
| Out Parameters | n.a. |
| Return Value | The return status of the operation. The return status indicates the success (TRI_OK) or failure (TRI_Error) of the operation. |
| Constraints | There was a preceding invocation of triStartClock(int lont ticksPerSecond) |
| Effect | The operation signals that the next sample step for a given port shall start at the specified point of time timepoint. At this point in time the PA will issue a triProcessStep(in TriPortIDListType ports) operation to inform the TE which ports shall be sampled next. The paremeter timepoint is expressed as the number of time units (ticks), that has elapsed since the the start of the clock (see triStartClock). A call to this operation returns immediately. The operation merely triggers the corresponding triProcessStep operation. If timepoint represent a point of time in the past then the operation returns a TRI_Error value and has no other effect. |

## 6.4	triBeginWait (TE → PA)

| Signature | TriStatus triBeginWait(in long timepoint, in TriComponentIDType component) |
| --- | --- |
| In Parameters | timepoint point in time until execution of a component should be suspended component component whose execution should be suspended |
| Out Parameters | n.a. |
| Return Value | The return status of the operation. The return status indicates the success (TRI_OK) or failure (TRI_Error) of the operation. |
| Constraints | There was a preceding invocation of triStartClock(int lont ticksPerSecond) |
| Effect | The operation signals that the execution of component component should be suspended until the specified point of time timepoint. At this point in time the PA will issue a triEndWait(component) operation. timepoint is expressed as the number of time units (ticks), that has elapsed since the the start of the clock (see triStartClock). A call to this operation returns immediately. The operation merely triggers the corresponding triEndWait operation, it does not schedule the execution of the component. If timepoint represent a point of time in the past then the operation returns a TRI_Error value and has no other effect. |

## 6.5	triProcessStep (PA → TE)

| Signature | void triProcessStep(in TriPortIDListType ports) |
| --- | --- |
| In Parameters | Ports a list of ports that shall be sampled at the operation call |
| Out Parameters | n.a. |
| Return Value | n .a |
| Constraints | There was a preceding invocation of triNextSampling(timepoint, port) |
| Effect | The operation signals that the point in time timepoint that was specified in the corresponding triNextSampling(timepoint, port) has been reached. |

## 6.6	triEndWait (PA → TE)

| Signature | void triEndWait(in TriComponentIDType component) |
| --- | --- |
| In Parameters | component component of the corresponding triBeginWait operation |
| Out Parameters | n.a. |
| Return Value | n .a |
| Constraints | There was a preceding invocation of triBeginWait(timepoint, component) |
| Effect | The operation signals that the point in time timepoint that was specified in the corresponding triBeginWait(timepoint, component) has been reached. |

## 6.7	triSetStreamValue (TE → SA)

## 6.8	triGetStreamValue (TE → SA)

# 7	TCI extensions for the package

## 7.1	tciSetStreamValueReq (TE → CH)

## 7.2 tciSetStreamValue (CH → TE)

# 8	xxx extensions for the package

If needed for the package definition.

<Text>

## 8.1	User defined subdivisions of clause(s) from here onwards

<Text>

<PAGE BREAK>

Annex A (normative):
BNF and static semantics

# A.1	First clause of the annex

# OpCall ::= ConfigurationOps | VerdictOps | TimerOps | TestcaseInstance |

FunctionInstance | TemplateOps | ActivateOp | NowOperation

NowOperation ::= NowKeyword

NowKeyword ::= "now"

AttribKeyword ::= EncodeKeyword |

VariantKeyword |

DisplayKeyword |

StepsizeKeyword |

ExtensionKeyword

StepsizeKeyword ::= "stepsize"

PortDefAttribs ::= StreamAttribs

| MessageAttribs

| ProcedureAttribs

| MixedAttribs

StreamAttribs ::= StreamKeyword "{" StreamDirection Type "}"

StreamList ::= Direction AllOrTypeList

StreamDirection ::= InParKeyword | OutParKeyword

StreamKeyword ::= "stream"

PortInstance ::= PortKeyword PortType PortElement {"," PortElement}

PortElement ::= PortIdentifier [ArrayDef] [AssignmentChar PortInitialValue]

PortIdentifier ::= Identifier

PortInitialValue ::= Expression

OpCall ::= 					  ConfigurationOps |

VerdictOps |

TimerOps |

TestcaseInstance |

FunctionInstance |

TemplateOps |

ActivateOp |

StreamDataOps|

StreamNavigationOps |

ModeLocalOps

CommunicationStatements ::= 	SendStatement |

CallStatement |

ReplyStatement |

RaiseStatement |

ReceiveStatement |

TriggerStatement |

GetCallStatement |

GetReplyStatement |

CatchStatement |

CheckStatement |

ClearStatement |

StartStatement |
StopStatement |

StreamEvalStatements

StreamDataOps ::= 				Port Dot PortDataOp

PortDataOp ::= 					PortValueOp |

PortTimestampOp |

PortDeltaOp |

PortHistoryOp |

PortValuesOp

StreamNavigationOps ::= 		Port Dot ( PortPrevOp | PortAtOp )

[ Dot PortDataOp ]

StreamEvalStatements ::= 		Port Dot (PortApplyOp | PortFindOp | PortViolatesOp)

PortValueOp ::= ValueOpKeyword

ValueOpKeyword ::= "value"

PortTimestampOp ::= TimestampOpKeyword

TimestampOpKeyword ::= "timestamp"

PortDeltaOp ::= DeltaOpKeyword

DeltaOpKeyword ::= "delta"

PortPrevOp ::= PrevOpKeyword ["(" IndexValue ")"]

IndexValue ::= Expression

PrevOpKeyword ::= "prev"

PortAtOp ::= AtOpKeyword ["(" TimeIndexValue ")"]

TimeIndexValue ::= Expression

AtOpKeyword ::= "at"

PortHistoryOp ::= HistoryOpKeyword ["(" StartValue [, EndValue]")"]

StartValue ::= Expression

EndValue ::= Expression

HistoryOpKeyword ::= "history"

PortValuesOp ::= HistoryOpKeyword ["(" StartValue [, EndValue]")"]

StartValue ::= Expression

EndValue ::= Expression

ValuesOpKeyword ::= "values"

PortApplyOp ::= ApplyKeyword "(" ApplyParameter ")"

ApplyKeyword ::= "apply"

ApplyParameter ::= TemplateInstance

PortFindOp ::= FindKeyword "(" FindParameter ")"

FindKeyword ::= "find"

FindParameter ::= TemplateInstance

PortViolatesOp ::= ViolatesKeyword "(" ViolatesParameter ")"

ViolatesKeyword ::= "violates"

ViolatesParameter ::= TemplateInstance

VerdictStatements ::= SetLocalVerdict | AssertStatement

AssertStatement ::= AssertKeyword "(" AssertionList ")"

AssertKeyword ::= "assert"

AssertionList ::= Expression {, Expression }

ModeSpecification ::= ( BasicMode | ComplexMode ) 
[ UntilBlock ]

InvariantBlock ::= InvKeyword "{" InvariantList "}"

InvKeyword ::= "inv"

InvariantList ::= [BooleanExpression {"," BooleanExpression }]

UntilBlock ::= UntilKeyword "{" UntilGuardList "}"

UntilKeyword ::= "until"

UntilGuardList ::= {UntilGuardStatement}

UntilGuardStatement ::= UntilGuardChar GuardOp StatementBlock [GotoClause]

UntilGuardChar ::= "[" [BooleanExpression] "]"

GotoClause ::= GotoKeyword Identifier

BasicMode ::= ContKeyword "{" {VarInstance}

[OnEntryBlock] [InvariantBlock] {BasicModeOp} [OnExitBlock]

"}"

ContKeyword ::= "cont"

BasicModeOp ::= Assignment | AssertStatement  … (e.g. IfStatement)

ComplexMode ::= (SeqKeyword | ParKeyword) "{" {VarInstance}

[OnEntryBlock] [InvariantBlock] ModeList [OnExitBlock]

"}"

ParKeyword ::= "par"

SeqKeyword ::= "seq"

ModeList ::= { [LabelStatement] ModeSpecification }

OnEntryBlock ::= OnEntryKeyword "{" StatementList "}"

OnEntryKeyword ::= "onentry"

OnexitBlock ::= OnexitKeyword "{" StatementList "}"

OnexitKeyword ::= "onexit"

WaitStatement::=  WaitKeyword "(" Expression ")"

WaitKeyword ::= "wait"

ModeLocalOps ::= DurationOp | FinishedOp | NotinvOp

DurationOp ::= DurationKeyword

DurationKeyword ::= "duration"

FinishedOp ::= FinishedKeyword

FinishedKeyword ::= "finished"

NotinvOp ::= NotinvKeyword

NotinvKeyword ::= "notinv"

ModeTypeDef ::= TypeKeyword ModeKeyword Identifier

["(" TemplateOrValueFormalParList ")"]

[RunsOnSpec]

ModeInstance ::= ModeKeyword Identifier

["(" TemplateOfValueFormalParList ")"]

[RunsOnSpec]

ModeSpecification

## A.1.1	First subdivided clause of the annex

<Text>

<PAGE BREAK>

Annex <B> (normative):
Title of normative annex

If needed for the package definition.

Each annex shall start on a new page (insert a page break between annex A and B, annex B and C, ...).

Use the Heading 8 style for the title and the Normal style for the text.

# A.1	First clause of the annex

<Text>

## A.1.1	First subdivided clause of the annex

<Text>

<PAGE BREAK>

Annex B (informative):

Annex C (normative):
Pre-defined TTCN-3 functions

This annex defines the additionally introduced TTCN-3 predefined functions that ease the handling of samples.

# C.1	sin

sin(any_number_type angle) return float

This function calculates the sine of an angle. The sine is the ratio of the length of the opposite side to the length of the hypotenuse. The sin function has a float parameter, which specifies the angle.

# C.2	cos

COS(any_number_type angle) return float

This function calculates the cosine of an angle. The cosine of an angle is the ratio of the length of the adjacent side to the length of the hypotenuse. The cos function has a float parameter, which specifies the angle.

# C.3	tan

tan(any_number_type angle) return float

This function calculates the sine of an angle. The tangent of an angle is the ratio of the length of the opposite side to the length of the adjacent side. The tan function has a float parameter, which specifies the angle.

# C.4	loge

loge(any_number_type value) return float

This function calculates the natural logarithm of a given number.

# C.5	loga

loga(any_number_type base, any_number_type angle) return float

# C.7	pow

pow(any_number_type base, any_number_type exponent) return float

# C.8	sqrt

sqrt(any_number_type value) return float

# C.9	root

root(any_number_type base, any_number_type value) return float

# C.10	max

max(any_number_type value1, any_number_type value2) return any_number_type

# C.11	min

min(any_number_type value1, any_number_type value2) return any_number_type

# C.12	pi

pi() return float

# C.13	abs

abs(any_number_type value) return any_number_type

# C.14	lengthof

lengthof(stream_port_reference port) return integer

Returns the number of samples that has reached or left the test system at the given ports since the start of the testcase. This function is fully equivalent to lengthof(port.history(0,now)).

Annex D (informative):
Example Test Specification with TTCN-3 embedded

If needed for the package definition.

Each annex shall start on a new page.

Use the Heading 8 style for the title and the Normal style for the text.

## B.1	Testing an Advanced Cruise Control

An ACC is a cruise control that automatically detects vehicles running ahead and --- in the case of a slow vehicle ahead (the target) --- it adjusts the actual speed (v_acc) so that a safe distance to the detected vehicle is guaranteed (the distance control mode). When there is no vehicle ahead, an ACC works like any other cruise control (the velocity control mode). Today there are different variants of ACC's available. We use a simplified example here (see Figure 1) that does not match the requirements of a real product but that is sufficient to demonstrate the new features that we have introduced for TTCN-3 embedded.

Abbildung 1 – The Advanced Cruise Control

| Symbol | Direction | Unit | Datatype |
| --- | --- | --- | --- |
| v_target | Out | m/s | Double |
| phi_gas | Out | % | Double |
| leverpos | Out |  | Enumeration |
| d_des | In | m/s | Double |
| acc_mode | In |  | Boolean |
| v_acc | In | m/s | Double |

In this example we test the changeover between distance control mode --- when there is a slow vehicle ahead --- and velocity control mode --- without any vehicle ahead. This forms one of the more complex tasks of an ACC and can be tested by the following test behavior (for a similar test specification (see CON04).

- Accelerate the vehicle phi_gas:=100 until velocity v_acc rises to more than 40 m/s. Than switch on the cruise control leverpos:=HOLD_ACC

- Activate Distance Control Mode

- Now, we introduce a vehicle ahead by setting the target velocity to v_target:= 35+sin(t) m/s. The initial distance d_init:=90 m was set before the test execution using the parameter interface in Matlab/Simulink. The ACC should switch to distance control mode after a few seconds. The safe distance to the vehicle ahead can be calculated with v_acc/2*df. The symbol df represents a distance factor that is set to the value of 2.0 here.

- Accelerate Target: To test whether the ACC switches back to velocity control mode, we accelerate the target vehicle using a smooth ramp. The ACC should now adjust the actual velocity according to the vehicle ahead as long as the velocity exceeds 40 m/s. We allow a tolerance of 10 % here. Afterwards, the ACC should switch back to velocity control mode.

EXAMPLE 1:

module ACCTEST{

type port FloatOut stream {out float};

type port FloatIn stream {in float};

type port BoolIn stream {in float};

type enumerated Lever { MIDDLE, 
HOLD_ACC, 
HOLD_DEC, 
OFF };

type port LeverOut message { out Lever };

type component ACCTester {

port FloatOut v_target, phi_gas;

port FloatIn d_des, v_acc;

port BoolIn acc_mode;

port LeverOut leverpos;

}

…

}with {stepsize “0.1”}

EXAMPLE 2:

const float INIT_SPEED:= 40.0;

const float INIT_T_SPEED:= 35.0;

const float TIMEOUT:= 20000.0;

testcase ACC_Mode_Test() runs on ACCTester {

setverdict(pass);

var float df:= 2.0;

cont {

phi_gas.value:= phi_gas.value+duration;

}

until{

[v_acc.value >= INIT_SPEED]{leverpos.send(HOLD_ACC)}

}

cont {

v_target.value:= 35.0+sin(now)

}

until{

[acc_mode.value]{assert(duration>3.0)}

}

cont {

v_target.value:= 35.0 + duration;

}

until(v_target.value > 40.0)

cont {} until {[duration>2]}

assert(not (acc_mode.value))

}

## B.2	Testing a window lifter application

Abbildung 2 – The Lifter Application

The following test program tests a window lifter application with the following properties. The Window lifter can be controlled by driver commands and passenger commands. The commands are either up, down or neutral. When a driver or a passenger enters and holds the up command the window position increases until the window is closed. When a driver or a passenger enters and holds the down command the window position decreases until the window is completely open. The window controller has an obstacle detection mechanism, that is when an obstacle is introduced during the window is closed, the obstacle must be detected and the closing process should stop immediately.

We introduce the following test case to test the basic mechanisms of the window lifter:

- Driver presses down button. The window opens (i.e. the position value increases)

- When the position reaches the value 4, the up button is pressed and the window is closing (i.e. the position value decreases).

- We check whether the decrease holds for 4 seconds

- Finally we close the window completely.

EXAMPLE 1:

type port StreamIn stream {in float}

type port StreamOut stream {out float}

type component Tester {

port StreamOut Driver_Up;

port StreamOut Driver_Down;

port StreamOut Passenger_Up;

port StreamOut Passenger_Down;

port StreamOut Obstacle;

port StreamOut ObstacleSize;

port StreamIn position;

port StreamIn move_up;

port StreamIn move_down;

}

EXAMPLE 2:

testcase DriverUpDown () runs on Tester {

setverdict(pass);

Driver_Up.value:= 0.0;

Driver_Down.value:=1.0;

log("Start test case");

log("Window Down");

cont {assert( position.value >= position.prev.value)}

until {[duration > 4.0] {Driver_Down.value:= 0.0}}

log("Window Up");

Driver_Up:=1.0;

log(position);

wait(now+ 0.2);

log("Check Window Up");

cont {assert( position <= position.prev.value )}

until {[duration > 4.0] {}}

// Clean up

cont {} until {[position.value < 0.0] {}}

Driver_Up:=0.0;

Driver_Down:=0.0;

} //testcase

We introduce the following test case to test the obstacle detection mechanism:

- The driver presses down button. The window opens (i.e. the position value increases)

- When the position reaches the value 8, the down button is released and after a while the up button is pressed and the window is closing (i.e. the position value decreases).

- When the position reaches the value 3, an obstacle is introduced and the window stops closing immediately.

- We check whether the window stops and holds the position for at least 2 second.

- Afterwards the obstacle is removed and the window closed completely.

EXAMPLE 3:

testcase PassengerUpDownObstacle () runs on Tester {

setverdict(pass);

Passenger_Up.value:= 0.0;

Passenger_Down.value:=1.0;

log("Start test case");

log("Window Down");

wait(now+ 0.2);

cont {assert( position.value >= position.prev.value )}

until {[duration > 4.0] {Passenger_Down.value:= 0.0}}

log("Window Up");

Passenger_Up.value:= 1.0;

log(position);

wait(now+ 0.2);

log("Check Window Up");

cont { assert( position.value <= position.prev.value )}

until {[position < 4.0] {Obstacle:=1.0;}}

cont {assert( position <= position.prev.value )}

until {[position.value < 4.0] {Obstacle.value:=1.0;}}

cont {assert( position.value >3.5 )}

until {[duration > 2.0] {}}

Obstacle.value:=0.0;

cont {} until {[position.value < 0.0] {}}

Passenger_Up.value:= 0.0;

Passenger_Down.value:=0.0;

} //testcase

Figure 3 shows the signal shapes of the logged test data.

Abbildung 3 – Logged Data of The Window Lifter Application

# First clause of the annex

<Text>

## B.1.1	First subdivided clause of the annex

<Text>

<PAGE BREAK>

Annex <y> (informative):
Bibliography

The annex entitled "Bibliography" is optional.

It shall contain a list of standards, books, articles, or other sources on a particular subject which are not mentioned in the document itselft  (see clause 12.2 of the EDRs http://portal.etsi.org/edithelp/other/EDRs_Navigator.chm).

It shall not include the following:

normative references (such references shall be listed in clause 2.1);

informative references (such references shall be listed in clause 2.2).

Use the Heading 8 style for the title and B1+ or Normal for the text.

[1]	ALUR, Rajeev ; COURCOUBETIS, Costas ; HENZINGER, Thomas A. ; HO, Pei-Hsin: Hybrid Automata: An Algorithmic Approach to the Specification and Verification of Hybrid Systems. In: Hybrid Systems, 1992, S. 209–229

[2] 	ALUR, Rajeev (Hrsg.) ; HENZINGER, Thomas A. (Hrsg.) ; SONTAG, Eduardo D. (Hrsg.): Hybrid Systems III: Verification and Control, Proceedings of the DIMACS/SYCONWorkshop, October 22-25, 1995, Ruttgers University, New Brunswick, NJ, USA. Bd. 1066. Springer, 1996 (Lecture Notes in Computer Science). – ISBN 3–540–61155–X

[3]	M. Conrad, E. Sax: Mixed Signals. In: E. Broekman, E. Notenboom: Testing Embedded Software. Addison-Wesley, London (GB), 2003, S. 229-249

[4] 	DIN 40146 Begriffe der Nachrichtenübertragung

[5] 	M. Conrad. Modell-basierter Test eingebetteter Software im Automobil: Auswahl und Beschreibung von Testszenarien. Dissertation, Deutscher Universitätsverlag, Wiesbaden (D), 2004

[6]	BROY, Manfred: Refinement of Time. In: BERTRAN, M. (Hrsg.) ; RUS, Th. (Hrsg.):Transformation-Based Reactive System Development, ARTS’97, TCS, 44 - 63

<PAGE BREAK>

# History

| Document history |
| --- |
| <Version> | <Date> | <Milestone> |
| 0.1 | 28.11.2008 | Initial Draft by TEMEA |

# Text boxes

TD <>

Draft ETSI ES XXX XXX V0.0.1 (yyyy-mm)

ETSI Standard

Methods for Testing and Specification (MTS);

Testing and Test Control Notation version 3 Extension;

Package xx: xxx

Reference

<Workitem>

Keywords

<keyword>

ETSI

650 Route des Lucioles

F-06921 Sophia Antipolis Cedex - FRANCE

Tel.: +33 4 92 94 42 00   Fax: +33 4 93 65 47 16

Siret N° 348 623 562 00017 - NAF 742 C

Association à but non lucratif enregistrée à la

Sous-Préfecture de Grasse (06) N° 7803/88

Important notice

Individual copies of the present document can be downloaded from:
http://www.etsi.org

The present document may be made available in more than one electronic version or in print. In any case of existing or perceived difference in contents between such versions, the reference version is the Portable Document Format (PDF). In case of dispute, the reference shall be the printing on ETSI printers of the PDF version kept on a specific network drive within ETSI Secretariat.

Users of the present document should be aware that the document may be subject to revision or change of status. Information on the current status of this and other ETSI documents is available at http://portal.etsi.org/tb/status/status.asp

If you find errors in the present document, please send your comment to one of the following services:
http://portal.etsi.org/chaircor/ETSI_support.asp

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© European Telecommunications Standards Institute yyyy.

All rights reserved.

DECTTM, PLUGTESTSTM, UMTSTM, TIPHONTM, the TIPHON logo and the ETSI logo are Trade Marks of ETSI registered for the benefit of its Members.
3GPPTM is a Trade Mark of ETSI registered for the benefit of its Members and of the 3GPP Organizational Partners.

| value | 1.2 | 1.4 | 1.5 | 1.7 | 1.7 | 1.5 | 1.2 | 1.0 | 1.1 | 1.4 | 1.5 | 1.2 | 1.0 | 1.1 | 1.4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| timestamp | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0 | 1.1 | 1.2 | 1.3 | 1.4 |

| Value | 0.0 | 0.0 | 0.2 | 0.1 | 0.0 |
| --- | --- | --- | --- | --- | --- |
| Timestamp | 0 | 0.1 | 0.3 | 0.4 | 0.7 |

| Value | 1.2 | 1.4 | 1.5 | 1.7 | 1.7 | 1.5 | 1.2 | 1.0 | 1.1 | 1.4 | 1.5 | 1.2 | 1.0 | 1.1 | 1.4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Timestamp | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0 | 1.1 | 1.2 | 1.3 | 1.4 |

| Value | 1.2 | 1.4 | 1.5 | 1.7 | 1.7 | 1.5 | 1.2 | 1.0 | 1.1 | 1.4 | 1.5 | 1.2 | 1.0 | 1.1 | 1.4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Timestamp | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0 | 1.1 | 1.2 | 1.3 | 1.4 |

| Value | 1.2 | 1.4 | 1.5 | 1.7 | 1.7 | 1.5 | 1.2 | 1.0 | 1.1 | 1.4 | 1.5 | 1.2 | 1.0 | 1.1 | 1.4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Timestamp | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0 | 1.1 | 1.2 | 1.3 | 1.4 |

| Value | 1.2 | 1.4 | 1.5 | 1.7 | 1.7 | 1.5 | 1.2 | 1.0 | 1.1 | 1.4 | 1.5 | 1.2 | 1.0 | 1.1 | 1.4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Timestamp | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0 | 1.1 | 1.2 | 1.3 | 1.4 |

| Value | 0.0 | 0.0 | 0.2 | 0.1 | 0.0 |
| --- | --- | --- | --- | --- | --- |
| Timestamp | 0 | 0.1 | 0.3 | 0.4 | 0.7 |

| Signature | TriStatusType triSetStreamValue( in TriComponentIdType componentId, in TriPortIdType tsiPortId, in TriAddressType SUTaddress, in TriMessageType streamValue) |
| --- | --- |
| In Parameters | componentId identifier of the sending test component tsiPortId identifier of the test system interface port via which the message is sent to the SUT Adapter SUTaddress (optional) destination address within the SUT streamValue the encoded stream value (message) to be sent |
| Out Parameters | n.a. |
| Return Value | The return status of the triSetStreamValue operation. The return status indicates the local success (TRI_OK) or failure (TRI_Error) of the operation. |
| Constraints | The TE calls this operation when it executes a new sampling step on a sampled output stream port, which has been mapped to a TSI port. The TE calls the operation for all sampling steps of all outgoing stream ports if no system component has been specified for a test case, i.e. only a MTC test component is created for a test case. The encoding of streamValue has to be done in the TE prior to this TRI operation call. |
| Effect | The SA can update the message to the SUT. The triSetStreamValue operation returns TRI_OK in case it has been completed successfully. Otherwise TRI_Error shall be returned. Notice that the return value TRI_OK does not imply that the SUT has received streamValue. |

| Signature | TriStatusType triGetStreamValue( in TriComponentIdType componentId, in TriPortIdType tsiPortId, in TriAddressType SUTaddress, out TriMessageType streamValue) |
| --- | --- |
| In Parameters | componentId identifier of the sending test component tsiPortId identifier of the test system interface port via which the message is sent to the SUT Adapter SUTaddress (optional) destination address within the SUT |
| Out Parameters | streamValue the encoded stream value (message) that has been received from the SUT |
| Return Value | The return status of the triGetStreamValue operation. The return status indicates the local success (TRI_OK) or failure (TRI_Error) of the operation. |
| Constraints | The TE calls this operation when it executes a new sampling step on a sampled input stream port, which has been mapped to a TSI port. The TE calls the operation for all sampling steps of all outgoing stream ports if no system component has been specified for a test case, i.e. only a MTC test component is created for a test case. The decoding of streamValue has to be done in the TE after to this TRI operation call. |
| Effect | The SA can update the stream value at the input port. The triGetStreamValue operation returns TRI_OK in case it has been completed successfully. Otherwise TRI_Error shall be returned. |

| Signature | TriStatusType tciSetStreamValueReq(in TriPortIdType sender, in TriComponentIdType receiver, in Value streamValue) |
| --- | --- |
| In Parameters | sender identifier of the port via which the message is sent to the receiving component. receiver identifier of the receiving component SUTaddress (optional) destination address within the SUT streamValue the encoded stream value (message) to be set |
| Out Parameters | n.a. |
| Return Value | The return status of the tciSetStreamValueReq operation. The return status indicates the local success (TRI_OK) or failure (TRI_Error) of the operation. |
| Constraints | The TE calls this operation at the CH when it executes a new sampling step on a sampled output stream port, which has been connected with a test component port. |
| Effect | The CH can call tciSetStreamValue in the TE on the node where the receiver component is deployed. The tciSetStreamValueReq operation returns TRI_OK in case it has been completed successfully. Otherwise TRI_Error shall be returned. Notice that the return value TRI_OK does not imply that the connected component has received streamValue. |

| Signature | TriStatusType tciSetStreamValue( in TriPortIdType sender,in TriComponentIdType receiver in Value streamValue) |
| --- | --- |
| In Parameters | sender identifier of the port from which the message is sampled. receiver identifier of the receiving component streamValue the stream value that has been sampled |
| Out Parameters | n.a. |
| Return Value | The return status of the tciSetStreamValue operation. The return status indicates the local success (TRI_OK) or failure (TRI_Error) of the operation. |
| Constraints | The CH calls this operation in the local TE where receiver is deployed when when tciSetStreamValueReq has been called. |
| Effect | The CH can update the respective stream input port on the test component. The tciGetStreamValue operation returns TRI_OK in case it has been completed successfully. Otherwise TRI_Error shall be returned. |