## 2.2	Informative references

The following referenced documents are not essential to the use of the present document but they assist the user with regard to a particular subject area. For non-specific references, the latest version of the referenced document (including any amendments) applies.

[i.1]	ISO 8601(2004): Data elements and interchange formats – Information interchange – Representation of dates and times..

[i.2]	ETSI ES 201 873-10: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; Part 10: TTCN-3 Documentation Comment Specification.

…

[i.22]	ETSI ES 202 784: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; TTCN-3 Language Extensions: Advanced Parameterization".

[i.23]	ETSI ES 202 785: "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; TTCN-3 Language Extensions: Behaviour Types".

# 10	Parameterization in ASN.1

It is not permitted to reference parameterized ASN.1 definitions from within the TTCN-3 module. However, non-parameterized ASN.1 definitions may reference parameterized ASN.1 definitions by providing the actual parameters. Such ASN.1 definitions can be imported to and used in TTCN-3 and when importing all definitions of an ASN.1 module, such definitions shall also be imported.

NOTE:	The TTCN-3 extension package “Advanced Parameterization” [i.3] specifies, how to support type parameterization in TTCN-3. When both this package and using ASN.1 with TTCN-3 are supported, parameterized ASN.1 definitions can be imported to TTCN-3. All further details are specified in the package “Advanced Parameterization” [i.22].