# C.6	Other functions

## C.6.3	The hostId function

hostid ( in charstring idkind := "IPv4orIPv6") return charstring

The hostid function shall return the host id of the test component or module control executing the hostid  function in form of a character string. The in parameter idkind allows to specify the expected id format to be returned by the hostid  function.

Predefined idkind values are:

- "IPv4orIPv6" : The contents of the returned character string is an IPv4 address. If no IPv4 address, but an IPv6 address is available, a character string representation of the IPv6 address is returned.

- "IPv4" : The contents of the returned character string shall be an IPv4 address.

- "IPv6" : The contents of the returned characterstring shall be an IPv6 address.

The hostid function shall return the empty string, if it cannot retrieve any host id or a host id of a kind different from the kind defined by the actual idkind parameter.

The general error causes in clause 16.1.2 apply.

EXAMPLE:

// assume

testcase MyTestCase () runs on MTC system TSI

{

:

var charstring v_MyHostId := hostid ("IPv4");

:

}

// assume further the following statement in module control

execute(MyTestCase(), -, "127.0.0.1");

// In this setting, v_MyHostId will have the value "127.0.0.1" after the execution of hostid.