ETSI ES 201 873-1 V4.5.1 (2013-04)

Methods for Testing and Specification (MTS);

The Testing and Test Control Notation version 3;

Part 1: TTCN-3 Core Language

ETSI Standard

Reference

RES/MTS-201873-1 T3ed451 cor

Keywords

language, methodology, testing, TTCN-3

ETSI

650 Route des Lucioles

F-06921 Sophia Antipolis Cedex - FRANCE

Tel.: +33 4 92 94 42 00   Fax: +33 4 93 65 47 16

Siret N° 348 623 562 00017 - NAF 742 C

Association à but non lucratif enregistrée à la

Sous-Préfecture de Grasse (06) N° 7803/88

Important notice

Individual copies of the present document can be downloaded from:
http://www.etsi.org

The present document may be made available in more than one electronic version or in print. In any case of existing or perceived difference in contents between such versions, the reference version is the Portable Document Format (PDF). In case of dispute, the reference shall be the printing on ETSI printers of the PDF version kept on a specific network drive within ETSI Secretariat.

Users of the present document should be aware that the document may be subject to revision or change of status. Information on the current status of this and other ETSI documents is available at http://portal.etsi.org/tb/status/status.asp

If you find errors in the present document, please send your comment to one of the following services:
http://portal.etsi.org/chaircor/ETSI_support.asp

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© European Telecommunications Standards Institute 2013.

All rights reserved.

DECTTM, PLUGTESTSTM, UMTSTM and the ETSI logo are Trade Marks of ETSI registered for the benefit of its Members.
3GPPTM and LTE™ are Trade Marks of ETSI registered for the benefit of its Members and
of the 3GPP Organizational Partners.
GSM® and the GSM logo are Trade Marks registered and owned by the GSM Association.

# 3	Definitions and abbreviations

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in Recommendation ITU-T X.290 [5], Recommendation ITU-T X.292 [3] and the following apply:

actual parameter: value, expression, template or name reference (identifier) to be passed as parameter to the invoked entity (function, test case, altstep, etc.) as defined at the place of invoking

assignment notation: notation that can be used for record, set, record of and set of values, where the fields or the elemens to which a value is assigned are identified explicitly within a pair of curly brackets ("{" and "}") by the field names or the positions of the elements

basic types: set of predefined TTCN-3 types described in clauses 6.1.0 and 6.1.1 of the present document

NOTE:	Basic types are referenced by their names.

communication port: abstract mechanism facilitating communication between test components

NOTE:	A communication port is modelled as a FIFO queue in the receiving direction. Ports can be message-based or procedure-based.

compatible type: TTCN-3 is not strongly typed but the language does require type compatibility

NOTE:	Variables, constants, templates, etc. have compatible types if conditions in clause 6.3 are met.

completely initialized: values and templates of simple types are completely initialized if they are partially initialized

NOTE:	Values and templates of structured types and arrays are completely initialized if all their fields and elements are completely initialized. In case of record of, set of, and array values and templates, this means at least the first n elements are initialized, where n is the minimal length imposed by the type length restriction or array definition (thus in case of n equals 0, the value "{}" also completely initializes a record of, a set of or an array).

data types: common name for simple basic types, basic string types, structured types, the special data type anytype and all user defined types based on them (see table 3 of the present document)

defined types (defined TTCN-3 types): set of all predefined TTCN-3 types (basic types, all structured types, the type anytype, the address, port and component types and the default type) and all user-defined types declared either in the module or imported from other TTCN-3 modules

dynamic parameterization: form of parameterization, in which actual parameters are dependent on run-time events; e.g. the value of the actual parameter is a value received during run-time or depends on a received value by a logical relation

exception: in cases of procedure-based communication, an exception (if defined) is raised by an answering entity if it cannot answer a remote procedure call with the normal expected response

formal parameter: typed name or typed template reference (identifier) not resolved at the time of the definition of an entity (function, test case, altstep, etc.) but at the time of invoking it

NOTE:	Actual values or templates (or their names) to be used at the place of formal parameters are passed from the place of invoking the entity (see also the definition of actual parameter).

fuzzy: a value or template is fuzzy if it is re-evaluated at each usage, except using it at the left hand side of an assignment or passing it to a fuzzy or lazy formal parameter. Thus, the evaluation is always delayed until the value or template is used. When a new content is assigned to a subpart of a fuzzy value or template, the other parts of the value or template, not effected by the assignment, are not re-evaluated.

global visibility: attribute of an entity (module parameter, constant, template, etc.) that its identifier can be referenced anywhere within the module where it is defined including all functions, test cases and altsteps defined within the same module and the control part of that module

implementation conformance statement (ICS): See Recommendation ITU-T X.290 [5].

implementation extra information for testing (IXIT): See Recommendation ITU-T X.290 [5].

implementation under test (IUT): See Recommendation ITU-T X.290 [5].

in parameterization: kind of parameterization where the value of the actual parameter (the argument) is bound to the formal parameter when the parameterized object is invoked, but the value of the formal parameter is not passed back to the actual parameter when the invoked object completes

NOTE 1:	The arguments are evaluated before the parameterized object is entered.

NOTE 2:	Only the values of the arguments are passed and changes to the arguments within the invoked object have no effect on the arguments as seen by the invoking object.

index notation: notation that can be used both on the right hand side and the left hand side of assignments for record of and set of values, where the element to which a value is assigned is identified explicitly by the position of that element (in index notation no pair of curly brackets ("{" and "}") is present)

inout parameterization: kind of parameterization where the actual parameter is bound to the formal parameter when the parameterized object is invoked

NOTE 1:	The invoked object uses the actual parameter directly, so that all changes made on the formal parameter become immediately effective on the actual parameter.

NOTE 2:	Inout parameters can be used for functions, altsteps, and test cases only.

known types: set of all TTCN-3 predefined types, types defined in a TTCN-3 module and types imported into that module from other TTCN-3 modules or from non-TTCN-3 modules

lazy: a value or template instance is called lazy, when it is subject to lazy evaluation. That means that evaluation is delayed during execution until the first actual usage, other than using it at the left hand side of an assignment or passing it to a fuzzy or lazy formal parameter. The result of this evaluation is stored in the value or template and the value or template is used further on like ordinary values and templates, without a modifier. If a lazy value or template instance is not used, it is never evaluated.

left hand side (of assignment): value or template variable identifier or a field name of a structured type value or template variable (including array index if any), which stands left to an assignment symbol (:=)

NOTE:	A constant, module parameter, timer, structured type field name or a template header (including template type, name and formal parameter list) standing left of an assignment symbol (:=) in declarations and or a modified template definitions are out of the scope of this definition as not being part of an assignment.

local visibility: attribute of an entity (constant, variable, etc.) that its identifier can be referenced only within the function, test case or altstep where it is defined

main test component (MTC): See Recommendation ITU-T X.292 [3].

out parameterization: kind of parameterization where the value of the actual parameter (the argument) is not bound to the formal parameter when the parameterized object is invoked, but the value of the formal parameter is passed back to the actual parameter when the invoked object completes

NOTE 1:	Out parameters can be used for functions, altsteps, and test cases only.

NOTE 2:	An out formal parameter is uninitialized (unbound) when the invoked object is entered.

NOTE 3:	The value is passed back to the actual parameter only if within the invoked object a value is assigned to it. If no value is assigned, the actual parameter remains unchanged when the invoked object completes.

parallel test component (PTC): See Recommendation ITU-T X.292 [3].

partially initialized: values are partially initialized if a concrete value has been assigned to it or to at least one of its fields or elements

NOTE 1:	A template variable is initialized if a matching mechanism has been assigned to it or to at least one of its fields or elements, directly or indirectly via expansion (see clause 15.6). A template is initialized if a matching mechanism has been assigned to it, directly or indirectly via expansion (see clause 15.6).

NOTE 2:	Thus, constants and templates are always initialized at declaration. Variables (both value and template) are initialized if they, or at least one of their fields or elements has been used on the left hand side of an assignment (including initial value assignment at declaration), except when they were uninitialized before the assignment and the right hand side does not change any of its field or element. Module parameters are initialized either at declaration or by the test system before test execution.

port parameterization: ability to pass a port as an actual parameter into a parameterized object via a port parameter

NOTE:	This actual port parameter is added to the specification of that object and may complete it.

qualified name: TTCN-3 elements can be identified unambiguously by qualified names

NOTE:	For modules, the qualified name is the <module name>. For global definitions such as testcases, functions, etc., the qualified name is <module name>.<definition name>. For control, the qualified name is <module name>.control. For local definitions, such as variables, local templates, etc. within a global definition, the qualified name is <module name>.<global definition name>.<local definition name>.

right hand side (of assignment): expression, template reference or signature parameter identifier which stands right to an assignment symbol (:=)

NOTE:	Expressions and template references standing right of an assignment symbol (:=) in constant, module parameter, timer, template or modified template declarations are out of the scope of this definition as not being part of an assignment.

root type: root types of types derived from TTCN-3 basic types are the respective basic types

NOTE 1:	The root type of user defined record types is record, the root type of user defined record of and array types is record of, the root type of user defined set types is set, the root type of user defined set of types is set of. The root type of user defined union types is union and the root type of anytypes is anytype. The root types of special configuration types are default or component, respectively. Port types do not have a root type.

NOTE 2:	As address is more a predefined type name than a distinct type with its own properties, the root type of an address type and all of its derivatives are the same, as the root type was, if the type was defined with a name different from address.

static parameterization: form of parameterization, in which actual parameters are independent of run-time events; i.e. known at compile time or in case of module parameters are known by the start of the test suite execution

NOTE 1:	A static parameter is to be known from the test suite specification, (including imported definitions), or the test system is aware of its value before execution time.

NOTE 2:	All types are known at compile time, i.e. are statically bound.

strong typing: strict enforcement of type compatibility by type name equivalence with no exceptions

system under test (SUT): See Recommendation ITU-T X.290 [5].

template: TTCN-3 templates are specific data structures for testing; used to either transmit a set of distinct values or to check whether a set of received values matches the template specification

template parameterization: ability to pass a template as an actual parameter into a parameterized object via a template parameter

NOTE 1:	This actual template parameter is added to the specification of that object and may complete it.

NOTE 2:	Values passed to template formal parameters are considered to be in-line templates (see clause 15.4).

test behaviour: (or behaviour) test case or a function started on a test component when executing an execute or a start component statement and all functions and altsteps called recursively

NOTE:	During a test case execution each test component has its own behaviour and hence several test behaviours may run concurrently in the test system (i.e. a test case can be seen as a collection of test behaviours).

test case: See Recommendation ITU-T X.290 [5].

test case error: See Recommendation ITU-T X.290 [5].

test suite: set of TTCN-3 modules that contains a completely defined set of test cases, optionally supplemented with one or more TTCN-3 control parts

test system: See Recommendation ITU-T X.290 [5].

test system interface: test component that provides a mapping of the ports available in the (abstract) TTCN-3 test system to those offered by the SUT

timer parameterization: ability to pass a timer as an actual parameter into a parameterized object via a timer parameter

NOTE:	This actual timer parameter is added to the specification of that object and may complete it.

type compatibility: language feature that allows to use values, expressions or templates of a given type as actual values of another type (e.g. at assignments, as actual parameters at calling a function, referencing a template, etc. or as a return value of a function)

type context: "In the context of a type" means that at least one object involved in the given TTCN-3 action (an assignment, operation, parameter passing etc.) identifies a concrete type unambiguously

NOTE:	Either directly (e.g. an in-line template) or by means of a typed TTCN-3 object (e.g. via a constant, variable, formal parameter etc.).

unqualified name: unqualified name of a TTCN-3 element is its name without any qualification

user-defined type: type that is defined by subtyping of a basic type or declaring a structured type

NOTE:	User-defined types are referenced by their identifiers (names).

value list notation: notation that can be used for record, set, record of and set of values, where the values of the subsequent fields or elements are listed within a pair of curly brackets ("{" and "}"), without an explicit identification of the field name or element position

value notation: notation by which an identifier is associated with a given value or range of a particular type

NOTE:	Values may be constants or variables.

value parameterization: ability to pass a value as an actual parameter into a parameterized object via a value parameter

NOTE:	This actual value parameter is added to the specification of that object and may complete it.

## 5.1	Identifiers and keywords

TTCN-3 identifiers are case sensitive. TTCN-3 keywords shall be written in all lowercase letters (see annex A). TTCN-3 keywords shall neither be used as identifiers of TTCN-3 objects nor as identifiers of objects imported from modules of other languages. The same rules apply to names of predefined TTCN-3 functions (see annex C).

### 5.4.1	Formal parameters

TTCN-3 modules, structured types, templates, functions, altsteps, and testcases may be defined incompletely, i.e. some entities (variables, templates, ports, timers, etc.) used by the above objects may not be resolved in the definition of the object. These objects are called parameterized objects. Formal entities replacing the unresolved entities in the parameterized object's definition are called formal parameters.

Formal parameters of parameterized templates, functions, altsteps, and testcases are defined in formal parameter lists. Formal parameters of modules are defined in module parameter definitions (see clause 8.2.1).

Formal parameters shall be in, inout or out parameters (see definitions in clause 3.1). If not stated otherwise, a formal parameter is an in parameter. For all these three sorts of parameter passing, the formal parameters can both be read and set (i.e. get new values being assigned) within the parameterized object. Formal parameters can be used directly as actual parameters for other parameterized objects, e.g. as actual parameters in function invocations or as actual parameters in template instances.

Formal in parameters may have default values. This default value is used when no actual parameter is provided.

#### NOTE:	Although out parameters can be read within the parameterized object, they do not inherit the value of their actual parameter; i.e. they should be set before they are read.Formal value or template parameters may be declared lazy using the @lazy modifier. In that case, the actual parameter used in place of the formal parameter is subject to lazy evaluation inside the parameterized definition. It shall not be evaluated before the instantiation of the parameterized entity but upon usage.

#### Formal value or template parameters may be declared fuzzy using the @fuzzy modifier. This means that the actual parameter used in place of the formal parameter is subject to lazy evaluation and for each usage of the parameter it is re-evaluated.

#### Lazy and fuzzy features are valid only in the scope, where the parameters’ names are visible. For example, if a fuzzy parameter is passed to a formal parameter declared without a modifier, it losts its fuzzy feature inside the called function. Similarly, if it is passed to a lazy formal parameter, it becomes lazy within the called function.

#### 5.4.1.1	Formal parameters of kind value

Values of all basic types, all user-defined types, address type, component type, and default can be passed as value parameters.

Syntactical Structure

[ ( in | inout | out ) ] [ @lazy | @fuzzy ] Type ValueParIdentifier [ ":=" ( Expression | "-" ) ]

Semantic Description

Value formal parameters can be used within the parameterized object the same way as values, for example in expressions.

Value formal parameters may be in, inout or out parameters. The default for value formal parameters is in parameterization which may optionally be denoted by the keyword in. Using of inout or out kind of parameterization shall be specified by the keywords inout or out respectively.

In parameters may have a default value, which is given by an expression assigned to the parameter. Formal parameters of modified templates may inherit the default values from the corresponding parameters of their parent templates; this shall explicitly be denoted by using a dash (don't change) symbol at the place of the modified template parameters' default value.

TTCN-3 supports value parameterization according to the following rules:

the language element module allows static value parameterization to support test suite parameters, i.e. this parameterization may or may not be resolvable at compile-time but shall be resolved by the commencement of run-time (i.e. static at run-time). This means that, at run-time, module parameter values are globally visible but not changeable (see more details in clause 8.2);

the language elements template, testcase, altstep and function support dynamic value parameterization (i.e. this parameterization shall be resolved at run-time).

NOTE:	Component and default references are also handled as value parameters. In the case of component references, the corresponding component type is the type of the formal parameter. In the case of default references the TTCN-3 type default is the type of the formal parameter.

Restrictions

a)	Language elements which cannot be parameterized are: const, var, timer, control, record of, set of, enumerated, port, component and subtype definitions, group and import.

b)	Formal value parameters of templates, and of altsteps activated as defaults (see clause 20.5.2) shall always be in parameters.

c)	Restrictions on module parameters are given in clause 8.2.

d)	Default values can be provided for in parameters only.

e)	The expression of the default value has to be compatible with the type of the parameter. The expression shall not refer to elements of the component type of the optional runs on clause. The expression shall not refer to other parameters of the same parameter list. The expression shall not contain the invocation of functions with a runs on clause.

f)	Default values of component type formal parameters shall be one of the special values null, mtc, self, or system.

g)	Default values of default type formal parameters shall be the special value null.

h)	The dash (don't change) symbol shall be used with formal parameters of modified templates only (see also clause 15.5).

i)	For formal value parameters of templates the restrictions specified in clause 15 shall apply.

j)	Only in parameters can be declared lazy or fuzzy.

Examples

EXAMPLE 1:	In, out and inout formal parameters

function MyFunction1(in boolean MyReferenceParameter){ … };

// MyReferenceParameter is an in value parameter. The parameter can be read. It can also be set	// within the function, however, the assignment is local to the function only

function MyFunction2(inout boolean MyReferenceParameter){ … };

// MyReferenceParameter is an inout value parameter. The parameter can be read and set

// within the function - the assignment is not local

function MyFunction3(out template boolean MyReferenceParameter){ … };

// MyReferenceParameter is an out value parameter. The parameter can be set within the function, 
	// the assignment is not local. It can also be read, but only after it has been set.

EXAMPLE 2:	Reading and setting parameters

type record MyMessage {

integer f1,

integer f2

}

function f_MyMessage (integer p_int) return MyMessage {

var integer f1, f2;

f1 := f_mult2 (p_int);

// parameter p_int is passed on; as the parameter of the called function f_mult2 is

// defined as an inout parameter, it passes back the changed value for p_int,

f2 := p_int;

return {f1, f2};

}

function f_mult2 (inout integer p_integer) return integer {

p_integer := 2 * p_integer;

// the value of the formal parameter is changed; this new value is passed back when

// f_mult2 completes

return p_integer-1

}

testcase tc_01 () runs on MTC_PT {

...

P1.send (f_MyMessage(5))

// the value sent is { f1 := 9 , f2 := 10 }

...

}

EXAMPLE 3:	Function with default value for parameter

function f_comp (in integer p_int1, in integer p_int2 := 3) return integer {

var integer v := p_int1 + p_int2;

:

return v;

}

	function f () {

var integer w;
	  …

w := f_comp(1);   // same as calling f_comp(1,3);
	  w := f_comp(1,2); // value 2 is taken for parameter p_int2 and not its default value 3

…

}

EXAMPLE 4:	Direct passing of formal parameters to functions

function f_MyFunc2(in bitstring p_refPar1, inout integer p_refPar2) return integer {

:

}

function f_MyFunc1(inout bitstring p_refPar1, out integer p_refPar2) return integer {

:

return f_MyFunc2(p_refPar1, p_refPar2);

}

// p_refPar1 and p_refPar2 can be passed directly to a function invocation

#### 5.4.1.2	Formal parameters of kind template

Template kind parameters are used to pass templates into parameterizable objects.

Syntactical Structure

[ in | inout | out ] template [ Restriction ] [ @lazy | @fuzzy ] Type ValueParIdentifier
														 [ ":=" ( TemplateInstance | "-" ) ]

Semantic Description

Templates parameters can be defined for templates, functions, altsteps, and test cases.

To enable a parameterized object to accept templates or matching symbols as actual parameters, the extra keyword template shall be added before the type field of the corresponding formal parameter. This makes the parameter a template parameter and in effect extends the allowed actual parameters for the associated type to include the appropriate set of matching attributes (see annex B) as well as the normal set of values.

Formal template parameters can be used within the parameterized object the same way as templates and template variables.

Formal template parameters may be in, inout or out parameters. The default for formal template parameters is in parameterization.

In parameters may have a default template, which is given by a template instance assigned to the parameter. Formal template parameters of modified templates may inherit their default templates from the corresponding parameters of their parent templates; this shall explicitly be denoted by using a dash (don't change) symbol at the place of the modified template parameter's default template.

Formal template parameters can be restricted to accept actual parameters containing a restricted set of matching mechanisms only. Such limitations can be expressed by the restrictions omit, present, and value. The restriction template (omit) can be replaced by the shorthand notation omit. The meaning of the restrictions is explained in clause 15.8.

Restrictions

a)	Only function, testcase, altstep and template definitions may have formal template parameters.

b)	Formal template parameters of templates, of functions started as test component behaviour (see clause 21.3.2) and of altsteps activated as defaults (see clause 20.5.2) shall always be in parameters.

c)	Default templates can be provided for in parameters only.

d)	The default template instance has to be compatible with the type of the parameter. The template instance shall not refer to elements of the component type in a runs on clause. The template instance shall not refer to other parameters in the same parameter list. The template instance shall not contain the invocation of functions with a runs on clause.

e)	Default templates of component type formal parameters shall be built from the special values null, mtc, self, or system.

f)	Restrictions specified in clause 15 shall apply.

g)	The dash (don't change) symbol shall be used with formal parameters of modified templates only (see also clause 15.5).

Examples

EXAMPLE 1:	Template with template parameter

// The template

template MyMessageType MyTemplate (template integer MyFormalParam):=

{	field1 := MyFormalParam,

field2 := pattern "abc*xyz",

field3 := true

}

// could be used as follows

pco1.receive(MyTemplate(?));

// Or as follows

pco1.receive(MyTemplate(omit)); // provided that field1 is declared in MyMessageType as optional

EXAMPLE 2:	Function with template parameter

function MyBehaviour(template MyMsgType MyFormalParameter)

runs on MyComponentType

{	 :

pco1.receive(MyFormalParameter);

:

}

EXAMPLE 3:	Template with restricted parameter

// The template

template MyMessageType MyTemplate1 (template ( omit ) integer MyFormalParam):=

{	field1 := MyFormalParam,

field2 := pattern "abc*xyz",

field3 := true

}

// could be used as follows

pco1.send(MyTemplate1(omit));

// but not as follows

pco1.receive(MyTemplate1(?)); // AnyValue is not within the restriction

// the same template can be written shorter as

template MyMessageType MyTemplate2 (omit integer MyFormalParam):=

{	field1 := MyFormalParam,

field2 := pattern "abc*xyz",

field3 := true

}

### 5.4.2	Actual parameters

Values, templates, timers and/or ports can be passed into parameterized TTCN-3 objects as actual parameters. Actual parameters can be provided both as a list in the same order as the formal parameters as well as in an assignment notation explicitly using the associated formal parameter names.

Syntactical Structure

( Expression |												// for value parameter

TemplateInstance |											// for template parameter

TimerRef |													// for timer parameter

Port 	|													// for port parameter

"-" ) |														// to skip a parameter with default
  ParameterId ":=" ( Expression | TemplateInstance | TimerRef | Port ) )

Semantic Description

Actual parameters that are passed by value to in formal value parameters shall be variables, literal values, module parameters, constants, variables, value returning (external) functions, formal value parameters (of in, inout or out parameterization) of the current scope or expressions composed of the above.

Actual parameters that are passed to inout or out formal value parameters shall be variables or formal value parameters (of in, inout or out parameterization).

Actual parameters that are passed to in formal template parameters shall be literal values, module parameters, constants, variables, value or template returning (external) functions, formal value parameters (of in, inout or out parameterization) of the current scope or expressions composed of the above, as well as templates, template variables or formal template parameters (of in, inout or out parameterization) of the current scope.

Actual parameters that are passed to inout or out formal template parameters shall be variables, template variables, formal value or template parameters (of in, inout or out parameterization) of the current scope.

Actual parameters that are passed to formal timer parameters shall be component timers, local timers or formal timer parameters of the current scope.

Actual parameters that are passed to formal port parameters shall be component ports or formal port parameters of the current scope.

When a formal parameter has been defined with a default value or template, respectively, then it is not necessary to provide an actual parameter. The actual parameters are evaluated in the order of their appearance. If for some formal parameters, no actual parameter has been provided, their default values are taken and evaluated in the order of the formal parameter list.

The empty brackets for instances of parameterized templates that have only parameters with default values are optional when no actual parameters are provided, i.e. all formal parameters use their default values.

When an actual parameter is passed to a formal parameter that is declared fuzzy, the un-evaluated actual parameter replaces the formal parameter in the parameterized definition instead of the evaluated actual parameter. That way, the actual parameter is evaluated for each usage inside the parameterized definition.

When an actual parameter is passed to a formal parameter that is declared lazy, the lazy formal parameter is treated like a lazy variable which is assigned the un-evaluated actual parameter inside the parameterized definition.

Restrictions

a)	When using list notation, the order of elements in the actual parameter list shall be the same as their order in the corresponding formal parameter list. For each formal parameter without a default there shall be an actual parameter. The actual parameter of a formal parameter with default value can be skipped by using dash "-" as actual parameter. An actual parameter can also be skipped by just leaving it out if no other actual parameter follows in the actual parameter list - either because the parameter is last or because all following formal parameters have default values and are left out.

b)	Either list notation or assignment notation shall be used in a single parameter list. They shall not be mixed.

c)	When using assignment notation, each formal parameter shall be assigned an actual parameter at most once. For each formal parameter without default value, there shall be an actual parameter. In order to use the default value of a formal parameter, no assignment for this specific parameter shall be provided.

d)	The type of each actual parameter shall be compatible with the type of each corresponding formal parameter.

e)	Actual parameters passed to restricted formal template parameters shall obey the restrictions given in clause 15.8.

f)	All parameterized entities specified as an actual parameter shall have their own parameters resolved in the top-level actual parameter list.

g)	If the formal parameter list of TTCN-3 objects function, testcase, signature, altstep or external function is empty, then the empty parentheses shall be included both in the declaration and in the invocation of that object. In all other cases the empty parentheses shall be omitted.

h)	Restrictions on the use of signature parameters are given in clauses 15.2 and 22.3.

i)	Restrictions on parameters passed to altsteps are given in clauses 16.2.1 and 20.5.2.

j)	Actual fuzzy or lazy parameters shall not contain function calls of functions with inout or out parameters. Called functions may use other functions with inout or out parameters internally.

Examples

EXAMPLE 1:	Formal and actual parameter lists have to match

// A function definition with a formal parameter list

function MyFunction(integer FormalPar1, boolean FormalPar2, bitstring FormalPar3) { … }

// A function call with an actual parameter list

MyFunction(123, true,'1100'B);

// A function call with assignment notation for actual parameters

MyFunction(FormalPar1 := 123, FormalPar3 := '1100'B, FormalPar2 := true);

EXAMPLE 2:	In parameters

function MyFunction(in template MyTemplateType MyValueParameter){ … };

// MyValueParameter is in parameter, the in keyword is optional

// A function call with an actual parameter

MyFunction(MyGlobalTemplate);

EXAMPLE 3:	Inout and out parameters

function MyFunction(inout boolean MyReferenceParameter){ … };

// MyReferenceParameter is an inout parameter

// A function call with an actual parameter

MyFunction(MyBooleanVariable);

// The actual parameter can be read and set within the function

function MyFunction(out template boolean MyReferenceParameter){ … };

// MyReferenceParameter is an out parameter

// A function call with an actual parameter

MyFunction(MyBooleanVariable);

// The actual parameter is initially unbound, but can be set and read within the function.

EXAMPLE 4:	Empty parameter lists

// A function definition with an empty parameter list shall be written as

function MyFunction(){ … }

// and shall be called as

MyFunction();

// A record definition with an empty parameter list shall be written as

type record MyRecord { … }

// and shall be used as

template MyRecord Mytemplate := { … }

EXAMPLE 5:	Nested parameter lists

// Given the message definition

type record MyMessageType

{

integer 	field1,

charstring	field2,

boolean		field3

}

// A message template might be

template MyMessageType MyTemplate(integer MyValue) :=

{

field1 := MyValue,

field2 := pattern "abc*xyz",

field3 := true

}

// A test case parameterized with a template might be

testcase TC001(template MyMessageType RxMsg) runs on PTC1 system TS1 {

:

MyPCO.receive(RxMsg);

}

// When the test case is called in the control part and the parameterized template is

// passed as an actual parameter, the template's actual parameters shall be provided

control

{	:

execute(TC001(MyTemplate(7)));

:

}

EXAMPLE 6:	lazy parameter

Modulepar boolean logSimpleMesssages := true;

function logMsg(@lazy charstring simple, @lazy charstring complex) {

if (logSimpleMessages) {

log(simple);

} else {

log(complex);

}

}

Function computeComplexMessage() return charstring {

// some complicated computation

}

logMsg(“foobar”, computeComplexMessage()); // computeComplexMessage() is only invoked if

// if printSimpleMessages is false

function lazyAnd(@lazy boolean a, @lazy boolean b) return boolean {

if (a) {

return b;

}

else {

return a; // not re-evaluated, must be false

}

}

lazyAnd(ischosen(f.x), f.x)) // correct also for f.x not being chosen => false

# 7	Expressions

TTCN-3 allows the specification of expressions using the operators defined in clause 7.1.

Syntactical Structure

SingleExpression |

"{" { ( FieldReference ":=" ( Expression | "-" )) [","] } "}" | 	// compound expression

"{" [ { ( Expression | "-" ) [","] } ] "}"						// compound expression

Semantic Description

Expressions may be built from other (simple) expressions. Functions used in expressions shall have a return clause. The operands of the operators used in an expression shall be values and their root types shall be the types specified for the appropriate operator in the subsequent clauses.

Compound expressions are used for expressions of array, record, record of and set of types.

Restrictions

In addition to the general static rules of TTCN-3 given in clause 5, the following restrictions apply:

a)	When an expression is evaluated, the evaluated operands of operators used in expressions shall be completely initialized values except where explicitly stated otherwise in the specific clause of the operator.

b)	The root types of the operands shall be the types specified for the appropriate operand.

This means also that all fields and elements of structured types referenced in an expression shall contain completely initialized values, while other fields and elements, not used in the expression, may be uninitialized or contain omit.

Examples

(x + y - increment(z))*3 			// single expression

{ a:= 1, b:= true }					// compound expression, field expression list

{ 1, true }							// compound expression, value list

## 7.1	Operators

TTCN-3 supports a number of predefined operators that may be used in the terms of TTCN-3 expressions. The predefined operators fall into seven categories:

a)	arithmetic operators;

b)	list operator;

c)	relational operators;

d)	logical operators;

e)	bitwise operators;

f)	shift operators;

g)	rotate operators.

Restrictions

In addition to the general static rules of TTCN-3 given in clause 5, the following restrictions apply:

a)	When an experssion is evaluated, the evaluated values used as the operands of operators shall be completely initialized, except for those operands for which it is explicitly allowed to be partially initialized (see clause 11.1).

These operators are listed in table 5.

Table 5: List of TTCN-3 operators

| Category | Operator | Symbol or Keyword |
| --- | --- | --- |
| Arithmetic operators | Addition | + |
|  | Subtraction | - |
|  | Multiplication | * |
|  | Division | / |
|  | Modulo | mod |
|  | Remainder | rem |
| String operators | Concatenation | & |
| Relational operators | Equal | == |
|  | less than | < |
|  | greater than | > |
|  | not equal | != |
|  | greater than or equal | >= |
|  | less than or equal | <= |
| Logical operators | logical not | not |
|  | logical and | and |
|  | logical or | or |
|  | logical xor | xor |
| Bitwise operators | bitwise not | not4b |
|  | bitwise and | and4b |
|  | bitwise or | or4b |
|  | bitwise xor | xor4b |
| Shift operators | shift left | << |
|  | shift right | >> |
| Rotate operators | rotate left | <@ |
|  | rotate right | @> |

The precedence of these operators is shown in table 6. Within any row in this table, the listed operators have equal precedence. If more than one operator of equal precedence appears in an expression, the operations are evaluated from left to right. Parentheses may be used to group operands in expressions, in which case a parenthesized expression has the highest precedence for evaluation.

Table 6: Precedence of Operators

| Priority | Operator type | Operator |
| --- | --- | --- |
| highest Lowest | Unary Binary Binary Unary Binary Binary Binary Binary Binary Binary Unary Binary Binary Binary | ( … ) +, - *, /, mod, rem +, -, & not4b and4b xor4b or4b <<, >>, <@, @> <, >, <=, >= ==, != not and xor or |

# 11	Declaring variables

TTCN-3 variables are statically typed variables. Variables are either value variables to store values or template variables to store templates.

Variables can be of simple basic types, basic string types, structured types, special data types (including subtypes derived from these types) as well as address, component or default types.

Variables can be declared and used in the module control part, test cases, functions and altsteps. Additionally, variables can be declared in component type definitions. These variables can be used in test cases, altsteps and functions which are running on a given component type.

Variables can be declared lazy using the @lazy modifier. .

Alternatively, variables can be declared fuzzy using the @fuzzy modifier.

If a variable is declared lazy or fuzzy, all variables on the right-hand-side of the assignment are substituted with their evaluation before assignment. Later assignments to these variables has no effect on the evaluation of the lazy or fuzzy variable.

Lazy and fuzzy features are valid only in the scope, where the variables’ names are visible. For example, if a fuzzy variable is passed to a formal parameter declared without a modifier, it losts its fuzzy feature inside the called function. Similarly, if it is passed to a lazy formal parameter, it becomes lazy within the called function.

## 11.1	Value variables

A TTCN-3 value variable stores values. It is declared by the var keyword followed by a type identifier and a variable identifier. An initial value can be assigned at variable declaration.

It may be used at the right hand side as well as at the left hand side of assignments, in expressions, following the return keyword in bodies of functions with a return clause in their headers and may be passed to both value and template-type formal parameters.

Syntactical Structure

var [ @lazy | @fuzzy ] Type VarIdentifier [ ArrayDef ] [ ":=" Expression ]

{ [ "," ] VarIdentifier [ ArrayDef ] [ ":=" Expression ] } [ ";" ]

Semantic Description

A value variable associates a name with the location of a value. A value variable may change its value during test execution several times. A value can be assigned several times to a value variable. The value variable can be referenced multiple times in a TTCN-3 module.

Restrictions

In addition to the general static rules of TTCN-3 given in clause 5, the following restrictions apply:

a)	Expression shall be of type Type.

b)	Value variables shall store values only.

c)	Value variables shall not be declared or used in a module definitions part (i.e. global variables are not supported in TTCN-3).

d)	Use of uninitialized value variables at other places than the left hand side of assignments or as actual parameters passed to formal parameters shall cause an error.

e)	Use of partially initialized value variables at other places than the left hand side or the right hand side of assignments, as actual parameters passed to formal parameters, in return statements, or the left operand to the rotate operator or the operands of the list concatenation (&) operator shall cause an error.

g)	The initialization or assignment of a fuzzy or lazy variable shall not contain function calls of functions with inout or out parameters. The called functions may use other functions with inout or out parameters internally.

h) 	If lazy or fuzzy value variables are used in deterministic contexts (i.e. during the evaluation of a snapshot or initialization of global non-fuzzy templates), the same restrictions apply to all functions used in the value assigned to the variable as for functions described in section 16.1.4.

Examples

var integer MyVar0;

var integer MyVar1 := 1;

var boolean MyVar2 := true, MyVar3 := false;

var @lazy integer MyLazyVar1 := 1;

var @lazy integer MyLazyVar2 := MyLazyVar1 + MyVar1; // evaluates to 1 + 1

MyLazyVar1 := MyLazyVar2 + 1; // evaluates to 2 + 1

## 11.2	Template variables

A TTCN-3 template variable stores templates. They are declared by the var template keyword followed by a type identifier and a variable identifier. An initial content can be assigned at declaration. In addition to values, template variables may also store matching mechanisms (see clause 15.7).

Template variables may be used on the right hand side as well as on the left hand side of assignments, following the return keyword in bodies of functions defining a template-type return value in their headers and may be passed as actual parameters to template-type formal parameters. It is also allowed to assign a template instance to a template variable or a template variable field.

Syntactical Structure

var template [ restriction ] [ @lazy | @fuzzy ] Type VarIdentifier [ ArrayDef ] ":=" TemplateBody

{ [ "," ] VarIdentifier [ ArrayDef ] ":=" TemplateBody } [ ";" ]

Semantic Description

A template variable associates a name with the location of a template or a value (as every value is also a template). 
A template variable may change its template during test execution several times. A template or value can be assigned several times to a template variable. The template variable can be referenced multiple times in a TTCN-3 module.

The content of a template variable can be restricted to the matching mechanisms specific value and omit in the same way as formal template parameters, see clause 5.4.1.2. The restriction template (omit) can be replaced by the shorthand notation omit.

NOTE 1:	String and list type templates can be concatenated, see clause 15.11.

Restrictions

In addition to the general static rules of TTCN-3 given in clause 5, the following restrictions apply:

a)	Template variables shall not be declared or used in a module definitions part (i.e. global variables are not supported in TTCN-3).

b)	When used on the right hand side of assignments template variables shall not be operands of TTCN-3 operators (see clause 7.1) and the variable on the left hand side shall be a template variable too.

c)	When accessing element of template variables either on the left hand side or on the right hand side of assignments, the rules given in clause 15.6 shall apply.

NOTE 2:	While it is not allowed to directly apply TTCN-3 operations to template variables, it is allowed to use the dot notation and the index notation to inspect and modify template variable fields.

d)	Use of uninitialized template variables at other places than the left hand side of assignments or as actual parameters passed to formal parameters shall cause an error.

e)	Use of partially initialized template variables at other places than the left hand side or the right hand side of assignments, as actual parameters passed to formal parameters, or in return statements shall cause an error.

f)	If the template variable is restricted, then the template used to initialize it shall contain only the matching mechanisms as described in clause 15.8.

g)	Template variables, similarly to global and local templates, shall be fully specified in order to be used in sending and receiving operations.

h)	Restrictions on templates in clause 15 shall apply.

j)	The initialization or assignment of a fuzzy or lazy variable shall not contain function calls of functions with inout or out parameters. The called functions may use other functions with inout or out parameters internally.

k)	If lazy or fuzzy template variables are used in deterministic contexts (i.e. during the evaluation of a snapshot or initialization of global non-fuzzy templates), the same restrictions apply to all functions used in the template body assigned to the variable as for functions described in section 16.1.4.

Examples

var template integer  MyVarTemp1 := ?;

var template MyRecord MyVarTemp2 := { field1 := true, field2 := * },
				    	   MyVarTemp3 := { field1 := ?, field2 := MyVarTemp1 };

var template @fuzzy float FuzzTemp1 := rnd(); // evaluated on every usage

var template @fuzzy MyRecord FuzzTemp2 := { rnd() < 0.5, float2int(rnd()) }

var template @lazy float LazyTemp1 := FuzzTemp1; // evaluates FuzzTemp1

var template @lazy MyRecord LazyTemp2 :=

{ LazyTemp1 < 0.5, float2int(FuzzTemp1) } // evaluates LazyTemp1 and FuzzTemp1

LazyTemp2.field1 := true; // evaluates LazyTemp2 and overwrites field1 with true

# 15	Declaring templates

Templates are used to either transmit a set of distinct values or to test whether a set of received values matches the template specification. Templates can be defined globally or locally.

Templates provide the following possibilities:

- they are a way to organize and to re-use test data, including a simple form of inheritance;

- they can be parameterized;

- they allow matching mechanisms;

- they can be used with either message-based or procedure-based communications.

Within a template values, ranges and matching attributes can be specified and then used in both message-based and procedure-based communications. Templates may be specified for any TTCN-3 type or procedure signature. The type-based templates are used for message-based communications and the signature templates are used in procedure-based communications.

A template can be declared fuzzy using the @fuzzy modifier

NOTE:	Using a fuzzy template from a non-fuzzy template causes evaluation of the fuzzy template. Thus, for unparameterized non-fuzzy templates, the result of the used fuzzy templates will stay the same for every usage.

A modified template declaration (see clause 15.5) specifies only the fields to be changed from the base template, i.e. it is a partial specification.

Restrictions

In addition to the general static rules of TTCN-3 given in clause 5, the following restrictions apply:

- Templates shall not be of default or port type.

- Templates shall not be of a structured type that contains fields of default or port type on any level of nesting.

- The body of a fuzzy or lazy template shall not contain function calls of functions with inout or out parameters. The called functions may use other functions with inout or out parameters internally.

NOTE:	The anytype type does not include the default type nor port types (see clause 6.2.6), so that restriction b) does not apply to anytype templates.

Examples

type record MyRecord {

default def

}

type union MyUnion {

integer choice1,

MyRecord choice2

}

template MyUnion t_integerChosen := { choice1 := 5 }

// shall cause an error as the type MyUnion contains MyRecord, which includes

// a field of default type.

external function garble(charstring str) return str;

template @fuzzy charstring t_fuzzy := garble(“foobar”); // every usage of t_fuzzy re-evaluates

// the function call

## 15.3	Global and local templates

TTCN-3 allows defining global templates and local templates.

Syntactical Structure

template [ restriction ] [ @fuzzy ] Type TemplateIdentifier  ["(" TemplateFormalParList ")"]

[ modifies TemplateRef ] ":=" TemplateBody

NOTE:	The optional restriction part is covered by clause 15.8.

Semantic Description

Global templates shall be defined in the module definitions part. Local templates shall be defined in module control, testcases, functions, altsteps or statement blocks. Both global and local templates shall adhere to the scoping rules specified in clause 5.

Both global and local templates can be parameterized. The actual parameters of a template can include values and templates. The rules for formal and actual parameter lists shall be followed as defined in clause 5.2.

Both global and local templates are initialized at the place of their declaration. This means, all template fields which are not affected by parameterization shall receive a value or matching mechanism. Template fields affected by parameterization are initialized at the time of template use.

At the time of their use (e.g. in communication operations send, receive, call, getcall, etc.), it is allowed to change template fields by in-line modified templates, to pass in values via value parameters as well as to pass in templates via template parameters. The effects of these changes on the values of the template fields do not persist in the template subsequent to the corresponding communication event.

Restrictions

In addition to restrictions in clause 15, the following restrictions apply:

a)	The dot notation such as MyTemplateId.FieldId shall not be used to set or retrieve values in templates in communication events. The "->" symbol shall be used for this purpose (see clause 23).

b)	Restrictions on referencing elements of templates or template fields are described in clause 15.6.

c)	There exist a number of restrictions on the functions used in expressions when specifying templates or template fields; these are specified in clause 16.1.4.

Examples

// The template

template MyMessageType MyTemplate (integer MyFormalParam):=

{

field1 := MyFormalParam,

field2 := pattern "abc*xyz",

field3 := true

}

// could be used as follows

pco1.send(MyTemplate(123));

## 15.5	Modified templates

Normally, a template specifies a set of base or default values or matching symbols for each and every field defined in the appropriate type or signature definition. In cases where small changes are needed to specify a new template, it is possible to specify a modified template. A modified template specifies modifications to particular fields of the original template, either directly or indirectly. As well as creating explicitly named modified templates, TTCN-3 allows the definition of in-line modified templates.

Syntactical Structure

Global or local modified template:

template [restriction] [@fuzzy] Type TemplateIdentifier  ["(" TemplateFormalParList ")"]

modifies TemplateRef ":=" TemplateBody

NOTE:	The optional restriction part is covered by clause 15.8.

In-line modified template:

[ Type ":" ] modifies TemplateRefWithParList ":=" TemplateBody

Semantic Description

The modifies keyword denotes the parent template from which the new, or modified template shall be derived. This parent template may be either an original template or a modified template.

The modifications occur in a linked fashion eventually tracing back to the original template. If a template field and its corresponding value or matching symbol is specified in the modified template, then the specified value or matching symbol replaces the one specified in the parent template. If a template field and its corresponding value or matching symbol is not specified in the modified template, then the value or matching symbol in the parent template shall be used. When the field to be modified is nested within a template field which is a structured field itself, no other field of the structured field is changed apart from the explicitly denoted one(s).

When individual values of a modified template or a modified template field of record of type wished to be changed, and only in these cases, the value assignment notation may also be used, where the left hand side of the assignment is the index of the element to be altered.

Formal value or template parameters of modified templates inherit the default value or respectively template of the corresponding parameter of their parent templates only, if this is denoted by the dash (don't change) symbol at the place of the parameters' default value or respectively template.

Modified templates may also be restricted. Template restrictions are specified in clause 15.8.

A modified template may also be declared fuzzy using the @fuzzy modifier.

NOTE: If a fuzzy modified template modifies a non-fuzzy unparameterized template, the inherited fields before modification will be the same for every evaluation of the fuzzy template.

Restrictions

In addition to the general static rules of TTCN-3 given in clause 5, the following restrictions apply:

a)	A modified template shall not refer to itself, either directly or indirectly, i.e. recursive derivation is not allowed.

b)	If a base template has a formal parameter list, the following rules apply to all modified templates derived from that base template, whether or not they are derived in one or several modification steps:

1)	the derived template shall not omit parameters defined at any of the modification steps between the base template and the actual modified template;

2)	a derived template can have additional (appended) parameters if wished;

3)	if the dash (don't change) symbol is used at the place of a default value or default template, the corresponding parameter of the parent template shall have a valid default value or default template, either assigned directly or inherited. If not, this shall cause an error.

c)	Restrictions on referencing elements of templates or template fields are described in clause 15.6: for modified templates the rules for the left hand side of assignments apply.

d)	Limitations on template restrictions described in clause 15.8 shall apply.

Examples

EXAMPLE 1:

// Given

type record MyRecordType

{

integer field1 optional,

charstring field2,

boolean field3

}

template MyRecordType MyTemplate1 :=

{

field1 := 123,

field2 := "A string",

field3 := true

}

// then writing

template MyRecordType MyTemplate2 modifies MyTemplate1 :=

{

field1 := omit,					// field1 is optional but present in MyTemplate1

field2 := "A modified string"

// field3 is unchanged

}

// is the same as writing

template MyRecordType MyTemplate2 :=

{

field1 := omit,

field2 := "A modified string",

field3 := true

}

EXAMPLE 2:	Modified record of template

template MyRecordOfType MyBaseTemplate := { 0, 1, 2, 3, 4, 5, 6, 7, 8, 9 };

template MyRecordOfType MyModifTemplate modifies MyBaseTemplate := { [2] := 3, [3] := 2 };
	// MyModifTemplate shall match the sequence of values { 0, 1, 3, 2, 4, 5, 6, 7, 8, 9 }

EXAMPLE 3:	Modified in-line template

// Given

template MyMessageType Setup :=

{	field1 := 75,

field2 := "abc",

field3 := true

}

// Could be used to define an in-line modified template of Setup

pco1.send (modifies Setup := {field1:= 76});

EXAMPLE 4:	Modified parameterized template

// Given

template MyRecordType MyTemplate1(integer MyPar):=

{

field1 := MyPar,

field2 := "A string",

field3 := true

}

// then a modification could be

template MyRecordType MyTemplate2(integer MyPar) modifies MyTemplate1 :=

{	// field1 is parameterized in Template1 and remains also parameterized in Template2

field2 := "A modified string"

}

EXAMPLE 5:	Default values of modified parameterized templates

// Given

template MyRecordType MyTemplate11 (integer p_int := 5 ):= {

// p_int has the default value 5

field1 := p_int,

field2 := "A string",

field3 := true

}

// then possible template modifications are

template MyRecordType MyTemplate12(integer p_int) modifies MyTemplate11 := {

// p_int had a default value in MyTemplate11 but has none in this template

field2 := "B string"

}

template MyRecordType MyTemplate13(integer p_int := 0) modifies MyTemplate12 := {

// p_int has the default value 0

// no change is made to the template's content, but only to the default value of p_int

}

template MyRecordType MyTemplate14(integer p_int := - ) modifies MyTemplate13 := {

// p_int inherits the default value 0 from its parent MyTemplate13

field2 := "C string"

}

template MyRecordType MyTemplate15(integer p_int := - ) modifies MyTemplate14 := {

// p_int inherits the default value 0 from MyTemplate13 via MyTemplate14

field2 := "D string"

}

template MyRecordType MyTemplate16(integer p_int) modifies MyTemplate15 := {

// p_int has no default value

}

template MyRecordType MyTemplate17(integer p_int := - ) modifies MyTemplate16 := {

// causes an error as p_int has no default value in the parent template MyTemplate16

field2 := "E string"

}

## 16.1	Functions

Functions are used in TTCN-3 to express test behaviour, to organize test execution or to structure computation in a module, for example, to calculate a single value, to initialize a set of variables or to check some condition.

Syntactical Structure

function FunctionIdentifier

"(" [ { ( FormalValuePar | FormalTimerPar | FormalTemplatePar | FormalPortPar ) [","] } ] ")"

[ runs on ComponentType ]

[ return [ template ] Type ]

StatementBlock

Semantic Description

Functions are portions of TTCN-3 behaviour, which perform a specific task and are relatively independent of the remaining behaviour.

Functions may return a value or a template. Value return is denoted by the return keyword followed by a type expression. Template return is denoted by the return template keywords followed by an optional restriction and a type expression. Execution of a return statement in the body of the function causes evaluation of the return value or template, the function to terminate and to return the result to the location of the call of the function.

The behaviour of a function can be defined by using statements and operations described in clauses 18 to 25 and clause 26.

Functions may be parameterized.

Restrictions

In addition to the general static rules of TTCN-3 given in clause 5, the following restrictions apply:

- A function without runs on clause shall never invoke a function or altstep or activate an altstep as default with a runs on clause locally.

Functions started by using the start test component operation shall always have a runs on clause (see clause 22.5) and are considered to be invoked in the component to be started, i.e. not locally. However, the start test component operation may be invoked in functions without a runs on clause.

NOTE 1:	The restrictions concerning the runs on clause are only related to functions and altsteps and not to test cases.

Functions used in the control part of a TTCN-3 module shall have no runs on clause.

NOTE 2:	Nevertheless, functions used in the control part are allowed to execute test cases.

The rules for formal parameter lists shall be followed as defined in clause 5.4.

For return template statements the restrictions specified in clause 15 shall apply.

Template return can be restricted to the matching mechanisms specific value and omit, see clause 5.4.1.2.

A return statement in a value returning function shall always have a value expression compatible to the type specified in the function header return clause.

A return statement in a template returning function shall always have a template expression or template instance compatible to the type specified in the function header return clause. If the return clause has a template restriction, this restriction shall be adhered to by the returned template.

If the function header includes a return clause the function, when terminating, shall do so by executing a return statement. The function will cause a test case error if it terminates (i.e. reaches the end of the function body) without executing a return statement.

If a function uses variables, constants, timers and ports that are declared in a component type definition, the component type shall be referenced using the runs on keywords in the function header. The one exception to this rule is if all the necessary component-wide information is passed in the function as parameters.

Examples

EXAMPLE 1:	Function with return

// Definition of MyFunction which has no parameters

function MyFunction() return integer

{

return 7; 	// returns the integer value 7 when the function terminates

}

EXAMPLE 2:	Function with template return

// Definition of functions which may return matching symbols or templates

function MyFunction2() return template integer

{

:

return ?; 	// returns the matching mechanism AnyValue

}

function MyFunction3() return template octetstring

{

:

return 'FF??FF'O; 	// returns an octetstring with AnyValue inside it

}

EXAMPLE 3:	Function with runs on clause

function MyFunction3() runs on MyPTCType {

lo			// MyFunction3 does not return a value, but

var integer MyVar := 5;		// does make use of the port operation

PCO1.send(MyVar);			// send and therefore requires a runs on

// clause to resolve the port identifiers

}								// by referencing a component type

EXAMPLE 4:	Parameterized function

function MyFunction2(inout integer MyPar1) {

// MyFunction2 does not return a value

MyPar1 := 10 * MyPar1;	// but changes the value of	MyPar1 which

}							// is passed in by reference

EXAMPLE 5:	Function without return statement

function MyFunction5(inout integer MyPar1) return integer {

if (MyPar1 > 5) {

MyPar1 := 5;

return MyPar1;

}

// in case of MyPar1 <= 5, MyFunction5 does not terminate in a return statement

// and will cause a test case error

}

### 16.1.1	Invoking functions

A function is invoked by referring to its name and providing the actual list of parameters.

Syntactical Structure

FunctionRef "(" [ { ActualPar [","] } ] ")"

Semantic Description

A function invocation results in the execution of the statement block of the invoked function. The invoked function is performed by the test component invoking it. Actual parameters are passed into the statement block. If the function returns (upon termination and potentially with a return value), the test components continues its behaviour right after the function invocation.

Restrictions

In addition to the general static rules of TTCN-3 given in clause 5, the following restrictions apply:

a)	Functions that do not return values shall be invoked directly. Functions that return values may be invoked directly or inside expressions.

b)	The rules for actual parameter lists shall be followed as defined in clause 5.4.

c)	Special restrictions apply to functions bound to test components using the start test component operation. These restrictions are described in clause 21.3.2.

d)	When invoking a function, the compatibility to the test component type of the invoking test component as described in clause 6.3.3 need to be fulfilled.

e)	Restrictions on invoking functions from specific places are described in clause 16.1.4.

Examples

MyVar := MyFunction4();	// The value returned by MyFunction4 is assigned to MyVar.

// The types of the returned value and MyVar have to be compatible

MyFunction2(MyVar2);	// MyFunction2 does not return a value and is called with the

// actual parameter MyVar2, which may be passed in by reference

MyVar3 := MyFunction6(4) + MyFunction7(MyVar3);	// Functions used in expressions

## 19.1	Assignments

Values or templates may be assigned to variables or template variables (see clause 11). This is indicated by the symbol ":=".

Syntactical Structure

VariableRef ":=" ( Expression | TemplateBody )

Semantic Description

During execution of an assignment, the right-hand side of the assignment shall evaluate to a value or template. The effect of an assignment is to bind the variable to the value of the expression or to a template. The expression shall contain no unbound variables. Assignments are processed from left to right, i.e. expressions in the left-hand-side are evaluated before those in the right-hand-side. The evaluations obey the operator precedence defined in table 6. Unless the assignment is to a lazy or fuzzy variable or parameter, the right-hand-side is evaluated completely before the resulting value or template is bound to the evaluated left-hand side of the assignment. Whenever assignments are used within the right-hand-side of an assignment (due to assignment notation), these rules apply recursively. When a variable which is neither lazy nor fuzzy is assigned, the right-hand-side is evaluated before assignment. When a direct or indirect element or field of a lazy or fuzzy variable is assigned, the variable is also evaluated as much as necessary before assignment, i.e. if an ancestor of that element or field is initialized with a function call, it must be evaluated. Thus, if the variable is fully assigned, it need not be evaluated before assignment.

NOTE 1:	If a sub-field or sub-element of a fuzzy variable is assgined that has an ancestor which was formerly assigned a function call, this function call will be evaluated once before the assignment and replaced by its result inside the variable. Thus, the other sub-fields and sub-elements of that ancestor, apart from the field or element being assigned become non-fuzzy.

Restrictions

In addition to the general static rules of TTCN-3 given in clause 5, the following restrictions apply:

- The right-hand side of an assignment shall evaluate to a value or template, which is type compatible with the variable at the left-hand side of the assignment.

- When the right-hand side of the assignment evaluates to a template (global or local template, in-line template or template variable), the variable at the left hand side shall be a template variable.

- .

Examples

MyVariable := (x + y - increment(z))*3;

type record MyRecord {

record { float x, float y } c,

integer a

}

var @lazy MyRecord r := {

c := computeC(),

a:= computeA()

} // not evaluated here

r.c.x := computeX();	// first replaces field c with result of computeC()

// then replaces field c.x with unevaluated computeX()

// field c.y remains fixed, field a remains unevaluated

## 19.10	The Return statement

The return statement terminates execution of functions or altsteps.

Syntactical Structure

return [ Expression | TemplateInstance ]

Semantic Description

The return statement terminates execution of a function or altstep and returns control to the point from which the function or altstep was called. When used in functions, a return statement may be optionally associated with a return value or template.

TTCN-3 allows optional statement blocks that may follow altstep calls within alt statements. If there is a statement block, the return statement returns control to the beginning of this statement block and the statement block is executed before the alt statement is left. If there is no statement block, test execution continues with the first statement following the alt statement.

The return value or template is first evaluated before returning.

Restrictions

In addition to the general static rules of TTCN-3 given in clause 5, the following restrictions apply:

- The return statement shall not be used in the statement block of a testcase.

Examples

function MyFunction() return boolean {

:

if (date == "1.1.2005") {

return false; 	// execution stops on the 1.1.2000 and returns the boolean false

}

:

return true;		// true is returned

}

function MyTemplateFunction() return template charstring {

:

if (date == "1.1.2005") {

return "2005"; 	// the string of the year is returned

}

:

return ?;			// the any template is returned

}

function MyBehaviour() return verdicttype {

:

if (MyFunction()) {

setverdict(pass); // use of MyFunction in an if statement

}

else {

setverdict(inconc);

}

:

return getverdict; 	// explicit return of the verdict

}

## A.1.5	TTCN-3 terminals

TTCN-3 terminal symbols and reserved words are listed in tables A.2 and A.3.

Table A.2: List of TTCN-3 special terminal symbols

| Begin/end block symbols | { } |
| --- | --- |
| Begin/end list symbols | ( ) |
| Element specifier symbols | [ ] |
| Range symbol | .. |
| Line and block comments | /* */ // |
| Statement separator symbol | ; |
| Arithmetic operator symbols | + / - * |
| Concatenation operator symbol | & |
| Relational operator symbols | != == >= <= < > |
| Shift operator symbols | << >> |
| Rotate operator symbols | <@ @> |
| String enclosure symbols | " ' |
| Wildcard/matching symbols | ? * |
| Assignment symbol | := |
| Communication operation assignment | -> |
| Bitstring, hexstring and Octetstring values | B H O |
| Float exponent | E |
| List element separator symbol | , |

The predefined function identifiers defined in table 14 and described in annex C shall also be treated as reserved words.

Table A.3: List of TTCN-3 terminals which are reserved words

| action activate address alive all alt altstep and and4b any anytype bitstring boolean break case call catch char charstring check clear complement component connect const continue control create deactivate default disconnect display do done else encode enumerated error except exception execute extends extension external | Fail false float for friend from function getverdict getcall getreply goto group halt hexstring if ifpresent import in inconc infinity inout integer interleave kill killed label language length log map match message mixed mod modifies module modulepar mtc | noblock none not not4b nowait null octetstring of omit on optional or or4b out override param pass pattern permutation port present private procedure public raise read receive record recursive rem repeat reply return running runs | select self send sender set setverdict signature start stop subset superset system template testcase timeout timer to trigger true type union universal unmap value valueof var variant verdicttype while with xor xor4b |
| --- | --- | --- | --- |

# The TTCN-3 terminals listed in table A.3 shall not be used as identifiers in a TTCN-3 module. These terminals shall be written in all lowercase letters.

#### A.1.6.1.3	Template definitions

83.TemplateDef ::= TemplateKeyword [TemplateRestriction] [FuzzyModifier] BaseTemplate

[DerivedDef] AssignmentChar TemplateBody

84.BaseTemplate ::= (Type | Signature) Identifier ["(" TemplateOrValueFormalParList

")"]

85.TemplateKeyword ::= "template"

86.DerivedDef ::= ModifiesKeyword ExtendedIdentifier

87.ModifiesKeyword ::= "modifies"

88.TemplateOrValueFormalParList ::= TemplateOrValueFormalPar {"," TemplateOrValueFormalPar}

89.TemplateOrValueFormalPar ::= FormalValuePar | FormalTemplatePar 

/* STATIC SEMANTICS - FormalValuePar shall resolve to an in parameter */

90.TemplateBody ::= (SimpleSpec |

FieldSpecList |

ArrayValueOrAttrib

) [ExtraMatchingAttributes] 

/* STATIC SEMANTICS - Within TeplateBody the ArrayValueOrAttrib can be used for array, record, record of and set of types. */

91.SimpleSpec ::= (SingleExpression ["&" SimpleTemplateSpec]) | SimpleTemplateSpec

92.SimpleTemplateSpec ::= SingleTemplateExpression ["&" SimpleSpec]

93.SingleTemplateExpression ::= MatchingSymbol | (TemplateRefWithParList

[ExtendedFieldReference])

94.FieldSpecList ::= "{" FieldSpec {"," FieldSpec} "}"

95.FieldSpec ::= FieldReference AssignmentChar (TemplateBody |  Minus)

96.FieldReference ::= StructFieldRef |

ArrayOrBitRef |

ParRef

97.StructFieldRef ::= Identifier |

PredefinedType |

TypeReference 

/* STATIC SEMANTICS - PredefinedType and TypeReference shall be used for anytype value notation only. PredefinedType shall not be AnyTypeKeyword.*/

98.ParRef ::= Identifier 

/* STATIC SEMANTICS - Identifier in ParRef shall be a formal parameter identifier from the associated signature definition */

99.ArrayOrBitRef ::= "[" FieldOrBitNumber "]" 

/* STATIC SEMANTICS - ArrayRef shall be optionally used for array types and TTCN-3 record of and set of. The same notation can be used for a Bit reference inside an TTCN-3 charstring, universal charstring, bitstring, octetstring and hexstring type */

100.FieldOrBitNumber ::= SingleExpression 

/* STATIC SEMANTICS - SingleExpression will resolve to a value of integer type */

101.ArrayValueOrAttrib ::= "{" [ArrayElementSpecList] "}"

102.ArrayElementSpecList ::= ArrayElementSpec {"," ArrayElementSpec}

103.ArrayElementSpec ::= Minus |

PermutationMatch |

TemplateBody

104.MatchingSymbol ::= Complement |

(AnyValue [WildcardLengthMatch]) |

(AnyOrOmit [WildcardLengthMatch]) |

ListOfTemplates |

Range |

BitStringMatch |

HexStringMatch |

OctetStringMatch |

CharStringMatch |

SubsetMatch |

SupersetMatch 

/* STATIC SEMANTIC – WildcardLengthMatch shall be used when MatchingSymbol is used in fractions of a concatenated string or list (see clause 15.11) and shall not be used in other cases. In this case, the Complement, TemplateList, Range, BitStringMatch, HexStringMatch, OctetStringMatch, CharStringMatch, SubsetMatch and SupersetMatch productions shall not be used. */

105.ExtraMatchingAttributes ::= StringLength |

IfPresentKeyword |

(StringLength IfPresentKeyword)

106.BitStringMatch ::= "'" {BinOrMatch} "'" "B"

107.BinOrMatch ::= Bin |

AnyValue |

AnyOrOmit

108.HexStringMatch ::= "'" {HexOrMatch} "'" "H"

109.HexOrMatch ::= Hex |

AnyValue |

AnyOrOmit

110.OctetStringMatch ::= "'" {OctOrMatch} "'" "O"

111.OctOrMatch ::= Oct |

AnyValue |

AnyOrOmit

112.CharStringMatch ::= PatternKeyword PatternParticle {"&" PatternParticle}

113.PatternParticle ::= Pattern | ReferencedValue

114.PatternKeyword ::= "pattern"

115.Pattern ::= """ {PatternElement} """

116.PatternElement ::= (("\" ("?" | "*" | "\" | "[" | "]" | "{" | "}" |

""" | "|" | "(" | ")" | "#" | "+" | "d" |

"w" | "t" | "n" | "r" | "s" | "b"

)) |

("?" | "*" | "\" | "|" | "+") |

("[" ["^"] [{PatternClassChar ["-" PatternClassChar]}]"]") |

("{" ["\"] ReferencedValue "}") |

("\" "N" "{" (ReferencedValue | Type) "}") |

(""" """) |

("(" PatternElement ")") |

("#" (Num |

("(" Num "," [Num] ")") | ("(" "," Num ")")

)) |

PatternChar

117.PatternChar ::= NonSpecialPatternChar | PatternQuadruple

/* STATIC SEMANTICS: Characters "?", "*", "\", "[", "]", "{", "}", """, "|", "(", ")", "#", "+", "d", "^", "N" have special semantics – they are metacharacters for the definition of pattern elements – only if they follow the BNF as defined above, if not they are interpreted like normal characters */

118.NonSpecialPatternChar ::= Char 
119.PatternClassChar ::= NonSpecialPatternClassChar |

PatternQuadruple |

"\" EscapedPatternClassChar

120.NonSpecialPatternClassChar ::= Char 
/* STATIC SEMANTICS: Characters "[", "-", "^", "]", "\", "q", ","have special semantics – they are metacharacters for the definition of pattern class characters – only if they follow the BNF as defined above, if not they are interpreted like normal characters */

121.EscapedPatternClassChar ::= "[" | "-" | "^" | "]"
121.PatternQuadruple ::= "\" "q" "(" Number "," Number "," Number ","

Number ")"

122.Complement ::= ComplementKeyword ListOfTemplates

123.ComplementKeyword ::= "complement"

124.ListOfTemplates ::= "(" TemplateListItem {"," TemplateListItem} ")"

125.TemplateListItem ::= TemplateBody | AllElementsFrom

126.AllElementsFrom ::= AllKeyword FromKeyword TemplateBody

127.SubsetMatch ::= SubsetKeyword ListOfTemplates

128.SubsetKeyword ::= "subset"

129.SupersetMatch ::= SupersetKeyword ListOfTemplates

130.SupersetKeyword ::= "superset"

131.PermutationMatch ::= PermutationKeyword ListOfTemplates

/* STATIC SEMANTICS: Restrictions on the content of TemplateBody within the ListOfTemplates are given in clause B.1.3.3. */

132.PermutationKeyword ::= "permutation"

134.AnyValue ::= "?"

135.AnyOrOmit ::= "*"

136.TemplateList ::= "(" TemplateBody {"," TemplateBody}+ ")"

137.WildcardLengthMatch ::= LengthKeyword "(" SingleExpression ")"

/* STATIC SEMANTICS: SingleExpression shall evaluate to type integer */

138.IfPresentKeyword ::= "ifpresent"

139.PresentKeyword ::= "present"

140.Range ::= "(" Bound ".." Bound ")"

141.Bound ::= (["!"] SingleExpression) | ([Minus] InfinityKeyword) 

/* STATIC SEMANTICS - Bounds shall evaluate to types integer, charstring, universal charstring or float. In case they evaluate to types charstring or universal charstring, the string length shall be 1. infinity as lower bound and –infinity as upper bound are allowed for float types only. */

142.InfinityKeyword ::= "infinity"

143.TemplateInstanceAssignment ::= Identifier ":=" InLineTemplate 

/* STATIC SEMANTICS – if a value parameter is used, the inline template shall evaluate to a value */

144.TemplateRefWithParList ::= ExtendedIdentifier [TemplateActualParList]

145.InLineTemplate ::= [(Type | Signature) Colon] [DerivedRefWithParList

AssignmentChar] TemplateBody

146.DerivedRefWithParList ::= ModifiesKeyword TemplateRefWithParList

147.TemplateActualParList ::= "(" [(TemplateInstanceActualPar {"," TemplateInstanceActualPar}) |

(TemplateInstanceAssignment {"," TemplateInstanceAssignment})]

")"

148.TemplateInstanceActualPar ::= InLineTemplate | Minus 

/* STATIC SEMANTICS - When the corresponding formal parameter is not of template type the TemplateInstance production shall resolve to one or more SingleExpressions */

149.TemplateOps ::= MatchOp | ValueofOp

150.MatchOp ::= MatchKeyword "(" Expression "," InLineTemplate ")"

151.MatchKeyword ::= "match"

152.ValueofOp ::= ValueofKeyword "(" InLineTemplate ")"

153.ValueofKeyword ::= "valueof"

#### A.1.6.1.4	Function definitions

154.FunctionDef ::= FunctionKeyword Identifier "(" [FunctionFormalParList]

")" [RunsOnSpec] [ReturnType] StatementBlock

155.FunctionKeyword ::= "function"

156.FunctionFormalParList ::= FunctionFormalPar {"," FunctionFormalPar}

157.FunctionFormalPar ::= FormalValuePar |

FormalTimerPar |

FormalTemplatePar |

FormalPortPar

158.ReturnType ::= ReturnKeyword [TemplateKeyword | RestrictedTemplate]

Type

159.ReturnKeyword ::= "return"

160.RunsOnSpec ::= RunsKeyword OnKeyword ComponentType

161.RunsKeyword ::= "runs"

162.OnKeyword ::= "on"

163.MTCKeyword ::= "mtc"

164.StatementBlock ::= "{" [FunctionDefList] [FunctionStatementList] "}"

165.FunctionDefList ::= {(FunctionLocalDef | FunctionLocalInst) [WithStatement] [SemiColon]}+

166.FunctionStatementList ::= {FunctionStatement [SemiColon]}+

167.FunctionLocalInst ::= VarInstance | TimerInstance

168.FunctionLocalDef ::= ConstDef | TemplateDef

169.FunctionStatement ::= ConfigurationStatements |

TimerStatements |

CommunicationStatements |

BasicStatements |

BehaviourStatements |

SetLocalVerdict |

SUTStatements |

TestcaseOperation

170.FunctionInstance ::= FunctionRef "(" [FunctionActualParList] ")"

171.FunctionRef ::= [Identifier Dot] (Identifier | PreDefFunctionIdentifier)

172.PreDefFunctionIdentifier ::= Identifier 

/* STATIC SEMANTICS - The Identifier shall be one of the pre-defined TTCN-3 Function Identifiers from Annex C of ES 201 873-1 */

173.FunctionActualParList ::= (FunctionActualPar {"," FunctionActualPar}) |

(FunctionActualParAssignment {"," FunctionActualParAssignment})

174.FunctionActualPar ::= ArrayIdentifierRef |

InLineTemplate |

ComponentRef |

Minus 

/* STATIC SEMANTICS - When the corresponding formal parameter is not of template type the TemplateInstance production shall resolve to one or more SingleExpressions i.e. equivalent to the Expression production */

175.FunctionActualParAssignment ::= TemplateInstanceAssignment |

ComponentRefAssignment |

ArrayIdentifierRefAssignment

176.ArrayIdentifierRefAssignment ::= Identifier ":=" ArrayIdentifierRef

#### A.1.6.1.5	Signature definitions

177.SignatureDef ::= SignatureKeyword Identifier "(" [SignatureFormalParList]

")" [ReturnType | NoBlockKeyword] [ExceptionSpec]

178.SignatureKeyword ::= "signature"

179.SignatureFormalParList ::= FormalValuePar {"," FormalValuePar}

180.ExceptionSpec ::= ExceptionKeyword "(" TypeList ")"

181.ExceptionKeyword ::= "exception"

182.Signature ::= ExtendedIdentifier

183.NoBlockKeyword ::= "noblock"

#### A.1.6.1.6	Testcase definitions

184.TestcaseDef ::= TestcaseKeyword Identifier "(" [TemplateOrValueFormalParList]

")" ConfigSpec StatementBlock

185.TestcaseKeyword ::= "testcase"

186.ConfigSpec ::= RunsOnSpec [SystemSpec]

187.SystemSpec ::= SystemKeyword ComponentType

188.SystemKeyword ::= "system"

189.TestcaseInstance ::= ExecuteKeyword "(" ExtendedIdentifier "(" [TestcaseActualParList]

")" ["," (Expression | Minus) ["," SingleExpression]]

")"

190.ExecuteKeyword ::= "execute"

191.TestcaseActualParList ::= (TemplateInstanceActualPar {"," TemplateInstanceActualPar}) |

(TemplateInstanceAssignment {"," TemplateInstanceAssignment}) 

/* STATIC SEMANTICS - When the corresponding formal parameter is not of template type the TemplateInstance production shall resolve to one or more SingleExpressions i.e. equivalent to the Expression production */

#### A.1.6.1.7	Altstep definitions

192.AltstepDef ::= AltstepKeyword Identifier "(" [FunctionFormalParList]

")" [RunsOnSpec] "{" AltstepLocalDefList AltGuardList

"}"

193.AltstepKeyword ::= "altstep"

194.AltstepLocalDefList ::= {AltstepLocalDef [WithStatement] [SemiColon]}

195.AltstepLocalDef ::= VarInstance |

TimerInstance |

ConstDef |

TemplateDef

196.AltstepInstance ::= ExtendedIdentifier "(" [FunctionActualParList]

")"

#### A.1.6.1.8	Import definitions

197.ImportDef ::= ImportKeyword ImportFromSpec (AllWithExcepts | ("{"

ImportSpec

"}"))

198.ImportKeyword ::= "import"

199.AllWithExcepts ::= AllKeyword [ExceptsDef]

200.ExceptsDef ::= ExceptKeyword "{" ExceptSpec "}"

201.ExceptKeyword ::= "except"

202.ExceptSpec ::= {ExceptElement [SemiColon]}

203.ExceptElement ::= ExceptGroupSpec |

ExceptTypeDefSpec |

ExceptTemplateSpec |

ExceptConstSpec |

ExceptTestcaseSpec |

ExceptAltstepSpec |

ExceptFunctionSpec |

ExceptSignatureSpec |

ExceptModuleParSpec

204.ExceptGroupSpec ::= GroupKeyword (QualifiedIdentifierList | AllKeyword)

205.IdentifierListOrAll ::= IdentifierList | AllKeyword

206.ExceptTypeDefSpec ::= TypeDefKeyword IdentifierListOrAll

207.ExceptTemplateSpec ::= TemplateKeyword IdentifierListOrAll

208.ExceptConstSpec ::= ConstKeyword IdentifierListOrAll

209.ExceptTestcaseSpec ::= TestcaseKeyword IdentifierListOrAll

210.ExceptAltstepSpec ::= AltstepKeyword IdentifierListOrAll

211.ExceptFunctionSpec ::= FunctionKeyword IdentifierListOrAll

212.ExceptSignatureSpec ::= SignatureKeyword IdentifierListOrAll

213.ExceptModuleParSpec ::= ModuleParKeyword IdentifierListOrAll

214.ImportSpec ::= {ImportElement [SemiColon]}

215.ImportElement ::= ImportGroupSpec |

ImportTypeDefSpec |

ImportTemplateSpec |

ImportConstSpec |

ImportTestcaseSpec |

ImportAltstepSpec |

ImportFunctionSpec |

ImportSignatureSpec |

ImportModuleParSpec |

ImportImportSpec

216.ImportFromSpec ::= FromKeyword ModuleId [RecursiveKeyword]

217.RecursiveKeyword ::= "recursive"

218.ImportGroupSpec ::= GroupKeyword (GroupRefListWithExcept | AllGroupsWithExcept)

219.GroupRefListWithExcept ::= QualifiedIdentifierWithExcept {"," QualifiedIdentifierWithExcept}

220.AllGroupsWithExcept ::= AllKeyword [ExceptKeyword QualifiedIdentifierList]

221.QualifiedIdentifierWithExcept ::= QualifiedIdentifier [ExceptsDef]

222.IdentifierListOrAllWithExcept ::= IdentifierList | AllWithExcept

223.ImportTypeDefSpec ::= TypeDefKeyword IdentifierListOrAllWithExcept

224.AllWithExcept ::= AllKeyword [ExceptKeyword IdentifierList]

225.ImportTemplateSpec ::= TemplateKeyword IdentifierListOrAllWithExcept

226.ImportConstSpec ::= ConstKeyword IdentifierListOrAllWithExcept

227.ImportAltstepSpec ::= AltstepKeyword IdentifierListOrAllWithExcept

228.ImportTestcaseSpec ::= TestcaseKeyword IdentifierListOrAllWithExcept

229.ImportFunctionSpec ::= FunctionKeyword IdentifierListOrAllWithExcept

230.ImportSignatureSpec ::= SignatureKeyword IdentifierListOrAllWithExcept

231.ImportModuleParSpec ::= ModuleParKeyword IdentifierListOrAllWithExcept

232.ImportImportSpec ::= ImportKeyword AllKeyword

#### A.1.6.1.9	Group definitions

233.GroupDef ::= GroupKeyword Identifier "{" [ModuleDefinitionsList] "}"

234.GroupKeyword ::= "group"

#### A.1.6.1.10	External function definitions

235.ExtFunctionDef ::= ExtKeyword FunctionKeyword Identifier "(" [FunctionFormalParList]

")" [ReturnType]

236.ExtKeyword ::= "external"

#### A.1.6.1.11	External constant definitions

237.ExtConstDef ::= ExtKeyword ConstKeyword Type IdentifierList

#### A.1.6.1.12	Module parameter definitions

238.ModuleParDef ::= ModuleParKeyword (ModulePar | ("{" MultitypedModuleParList

"}"))

239.ModuleParKeyword ::= "modulepar"

240.MultitypedModuleParList ::= {ModulePar [SemiColon]}

241.ModulePar ::= Type ModuleParList

242.ModuleParList ::= Identifier [AssignmentChar ConstantExpression] {","

Identifier

[AssignmentChar

ConstantExpression]}

#### A.1.6.1.13	Friend module definitions

243.FriendModuleDef ::= "friend" "module" IdentifierList [SemiColon]

### A.1.6.2	Control part

244.ModuleControlPart ::= ControlKeyword "{" ModuleControlBody "}" [WithStatement]

[SemiColon]

245.ControlKeyword ::= "control"

246.ModuleControlBody ::= [ControlStatementOrDefList]

247.ControlStatementOrDefList ::= {ControlStatementOrDef [SemiColon]}+

248.ControlStatementOrDef ::= ( FunctionLocalDef |

FunctionLocalInst ) [WithStatement] |

ControlStatement

249.ControlStatement ::= TimerStatements |

BasicStatements |

BehaviourStatements |

SUTStatements |

StopKeyword

### A.1.6.3	Local definitions

#### A.1.6.3.1	Variable instantiation

250.VarInstance ::= VarKeyword (([LazyModifier | FuzzyModifier] Type VarList) |

((TemplateKeyword | RestrictedTemplate)

[LazyModifier | FuzzyModifier] Type TempVarList))

251.VarList ::= SingleVarInstance {"," SingleVarInstance}

252.SingleVarInstance ::= Identifier [ArrayDef] [AssignmentChar Expression]

253.VarKeyword ::= "var"

254.TempVarList ::= SingleTempVarInstance {"," SingleTempVarInstance}

255.SingleTempVarInstance ::= Identifier [ArrayDef] [AssignmentChar TemplateBody]

256.VariableRef ::= Identifier [ExtendedFieldReference]

#### A.1.6.3.2	Timer instantiation

257.TimerInstance ::= TimerKeyword VarList

258.TimerKeyword ::= "timer"

259.ArrayIdentifierRef ::= Identifier {ArrayOrBitRef}

### A.1.6.4	Operations

#### A.1.6.4.1	Component operations

260.ConfigurationStatements ::= ConnectStatement |

MapStatement |

DisconnectStatement |

UnmapStatement |

DoneStatement |

KilledStatement |

StartTCStatement |

StopTCStatement |

KillTCStatement

261.ConfigurationOps ::= CreateOp |

SelfOp |

SystemKeyword |

MTCKeyword |

RunningOp |

AliveOp

262.CreateOp ::= ComponentType Dot CreateKeyword ["(" (SingleExpression |

Minus) ["," SingleExpression]

")"] [AliveKeyword]

263.SelfOp ::= "self"

264.DoneStatement ::= ComponentId Dot DoneKeyword

265.KilledStatement ::= ComponentId Dot KilledKeyword

266.ComponentId ::= ComponentOrDefaultReference | (AnyKeyword | AllKeyword)

ComponentKeyword

267.DoneKeyword ::= "done"

268.KilledKeyword ::= "killed"

269.RunningOp ::= ComponentId Dot RunningKeyword

270.RunningKeyword ::= "running"

271.AliveOp ::= ComponentId Dot AliveKeyword

272.CreateKeyword ::= "create"

273.AliveKeyword ::= "alive"

274.ConnectStatement ::= ConnectKeyword SingleConnectionSpec

275.ConnectKeyword ::= "connect"

276.SingleConnectionSpec ::= "(" PortRef "," PortRef ")"

277.PortRef ::= ComponentRef Colon ArrayIdentifierRef

278.ComponentRef ::= ComponentOrDefaultReference |

SystemKeyword |

SelfOp |

MTCKeyword

279.ComponentRefAssignment ::= Identifier ":=" ComponentRef

280.DisconnectStatement ::= DisconnectKeyword [SingleConnectionSpec |

AllConnectionsSpec |

AllPortsSpec |

AllCompsAllPortsSpec]

281.AllConnectionsSpec ::= "(" PortRef ")"

282.AllPortsSpec ::= "(" ComponentRef ":" AllKeyword PortKeyword ")"

283.AllCompsAllPortsSpec ::= "(" AllKeyword ComponentKeyword ":" AllKeyword

PortKeyword ")"

284.DisconnectKeyword ::= "disconnect"

285.MapStatement ::= MapKeyword SingleConnectionSpec [ParamClause]

286.ParamClause ::= ParamKeyword FunctionActualParList

287.MapKeyword ::= "map"

288.UnmapStatement ::= UnmapKeyword [SingleConnectionSpec [ParamClause] |

AllConnectionsSpec [ParamClause] |

AllPortsSpec |

AllCompsAllPortsSpec]

289.UnmapKeyword ::= "unmap"

290.StartTCStatement ::= ComponentOrDefaultReference Dot StartKeyword

"(" FunctionInstance ")"

291.StartKeyword ::= "start"

292.StopTCStatement ::= StopKeyword | (ComponentReferenceOrLiteral | AllKeyword

ComponentKeyword) Dot StopKeyword

293.ComponentReferenceOrLiteral ::= ComponentOrDefaultReference |

MTCKeyword |

SelfOp

294.KillTCStatement ::= KillKeyword | ((ComponentReferenceOrLiteral |

AllKeyword ComponentKeyword) Dot

KillKeyword)

295.ComponentOrDefaultReference ::= VariableRef | FunctionInstance

296.KillKeyword ::= "kill"

#### A.1.6.4.2	Port operations

297.CommunicationStatements ::= SendStatement |

CallStatement |

ReplyStatement |

RaiseStatement |

ReceiveStatement |

TriggerStatement |

GetCallStatement |

GetReplyStatement |

CatchStatement |

CheckStatement |

ClearStatement |

StartStatement |

StopStatement |

HaltStatement |

CheckStateStatement

298.SendStatement ::= ArrayIdentifierRef Dot PortSendOp

299.PortSendOp ::= SendOpKeyword "(" InLineTemplate ")" [ToClause]

300.SendOpKeyword ::= "send"

301.ToClause ::= ToKeyword (InLineTemplate |

AddressRefList |

AllKeyword ComponentKeyword

)

302.AddressRefList ::= "(" InLineTemplate {"," InLineTemplate} ")"

303.ToKeyword ::= "to"

304.CallStatement ::= ArrayIdentifierRef Dot PortCallOp [PortCallBody]

305.PortCallOp ::= CallOpKeyword "(" CallParameters ")" [ToClause]

306.CallOpKeyword ::= "call"

307.CallParameters ::= InLineTemplate ["," CallTimerValue]

308.CallTimerValue ::= Expression | NowaitKeyword

309.NowaitKeyword ::= "nowait"

310.PortCallBody ::= "{" CallBodyStatementList "}"

311.CallBodyStatementList ::= {CallBodyStatement [SemiColon]}+

312.CallBodyStatement ::= CallBodyGuard StatementBlock

313.CallBodyGuard ::= AltGuardChar CallBodyOps

314.CallBodyOps ::= GetReplyStatement | CatchStatement

315.ReplyStatement ::= ArrayIdentifierRef Dot PortReplyOp

316.PortReplyOp ::= ReplyKeyword "(" InLineTemplate [ReplyValue] ")" [ToClause]

317.ReplyKeyword ::= "reply"

318.ReplyValue ::= ValueKeyword Expression

319.RaiseStatement ::= ArrayIdentifierRef Dot PortRaiseOp

320.PortRaiseOp ::= RaiseKeyword "(" Signature "," InLineTemplate ")"

[ToClause]

321.RaiseKeyword ::= "raise"

322.ReceiveStatement ::= PortOrAny Dot PortReceiveOp

323.PortOrAny ::= ArrayIdentifierRef | AnyKeyword PortKeyword

324.PortReceiveOp ::= ReceiveOpKeyword ["(" InLineTemplate ")"] [FromClause]

[PortRedirect]

325.ReceiveOpKeyword ::= "receive"

326.FromClause ::= FromKeyword (InLineTemplate |

AddressRefList |

AnyKeyword ComponentKeyword

)

327.FromKeyword ::= "from"

328.PortRedirect ::= PortRedirectSymbol (ValueSpec [SenderSpec] | SenderSpec)

329.PortRedirectSymbol ::= "->"

330.ValueSpec ::= ValueKeyword (VariableRef | ("(" SingleValueSpec {","

SingleValueSpec}

")"))

331.SingleValueSpec ::= VariableRef [AssignmentChar FieldReference ExtendedFieldReference] 

/*STATIC SEMANTICS – FieldReference shall not be ParRef and ExtendedFieldReference shall not be TypeDefIdentifier*/

332.ValueKeyword ::= "value"

333.SenderSpec ::= SenderKeyword VariableRef

334.SenderKeyword ::= "sender"

335.TriggerStatement ::= PortOrAny Dot PortTriggerOp

336.PortTriggerOp ::= TriggerOpKeyword ["(" InLineTemplate ")"] [FromClause]

[PortRedirect]

337.TriggerOpKeyword ::= "trigger"

338.GetCallStatement ::= PortOrAny Dot PortGetCallOp

339.PortGetCallOp ::= GetCallOpKeyword ["(" InLineTemplate ")"] [FromClause]

[PortRedirectWithParam]

340.GetCallOpKeyword ::= "getcall"

341.PortRedirectWithParam ::= PortRedirectSymbol RedirectWithParamSpec

342.RedirectWithParamSpec ::= ParamSpec [SenderSpec] | SenderSpec

343.ParamSpec ::= ParamKeyword ParamAssignmentList

344.ParamKeyword ::= "param"

345.ParamAssignmentList ::= "(" (AssignmentList | VariableList) ")"

346.AssignmentList ::= VariableAssignment {"," VariableAssignment}

347.VariableAssignment ::= VariableRef AssignmentChar Identifier

348.VariableList ::= VariableEntry {"," VariableEntry}

349.VariableEntry ::= VariableRef | Minus

350.GetReplyStatement ::= PortOrAny Dot PortGetReplyOp

351.PortGetReplyOp ::= GetReplyOpKeyword ["(" InLineTemplate [ValueMatchSpec]

")"] [FromClause] [PortRedirectWithValueAndParam]

352.PortRedirectWithValueAndParam ::= PortRedirectSymbol RedirectWithValueAndParamSpec

353.RedirectWithValueAndParamSpec ::= ValueSpec [ParamSpec] [SenderSpec] |

RedirectWithParamSpec

354.GetReplyOpKeyword ::= "getreply"

355.ValueMatchSpec ::= ValueKeyword InLineTemplate

356.CheckStatement ::= PortOrAny Dot PortCheckOp

357.PortCheckOp ::= CheckOpKeyword ["(" CheckParameter ")"]

358.CheckOpKeyword ::= "check"

359.CheckParameter ::= CheckPortOpsPresent |

FromClausePresent |

RedirectPresent

360.FromClausePresent ::= FromClause [PortRedirectSymbol SenderSpec]

361.RedirectPresent ::= PortRedirectSymbol SenderSpec

362.CheckPortOpsPresent ::= PortReceiveOp |

PortGetCallOp |

PortGetReplyOp |

PortCatchOp

363.CatchStatement ::= PortOrAny Dot PortCatchOp

364.PortCatchOp ::= CatchOpKeyword ["(" CatchOpParameter ")"] [FromClause]

[PortRedirect]

365.CatchOpKeyword ::= "catch"

366.CatchOpParameter ::= Signature "," InLineTemplate | TimeoutKeyword

367.ClearStatement ::= PortOrAll Dot ClearOpKeyword

368.PortOrAll ::= ArrayIdentifierRef | AllKeyword PortKeyword

369.ClearOpKeyword ::= "clear"

370.StartStatement ::= PortOrAll Dot StartKeyword

371.StopStatement ::= PortOrAll Dot StopKeyword

372.StopKeyword ::= "stop"

373.HaltStatement ::= PortOrAll Dot HaltKeyword

374.HaltKeyword ::= "halt"

375.AnyKeyword ::= "any"

376.CheckStateStatement ::= PortOrAllAny Dot CheckStateKeyword "(" SingleExpression ")"

377.PortOrAllAny ::= PortOrAll | AnyKeyword PortKeyword

378.CheckStateKeyword ::= "checkstate"

#### A.1.6.4.3	Timer operations

379.TimerStatements ::= StartTimerStatement |

StopTimerStatement |

TimeoutStatement

380.TimerOps ::= ReadTimerOp | RunningTimerOp

381.StartTimerStatement ::= ArrayIdentifierRef Dot StartKeyword ["(" Expression

")"]

382.StopTimerStatement ::= TimerRefOrAll Dot StopKeyword

383.TimerRefOrAll ::= ArrayIdentifierRef | AllKeyword TimerKeyword

384.ReadTimerOp ::= ArrayIdentifierRef Dot ReadKeyword

385.ReadKeyword ::= "read"

386.RunningTimerOp ::= TimerRefOrAny Dot RunningKeyword

387.TimeoutStatement ::= TimerRefOrAny Dot TimeoutKeyword

388.TimerRefOrAny ::= ArrayIdentifierRef | (AnyKeyword TimerKeyword)

389.TimeoutKeyword ::= "timeout"

#### A.1.6.4.4	Testcase operation

390.TestcaseOperation ::= TestcaseKeyword "." StopKeyword ["(" {(FreeText |

InLineTemplate)

[","]}

")"]

### A.1.6.5	Type

391.Type ::= PredefinedType | ReferencedType

392.PredefinedType ::= BitStringKeyword |

BooleanKeyword |

CharStringKeyword |

UniversalCharString |

IntegerKeyword |

OctetStringKeyword |

HexStringKeyword |

VerdictTypeKeyword |

FloatKeyword |

AddressKeyword |

DefaultKeyword |

AnyTypeKeyword

393.BitStringKeyword ::= "bitstring"

394.BooleanKeyword ::= "boolean"

395.IntegerKeyword ::= "integer"

396.OctetStringKeyword ::= "octetstring"

397.HexStringKeyword ::= "hexstring"

398.VerdictTypeKeyword ::= "verdicttype"

399.FloatKeyword ::= "float"

400.AddressKeyword ::= "address"

401.DefaultKeyword ::= "default"

402.AnyTypeKeyword ::= "anytype"

403.CharStringKeyword ::= "charstring"

404.UniversalCharString ::= UniversalKeyword CharStringKeyword

405.UniversalKeyword ::= "universal"

406.ReferencedType ::= ExtendedIdentifier [ExtendedFieldReference]

407.TypeReference ::= Identifier

408.ArrayDef ::= {"[" SingleExpression [".." SingleExpression] "]"}+ 

/* STATIC SEMANTICS - ArrayBounds will resolve to a non negative value of integer type */

### A.1.6.6	Value

409.Value ::= PredefinedValue | ReferencedValue

410.PredefinedValue ::= Bstring |

BooleanValue |

CharStringValue |

Number | /* IntegerValue */

Ostring |

Hstring |

VerdictTypeValue |

Identifier | /* EnumeratedValue */

FloatValue |

AddressValue |

OmitKeyword

411.BooleanValue ::= "true" | "false"

412.VerdictTypeValue ::= "pass" |

"fail" |

"inconc" |

"none" |

"error"

413.CharStringValue ::= Cstring | Quadruple

414.Quadruple ::= CharKeyword "(" Number "," Number "," Number "," Number

")"

415.CharKeyword ::= "char"

416.FloatValue ::= FloatDotNotation |

FloatENotation |

NaNKeyword

417.NaNKeyword ::= "not_a_number"

418.FloatDotNotation ::= Number Dot DecimalNumber

419.FloatENotation ::= Number [Dot DecimalNumber] Exponential [Minus]

Number

420.Exponential ::= "E"

421.ReferencedValue ::= ExtendedIdentifier [ExtendedFieldReference]

422.Number ::= (NonZeroNum {Num}) | "0"

423.NonZeroNum ::= "1" | "2" | "3" | "4" | "5" | "6" | "7" | "8" | "9"

424.DecimalNumber ::= {Num}+

425.Num ::= "0" | NonZeroNum

426.Bstring ::= "'" {Bin} "'" "B"

427.Bin ::= "0" | "1"

428.Hstring ::= "'" {Hex} "'" "H"

429.Hex ::= Num | "A" | "B" | "C" | "D" | "E" | "F" | "a" | "b" | "c" |

"d" | "e" | "f"

430.Ostring ::= "'" {Oct} "'" "O"

431.Oct ::= Hex Hex

432.Cstring ::= """ {Char} """

433.Char ::= /* REFERENCE - A character defined by the relevant CharacterString type. For charstring a character from the character set defined in ITU-T T.50. For universal charstring a character from any character set defined in ISO/IEC 10646 */

434.Identifier ::= Alpha {AlphaNum | Underscore}

435.Alpha ::= UpperAlpha | LowerAlpha

436.AlphaNum ::= Alpha | Num

437.UpperAlpha ::= "A" | "B" | "C" | "D" | "E" | "F" | "G" | "H" | "I" |

"J" | "K" | "L" | "M" | "N" | "O" | "P" | "Q" | "R" |

"S" | "T" | "U" | "V" | "W" | "X" | "Y" | "Z"

438.LowerAlpha ::= "a" | "b" | "c" | "d" | "e" | "f" | "g" | "h" | "i" |

"j" | "k" | "l" | "m" | "n" | "o" | "p" | "q" | "r" |

"s" | "t" | "u" | "v" | "w" | "x" | "y" | "z"

439.ExtendedAlphaNum ::= /* REFERENCE - A graphical character from the BASIC LATIN or from the LATIN-1 SUPPLEMENT character sets defined in ISO/IEC 10646 (characters from char (0,0,0,32) to char (0,0,0,126), from char (0,0,0,161) to char (0,0,0,172) and from char (0,0,0,174) to char (0,0,0,255) */

440.FreeText ::= """ {ExtendedAlphaNum} """

441.AddressValue ::= "null"

442.OmitKeyword ::= "omit"

### A.1.6.7	Parameterization

443.InParKeyword ::= "in"

444.OutParKeyword ::= "out"

445.InOutParKeyword ::= "inout"

446.FormalValuePar ::= [(InParKeyword |

InOutParKeyword |

OutParKeyword

)] [LazyModifier | FuzzyModifier] Type Identifier [":=" (Expression | Minus)]

447.FormalPortPar ::= [InOutParKeyword] Identifier Identifier 

/* The first Identifier refers to the port type. The second Identifier refers to the port parameter identifier */

448.FormalTimerPar ::= [InOutParKeyword] TimerKeyword Identifier

449.FormalTemplatePar ::= [(InParKeyword |

OutParKeyword |

InOutParKeyword

)] (TemplateKeyword | RestrictedTemplate)

[LazyModifier | FuzzyModifier] Type

Identifier [":=" (InLineTemplate | Minus)]

450.RestrictedTemplate ::= OmitKeyword | (TemplateKeyword TemplateRestriction)

451.TemplateRestriction ::= "(" (OmitKeyword |

ValueKeyword |

PresentKeyword

) ")"

### A.1.6.8	Statements

#### A.1.6.8.1	With statement

452.WithStatement ::= WithKeyword WithAttribList

453.WithKeyword ::= "with"

454.WithAttribList ::= "{" MultiWithAttrib "}"

455.MultiWithAttrib ::= {SingleWithAttrib [SemiColon]}

456.SingleWithAttrib ::= AttribKeyword [OverrideKeyword] [AttribQualifier]

FreeText

457.AttribKeyword ::= EncodeKeyword |

VariantKeyword |

DisplayKeyword |

ExtensionKeyword |

OptionalKeyword

458.EncodeKeyword ::= "encode"

459.VariantKeyword ::= "variant"

460.DisplayKeyword ::= "display"

461.ExtensionKeyword ::= "extension"

462.OverrideKeyword ::= "override"

463.AttribQualifier ::= "(" DefOrFieldRefList ")"

464.DefOrFieldRefList ::= DefOrFieldRef {"," DefOrFieldRef}

465.DefOrFieldRef ::= QualifiedIdentifier |

( (FieldReference | "[" Minus "]" ) [ExtendedFieldReference] ) |                       
                       AllRef

466.QualifiedIdentifier ::= { Identifier Dot } Identifier

467.AllRef ::= (GroupKeyword AllKeyword [ExceptKeyword "{" QualifiedIdentifierList

"}"]) | ((TypeDefKeyword |

TemplateKeyword |

ConstKeyword |

AltstepKeyword |

TestcaseKeyword |

FunctionKeyword |

SignatureKeyword |

ModuleParKeyword

) AllKeyword [ExceptKeyword

"{" IdentifierList

"}"])

#### A.1.6.8.2	Behaviour statements

468.BehaviourStatements ::= TestcaseInstance |

FunctionInstance |

ReturnStatement |

AltConstruct |

InterleavedConstruct |

LabelStatement |

GotoStatement |

RepeatStatement |

DeactivateStatement |

AltstepInstance |

ActivateOp |

BreakStatement |

ContinueStatement

469.SetLocalVerdict ::= SetVerdictKeyword "(" SingleExpression {"," LogItem}

")"

470.SetVerdictKeyword ::= "setverdict"

471.GetLocalVerdict ::= "getverdict"

472.SUTStatements ::= ActionKeyword "(" ActionText {StringOp ActionText}

")"

473.ActionKeyword ::= "action"

474.ActionText ::= FreeText | Expression

475.ReturnStatement ::= ReturnKeyword [Expression | InLineTemplate] 

/* STATIC SEMANTICS - Expression shall evaluate to a value of a type compatible with the return type for functions returning a value. It shall evaluate to a value, template (literal or template instance), or a matching mechanism compatible with the return type for functions returning a template. */

476.AltConstruct ::= AltKeyword "{" AltGuardList "}"

477.AltKeyword ::= "alt"

478.AltGuardList ::= {GuardStatement | ElseStatement [SemiColon]}

479.GuardStatement ::= AltGuardChar (AltstepInstance [StatementBlock] |

GuardOp StatementBlock)

480.ElseStatement ::= "[" ElseKeyword "]" StatementBlock

481.AltGuardChar ::= "[" [BooleanExpression] "]"

482.GuardOp ::= TimeoutStatement |

ReceiveStatement |

TriggerStatement |

GetCallStatement |

CatchStatement |

CheckStatement |

GetReplyStatement |

DoneStatement |

KilledStatement

483.InterleavedConstruct ::= InterleavedKeyword "{" InterleavedGuardList

"}"

484.InterleavedKeyword ::= "interleave"

485.InterleavedGuardList ::= {InterleavedGuardElement [SemiColon]}+

486.InterleavedGuardElement ::= InterleavedGuard StatementBlock

487.InterleavedGuard ::= "[" "]" GuardOp

488.LabelStatement ::= LabelKeyword Identifier

489.LabelKeyword ::= "label"

490.GotoStatement ::= GotoKeyword Identifier

491.GotoKeyword ::= "goto"

492.RepeatStatement ::= "repeat"

493.ActivateOp ::= ActivateKeyword "(" AltstepInstance ")"

494.ActivateKeyword ::= "activate"

495.DeactivateStatement ::= DeactivateKeyword ["(" ComponentOrDefaultReference

")"]

496.DeactivateKeyword ::= "deactivate"

497.BreakStatement ::= "break"

498.ContinueStatement ::= "continue"

#### A.1.6.8.3	Basic statements

499.BasicStatements ::= Assignment |

LogStatement |

LoopConstruct |

ConditionalConstruct |

SelectCaseConstruct |

StatementBlock

500.Expression ::= SingleExpression | CompoundExpression

501.CompoundExpression ::= FieldExpressionList | ArrayExpression 

/* STATIC SEMANTICS - Within CompoundExpression the ArrayExpression can be used for Arrays, record, record of and set of types. */

502.FieldExpressionList ::= "{" FieldExpressionSpec {"," FieldExpressionSpec}

"}"

503.FieldExpressionSpec ::= FieldReference AssignmentChar NotUsedOrExpression

504.ArrayExpression ::= "{" [ArrayElementExpressionList] "}"

505.ArrayElementExpressionList ::= NotUsedOrExpression {"," NotUsedOrExpression}

506.NotUsedOrExpression ::= Expression | Minus

507.ConstantExpression ::= SingleExpression | CompoundConstExpression

508.BooleanExpression ::= SingleExpression 

/* STATIC SEMANTICS - BooleanExpression shall resolve to a Value of type Boolean */

509.CompoundConstExpression ::= FieldConstExpressionList | ArrayConstExpression 

/* STATIC SEMANTICS - Within CompoundConstExpression the ArrayConstExpression can be used for arrays, record, record of and set of types. */

510.FieldConstExpressionList ::= "{" FieldConstExpressionSpec {"," FieldConstExpressionSpec}

"}"

511.FieldConstExpressionSpec ::= FieldReference AssignmentChar ConstantExpression

512.ArrayConstExpression ::= "{" [ArrayElementConstExpressionList] "}"

513.ArrayElementConstExpressionList ::= ConstantExpression {"," ConstantExpression}

514.Assignment ::= VariableRef AssignmentChar (Expression | TemplateBody) 

/* STATIC SEMANTICS - The Expression on the right hand side of Assignment shall evaluate to an explicit value of a type compatible with the type of the left hand side for value variables and shall evaluate to an explicit value, template (literal or a template instance) or a matching mechanism compatible with the type of the left hand side for template variables. */

515.SingleExpression ::= XorExpression {"or" XorExpression} 

/* STATIC SEMANTICS - If more than one XorExpression exists, then the XorExpressions shall evaluate to specific values of compatible types */

516.XorExpression ::= AndExpression {"xor" AndExpression} 

/* STATIC SEMANTICS - If more than one AndExpression exists, then the AndExpressions shall evaluate to specific values of compatible types */

517.AndExpression ::= NotExpression {"and" NotExpression} 

/* STATIC SEMANTICS - If more than one NotExpression exists, then the NotExpressions shall evaluate to specific values of compatible types */

518.NotExpression ::= ["not"] EqualExpression 

/* STATIC SEMANTICS - Operands of the not operator shall be of type boolean or derivatives of type Boolean. */

519.EqualExpression ::= RelExpression {EqualOp RelExpression} 

/* STATIC SEMANTICS - If more than one RelExpression exists, then the RelExpressions shall evaluate to specific values of compatible types. If only one RelExpression exists, it shall not derive to a CompoundExpression.  */

520.RelExpression ::= ShiftExpression [RelOp ShiftExpression] | CompoundExpression

/* STATIC SEMANTICS - If both ShiftExpressions exist, then each ShiftExpression shall evaluate to a specific integer, Enumerated or float Value or derivatives of these types */

521.ShiftExpression ::= BitOrExpression {ShiftOp BitOrExpression} 

/* STATIC SEMANTICS - Each Result shall resolve to a specific Value. If more than one Result exists the right-hand operand shall be of type integer or derivatives and if the shift op is "<<" or ">>" then the left-hand operand shall resolve to either bitstring, hexstring or octetstring type or derivatives of these types. If the shift op is " */

522.BitOrExpression ::= BitXorExpression {"or4b" BitXorExpression} 

/* STATIC SEMANTICS - If more than one BitXorExpression exists, then the BitXorExpressions shall evaluate to specific values of compatible types */

523.BitXorExpression ::= BitAndExpression {"xor4b" BitAndExpression} 

/* STATIC SEMANTICS - If more than one BitAndExpression exists, then the BitAndExpressions shall evaluate to specific values of compatible types */

524.BitAndExpression ::= BitNotExpression {"and4b" BitNotExpression} 

/* STATIC SEMANTICS - If more than one BitNotExpression exists, then the BitNotExpressions shall evaluate to specific values of compatible types */

525.BitNotExpression ::= ["not4b"] AddExpression 

/* STATIC SEMANTICS - If the not4b operator exists, the operand shall be of type bitstring, octetstring or hexstring or derivatives of these types. */

526.AddExpression ::= MulExpression {AddOp MulExpression} 

/* STATIC SEMANTICS - Each MulExpression shall resolve to a specific Value. If more than one MulExpression exists and the AddOp resolves to StringOp then the MulExpressions shall be valid operands for StringOp. If more than one MulExpression exists and the AddOp does not resolve to StringOp then the MulExpression shall both resolve to type integer or float or derivatives of these types. If only one MulExpression exists, it shall not derive to a CompoundExpression. */

527.MulExpression ::= UnaryExpression {MultiplyOp UnaryExpression} | CompoundExpression

/* STATIC SEMANTICS - Each UnaryExpression shall resolve to a specific Value. If more than one UnaryExpression exists then the UnaryExpressions shall resolve to type integer or float or derivatives of these types. */

528.UnaryExpression ::= [UnaryOp] Primary 

/* STATIC SEMANTICS - Primary shall resolve to a specific Value of type integer or float or derivatives of these types.*/

529.Primary ::= OpCall |

Value |

"(" SingleExpression ")"

530.ExtendedFieldReference ::= {(Dot ( Identifier | PredefinedType)) |

ArrayOrBitRef |

("[" Minus "]")

}+ 

/* STATIC SEMANTIC - The Identifier refers to a type definition if the type of the VarInstance or ReferencedValue in which the ExtendedFieldReference is used is anytype. ArrayOrBitRef shall be used when referencing elements of values or arrays. The square brackets with dash shall be used when referencing inner types of a record of or set of type. */

531.OpCall ::= ConfigurationOps |

GetLocalVerdict |

TimerOps |

TestcaseInstance |

(FunctionInstance [ExtendedFieldReference]) |

(TemplateOps [ExtendedFieldReference]) |

ActivateOp

532.AddOp ::= "+" |

"-" |

StringOp 

/* STATIC SEMANTICS - Operands of the "+" or "-" operators shall be of type integer or float or derivations of integer or float (i.e. subrange) */

533.MultiplyOp ::= "*" | "/" | "mod" | "rem" 

/* STATIC SEMANTICS - Operands of the "*", "/", rem or mod operators shall be of type integer or float or derivations of integer or float (i.e. subrange) */

534.UnaryOp ::= "+" | "-" 

/* STATIC SEMANTICS - Operands of the "+" or "-" operators shall be of type integer or float or derivations of integer or float (i.e. subrange) */

535.RelOp ::= "<" | ">" | ">=" | "<=" 

/* STATIC SEMANTICS - the precedence of the operators is defined in Table 6 */

536.EqualOp ::= "==" | "!="

537.StringOp ::= "&" 

/* STATIC SEMANTICS - Operands of the list operator shall be bitstring, hexstring, octetstring, (universal) character string, record of, set of, or array types, or derivates of these types */

538.ShiftOp ::= "<<" | ">>" | "<@" | "@>"

539.LogStatement ::= LogKeyword "(" LogItem {"," LogItem} ")"

540.LogKeyword ::= "log"

541.LogItem ::= FreeText | InLineTemplate

542.LoopConstruct ::= ForStatement |

WhileStatement |

DoWhileStatement

543.ForStatement ::= ForKeyword "(" Initial SemiColon BooleanExpression

SemiColon Assignment ")" StatementBlock

544.ForKeyword ::= "for"

545.Initial ::= VarInstance | Assignment

546.WhileStatement ::= WhileKeyword "(" BooleanExpression ")" StatementBlock

547.WhileKeyword ::= "while"

548.DoWhileStatement ::= DoKeyword StatementBlock WhileKeyword "(" BooleanExpression

")"

549.DoKeyword ::= "do"

550.ConditionalConstruct ::= IfKeyword "(" BooleanExpression ")" StatementBlock

{ElseIfClause} [ElseClause]

551.IfKeyword ::= "if"

552.ElseIfClause ::= ElseKeyword IfKeyword "(" BooleanExpression ")" StatementBlock

553.ElseKeyword ::= "else"

554.ElseClause ::= ElseKeyword StatementBlock

555.SelectCaseConstruct ::= SelectKeyword "(" SingleExpression ")" SelectCaseBody

556.SelectKeyword ::= "select"

557.SelectCaseBody ::= "{" {SelectCase}+ "}"

558.SelectCase ::= CaseKeyword ("(" InLineTemplate {"," InLineTemplate}

")" | ElseKeyword) StatementBlock

559.CaseKeyword ::= "case"

560.ExtendedIdentifier ::= [Identifier Dot] Identifier

561.IdentifierList ::= Identifier {"," Identifier}

562.QualifiedIdentifierList ::= QualifiedIdentifier {"," QualifiedIdentifier}

### A.1.6.9	Miscellaneous productions

563.Dot ::= "."

564.Minus ::= "-"

565.SemiColon ::= ";"

566.Colon ::= ":"

567.Underscore ::= "_"

568.AssignmentChar ::= ":="

LazyModifier ::= "@lazy"

FuzzyModifier ::= "@fuzzy"

# Comments

Ii think it is covered by the above amended definition.

this goes to CR6422, we should not confuse the editor by having it twice in different CRs.

Not needed, given in the definitions.

For me the reason of this restriction is unclear. I think that the fields of fuzzy variables can be filled up dynamically before its first use at the RHS, just like any other variables.

Restriction removed

The same question as for value fuzzy variables.

Also deleted

This is in the definition

moved to a definition

added Gyorgy also causes side effect at the first use.

Moved to clause 16.1.

deleted

What is the sense of this? This would cause loss of tool performance and complicates feature for the user without obvoius benefit. For lazy it would just have reverse effect, re-evaluationg all fields all the time, that would not been re-evaluated for an ordinary variable or parameter. For fuzzy it causes one semi-random is number is skipped each time a field is initialized that may make the tests unrepeatable.

Why this restriction is needed?

deleted

To be put to CR 6622.