Annex B (normative):
Encoding instructions

## B.3.28	XML header control

Syntactical structure(s)

"noXmlHeader"|"xmlHeader"

Applicable to (TTCN-3)

See description below.

Description

This encoding instruction is not applied to TTCN-3 definitions as a variant attribute but to the encoding or decoding process, when it is invoked by the encvalue, decvalue, encvalue_unichar and decvalue_unichar predefined functions (see clause C.5 of ES 201 873-1 [1]). The encoding instruction shall be passed to the encoding or decoding process in the encoding_info and decoding_info parameters appropriately. The default value of this encoding instruction is "xmlHeader", i.e. in case of XML encoding this default value overrides the default value "" defined in ES 201 873-1 [1].

At encoding the instruction controls the presence of the XML prolog, specified in clause 2.8 of the XML 1.1 specification [5], the xsi:schemalocation and namespace specification attributes in the encoded XML value. If its value is "noXmlHeader", neither the XML prolog nor the schemalocation attribute shall be present. Namespace specification (the xmlns attribute) shall be included, if the namespace of the elements to be encoded is specified (by inheriting the "namespace as" encoding instruction from a higher scope unit or it being applied directly; a directly applied instruction takes precedence) (see clause B.3.14	Namespace identification of the present document). If the value is "xmlHeader" – specified directly or by defaulting to it – a complete valid XML documents shall be produced.

At decoding the "noXmlHeader" value instructs the decoder to accept and decode the received XML value as an XML 1.1 document, even without the XML prolog specified in clause 2.8 of the XML 1.1 specification [5], provided all further information (e.g. namespace prefixes and their values) are available for the decoding process. Note that the value "noXmlHeader" has no effect when a complete XML 1.1 document is passed for decoding. The "xmlHeader" value has no effect on the decoding process (i.e. the XML value shall be decoded according to the XML well-formedness and validation rules).